## Slide 1
Constructive Computer Architecture
Sequential Circuits
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Combinational circuits
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
Sel
O0
O1
On-1
A
Demux
.
.
.
lg(n)
A
Decoder
.
.
.
O0
O1
On-1
lg(n)
Such circuits have no cycles (feedback) or state elements

## Slide 3: Flip flop: The basic building block of Sequential Circuits
ff
Q
D
C
C
D
Q
Metastability
Data is sampled at the rising edge of the clock
Edge-Triggered Flip-flop
Notes: Metastability?

## Slide 4: Flip-flops with Write Enables
ff
Q
D
C
EN
C
D
Q
EN
ff
Q
D
C
EN
0
1
ff
Q
D
C
EN
dangerous!
Data is captured only if EN is on
Notes: Why dangerous?
Glitches

## Slide 5: Registers
Register: A group of flip-flops with a common
clock and enable
Register file: A group of registers with a common
clock, input and output port(s)
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
Q
Q
Q
Q
Q
Q
Q
Q
D
C
En

## Slide 6: An example Modulo-4 counter
Prev State | NextState | 
q1q0 | inc = 0 | inc = 1
00 | 00 | 01
01 | 01 | 10
10 | 10 | 11
11 | 11 | 00
q0t+1 = ~inc∙q0t + inc∙~q0t
q1t+1 = ~inc∙q1t + inc∙~q1t∙q0t + inc∙q1t∙~q0t
00
01
10
11
inc=1
inc=1
inc=1
inc=1
inc=0
inc=0
inc=0
inc=0

## Slide 7: Modulo-4 counter circuit
Modulo-4
counter
inc
Read the
counter
q0t+1 = ~inc∙q0t + inc∙~q0t
q1t+1 = ~inc∙q1t + inc∙~q1t∙q0t + inc∙q1t∙~q0t
“Optimized” logic
q0t+1 = inc  q0t
q1t+1 = (inc == 1) ? q0t  q1t : q1t
q0
inc
1
0
q1

## Slide 8: Finite State Machines (Sequential Ckts)
A computer (in fact all digital hardware) is an FSM
Neither State tables nor diagrams is suitable for describing very large digital designs
  large circuits must be described in a modular fashion -- as a collection of cooperating FSMs
BSV is a modern programming language to describe cooperating FSMs
  We will give various examples of FSMs in BSV

## Slide 9: modulo4 counter in BSV
module moduloCounter(Counter);
Reg#(Bit#(2)) cnt <- mkReg(0);
method Action inc;
cnt <={~cnt[1]&cnt[0] | cnt[1]&~cnt[0],
~cnt[0]};
endmethod
method Bit#(2) read;
return cnt;
endmethod
endmodule
~cnt[1]&…
inc.en
read
cnt
Can be replaced by cnt+1

## Slide 10: Interface
Modulo counter has the following interface, i.e., type
An interface can have many different implementations
  For example, the numbers may be represented as Gray code.
interface Counter;
method Action inc;
method Bit#(2) read;
endinterface

## Slide 11: FIFO Interface
interface Fifo#(numeric type size, type t);
method Bool notFull;
method Bool notEmpty;
method Action enq(t x);
method Action deq;
method t first;
endinterface
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first

## Slide 12: One-Element FIFO Implementation
module mkCFFifo (Fifo#(1, t));
Reg#(t) data <- mkRegU;
Reg#(Bool) full <- mkReg(False);
method Bool notFull;
return !full;
endmethod
method Bool notEmpty;
return full;
endmethod
method Action enq(t x);
full <= True; data <= x;
endmethod
method Action deq;
full <= False;
endmethod
method t first;
return data;
endmethod
endmodule
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first

## Slide 13: Two-Element FIFO
module mkCFFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False);
method Bool notFull; return !vb; endmethod
method Bool notEmpty; return va; endmethod
method Action enq(t x);
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
method t first; return da; endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
db da
no change in fifo interface
parallel composition of actions

## Slide 14: Switch
if (inQ.first.color == Red) begin
redQ.enq(inQ.first.value); inQ.deq;
end else begin
greenQ.enq(inQ.first.value); inQ.deq;
end
inQ
redQ
greenQ
let x = inQ.first;
if (x.color == Red) redQ.enq(x.value);
else greenQ.enq(x.value);
inQ.deq;
parallel composition of actions. Effect of inQ.deq is not visible to inQ.first
The code does not deal with empty inQ or full redQ or full greenQ conditions!
Notes: Effect of inQ.deq is not visible to inQ.first

## Slide 15: Switch with empty/full tests on queues
if (inQ.notEmpty) begin
if (inQ.first.color == Red) begin
if (redQ.notFull) begin
redQ.enq(inQ.first.value); inQ.deq;
end
end else begin
if (greenQ.notFull) begin
greenQ.enq(inQ.first.value); inQ.deq;
end
end
end
What’s wrong if the deq is moved here?
inQ
redQ
greenQ

## Slide 16: Switch with counters
if (inQ.first.color == Red) begin
redQ.enq(inQ.first.value); inQ.deq;
redC <= redC+1;
end else begin
greenQ.enq(inQ.first.value); inQ.deq;
greenC <= greenC+1;
end
redC
greenC
Ignoring full/empty conditions
inQ
redQ
greenQ

## Slide 17: Shared counters
redC
greenC
if (inQA.first.color == Red) begin
redQA.enq(inQA.first.value);
inQA.deq; redC <= redC+1;
end else begin
greenQA.enq(inQA.first.value);
inQA.deq; greenC <= greenC+1;
end
if (inQB.first.color == Red) begin
redQB.enq(inQB.first.value);
inQB.deq; redC <= redC+1;
end else begin
greenQB.enq(inQB.first.value);
inQB.deq; greenC <= greenC+1;
end
What is wrong with this code?
Double write error
Ignoring full/empty conditions
inQA
redQA
greenQA
inQB
redQB
greenQB

## Slide 18: Double-write problem
Parallel composition is illegal if a double-write possibility exists
If the BSV compiler cannot prove that the predicates for writes into a register or a method call are mutually exclusive, it rejects the program

## Slide 19: Observations
These programs are not very complex and yet it would have been tedious to express these programs in a state table or as a circuit directly
BSV method calls are not available in Verilog/VHDL, and thus such programs sometimes require tedious programming
Even the meaning of double-write errors is not standardized across tool implementations in Verilog