## Slide 1
Constructive Computer Architecture:
Data Hazards
in Pipelined Processors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Delivered by Andy Wright

## Slide 2: Data Hazard
Data hazard depends upon the match between the source registers of the fetched instruction and the destination register of an instruction already in the pipeline
Both the source and destination registers must be Valid for a hazard to exist
function Bool isFound
(Maybe#(FullIndx) x, Maybe#(FullIndx) y);
if(x matches Valid .xv &&& y matches Valid .yv
&&& yv == xv) return True; else return False;
endfunction

## Slide 3: Scoreboard: Keeping track of instructions in execution
Scoreboard: a data structure to keep track of the destination registers of the instructions beyond the fetch stage
  method insert: inserts the destination (if any) of an instruction in the scoreboard when the instruction is decoded
  method search1(src): searches the scoreboard for a data hazard
  method search2(src): same as search1
  method remove: deletes the oldest entry when an instruction commits

## Slide 4: 2-Stage-DH pipeline: Scoreboard and Stall logic
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
d2e
redirect
fEpoch
eEpoch
pred
scoreboard
Notes: 4

## Slide 5: 2-Stage-DH pipeline corrected
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkFifo;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) execRedirect <- mkFifo;
Scoreboard#(1) sb <- mkScoreboard;
// contains only one slot because Execute
// can contain at most one instruction
rule doFetch …
rule doExecute …
Notes: 5

## Slide 6: 2-Stage-DH pipeline doFetch rule second attempt
rule doFetch; if(execRedirect.notEmpty) begin fEpoch <= !fEpoch; pc <= execRedirect.first;
execRedirect.deq; end else
begin let instF = iMem.req(pc);
let ppcF = nextAddrPredictor(pc); pc <= ppcF;
let dInst = decode(instF);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppcF,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); end
end endrule
What should happen to pc when Fetch stalls?
pc should change only when the instruction is enqueued in d2e

## Slide 7: 2-Stage-DH pipeline doFetch rule corrected
rule doFetch; if(execRedirect.notEmpty) begin fEpoch <= !fEpoch; pc <= execRedirect.first;
execRedirect.deq; end else
begin let instF = iMem.req(pc);
let ppcF = nextAddrPredictor(pc); pc <= ppcF;
let dInst = decode(instF);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppcF,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); end
end endrule
pc <= ppcF; end
To avoid structural hazards, scoreboard must allow two search ports

## Slide 8: 2-Stage-DH pipeline doExecute rule corrected
rule doExecute; let x = d2e.first;
let dInstE = x.dInst; let pcE = x.pc;
let ppcE = x.ppc; let epoch = x.epoch;
let rVal1E = x.rVal1; let rVal2E = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInstE, rVal1E, rVal2E, pcE, ppcE); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst))
rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin execRedirect.enq(eInst.addr); eEpoch <= !eEpoch; end end d2e.deq; sb.remove; endrule

## Slide 9: A correctness issues
If the search by Decode does not see an instruction in the scoreboard, then its effect must have taken place. This means that any updates to the register file by that instruction must be visible to the subsequent register reads 
  remove and wr should happen atomically
  search and rd1, rd2 should happen atomically
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
Fetch and Execute can execute in any order

## Slide 10: Concurrently executable Fetch and Execute
Case 1: doExecute < dofetch 
  rf: wr < rd (bypass rf)
  sb: remove < {search, insert}
  d2e: {first, deq} {<, CF} enq (pipelined or CF Fifo)
  redirect: enq {<, CF} {deq, first} (bypass or CF Fifo)
Case 2: doFetch < doExecute 
  rf: rd < wr (normal rf)
  sb: {search, insert} < remove
  d2e: enq {<, CF} {deq, first} (bypass or CF Fifo)
  redirect: {first, deq} {<, CF} enq (pipelined or CF Fifo)
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
which is better?

## Slide 11: Performance issues
To avoid a stall due to a RAW hazard between successive instructions
  sb: remove ? search
  rf: wr ? rd
To minimize stalls due to control hazards
  redirect: ?
What kind of fifo should be used for d2e ?
  Either a pipeline or CF fifo would do fine
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
<
<
  (bypass rf)
bypass fifo

## Slide 12: 2-Stage-DH pipeline with proper specification of Fifos, rf, scoreboard
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkPipelineFifo;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) execRedirect <- mkBypassFifo;
Scoreboard#(1) sb <- mkPipelineScoreboard;
// contains only one slot because Execute
// can contain at most one instruction
rule doFetch …
rule doExecute …
Can a destination register name appear more than once in the scoreboard ?
Notes: 12

## Slide 13: WAW hazards
If multiple instructions in the scoreboard can update the register which the current instruction wants to read, then the current instruction has to read the update for the youngest of those instructions
This is not a problem in our design because
  instructions are committed in order
  the RAW hazard for the instruction at the decode stage will remain as long as the any instruction with the required destination is present in sb
Notes: WAW – Write-after-write Hazard

## Slide 14: An alternative design for sb
Instead of keeping track of the destination of every instruction in the pipeline, we can associated a bit with every register to indicate if that register is the destination of some instruction in the pipeline
  Appropriate register bit is set when an instruction enters the execute stage and cleared when the instruction is committed
The design will not work if multiple instructions in the pipeline have the same destination
  don’t let an instruction with WAW hazard enter the pipeline

## Slide 15: Fetch rule to avoid WAW hazard
rule doFetch; if(execRedirect.notEmpty) begin fEpoch <= !fEpoch; pc <= execRedirect.first;
execRedirect.deq; end else
begin let instF = iMem.req(pc); let ppcF = nextAddrPredictor(pc); let dInst = decode(instF);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
|| sb.search3(dInst.dst);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppcF,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); pc <= ppcF; end
end endrule

## Slide 16: Summary
Instruction pipelining requires dealing with control and data hazards
Speculation is necessary to deal with control hazards
Data hazards are avoided by withholding instructions in the decode stage until the hazard disappears
Performance issues are subtle
  For instance, the value of having a bypass network depends on how frequently it is exercised by programs
  Bypassing necessarily increases combinational paths which can slow down the clock
next – module implementations and multistage pipelines

## Slide 17: Normal Register File
module mkRFile(RFile);
Vector#(32,Reg#(Data)) rfile <- replicateM(mkReg(0));
method Action wr(RIndx rindx, Data data);
if(rindx!=0) rfile[rindx] <= data;
endmethod
method Data rd1(RIndx rindx) = rfile[rindx];
method Data rd2(RIndx rindx) = rfile[rindx];
endmodule
{rd1, rd2} < wr
Notes: 17

## Slide 18: Bypass Register File using EHR
module mkBypassRFile(RFile);
Vector#(32,Ehr#(2, Data)) rfile <-
replicateM(mkEhr(0));
method Action wr(RIndx rindx, Data data);
if(rindex!=0) (rfile[rindex])[0] <= data;
endmethod
method Data rd1(RIndx rindx) = (rfile[rindx])[1];
method Data rd2(RIndx rindx) = (rfile[rindx])[1];
endmodule
wr < {rd1, rd2}
Notes: 18

## Slide 19: Bypass Register File with external bypassing
module mkBypassRFile(BypassRFile);
RFile rf <- mkRFile;
Fifo#(1, Tuple2#(RIndx, Data))
bypass <- mkBypassSFifo;
rule move;
begin rf.wr(bypass.first); bypass.deq end;
endrule
method Action wr(RIndx rindx, Data data);
if(rindex!=0) bypass.enq(tuple2(rindx, data));
endmethod
method Data rd1(RIndx rindx) =
return (!bypass.search1(rindx)) ? rf.rd1(rindx)
: bypass.read1(rindx);
method Data rd2(RIndx rindx) =
return (!bypass.search2(rindx)) ? rf.rd2(rindx)
: bypass.read2(rindx);
endmodule
wr < {rd1, rd2}
rf
move
rd
Notes: 19

## Slide 20: Scoreboard implementation using searchable Fifos
function Bool isFound
(Maybe#(RIndx) dst, Maybe#(RIndx) src);
return isValid(dst) && isValid(src) &&
(validValue(dst)==validValue(src));
endfunction
module mkCFScoreboard(Scoreboard#(size));
SFifo#(size, Maybe#(RIndx), Maybe#(RIndx))
f <- mkCFSFifo(isFound);
method insert = f.enq;
method remove = f.deq;
method search1 = f.search1;
method search2 = f.search2;
endmodule