## Slide 1
Constructive Computer Architecture
Caches-2
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Blocking vs. Non-Blocking cache
Blocking cache:
  At most one outstanding miss
  Cache must wait for memory to respond
  Cache does not accept requests in the meantime
Non-blocking cache:
  Multiple outstanding misses
  Cache can continue to process requests while waiting for memory to respond to misses
We will first design a write-back, Write-miss allocate, Direct-mapped, blocking cache

## Slide 3: Blocking Cache Interface
interface Cache; method Action req(MemReq r);
method ActionValue#(Data) resp;
method ActionValue#(MemReq) memReq;
method Action memResp(Line r);
endinterface
cache
req
resp
memReq
memResp
Processor
DRAM or next level cache
hitQ
mReqQ
mRespQ
missReq
status

## Slide 4: Interface dynamics
The cache either gets a hit and responds immediately, or it gets a miss, in which case it takes several steps to process the miss
Reading the response dequeues it
Requests and responses follow the FIFO order
Methods are guarded, e.g., the cache may not be ready to accept a request because it is processing a miss
A status register keeps track of the state of the cache while it is processing a miss
typedef enum {Ready, StartMiss, SendFillReq, WaitFillResp} CacheStatus deriving (Bits, Eq);

## Slide 5: Blocking Cache code structure
module mkCache(Cache); RegFile#(CacheIndex, Line) dataArray <-
mkRegFileFull; … rule startMiss … endrule;
method Action req(MemReq r) … endmethod; method ActionValue#(Data) resp … endmethod; method ActionValue#(MemReq) memReq … endmethod; method Action memResp(Line r) … endmethod; endmodule

## Slide 6: Extracting cache tags & index
Processor requests are for a single word but internal communications are in line sizes (2L words, typically L=2)
AddrSz = CacheTagSz + CacheIndexSz + LS + 2
Need getIdx, getTag, getOffset functions
tag index L 2
Cache size in bytes
Byte addresses
function CacheIndex getIdx(Addr addr) = truncate(addr>>4);
function Bit#(2) getOffset(Addr addr) = truncate(addr >> 2);
function CacheTag getTag(Addr addr) = truncateLSB(addr);
truncate = truncateMSB

## Slide 7: Blocking cache state elements
RegFile#(CacheIndex, Line) dataArray <- mkRegFileFull;
RegFile#(CacheIndex, Maybe#(CacheTag))
tagArray <- mkRegFileFull;
RegFile#(CacheIndex, Bool) dirtyArray <- mkRegFileFull;
Fifo#(1, Data) hitQ <- mkBypassFifo;
Reg#(MemReq) missReq <- mkRegU;
Reg#(CacheStatus) status <- mkReg(Ready);
Fifo#(2, MemReq) memReqQ <- mkCFFifo;
Fifo#(2, Line) memRespQ <- mkCFFifo;
CF Fifos are preferable because they provide better decoupling. An extra cycle here may not affect the performance by much
Tag and valid bits are kept together as a Maybe type

## Slide 8: Req method hit processing
method Action req(MemReq r) if(status == Ready);
let idx = getIdx(r.addr); let tag = getTag(r.addr);
Bit#(2) wOffset = truncate(r.addr >> 2);
let currTag = tagArray.sub(idx);
let hit = isValid(currTag)?
fromMaybe(?,currTag)==tag : False;
if(hit) begin
let x = dataArray.sub(idx);
if(r.op == Ld) hitQ.enq(x[wOffset]);
else begin x[wOffset]=r.data;
dataArray.upd(idx, x);
dirtyArray.upd(idx, True); end
else begin missReq <= r; status <= StartMiss; end
endmethod
It is straightforward to extend the cache interface to include a cacheline flush command
overwrite the appropriate word of the line

## Slide 9: Rest of the methods
method ActionValue#(Data) resp;
hitQ.deq;
return hitQ.first;
endmethod
method ActionValue#(MemReq) memReq;
memReqQ.deq;
return memReqQ.first;
endmethod
method Action memResp(Line r);
memRespQ.enq(r);
endmethod
Memory side methods

## Slide 10: Start-miss and Send-fill rules
rule startMiss(status == StartMiss);
let idx = getIdx(missReq.addr);
let tag=tagArray.sub(idx); let dirty=dirtyArray.sub(idx);
if(isValid(tag) && dirty) begin // write-back
let addr = {fromMaybe(?,tag), idx, 4'b0};
let data = dataArray.sub(idx);
memReqQ.enq(MemReq{op: St, addr: addr, data: data});
end
status <= SendFillReq;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule sendFillReq (status == SendFillReq);
memReqQ.enq(missReq); status <= WaitFillResp;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready

## Slide 11: Wait-fill rule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule waitFillResp(status == WaitFillResp);
let idx = getIdx(missReq.addr);
let tag = getTag(missReq.addr);
let data = memRespQ.first;
tagArray.upd(idx, Valid (tag));
if(missReq.op == Ld) begin
dirtyArray.upd(idx,False);dataArray.upd(idx, data);
hitQ.enq(data[wOffset]); end
else begin data[wOffset] = missReq.data;
dirtyArray.upd(idx,True); dataArray.upd(idx, data);
end
memRespQ.deq; status <= Ready;
endrule
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 12: Hit and miss performance
Hit
  Combinational read/write, i.e. 0-cycle response
  Requires req and resp methods to be concurrently schedulable, which in turn requires
  hitQ.enq < {hitQ.deq, hitQ.first}
  i.e., hitQ should be a bypass Fifo
Miss
  No evacuation: memory load latency plus combinational read/write
  Evacuation: memory store followed by memory load latency plus combinational read/write
Adding an extra cycle here and there in the miss case should not have a big negative performance impact

## Slide 13: Non-blocking cache
Requests have to be tagged because responses come out-of-order (OOO)
We will assume that all tags are unique and the processor is responsible for reusing tags properly
cache
req
resp
mReq
mResp
mReqQ
mRespQ
req proc
Out-of-Order
responses
Processor

## Slide 14: Non-blocking Cache
St
Q
Ld
Buff
W
Tag
Data
wbQ
mReqQ
mRespQ
hitQ
resp
req
An extra bit in the cache to indicate if the data for a line is present
load reqs waiting for data
Behavior to be described by 2 concurrent FSMs to process input requests and memory responses, respectively
St req goes into StQ and waits until data can be written into the cache
D
V
Notes: 14

## Slide 15: Incoming req
Type of request
Put in StQ
send memReq
set W
If (evacuate)
send wbResp
In StQ?
bypass hit
Cache state V?
hit
st
ld
yes
no
no
no
Cache state W?
Put in StQ
yes
Put in LdBuf
Cache W?
yes
no
Put in LdBuf
send memReq
set W
If (evacuate)
send wbResp
cache state V?
yes
no
Write in cache
yes
StQ empty?
yes
no
Put in StQ

## Slide 16: Mem Resp (line)
1. Update cache line (set V and unset W)
2. Process all matching ldBuff entries and send responses
3. L: If cachestate(oldest StQ entry address) = V
then
update the cache word with StQ entry;
remove the oldest entry;
Loop back to L
else if cachestate(oldest StQ entry address) = !W
then if(evacuate) wbResp;
memReq for this store entry;
set W