## Slide 1
Constructive Computer Architecture
Cache Coherence
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Shared Memory Systems
M
L1
P
L1
P
L1
P
L1
P
L2
L2
L1
P
L1
P
Interconnect
Modern systems often have hierarchical caches
Each cache has exactly one parent but can have zero or more children
Logically only a parent and its children can communicate directly
Inclusion property is maintained between a parent and its children, i.e.,
a  Li  a  Li+1
Because usually
Li+1 >> Li

## Slide 3: Cache-coherence problem
Suppose CPU-1 updates A to 200.
  write-back: memory and cache-2 have stale values
  write-through: cache-2 has a stale value
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100
200
200
Do these stale values matter?
What is the view of shared memory for programming?

## Slide 4: Cache-Coherent Memory
A monolithic or instantaneous memory processes one request at a time and responds to requests immediately
A memory with hierarchy of caches is said to be coherent or atomic, if functionally it behaves like the monolithic memory
req
res
req
res
Monolithic Memory
...

## Slide 5: Maintaining Store Atomicity
Store atomicity requires all processors to see writes occur in the same order
  multiple copies of an address in various caches can cause this to be violated
This property can be ensured if:
  Only one cache at a time has the write permission for an address
  No cache can have a stale copy of the data after a write to the address has been performed
      cache coherence protocols are used
      to implement store atomicity

## Slide 6: Cache Coherence Protocols
Write request:
  the address is invalidated in all other caches before the write is performed
Read request:
  if a dirty copy is found in some cache, that value must be used by doing a write-back and then reading the memory or forwarding that dirty value directly to the reader
Such protocols are called Invalidation-based

## Slide 7: State needed to maintain Cache Coherence
Use MSI encoding in caches where
  I means this cache does not contain the address
  S means this cache has the address but so may other caches; hence it can only be read
  M means only this cache has the address; hence it can be read and written
The states M, S, I can be thought of as an order M > S > I
  A transition from a lower state to a higher state is called an Upgrade
  A transition from a higher state to a lower state is called a Downgrade

## Slide 8: Sibling invariant and compatibility
Sibling invariant:
  Cache is in state M  its siblings are in state I
  That is, the sibling states are “compatible”
    IsCompatible(M, M) = False
    IsCompatible(M, S) = False
    IsCompatible(S, M) = False
    All other cases = True

## Slide 9: Cache State Transitions
S
M
I
store
load
write-back
invalidate
flush
store
optimizations
This state diagram is helpful as long as one remembers that each transition involves cooperation of other caches and the main memory to maintain the sibling invariants

## Slide 10: Cache Actions
On a read miss (i.e., Cache state is I):
  In case some other cache has the address in state M then write back the dirty data to Memory
  Read the value from Memory and set the state to S
On a write miss (i.e., Cache state is I or S):
  Invalidate the address in all other caches and in case some cache has the address in state M then write back the dirty data
  Read the value from Memory if necessary and set the state to M
Misses cause Cache upgrade actions which in turn may cause further downgrades or upgrades on other caches

## Slide 11: MSI protocol: some issues
It never makes sense to have two outstanding requests for the same address from the same processor/cache
It is possible to have multiple requests for the same address from different processors. Hence there is a need to arbitrate requests
A cache needs to be able to evict an address in order to make room for a different address
  Voluntary downgrade
Memory system (higher-level cache) should be able to force a lower-level cache to downgrade
  caches need to keep track of the state of their children’s caches

## Slide 12: Directory State Encoding Two-level (L1, M) system
For each address in a cache, the directory keeps two types of info
  c.state[a] (sibling info): do c’s siblings have a copy of address a; M (means no), S (means maybe)
  m.child[ck][a] (children info): the state of child ck for address a; At most one child can be in state M
a
a
P
L1
P
L1
L1
Interconnect
<S,I,I,I>
S
P
P

## Slide 13: Directory state encoding wait states
New states to deal with waiting for responses:
  c.waitp[a] : Denotes if cache c is waiting for a response from its parent
    No means not waiting
    Yes (S|I) means waiting for a response to transition to state S or I, respectively
  m.waitc[ck][a] : Denotes if memory m is waiting for a response from its child ck
    No | Yes (M|S)
Cache state in L1:
    <(M|S|I), (No | Yes(M|S))>
Directory state in home memory (for each child):
  <[(M|S|I), (No | Yes(S|I))]>
Child’s state
Waiting for downgrade response

## Slide 14: A Directory-based Protocol an abstract view
interconnect
PP
P
c2m
m2c
L1
p2m
m2p
m
PP
in
out
PP
P
c2m
m2c
L1
p2m
m2p
Each cache has 2 pairs of queues
  (c2m, m2c) to communicate with the memory
  (p2m, m2p) to communicate with the processor
Message format: <cmd, srcdst, a, s, data>
FIFO message passing between each (srcdst) pair except a Req cannot block a Resp
Messages in one srcdst path cannot block messages in another srcdst path
Req/Resp
address
state

## Slide 15: Processor Hit Rules
Load-hit rule
  p2m.msg=(Load a) &
  (c.state[a]>I)
 p2m.deq;
m2p.enq(c.data[a]);
Store-hit rule
    p2m.msg=(Store a v) &
  c.state[a]=M
 p2m.deq;
m2p.enq(Ack);
c.data[a]:=v;
PP
P
c2m
m2c
L1
p2m
m2p

## Slide 16: Processing misses: Requests and Responses
1 Up-req send (cache)
2 Up-req proc, Up resp send (memory)
3 Up-resp proc (cache)
4 Dn-req send (memory)
5 Dn-req proc, Dn resp send (cache)
6 Dn-resp proc (memory)
7 Dn-req proc, drop (cache)
8 Voluntary Dn-resp (cache)
Cache
1,5,8
3,5,7
Memory
2,4
2,6
Cache
1,5,8
3,5,7
1
2
4
3
6
5

## Slide 17: Invariants for a CC-protocol design
Directory state is always a conservative estimate of a child’s state
  E.g., if directory thinks that a child cache is in S state then the cache has to be in either I or S state
For every request there is a corresponding response, though sometimes a response may have been generated even before the request was processed
Communication system has to ensure that
  responses cannot be blocked by requests
  a request cannot overtake a response for the same address
At every merger point for requests, we will assume fair arbitration to avoid starvation