## Slide 1
Constructive Computer Architecture:
FIFO Lab Comments
Revisiting CF FIFOs
Andy Wright
6.175 TA

## Slide 2: Notes
The FIFO lab has been graded
Everyone did a great job on the conflicting, pipeline, and bypass FIFOs
All difficulties came from the Conflict-Free FIFO and the discussion questions

## Slide 3: What is a Conflict-Free FIFO?
Is it a FIFO with a conflict matrix filled with CFs?
  Not really...
Is it a FIFO that, in its typical use, doesn’t impose any more conflicts than necessary?
  Yes!

## Slide 4: Typical FIFO use
Enqueuing:
  check notFull and call enq(x)
Dequeuing:
  check notEmpty and call first and deq
Clearing:
  call clear
These are the methods that commonly appear in the same rule
  A CF FIFO says enqueuing and dequeuing rules will have no scheduling conflict imposed by the FIFO.
  {notFull, enq} CF {notEmpty, first, deq}

## Slide 5: Sequential FIFO Execution
enq(1)
first
deq
enq(2)
clear
enq(3)
enq(4)
first
deq
What is the state of the fifo here?
Assume FIFO is empty initially
What does first return?
How many elements are in the FIFO at the end?
How many clock cycles does this take?
Should that change the answer to these questions?

## Slide 6: Concurrent FIFO Execution With Clock Cycles
enq(1)
first
deq
enq(2)
clear
enq(3)
enq(4)
first
deq
Clock cycle boundary
enq(1)
first
deq
enq(2)
clear
enq(3)
enq(4)
first
deq
If these are both valid executions for a given FIFO, they should produce the same results.

## Slide 7: Concurrent FIFO Execution Clear-Enq Interactions
enq(1)
first
deq
enq(2)
clear
enq(3)
enq(4)
first
deq
enq(1)
first
deq
enq(2)
clear
enq(3)
enq(4)
first
deq
What should clear and enq do when they happen in the same cycle?
If both executions are valid, then the action has to be dynamic based on the order.

## Slide 8: Can we detect the order of methods firing?
In order for a method to know if it fired after another method fired, it has to always be scheduled after that method
If you want two methods to be able to tell if either of them came after the other, they have to conflict
  They will never fire in the same cycle making this problem of who fired first trivial...

## Slide 9: Concurrent FIFO Execution CF FIFO solution
enq(1)
first
deq
enq(2)
clear
enq(3)
enq(4)
first
deq
enq(1)
first
deq
enq(2)
clear
enq(3)
enq(4)
first
deq
Invalid Execution
Force enq < clear

## Slide 10: What does a CF FIFO do?
It allows the most flexible scheduling constraints possible while still requiring all valid concurrent executions to match the expected result from sequential execution.
  That is why {enq, deq} < clear and not {enq, deq} CF clear

## Slide 11: What about the canonicalize rule?
What happens if you have:
  {enq, deq} < canonicalize < clear
    If deq and clear occur in the same rule, that rule conflicts with canonicalize. This may or may not be a problem depending on the exact use.
  {enq, deq} < clear < canonicalize
    canonicalize can always fire at the end of the cycle independent of how enq, deq, and clear are used in rules