## Slide 1: Global Epoch
Sizhuo Zhang
6.175 TA

## Slide 2: N-Stage pipeline: Two predictors
Both Decode and Execute can redirect the PC; Execute redirect should never be overruled
Global epoch for each redirecting stage
  eEpoch: flipped when redirect from Execute takes effect
  dEpoch: flipped when redirect from Decode takes effect
  Initially set all epochs to 0
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
redirect PC
eEpoch
dEpoch
...
Redirect

## Slide 3: Execute stage
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
{pc, newpc}
{pc, newpc}
eEpoch
dEpoch
...
{…, ieEp, idEp}
{pc, ppc, ieEp}
Is ieEp == eEpoch?
yes
no
Wrong path instruction;
poison it
Current instruction is OK;
check the ppc prediction by execution, signal a redirect message (i.e. combinational pulse) on misprediction
Redirect

## Slide 4: Decode stage
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
{pc, newpc}
{pc, newpc}
eEpoch
dEpoch
...
{pc, ppc, ieEp, idEp}
{..., ieEp}
Is ieEp == eEpoch && idEp == dEpoch ?
yes
no
Wrong path instruction; drop it
Current instruction is OK;
check the ppc prediction via BHT, signal a redirect message (i.e. combinational pulse) on misprediction
Redirect

## Slide 5: Fetch stage: redirect PC, change epoch
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
{pc, newpc}
{pc, newpc}
eEpoch
dEpoch
...
Redirect
If there is redirect message from Execute
  Set PC to correct value, Flip eEpoch
Else if there is redirect message from Decode
  Set PC to correct value, Flip dEpoch
We can always request IMem to fetch new instruction
  New instruction will be tagged with current eEpoch and dEpoch
  PC redirection overrides next-PC prediction
  When PC redirects, new instruction must be killed at Decode stage

## Slide 6: Proof of correctness
Assume epochs are unbounded instead of just 1-bit
  On PC redirection, increment epoch instead of flipping it
  Obviously correct
At cycle , instructions between Fetch and Execute:
  at Fetch, at Execute, at Decode
Invariant:
  Proved by induction on
Observation: only need last bit of epoch – 1-bit epochs
eEpoch
dEpoch
...
Execute
...
Fetch
Decode
...

## Slide 7: 4-stage Pipeline: code sketch
module mkProc(Proc);
// stage 1: Fetch
// stage 2: Decode & read register
// stage 3: Execute & access memory
// stage 4: Commit (write register file)
Ehr#(2, Addr) pc <- mkEhr(?);
IMemory iMem <- mkIMemory;
...
Fifo#(2, Fetch2Decode) f2d <- mkCFFifo;
Fifo#(2, Decode2Execute) d2e <- mkCFFifo;
Fifo#(2, Execute2Commit) e2c <- mkCFFifo;
Reg#(Bool) eEpoch <- mkReg(False);
Reg#(Bool) dEpoch <- mkReg(False);
Ehr#(2, Maybe#(ExeRedirect)) exeRedirect <- mkEhr(Invalid);
Ehr#(2, Maybe#(DecRedirect)) decRedirect <- mkEhr(Invalid);
BTB#(16) btb <- mkBTB;
BHT#(1024) bht <- mkBHT;
Notes: 7

## Slide 8: Execute stage
rule doExecute;
d2e.deq; let x = d2e.first;
if(x.ieEp == eEpoch) begin
let eInst = exec(...); if(eInst.mispredict)
exeRedirect[0] <= Valid ({pc: x.pc,
newpc: eInst.addr});
...
end
else e2c.enq(Exec2Commit{poisoned: True, ...});
// wrong path instruction, poison it endrule
BHT training is missing here

## Slide 9: Decode stage
rule doDecode;
f2d.deq; let x = f2d.first;
if(x.ieEp == eEpoch && x.idEp == dEpoch) begin
let stall = ...; // check scoreboard for stall
if(!stall) begin
if(x.iType == Br) begin
let bht_ppc = ...; // BHT prediction
if(bht_ppc != x.ppc)
decRedirect[0] <= Valid ({pc: x.pc,
newpc: bht_ppc});
end
...
d2e.enq(Decode2Execute{ieEp: x.ieEp, ...});
end
end
// else: wrong path instruction, killed
endrule

## Slide 10: Fetch stage
rule doFetch;
let inst = iMem.req(pc[0]);
let ppc = btb.predPc(pc[0]);
pc[0] <= ppc;
f2d.enq(Fetch2Decode{pc: pc[0], ppc: ppc, inst: inst,
ieEp: eEpoch, idEp: dEpoch});
endrule
rule cononicalizeRedirect;
if(exeRedirect[1] matches tagged Valid .r) begin
pc[1] <= r.newpc; btb.update(r.pc, r.newpc);
eEpoch <= !eEpoch;
end else if(decRedirect[1] matches tagged Valid .r) begin
pc[1] <= r.newpc; btb.update(r.pc, r.newpc);
dEpoch <= !dEpoch;
end
exeRedirect[1] <= Invalid; decRedirect[1] <= Invalid;
endrule