## Slide 1
Constructive Computer Architecture
Combinational circuits
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Content
Design of a combinational ALU starting with primitive gates And, Or and Not
Combinational circuits as acyclic wiring diagrams of primitive gates
Introduction to BSV
  Intro to types – enum, typedefs, numeric types, Int#(32) vs Integer, Bool vs Bit#(1), Vector
  Simple operations: concatenation, conditionals, loops
  Functions
  Static elaboration and a structural interpretation of the textual code

## Slide 3
Combinational circuits

## Slide 4: Combinational circuits are acyclic interconnections of gates
And, Or, Not
Nand, Nor, Xor
…

## Slide 5: Arithmetic-Logic Unit (ALU)
ALU performs all the arithmetic and logical functions
Op
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Each individual function can be described as a combinational circuit

## Slide 6: Half Adder
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Boolean equations
s = (~a∙b) + (a∙~b)
c = a∙b
“Optimized”
s = a  b

## Slide 7: Full Adder
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Boolean equations
s = (~a∙~b∙cin)+(~a∙b∙~cin)+(a∙~b∙~cin)+(a∙b∙cin)
cout = (~a∙b∙cin) +(a∙~b∙cin) +(a∙b∙~cin) +(a∙b∙cin)
“Optimized”
t = ab s = tcin cout = a∙b + cin∙t
t

## Slide 8: Full Adder: A one-bit adder
function fa(a, b, c_in);
t = (a ^ b);
s = t ^ c_in;
c_out = (a & b) | (c_in & t);
return {c_out,s};
endfunction
Structural code – only specifies interconnection between boxes
Not quite correct –needs type annotations
t

## Slide 9: Full Adder: A one-bit adder corrected
function Bit#(2) fa(Bit#(1) a, Bit#(1) b,
Bit#(1) c_in);
Bit#(1) t = a ^ b;
Bit#(1) s = t ^ c_in;
Bit#(1) c_out = (a & b) | (c_in & t);
return {c_out,s};
endfunction
“Bit#(1) a” type declaration says that a is one bit wide
{c_out,s} represents bit concatenation
How big is {c_out,s}?
2 bits
t

## Slide 10: Types
A type is a grouping of values:
  Integer: 1, 2, 3, …
  Bool: True, False
  Bit: 0,1
  A pair of Integers: Tuple2#(Integer, Integer)
  A function fname from Integers to Integers:
  function Integer fname (Integer arg)
Every expression in a BSV program has a type; sometimes it is specified explicitly and sometimes it is deduced by the compiler
Thus we say an expression has a type or belongs to a type
The type of each expression is unique

## Slide 11: Parameterized types: #
A type declaration itself can be parameterized by other types
Parameters are indicated by using the syntax ‘#’
  For example Bit#(n) represents n bits and can be instantiated by specifying a value of n
  Bit#(1), Bit#(32), Bit#(8), …

## Slide 12: Type synonyms
typedef bit [7:0] Byte;
typedef Bit#(8) Byte;
typedef Bit#(32) Word;
typedef Tuple2#(a,a) Pair#(type a);
typedef Int#(n) MyInt#(type n);
typedef Int#(n) MyInt#(numeric type n);
The same
The same

## Slide 13: Type declaration versus deduction
The programmer writes down types of some expressions in a program and the compiler deduces the types of the rest of expressions
If the type deduction cannot be performed or the type declarations are inconsistent then the compiler complains
function Bit#(2) fa(Bit#(1) a, Bit#(1) b,
Bit#(1) c_in);
Bit#(1) t = a ^ b;
Bit#(1) s = t ^ c_in;
Bit#(2) c_out = (a & b) | (c_in & t);
return {c_out,s};
endfunction
type error
Type checking prevents lots of silly mistakes

## Slide 14: 2-bit Ripple-Carry Adder
function Bit#(3) add(Bit#(2) x, Bit#(2) y,
Bit#(1) c0);
Bit#(2) s = 0; Bit#(3) c=0; c[0] = c0;
let cs0 = fa(x[0], y[0], c[0]);
c[1] = cs0[1]; s[0] = cs0[0];
let cs1 = fa(x[1], y[1], c[1]);
c[2] = cs1[1]; s[1] = cs1[0];
return {c[2],s};
endfunction
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
fa can be used as a black-box as long as we understand its type signature
The “let” syntax avoids having to write down types explicitly

## Slide 15: “let” syntax
The “let” syntax: No need to write the type if the compiler can deduce it:
  let cs0 = fa(x[0], y[0], c[0]);
  Bit#(2) cs0 = fa(x[0], y[0], c[0]);
The same

## Slide 16: Selecting a wire: x[i]
Constant Selector: e.g., x[2]
Dynamic selector: x[i]
[2]
x0
x1
x2
x3
x0
x1
x2
x3
[i]
x0
x1
x2
x3
i
x0
x1
x2
x3
i
no hardware; x[2] is just the name of a wire
4-way mux
assume x is 4 bits wide

## Slide 17: A 2-way multiplexer
(s==0)? A : B
A
B
S
Gate-level implementation
Conditional expressions are also synthesized using muxes
AND
AND
OR
S
A
B

## Slide 18: A 4-way multiplexer
case {s1,s0} matches
0: A;
1: B;
2: C;
3: D;
endcase
S0
S0
S1
A
B
C
D

## Slide 19: An w-bit Ripple-Carry Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(w+1) c=0; c[0] = c0;
for(Integer i=0; i<w; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[w],s};
endfunction
Not quite correct
Unfold the loop to get the wiring diagram
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
cs
fa
x[w-1]
y[w-1]
s[w-1]
c[w]
c[w-1]
…

## Slide 20: Instantiating the parametric Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
// concrete instances of addN!
function Bit#(33) add32(Bit#(32) x, Bit#(32) y,
Bit#(1) c0) =
addN(x,y,c0);
function Bit#(4) add3(Bit#(3) x, Bit#(3) y,
Bit#(1) c0) = addN(x,y,c0);
Now we define add32, add3 … using addN

## Slide 21: valueOf(w) versus w
Each expression has a type and a value and these come from two entirely disjoint worlds
w in Bit#(w) resides in the types world
Sometimes we need to use values from the types world into actual computation. The function valueOf allows us to do that
  Thus
  i<w is not type correct
  i<valueOf(w)is type correct

## Slide 22: TAdd#(w,1) versus w+1
Sometimes we need to perform operations in the types world that are very similar to the operations in the value world
  Examples: Add, Mul, Log
We define a few special operators in the types world for such operations
  Examples: TAdd#(m,n), TMul#(m,n), …

## Slide 23: A w-bit Ripple-Carry Adder corrected
function Bit#(TAdd#(w,1)) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(TAdd#(w,1)) c; c[0] = c0;
let valw = valueOf(w);
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[valw],s};
endfunction
types world
equivalent of w+1
Lifting a type into the value world
Structural interpretation of a loop – unfold it to generate an acyclic graph

## Slide 24: Static Elaboration phase
When BSV programs are compiled, first type checking is done and then the compiler gets rid of many constructs which have no direct hardware meaning, like Integers, loops
cs0 = fa(x[0], y[0], c[0]); c[1]=cs0[1]; s[0]=cs0[0];
cs1 = fa(x[1], y[1], c[1]); c[2]=cs1[1]; s[1]=cs1[0];
…
csw = fa(x[valw-1], y[valw-1], c[valw-1]);
c[valw] = csw[1]; s[valw-1] = csw[0];
for(Integer i=0; i<valw; i=i+1) begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 25: Integer versus Int#(32)
In mathematics integers are unbounded but in computer systems integers always have a fixed size
BSV allows us to express both types of integers, though unbounded integers are used only as a programming convenience
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 26: Shift operators

## Slide 27: Logical right shift by 2
0
0
Fixed size shift operation is cheap in hardware – just wire the circuit appropriately
Rotate, sign-extended shifts – all are equally easy
a b c d
0 0 a b

## Slide 28: Conditional operation: shift versus no-shift
We need a mux to select the appropriate wires: if s is one the mux will select the wires on the left otherwise it would select wires on the right
s
(s==0)?{a,b,c,d}:{0,0,a,b};
0
0

## Slide 29: Logical right shift by n
Shift n can be broken down in log n steps of fixed-length shifts of size 1, 2, 4, …
  Shift 3 can be performed by doing a shift 2 and shift 1
We need a mux to omit a particular size shift
Shift circuit can be expressed as log n nested conditional expressions
0
0
0
s0
s1

## Slide 30: A digression on types
Suppose we have a variable c whose values can represent three different colors
  We can declare the type of c to be Bit#(2) and say that 00 represents Red, 01 Blue and 10 Green
A better way is to create a new type called Color as follows:
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
The compiler will automatically assign some bit representation to the three colors and also provide a function to test if the two colors are equal. If you do not use “deriving” then you will have to specify the representation and equality
Types prevent us from mixing bits that represent color from raw bits

## Slide 31: Enumerated types
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT}
BrFunc deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu, LShift, RShift, Sra}
AluFunc deriving(Bits, Eq);
Each enumerated type defines a new type

## Slide 32: Combinational ALU
function Data alu(Data a, Data b, AluFunc func);
Data res = case(func)
Add : (a + b);
Sub : (a - b);
And : (a & b);
Or : (a | b);
Xor : (a ^ b);
Nor : ~(a | b);
Slt : zeroExtend( pack( signedLT(a, b) ) );
Sltu : zeroExtend( pack( a < b ) );
LShift: (a << b[4:0]);
RShift: (a >> b[4:0]);
Sra : signedShiftRight(a, b[4:0]);
endcase;
return res;
endfunction
Given an implementation of the primitive operations like addN, Shift, etc. the ALU can be implemented simply by introducing a mux controlled by op to select the appropriate circuit

## Slide 33: Comparison operators
function Bool aluBr(Data a, Data b, BrFunc brFunc);
Bool brTaken = case(brFunc)
Eq : (a == b);
Neq : (a != b);
Le : signedLE(a, 0);
Lt : signedLT(a, 0);
Ge : signedGE(a, 0);
Gt : signedGT(a, 0);
AT : True;
NT : False;
endcase;
return brTaken;
endfunction
Notes: 33

## Slide 34: ALU including Comparison operators
mux
a
func
…
mux
brFunc
Add
LShift
Eq
…
b