## Slide 1
Constructive Computer Architecture
Combinational circuits-2
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: An w-bit Ripple-Carry Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(w+1) c=0; c[0] = c0;
for(Integer i=0; i<w; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[w],s};
endfunction
Not quite correct
Unfold the loop to get the wiring diagram
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
cs
fa
x[w-1]
y[w-1]
s[w-1]
c[w]
c[w-1]
…

## Slide 3: Instantiating the parametric Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
// concrete instances of addN!
function Bit#(33) add32(Bit#(32) x, Bit#(32) y,
Bit#(1) c0) =
addN(x,y,c0);
The numeric type w on the RHS implicitly gets instantiated to 32 because of the LHS declaration
function Bit#(4) add3(Bit#(3) x, Bit#(3) y,
Bit#(1) c0) = addN(x,y,c0);
How do we define a add32, add3 … using addN ?

## Slide 4: valueOf(w) versus w
Each expression has a type and a value and these come from two entirely disjoint worlds
w in Bit#(w) resides in the types world
Sometimes we need to use values from the types world into actual computation. The function valueOf allows us to do that
  Thus
  i<w is not type correct
  i<valueOf(w)is type correct

## Slide 5: TAdd#(w,1) versus w+1
Sometimes we need to perform operations in the types world that are very similar to the operations in the value world
  Examples: Add, Mul, Log
We define a few special operators in the types world for such operations
  Examples: TAdd#(m,n), TMul#(m,n), …

## Slide 6: Integer versus Int#(32)
In mathematics integers are unbounded but in computer systems integers always have a fixed size
BSV allows us to express both types of integers, though unbounded integers are used only as a programming convenience
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 7: A w-bit Ripple-Carry Adder corrected
function Bit#(TAdd#(w,1)) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(TAdd#(w,1)) c; c[0] = c0;
let valw = valueOf(w);
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[valw],s};
endfunction
types world
equivalent of w+1
Lifting a type into the value world
Structural interpretation of a loop – unfold it to generate an acyclic graph

## Slide 8: Static Elaboration phase
When BSV programs are compiled, first type checking is done and then the compiler gets rid of many constructs which have no direct hardware meaning, like Integers, loops
cs0 = fa(x[0], y[0], c[0]); c[1]=cs0[1]; s[0]=cs0[0];
cs1 = fa(x[1], y[1], c[1]); c[2]=cs1[1]; s[1]=cs1[0];
…
csw = fa(x[valw-1], y[valw-1], c[valw-1]);
c[valw] = csw[1]; s[valw-1] = csw[0];
for(Integer i=0; i<valw; i=i+1) begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 9: Shift operators

## Slide 10: Logical right shift by 2
0
0
Fixed size shift operation is cheap in hardware – just wire the circuit appropriately
Rotate, sign-extended shifts – all are equally easy
a b c d
0 0 a b

## Slide 11: Conditional operation: shift versus no-shift
We need a mux to select the appropriate wires: if s is one the mux will select the wires on the left otherwise it would select wires on the right
s
(s==0)?{a,b,c,d}:{0,0,a,b};
0
0

## Slide 12: Logical right shift by n
Shift n can be broken down in log n steps of fixed-length shifts of size 1, 2, 4, …
  Shift 3 can be performed by doing a shift 2 and shift 1
We need a mux to omit a particular size shift
Shift circuit can be expressed as log n nested conditional expressions
0
0
0
s0
s1

## Slide 13: A digression on types
Suppose we have a variable c whose values can represent three different colors
  We can declare the type of c to be Bit#(2) and say that 00 represents Red, 01 Blue and 10 Green
A better way is to create a new type called Color as follows:
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
The compiler will automatically assign some bit representation to the three colors and also provide a function to test if the two colors are equal. If you do not use “deriving” then you will have to specify the representation and equality
Types prevent us from mixing bits that represent color from raw bits

## Slide 14: Enumerated types
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT}
BrFunc deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu, LShift, RShift, Sra}
AluFunc deriving(Bits, Eq);
Each enumerated type defines a new type

## Slide 15: Arithmetic-Logic Unit (ALU)
ALU performs all the arithmetic and logical functions
Op
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Each individual function can be described as a combinational circuit

## Slide 16: Combinational ALU
function Data alu(Data a, Data b, AluFunc func);
Data res = case(func)
Add : (a + b);
Sub : (a - b);
And : (a & b);
Or : (a | b);
Xor : (a ^ b);
Nor : ~(a | b);
Slt : zeroExtend( pack( signedLT(a, b) ) );
Sltu : zeroExtend( pack( a < b ) );
LShift: (a << b[4:0]);
RShift: (a >> b[4:0]);
Sra : signedShiftRight(a, b[4:0]);
endcase;
return res;
endfunction
Given an implementation of the primitive operations like addN, Shift, etc. the ALU can be implemented simply by introducing a mux controlled by op to select the appropriate circuit

## Slide 17: Comparison operators
function Bool aluBr(Data a, Data b, BrFunc brFunc);
Bool brTaken = case(brFunc)
Eq : (a == b);
Neq : (a != b);
Le : signedLE(a, 0);
Lt : signedLT(a, 0);
Ge : signedGE(a, 0);
Gt : signedGT(a, 0);
AT : True;
NT : False;
endcase;
return brTaken;
endfunction
Notes: 17

## Slide 18: ALU including Comparison operators
mux
a
func
…
mux
brFunc
Add
LShift
Eq
…
b

## Slide 19: Complex Combinational Circuits

## Slide 20: Multiplication by repeated addition
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
a1
m1
a2
m2
a3
m3
add4
0
add4
add4
a0
m0

## Slide 21: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) tp = 0; Bit#(32) prod = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0];
tp = sum[32:1];
end return {tp,prod}; endfunction
Combinational circuit uses 31 add32 circuits
We can reuse the same add32 circuit if we store the partial results in a register

## Slide 22: Design issues with combinational multiply
Lot of hardware
  32-bit multiply uses 31 add32 circuits
Long chains of gates
  32-bit ripple carry adder has a 31-long chain of gates
  32-bit multiply has 31 ripple carry adders in sequence! Total delay ?
The speed of a combinational circuit is determined by its longest input-to-output path
Can we do better?
Yes – Sequential Circuits; Circuits with state
  2(n-1) FAs?