## Slide 1: Constructive Computer Architecture: Guards
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first)); inQ.deq; end endrule
rule stage2;
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f2(fifo1.first)); fifo1.deq; end endrule
rule stage3;
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f3(fifo2.first)); fifo2.deq; end endrule
Proper use of FIFOs always involves checking for emptiness or fullness conditions

## Slide 3: Easy mistakes
rule stage1E;
if(inQ.notEmpty && fifo1.notFull)
fifo1.enq(f1(inQ.first);
if(inQ.notEmpty) inQ.deq;
endrule
rule stage1;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first);
inQ.deq; end
endrule
What is the difference?
stage1E may dequeue something even though the value read has not been processed (ie enqueued into fifo1)
Guards is an abstraction to deal with such “atomicity” issues
versus

## Slide 4: FIFO Module: methods with guarded interfaces
Every method has a guard (rdy wire)
The compiler ensures that an action method is invoked (en) only if the guard is true. Similarly the value returned by a value method is meaningful only if its guard is true
Guards make it possible to transfer the responsibility of the correct use of a method from the user to the compiler
Guards are extraordinarily convenient for programming and also enhance modularity of the code
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
interface Fifo#(numeric type size,
type t);
method Action enq(t x);
method Action deq;
method t first;
endinterface

## Slide 5: One-Element FIFO Implementation with guards
module mkCFFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action deq if (v);
v <= False;
endmethod
method t first if (v);
return d;
endmethod
endmodule
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO

## Slide 6: Elastic pipeline with guards
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1 (True);
fifo1.enq(f1(inQ.first);
inQ.deq(); endrule
rule stage2 (True);
  fifo2.enq(f2(fifo1.first);
fifo1.deq; endrule
rule stage3 (True);
outQ.enq(f3(fifo2.first);
fifo2.deq; endrule
When can stage1 rule fire?
The explicit guard is true but the compiler lifts all the implicit guards of the methods to the top of the rule
guard
- inQ has an element
- fifo1 has space

## Slide 7: Switch with guards
rule switch (True);
if (inQ.first.color == Red)
begin redQ.enq (inQ.first.value); inQ.deq; end
else begin greenQ.enq(inQ.first.value); inQ.deq; end
endrule
inQ
redQ
greenQ
rule switchRed (inQ.first.color == Red);
redQ.enq(inQ.first.value); inQ.deq;
endrule;
rule switchGreen (inQ.first.color == Green);
greenQ.enq(inQ.first.value); inQ.deq;
endrule;

## Slide 8: GCD module with Guards
Reg#(Bit#(32)) x <- mkReg(0);
Reg#(Bit#(32)) y <- mkReg(0);
rule gcd (x != 0);
if (x >= y) begin
x <= x – y; end
else begin
x <= y; y <= x; end
endrule
method Action start(Bit#(32) a, Bit#(32) b) if (x == 0);
x <= a; y <= b; endmethod
method Bit#(32) result if (x == 0);
return y; endmethod
If x is 0 then the rule cannot fire
Start method can be invoked only if x is 0
The result is available only when x is 0 is True.
Notes: (Andy) Changed code to conform with BSV syntax

## Slide 9: All methods have implicit guards
Every method call has an implicit guard associated with it
  m.enq(x), the guard indicated whether one can enqueue into fifo m or not
Methods of primitive modules like registers and EHRs have their guards always set to True
Guards play an important role in scheduling; a rule is considered for scheduling only if its guard is true (“can fire”)
Nevertheless guards are merely syntactic sugar and are lifted to the top of each rule by the compiler
Information a guard carries can be encoded in a value method

## Slide 10: Guard Elimination

## Slide 11: Making guards explicit in compilation
Make the guards explicit in every method call by naming the guard and separating it from the unguarded body of the method call, i.e., syntactically replace m.g(e) by
m.gB(e) when m.gG
  Notice m.gG has no parameter because the guard value should not depend upon the input

## Slide 12: Lifting implicit guards
rule foo if (True);
(if (p) fifo.enq(8)); x.w(7)
rule foo if (p && fifo.enqG || !p);
if (p) fifo.enqB(8); x.w(7)
All implicit guards are made explicit, and lifted and conjoined to the rule guard
rule foo if (fifo.enqG || !p);
if (p) fifo.enqB(8); x.w(7)

## Slide 13: Make implicit guards explicit
<a> ::= <a> | <a>
| if (<e>) <a>
| m.g(<e>)
| let t = <e> in <a>
m.gB(<e>) when m.gG
<a> ::= <a> | <a>
| if (<e>) <a>
| m.g(<e>)
| let t = <e> in <a>
| <a> when <e>
methods without guards
The new kernel language
guarded action
The kernel language with abstract syntax
We use “|” instead of “;” for parallel composition.
“|” and “::=” represent meta-syntax.

## Slide 14: Syntax for guards
rule x (g);
a
endrule
is the same as rule x (a when g)
method foo(x, y) if (g);
a
endmethod
is the same as
method foo(x, y) (a when g) endmethod
If no guard is explicitly supplied, the guard is assumed to be True

## Slide 15: Guards vs If’s
The predicate in a Conditional action only affects the actions within the scope of the conditional action
(if (p1) a1) | a2
p1 has no effect on a2 ...
The guard on one action of a parallel group of actions affects every action within the group
(a1 when p1) | a2
==> (a1 | a2) when p1
Mixing ifs and whens
(if (p) (a1 when q)) | a2
 ((if (p) a1) | a2) when ((p && q) || !p)
 ((if (p) a1) | a2) when (q || !p)

## Slide 16: Guard Lifting Axioms without Let-blocks
All the guards can be “lifted” to the top of a rule
  (a1 when p) | a2 
  a1 | (a2 when p) 
  if (p when q) a 
  if (p) (a when q) 
  (a when p1) when p2 
  m.gB(e when p) 
similarly for expressions ...
  Rule r (a when p) 
  (a1 | a2) when p
  (a1 | a2) when p
  (if (p) a) when q
  (if (p) a) when (q || !p)
  a when (p1 && p2)
  m.gB(e) when p
  Rule r (if (p) a)
We will call this guard lifting transformation WIF, for when-to-if
A complete guard lifting procedure also requires rules for let-blocks

## Slide 17: Scheduling with guards
At the top level a guard behaves just like an “if”
A rule whose guard is False at a given cycle will result in no state change even if it is scheduled
The guards of most rules can be evaluated in parallel, often with small amount of computation (The exceptions are 1. if two guards call the same method and the method has parameters; 2. if guards involve EHRs)
The scheduler takes advantage of this fact by considering only those rules for scheduling in a given cycle whose guards are True

## Slide 18: Scheduling and control logic
Modules
(Current state)
Rules
a1
p1
Scheduler
wf1
wfn
cf1
cfn
Muxing
ns1
nsn
an
pn
Modules
(Next state)
cond
action
“CAN_FIRE”
“WILL_FIRE”
Compiler synthesizes a scheduler such that at any given time will-fire for only non-conflicting rules are true
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 19: Hierarchical scheduling
interface
module
According to Bluespec semantics, at most one rule from any module should execute in a given cycle
Which module?
Modules form a natural hierarchy;
  Schedule inside out or outside in?

## Slide 20: Hierarchical scheduling
Scheduling is done outside-in:
First, the rules of the outermost modules are scheduled, which may call (enable) methods of inner modules
Then the rules of subsequent inner modules are scheduled, as long as they can be scheduled concurrently with the called methods
BSV provides annotation to reverse this priority on a module basis
It is because of scheduling complications that current BSV doesn’t allow modular compilation in the presence of interface parameters