## Slide 1
Constructive Computer Architecture:
Data Hazards
in Pipelined Processors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Consider a different two-stage pipeline
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
pred
f2d
Suppose we move the pipeline stage from Fetch to after Decode and Register fetch for a better balance of work in two stages
Fetch
Execute, Memory, WriteBack
Insti
Insti+1
Pipeline will still have control hazards
Decode,
RegisterFetch
Notes: 2

## Slide 3: A different 2-Stage pipeline: 2-Stage-DH pipeline
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
d2e
redirect
fEpoch
eEpoch
pred
Fifos
Use the same epoch solution for control hazards as before
Fetch, Decode, RegisterFetch
Execute, Memory, WriteBack
Notes: 3

## Slide 4: Converting the old pipeline into the new one
rule doFetch;
... let instF = iMem.req(pc);
f2d.enq(Fetch2Execute{... inst: instF ...}); ...
endrule
rule doExecute; ... let dInst = decode(instD); let rVal1 = rf.rd1(fromMaybe(?, dInst.src1)); let rVal2 = rf.rd2(fromMaybe(?, dInst.src2)); let eInst = exec(dInst, rVal1, rVal2, pcD, ppcD); ... endrule
instF
Not quite correct. Why?
Fetch is potentially reading stale values from rf

## Slide 5: Data Hazards
fetch & decode
execute
d2e
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
FDstage FD1 FD2 FD3 FD4 FD5
EXstage EX1 EX2 EX3 EX4 EX5
I1 R1  R2+R3
I2 R4  R1+R2
I2 must be stalled until I1 updates the register file
pc
rf
dMem
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
FDstage FD1 FD2 FD2 FD3 FD4 FD5
EXstage EX1 EX2 EX3 EX4 EX5
Notes: 5

## Slide 6: Dealing with data hazards
Keep track of instructions in the pipeline and determine if the register values to be fetched are stale, i.e., will be modified by some older instruction still in the pipeline. This condition is referred to as a read-after-write (RAW) hazard
Stall the Fetch from dispatching the instruction as long as RAW hazard prevails
RAW hazard will disappear as the pipeline drains
Scoreboard: A data structure to keep track of the instructions in the pipeline beyond the Fetch stage

## Slide 7: Data Hazard
Data hazard depends upon the match between the source registers of the fetched instruction and the destination register of an instruction already in the pipeline
Both the source and destination registers must be Valid for a hazard to exist
function Bool isFound
(Maybe#(RIndex) x, Maybe#(RIndex) y);
if(x matches Valid .xv &&& y matches Valid .yv
&&& yv == xv) return True; else return False;
endfunction

## Slide 8: Scoreboard: Keeping track of instructions in execution
Scoreboard: a data structure to keep track of the destination registers of the instructions beyond the fetch stage
  method insert: inserts the destination (if any) of an instruction in the scoreboard when the instruction is decoded
  method search1(src): searches the scoreboard for a data hazard
  method search2(src): same as search1
  method remove: deletes the oldest entry when an instruction commits

## Slide 9: 2-Stage-DH pipeline: Scoreboard and Stall logic
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
d2e
redirect
fEpoch
eEpoch
pred
scoreboard
Notes: 9

## Slide 10: 2-Stage-DH pipeline
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkFifo;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) redirect <- mkFifo;
Scoreboard#(1) sb <- mkScoreboard;
// contains only one slot because Execute
// can contain at most one instruction
rule doFetch …
rule doExecute …
Notes: 10

## Slide 11: 2-Stage-DH pipeline doFetch rule
rule doFetch; if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end else
begin let instF = iMem.req(pc);
let ppcF = nextAddrPredictor(pc); pc <= ppcF;
let dInst = decode(instF);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(fromMaybe(?, dInst.src1)); let rVal2 = rf.rd2(fromMaybe(?, dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppcF,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); end
end endrule
What should happen to pc when Fetch stalls?
pc should change only when the instruction is enqueued in d2e

## Slide 12: 2-Stage-DH pipeline doFetch rule corrected
rule doFetch; if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end else
begin let instF = iMem.req(pc);
let ppcF = nextAddrPredictor(pc); pc <= ppcF;
let dInst = decode(instF);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(fromMaybe(?, dInst.src1)); let rVal2 = rf.rd2(fromMaybe(?, dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppcF,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); end
end endrule
pc <= ppcF; end
To avoid structural hazards, scoreboard must allow two search ports

## Slide 13: 2-Stage-DH pipeline doExecute rule
rule doExecute; let x = d2e.first;
let dInstE = x.dInst; let pcE = x.pc;
let ppcE = x.ppc; let epoch = x.epoch;
let rVal1E = x.rVal1; let rVal2E = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInstE, rVal1E, rVal2E, pcE, ppcE); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst))
rf.wr(fromMaybe(?, eInst.dst), eInst.data); if(eInst.mispredict) begin redirect.enq(eInst.addr); eEpoch <= !eEpoch; end end d2e.deq; sb.remove; endrule

## Slide 14: A correctness issues
If the search by Decode does not see an instruction in the scoreboard, then its effect must have taken place. This means that any updates to the register file by that instruction must be visible to the subsequent register reads 
  remove and wr should happen atomically
  search and rd1, rd2 should happen atomically
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
Fetch and Execute can execute in any order

## Slide 15: Concurrently executable Fetch and Execute
Case 1: doExecute < dofetch 
  rf: wr < rd (bypass rf)
  sb: remove < {search, insert}
  d2e: {first, deq} {<, CF} enq (pipelined or CF Fifo)
  redirect: enq {<, CF} {deq, first} (bypass or CF Fifo)
Case 2: doFetch < doExecute 
  rf: rd < wr (normal rf)
  sb: {search, insert} < remove
  d2e: enq {<, CF} {deq, first} (bypass or CF Fifo)
  redirect: {first, deq} {<, CF} enq (pipelined or CF Fifo)
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
which is better?

## Slide 16: Performance issues
To avoid a stall due to a RAW hazard between successive instructions
  sb: remove ? search
  rf: wr ? rd
To minimize stalls due to control hazards
  redirect: ?
What kind of fifo should be used for d2e ?
  Either a pipeline or CF fifo would do fine
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
<
<
  (bypass rf)
bypass fifo

## Slide 17: 2-Stage-DH pipeline with proper specification of Fifos, rf, scoreboard
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkPipelineFifo;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) redirect <- mkBypassFifo;
Scoreboard#(1) sb <- mkPipelineScoreboard;
// contains only one slot because Execute
// can contain at most one instruction
rule doFetch …
rule doExecute …
Can a destination register name appear more than once in the scoreboard ?
Notes: 17

## Slide 18: WAW hazards
If multiple instructions in the scoreboard can update the register which the current instruction wants to read, then the current instruction has to read the update for the youngest of those instructions
This is not a problem in our design because
  instructions are committed in order
  the RAW hazard for the instruction at the decode stage will remain as long as the any instruction with the required destination is present in sb
Notes: WAW – Write-after-write Hazard

## Slide 19: An alternative design for sb
Instead of keeping track of the destination of every instruction in the pipeline, we can associated a counter with every register to indicate the number of instructions in the pipeline for which this register is the destination
  The appropriate counter is incremented when an instruction enters the execute stage and decremented when the instruction is committed
This design is more efficient (less hardware) because it avoids an associative search

## Slide 20: Summary
Instruction pipelining requires dealing with control and data hazards
Speculation is necessary to deal with control hazards
Data hazards are avoided by withholding instructions in the decode stage until the hazard disappears
Performance issues are subtle
  For instance, the value of having a bypass network depends on how frequently it is exercised by programs
  Bypassing necessarily increases combinational path lenths which can slow down the clock
The rest of the slides will be discussed in the Recitation

## Slide 21: Normal Register File
module mkRFile(RFile);
Vector#(32,Reg#(Data)) rfile <- replicateM(mkReg(0));
method Action wr(RIndx rindx, Data data);
if(rindx!=0) rfile[rindx] <= data;
endmethod
method Data rd1(RIndx rindx) = rfile[rindx];
method Data rd2(RIndx rindx) = rfile[rindx];
endmodule
{rd1, rd2} < wr
Notes: 21

## Slide 22: Bypass Register File using EHR
module mkBypassRFile(RFile);
Vector#(32,Ehr#(2, Data)) rfile <-
replicateM(mkEhr(0));
method Action wr(RIndx rindx, Data data);
if(rindex!=0) (rfile[rindex])[0] <= data;
endmethod
method Data rd1(RIndx rindx) = (rfile[rindx])[1];
method Data rd2(RIndx rindx) = (rfile[rindx])[1];
endmodule
wr < {rd1, rd2}
Notes: 22

## Slide 23: Bypass Register File with external bypassing
module mkBypassRFile(BypassRFile);
RFile rf <- mkRFile;
Fifo#(1, Tuple2#(RIndx, Data))
bypass <- mkBypassSFifo;
rule move;
begin rf.wr(bypass.first); bypass.deq end;
endrule
method Action wr(RIndx rindx, Data data);
if(rindex!=0) bypass.enq(tuple2(rindx, data));
endmethod
method Data rd1(RIndx rindx) =
return (!bypass.search1(rindx)) ? rf.rd1(rindx)
: bypass.read1(rindx);
method Data rd2(RIndx rindx) =
return (!bypass.search2(rindx)) ? rf.rd2(rindx)
: bypass.read2(rindx);
endmodule
wr < {rd1, rd2}
rf
move
rd
Notes: 23

## Slide 24: Scoreboard implementation using searchable Fifos
function Bool isFound
(Maybe#(RIndx) dst, Maybe#(RIndx) src);
return isValid(dst) && isValid(src) &&
(fromMaybe(?,dst)==fromMaybe(?,src));
endfunction
module mkCFScoreboard(Scoreboard#(size));
SFifo#(size, Maybe#(RIndx), Maybe#(RIndx))
f <- mkCFSFifo(isFound);
method insert = f.enq;
method remove = f.deq;
method search1 = f.search1;
method search2 = f.search2;
endmodule