## Slide 1
Constructive Computer Architecture:
Branch Prediction
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Control Flow Penalty
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
  Loop length x pipeline width
What fraction of executed instructions are branch instructions?
superscalarity

## Slide 3: How frequent are branches? ARM Cortex 7
Blem et al [HPCA 2013] Spec INT 2006
 | ARM Cortex-A9; ARMv7 ISA |  |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
astar | 1.47E+10 | 16.0 | 55.6 | 13.0 | 15.4
bzip2 | 2.41E+10 | 8.7 | 34.6 | 14.4 | 42.2
gcc | 5.61E+09 | 10.2 | 19.1 | 11.2 | 59.5
gobmk | 5.75E+10 | 10.7 | 25.4 | 7.2 | 56.8
hmmer | 1.56E+10 | 5.1 | 41.8 | 18.1 | 35.0
h264 | 1.06E+11 | 5.5 | 30.4 | 10.4 | 53.6
libquantum | 3.97E+08 | 11.5 | 8.1 | 11.7 | 68.7
omnetpp | 2.67E+09 | 11.7 | 19.3 | 8.9 | 60.1
perlbench | 2.69E+09 | 10.7 | 24.6 | 9.3 | 55.5
sjeng | 1.34E+10 | 11.5 | 39.3 | 13.7 | 35.5
Average |  | 8.2 | 31.9 | 10.9 | 49.0
Every 12th instruction is a branch

## Slide 4: How frequent are branches? X86
 |  | core i7; x86 ISA |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
astar | 5.71E+10 | 6.9 | 19.5 | 6.9 | 66.7
bzip2 | 4.25E+10 | 11.1 | 31.2 | 11.8 | 45.9
hmmer | 2.57E+10 | 5.3 | 30.5 | 9.4 | 54.8
gcc | 6.29E+09 | 15.1 | 22.1 | 14.1 | 48.7
gobmk | 8.93E+10 | 12.1 | 21.7 | 13.4 | 52.7
h264 | 1.09E+11 | 7.1 | 46.8 | 18.5 | 27.6
libquantum | 4.18E+08 | 13.2 | 39.3 | 6.8 | 40.7
omnetpp | 2.55E+09 | 16.4 | 28.6 | 21.4 | 33.7
perlbench | 2.91E+09 | 17.3 | 25.9 | 16.0 | 40.8
sjeng | 2.11E+10 | 14.8 | 22.8 | 11.0 | 51.4
Average |  | 9.4 | 31.0 | 13.4 | 46.2
Blem et al [HPCA 2013] Spec INT 2006
Every 10th or 11th instruction is a branch

## Slide 5: How frequent are branches? ARM Cortex 7
Blem et al [HPCA 2013] Spec FP 2006
 | ARM Cortex-A9; ARMv7 ISA |  |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
bwaves | 3.84E+11 | 13.5 | 1.4 | 0.5 | 84.7
cactusADM | 1.02E+10 | 0.5 | 51.4 | 17.9 | 30.1
leslie3D | 4.92E+10 | 6.2 | 2.0 | 3.7 | 88.1
milc | 1.38E+10 | 6.5 | 38.2 | 13.3 | 42.0
tonto | 1.30E+10 | 10.0 | 40.5 | 14.1 | 35.4
Average |  | 12.15 | 4.68 | 1.95 | 81.22
Every 8th instruction is a branch

## Slide 6: How frequent are branches? X86
Blem et al [HPCA 2013] Spec FP 2006
 |  | core i7; x86 ISA |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
bwaves | 3.41E+10 | 3.2 | 51.4 | 16.8 | 28.7
cactusADM | 1.05E+10 | 0.4 | 55.3 | 18.6 | 25.8
leslie3D | 6.25E+10 | 4.9 | 35.3 | 12.8 | 46.9
milc | 3.29E+10 | 2.2 | 32.2 | 13.8 | 51.8
tonto | 4.88E+09 | 7.1 | 27.2 | 12.4 | 53.3
Average |  | 3.6 | 39.6 | 14.4 | 42.4
Every 27th instruction is a branch

## Slide 7: Observations
Control transfer happens every 8th to 30th instruction
There is a plethora of branch prediction schemes – their importance grows with the depth of processor pipeline
Static vs dynamic predictors: Does the prediction depend upon the execution history?
Processors often use more than one predictor
It takes considerable effort to
  Integrate a prediction scheme in the pipeline
  Understand the interactions between various schemes
  Understand the performance implications
we will start with the basics ...

## Slide 8: RISC V Branches & Jumps
Instruction Direction known after Target known after
JAL
JALR
BEQ/BNE ...
Each instruction fetch depends on some information from the preceding instruction:
1. Is the preceding instruction a taken branch?
2. If so, what is the target address?
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Reg. Fetch (?)
After Exec
A predictor can redirect the pc only after the relevant information required by the predictor is available

## Slide 9: Overview of control prediction
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
Given (pc, ppc), a misprediction can be corrected (used to redirect the pc) as soon as it is detected. In fact, pc can be redirected as soon as we have a “better” prediction. However, for forward progress it is important that a correct pc should never be redirected.
mispred insts must be filtered
correct mispred
correct mispred
correct mispred
Notes: With respect to branches the important steps are…
With ‘stall style’ dependence resolution - correct next PC calculation waits for …
To alleviate stalls speculate next PC – now dependence info is speculation check

## Slide 10: Static Branch Prediction
Since most instructions do not result in a control transfer, pc+4 is a good predictor
Overall probability a branch is taken is ~60-70% but:
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64
  reported as ~80% accurate
JZ
JZ
backward
90%
forward
50%
... but our ISA is fixed!

## Slide 11: Dynamic Branch Prediction learning based on past behavior
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)
pc
Truth/Feedback
Prediction
Predictor
update
predict

## Slide 12: Next Address Predictor: Branch Target Buffer (BTB)
iMem
pc
pci
targeti
BTB permits ppc to be determined before the instruction is decoded
valid
match
k
2k-entry direct-mapped BTB
BTB remembers recent targets for a set of control instructions
  Fetch: looks for the pc and the associated target in BTB; if pc in not found then ppc is pc+4
  Execute: checks prediction, if wrong kills the instruction and updates BTB (only for branches and jumps)
Even small BTBs are effective

## Slide 13: Next Addr Predictor interface
interface AddrPred; method Addr nap(Addr pc); method Action update(Redirect rd); endinterface
Two implementations:
Simple PC+4 predictor
Predictor using BTB

## Slide 14: Simple PC+4 predictor
module mkPcPlus4(AddrPred); method Addr nap(Addr pc);
return pc + 4;
endmethod
method Action update(Redirect rd); endmethod endmodule

## Slide 15: BTB predictor
module mkBtb(AddrPred); RegFile#(BtbIndex, Addr) ppcArr <- mkRegFileFull; RegFile#(BtbIndex, BtbTag) entryPcArr <- mkRegFileFull; Vector#(BtbEntries, Reg#(Bool))
validArr <- replicateM(mkReg(False));
function BtbIndex getIndex(Addr pc)=truncate(pc>>2); function BtbTag getTag(Addr pc) = truncateLSB(pc);
method Addr nap(Addr pc); BtbIndex index = getIndex(pc); BtbTag tag = getTag(pc); if(validArr[index] && tag == entryPcArr.sub(index)) return ppcArr.sub(index); else return (pc + 4); endmethod
method Action update(Redirect redirect); ...
endmodule

## Slide 16: BTB predictor update method
method Action update(Redirect redirect);
if(redirect.taken)
begin let index = getIndex(redirect.pc); let tag = getTag(redirect.pc);
validArr[index] <= True; entryPcArr.upd(index, tag); ppcArr.upd(index, redirect.nextPc);
end
else if(tag == entryPcArr.sub(index))
validArr[index] <= False; endmethod
redirect input contains a pc, the correct next pc and
whether the branch was taken or not (to avoid making
entries for not-taken branches)

## Slide 17: Integrating BTB in the 2-Stage pipeline
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkFifo;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) redirect <- mkFifo;
AddrPred btb <- mkBtb
Scoreboard#(1) sb <- mkScoreboard;
rule doFetch …
rule doExecute …
Notes: 17

## Slide 18: 2-Stage pipeline doExecute rule
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst))
rf.wr(fromMaybe(?, eInst.dst), eInst.data); if(eInst.mispredict) begin redirect.enq(eInst.addr); eEpoch <= !eEpoch; end end d2e.deq; sb.remove; endrule
send information about all branch resolutions for btb training
if(eInst.iType == J || eInst.iType == Jr || eInst.iType == Br) redirect.enq(Redirect{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken, mispredict: eInst.mispredict,
brType: eInst.iType}); if(eInst.mispredict) eEpoch <= !eEpoch; d2e.deq; sb.remove; endrule

## Slide 19: 2-Stage pipeline doFetch rule
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end
else begin let ppc = nextAddrPredictor(pc); let dInst = decode(inst);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(fromMaybe(?, dInst.src1)); let rVal2 = rf.rd2(fromMaybe(?, dInst.src2)); d2e.enq(Decode2Execute{pc: pc, nextPC: ppc,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); pc <= ppc; end
end
endrule
update btb but
change pc only on a mispredict
btb.nap(pc)
btb.update(redirect.first); redirect.deq; end
if(redirect.notEmpty && redirect.first.mispredict)
begin pc <= redirect.first.ppc; fEpoch <= !fEpoch; end

## Slide 20: Multiple Predictors: BTB + Branch Direction Predictors
Suppose we maintain a table of how a particular Br has resolved before. At the decode stage we can consult this table to check if the incoming (pc, ppc) pair matches our prediction. If not redirect the pc
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
correct mispred
correct mispred
stay tuned