## Slide 1
Constructive Computer Architecture
Cache Coherence
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Shared Memory Systems
M
L1
P
L1
P
L1
P
L1
P
L2
L2
L1
P
L1
P
Interconnect
Modern systems often have hierarchical caches
Each cache has exactly one parent but can have zero or more children
Logically only a parent and its children can communicate directly
Inclusion property is maintained between a parent and its children, i.e.,
a  Li  a  Li+1
Because usually
Li+1 >> Li

## Slide 3: Cache-coherence problem
Suppose CPU-1 updates A to 200.
  write-back: memory and cache-2 have stale values
  write-through: cache-2 has a stale value
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100
200
200
Do these stale values matter?
What is the view of shared memory for programming?

## Slide 4: Cache-Coherent Memory
A monolithic memory processes one request at a time; it can be viewed as processing requests instantaneously
A memory with hierarchy of caches is said to be coherent, if functionally it behaves like the monolithic memory
req
res
req
res
Monolithic Memory
...

## Slide 5: Maintaining Coherence
In a coherent memory all loads and stores can be placed in a global order
  multiple copies of an address in various caches can cause this property to be violated
This property can be ensured if:
  Only one cache at a time has the write permission for an address
  No cache can have a stale copy of the data after a write to the address has been performed
      cache coherence protocols are used
      to maintain coherence

## Slide 6: Cache Coherence Protocols
Write request:
  the address is invalidated in all other caches before the write is performed
Read request:
  if a dirty copy is found in some cache then that value is written back to the memory and supplied to the reader. Alternatively the dirty value can be forwarded directly to the reader
Such protocols are called Invalidation-based

## Slide 7: State needed to maintain Cache Coherence
MSI encoding
  I - cache doesn’t contain the address
  S- cache has the address but so may other caches; hence it can only be read
  M- only this cache has the address; hence it can be read and written
S
M
I
store
load
write-back
invalidate
flush
store
The states M, S, I can be thought of as an order M > S > I
  Upgrade: A cache miss causes transition from a lower state to a higher state
  Downgrade: A write-back or invalidation causes a transition from a higher state to a lower state

## Slide 8: Cache Actions
On a read miss (i.e., Cache state is I):
  In case some other cache has the address in state M then write back the dirty data to Memory
  Read the value from Memory and set the state to S
On a write miss (i.e., Cache state is I or S):
  Invalidate the address in all other caches and in case some cache has the address in state M then write back the dirty data
  Read the value from Memory if necessary and set the state to M
How do we know the state of other caches?
Directory

## Slide 9: Directory State Encoding Two-level (L1, M) system
A directory is maintained at each cache to keep track of the state of its children’s caches
  m.child[ck][a]: the state of child ck for address a; At most one child can be in state M
In case of cache hierarchy > 2, the directory also keeps track of the sibling information
  c.state[a]: M means c’s siblings do not have a copy of address a; S means they might
a
a
P
L1
P
L1
L1
Interconnect
<S,I,I,I>
S
P
P

## Slide 10: Directory state encoding transient states to deal with waiting for responses
L1
  wait state is captured in mshr
Directory in home memory
  m.waitc[ck][a] : Denotes if memory m is waiting for a response from its child ck
    No | Yes
  <[(M|S|I), (No | Yes)]>
Child’s state
Waiting for downgrade response

## Slide 11: A Directory-based Protocol an abstract view
interconnect
PP
P
c2m
m2c
L1
p2m
m2p
m
PP
in
out
PP
P
c2m
m2c
L1
p2m
m2p
Each cache has 2 pairs of queues
  (c2m, m2c) to communicate with the memory
  (p2m, m2p) to communicate with the processor
Message format: <cmd, srcdst, a, s, data>
FIFO message passing between each (srcdst) pair except a Req cannot block a Resp
Messages in one srcdst path cannot block messages in another srcdst path
Req/Resp
address
state

## Slide 12: Processing misses: Requests and Responses
1 Up-req send (cache)
2 Up-req proc, Up resp send (memory)
3 Up-resp proc (cache)
4 Dn-req send (memory)
5 Dn-req proc, Dn resp send (cache)
6 Dn-resp proc (memory)
7 Dn-req proc, drop (cache)
8 Voluntary Dn-resp (cache)
Cache
1,5,8
3,5,7
Memory
2,4
2,6
Cache
1,5,8
3,5,7
1
2
4
3
6
5

## Slide 13: CC protocol for blocking caches
Extension to the Blocking L1 design discussed in L17-18

## Slide 14: Req method hit processing
method Action req(MemReq r) if(mshr == Ready);
let a = r.addr;
let hit = contains(state, a);
if(hit) begin
let slot = getSlot(state, a);
let x = dataArray[slot];
if(r.op == Ld) hitQ.enq(x);
else // it is store
if (isStateM(state[slot])
dataArray[slot] <= r.data;
else begin missReq <= r; mshr <= SendFillReq;
missSlot <= slot; end
end
else begin missReq <= r; mshr <= StartMiss; end // (1)
endmethod
PP
P
c2m
m2c
L1
p2m
m2p

## Slide 15: Start-miss and Send-fill rules
rule startMiss(mshr == StartMiss);
let slot = findVictimSlot(state);
if(!isStateI(state[slot]))
begin // write-back (Evacuate)
let a = getAddr(state[slot]);
let d = (isStateM(state[slot])? dataArray[slot]: -);
state[slot] <= (I, _);
c2m.enq(<Resp, c->m, a, I, d>); end
mshr <= SendFillReq; missSlot <= slot; endrule
Rdy -> StrtMiss -> SndFillReq -> WaitFillResp -> Resp -> Rdy
rule sendFillReq (mshr == SendFillReq);
let upg = (missReq.op == Ld)? S : M;
c2m.enq(<Req, c->m, missReq.addr, upg, - >);
mshr <= WaitFillResp; endrule // (1)

## Slide 16: Wait-fill rule and Proc Resp rule
rule waitFillResp(mshr == WaitFillResp);
let <Resp, m->c, a, cs, d> = m2c.msg;
let slot = missSlot;
dataArray[slot] <=
(missReq.op == Ld)? d : missReq.data;
state[slot] <= (cs, a);
m2c.deq;
mshr <= Resp;
endrule // (3)
Rdy -> StrtMiss -> SndFillReq -> WaitFillResp -> Resp -> Rdy
rule sendProc(mshr == Resp);
if(missReq.op == Ld) begin
c2p.enq(dataArray[slot]); end
mshr <= Ready;
endrule
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 17: Parent Responds
rule parentResp;
  let <Req,c->m,a,y,-> = c2m.msg;
  if((i≠c, isCompatible(m.child[i][a],y))
  && (m.waitc[c][a]=No)) begin
  let d = ((m.child[c][a]=I)? m.data[a]: -);
  m2c.enq(<Resp, m->c, a, y, d);
  m.child[c][a]:=y;
  c2m.deq;
  end
endrule
IsCompatible(M, M) = False
IsCompatible(M, S) = False
IsCompatible(S, M) = False
All other cases = True

## Slide 18: Parent (Downgrade) Requests
rule dwn;
let <Req,c->m,a,y,-> = c2m.msg;
if (!isCompatible(m.child[i][a], y) &&
(m.waitc[i][a]=No))
begin
m.waitc[i][a] <= Yes;
m2c.enq(<Req, m->c, a, (y==M?I:S), - >);
end
Endrule // (4)
This rule will execute as long some child cache is not compatible with the incoming request

## Slide 19: Parent receives Response
rule dwnRsp;
let <Resp, c->m, a, y, data> = c2m.msg;
c2m.deq;
if(m.child[c][a]=M) m.data[a]<=data;
m.child[c][a]<=y;
m.waitc[c][a]<=No;
endrule // (6)

## Slide 20: Child Responds
rule dng(mshr != Resp);
let <Req,mc,a,y,-> = m2c.msg;
let slot = getSlot(state,a);
if(getCacheState(state[slot])>y) begin
let d = (isStateM(state[slot])? dataArray[slot]: -);
c2m.enq(<Resp, c->m, a, y, d>);
state[slot] := (M,a);
end
// the address has already been downgraded
m2c.deq;
endrule // (5) and (7)

## Slide 21: Child Voluntarily downgrades
Rules 1 to 8 are complete - cover all possibilities and cannot deadlock or violate cache invariants
rule startMiss(mshr == Ready);
let slot = findVictimSlot(state);
if(!isStateI(state[slot]))
begin // write-back (Evacuate)
let a = getAddr(state[slot]);
let d = (isStateM(state[slot])? dataArray[slot]: -);
state[slot] <= (I, _);
c2m.enq(<Resp, c->m, a, I, d>);
end
endrule // (8)

## Slide 22: Invariants for a CC-protocol design
Directory state is always a conservative estimate of a child’s state
  E.g., if directory thinks that a child cache is in S state then the cache has to be in either I or S state
For every request there is a corresponding response, though sometimes it is generated even before the request is processed
Communication system has to ensure that
  responses cannot be blocked by requests
  a request cannot overtake a response for the same address
At every merger point for requests, we will assume fair arbitration to avoid starvation

## Slide 23: MSI protocol: some issues
It never makes sense to have two outstanding requests for the same address from the same processor/cache
It is possible to have multiple requests for the same address from different processors. Hence there is a need to arbitrate requests
A cache needs to be able to evict an address in order to make room for a different address
  Voluntary downgrade
Memory system (higher-level cache) should be able to force a lower-level cache to downgrade
  caches need to keep track of the state of their children’s caches