## Slide 1
Constructive Computer Architecture
Tutorial 1
BSV
Sizhuo Zhang
6.175 TA

## Slide 2: Bit#(numeric type n)
Literal values:
  Decimal: 0, 1, 2, … (each have type Bit#(n)
  Binary: 5’b01101, 2’b11
  Hex: 5’hD, 2’h3, 16’h1FF0
Common functions:
  Bitwise Logic: |, &, ^, ~, etc.
  Arithmetic: +, -, *, %, etc.
  Indexing: a[i], a[3:1]
  Concatenation: {a, b}
  truncate, truncateLSB
  zeroExtend, signExtend

## Slide 3: Bool
Literal values:
  True, False
Common functions:
  Boolean Logic: ||, &&, !, ==, !=, etc.
All comparison operators (==, !=, >, <, >=, <=) return Bools

## Slide 4: Int#(n), UInt#(n)
Literal values:
  Decimal:
    0, 1, 2, … (Int#(n) and UInt#(n))
    -1, -2, … (Int#(n))
Common functions:
  Arithmetic: +, -, *, %, etc.
    Int#(n) performs signed operations
    UInt#(n) performs unsigned operations
  Comparison: >, <, >=, <=, ==, !=, etc.

## Slide 5: Constructing new types
Renaming types:
  typedef
Enumeration types:
  enum
Compound types:
  struct
  vector
  maybe
  tagged union

## Slide 6: typedef
Syntax:
  typedef <type> <new_type_name>;
Basic:
  typedef 8 BitsPerWord;
  typedef Bit#(BitsPerWord) Word;
    Can’t be used with parameter: Word#(n)
Parameterized:
  typedef Bit#(TMul#(BitsPerWord,n)) Word#(numeric type n);
    Can’t be used without parameter: Word

## Slide 7: enum
    Creates the type Color with values Red and Blue
    Can create registers containing colors
  Reg#(Color)
    Values can be compared with == and !=
    typedef enum {Red, Blue} Color
    deriving (Bits, Eq);

## Slide 8: struct
  Elements from MemReq x can be accessed with x.addr, x.data, x.wren
  Struct Expression
    X = MemReq{addr: 0, data: 1, wren: True};
typedef struct {
Bit#(12) addr;
Bit#(8) data;
Bool wren;
} MemReq deriving (Bits, Eq);

## Slide 9: struct
Parametrized struct
typedef struct {
t a;
Bit#(n) b;
} Req#(type t, numeric type n) deriving (Bits, Eq);

## Slide 10: Tuple
Types:
  Tuple2#(type t1, type t2)
  Tuple3#(type t1, type t2, type t3)
  up to Tuple8
Construct tuple: tuple2( x, y ), tuple3( x, y, z ) …
Accessing an element:
  tpl_1( tuple2(x, y) ) // x
  tpl_2( tuple3(x, y, z) ) // y
  Pattern matching
Tuple2#(Bit#(2), Bool) tup = tuple2(2, True);
match {.a, .b} = tup;
// a = 2, b = True

## Slide 11: Vector
Type:
  Vector#(numeric type size, type data_type)
Values:
  newVector(), replicate(val)
Functions:
  Access an element: []
  Rotate functions
  Advanced functions: zip, map, fold
Can contain registers or modules
Must have ‘import Vector::*;’ in BSV file

## Slide 12: Maybe#(t)
Type:
  Maybe#(type t)
Values:
  tagged Invalid
  tagged Valid x (where x is a value of type t)
Functions:
  isValid(x)
    Returns true if x is valid
  fromMaybe(default, m)
    If m is valid, returns the valid value of m if m is valid, otherwise returns default
    Commonly used fromMaybe(?, m)

## Slide 13: tagged union
Maybe is a special type of tagged union
Tagged unions are collections of types and tags. The type contained in the union depends on the tag of the union.
  If tagged Valid, this type contains a value of type t
typedef union tagged {
void Invalid;
t Valid;
} Maybe#(type t) deriving (Eq, Bits);

## Slide 14: tagged union
Values:
  tagged <tag> value
Pattern matching to get values:
case (x) matches
tagged Valid .a : return a;
tagged Invalid : return 0;
endcase
if(x matches tagged Valid .a &&& a > 1)
begin
$display(“%d”, a);
end

## Slide 15: Reg#(t)
Main state element in BSV
Type: Reg#(type data_type)
Instantiated differently from normal variables
  Uses <- notation
Written to differently from normal variables
  Uses <= notation
  Can only be done inside of rules and methods
Reg#(Bit#(32)) a_reg <- mkReg(0); // value set to 0
Reg#(Bit#(32)) b_reg <- mkRegU(); // uninitialized

## Slide 16: Reg and Vector
Register of Vectors
  Reg#( Vector#(32, Bit#(32) ) ) rfile;
  rfile <- mkReg( replicate(0) );
Vector of Registers
  Vector#( 32, Reg#(Bit#(32)) ) rfile;
  rfile <- replicateM( mkReg(0) );
Each has its own advantages and disadvantages

## Slide 17: Partial Writes
Reg#(Bit#(8)) r;
  r[0] <= 0 counts as a read & write to the entire reg r
    let r_new = r; r_new[0] = 0; r <= r_new
Reg#(Vector#(8, Bit#(1))) r
  Same problem, r[0] <= 0 counts as a read and write to the entire register
  r[0] <= 0; r[1] <= 1 counts as two writes to register
    double write problem
Vector#(8,Reg#(Bit#(1))) r
  r is 8 different registers
  r[0] <= 0 is only a write to register r[0]
  r[0] <= 0 ; r[1] <= 1 is not a double write problem

## Slide 18: Modules
Modules are building blocks for larger systems
  Modules contain other modules and rules
  Modules are accessed through their interface
module mkAdder( Adder#(32) );
  Adder#(32) is the interface
Module can be parametrized
  module name#(params)(args …, interface);
  module mkMul#(Bool signed)(Adder#(n) a, Mul#(n) x);

## Slide 19: Interfaces
Contain methods for other modules to interact with the given module
  Interfaces can also contain sub-interfaces
Special interface: Empty
  No method, used in testbench
interface MyIfc#(numeric type n);
method ActionValue#(Bit#(n)) f();
interface SubIfc#(n) s;
endinterface
module mkTb(Empty);
module mkTb(); // () are necessary

## Slide 20: Interface Methods
Method
  Returns value, doesn’t change state
  method Bit#(32) first;
Action
  Changes state, doesn’t return value
  method Action enq(Bit#(32) x);
ActionValue
  Changes state, returns value
  method ActionValue#(Bit#(32)) deq;

## Slide 21: Implement Interface of Module
Instantiate methods at the end of module
interface MyIfc#(numeric type n);
method ActionValue#(Bit#(n)) f();
interface SubIfc#(n) s;
endinterface
module mkDut(MyIfc#(n));
……
method ActionValue#(Bit#(n)) f();
……
endmethod
interface SubIfc s; // no param “n”
// methods of SubIfc
endinterface
endmodule

## Slide 22: Implement Interface of Module
Return interface at the end of module
  Interface expression
module mkDut(MyIfc#(n));
……
MyIfc ret = (interface MyIfc;
method ActionValue#(Bit#(n)) f();
……
endmethod
interface SubIfc s; // no param “n”
// methods of SubIfc
endinterface
endinterface);
return ret;
endmodule

## Slide 23: Vector Sub-interface
Sub-interface can be vector
BSV reference guide Section 5
interface VecIfc#(numeric type m, numeric type n);
interface Vector#(m, SubIfc#(n)) s;
endinterface
Vector#(m, SubIfc) vec = ?;
for(Integer i=0; i<valueOf(m); i=i+1) begin
// implement vec[i]
end
VecIfc ifc = (interface VecIfc;
interface Vector s = vec; // interface s = vec;
Endinterface);

## Slide 24: Best way to learn BSV
BSV Reference guide
Lab code
Try it
  Makefile in lab 1,2,3…

## Slide 25: Scheduling
Compile flag (BSV user guide)
  -aggressive-conditions (Section 7.12)
    predicated implicit guards
  -show-schedule (Section 8.2.2)
    method/rule schedule information
    Output file: info-dir/*.sched
  -show-rule-rel r1 r2 (Section 8.2.2)
    Print conflict information