## Slide 1: Constructive Computer Architecture Tutorial 4 Debugging
Sizhuo Zhang
6.175 TA

## Slide 2: BSV Debug -- $display
See a bug, not sure what causes it
Add $display statements
Recompile
Run
Still see bug, but you have narrowed it down to a smaller portion of code
Repeat with more display statements…
Find bug, fix bug, and remove display statements

## Slide 3: BSV Display Statements
The $display() command is an action that prints statements to the simulation console
Examples:
  $display(“Hello World!”);
  $display(“The value of x is %d”, x);
  $display(“The value of y is “, fshow(y));

## Slide 4: Ways to Display Values Format Specifiers
%d – decimal
%b – binary
%o – octal
%h – hexadecimal
%0d, %0b, %0o, %0h
  Show value without extra whitespace padding

## Slide 5: Ways to Display Values fshow
fshow is a function in the FShow typeclass
It can be derived for enumerations and structures
Example:
typedef emun {Red, Blue} Colors deriving(FShow);
Color c = Red;
$display(“c is “, fshow(c));
Prints “c is Red”

## Slide 6: BSV Debugging Waveform Viewer
Simulation executables can dump VCD waveforms
  ./bsim_dut –V test.vcd
Produces test.vcd containing the values of all the signals used in the simulator
  Not the same as normal BSV signals
VCD files can be viewed by a waveform viewer
  Such as gtkwave
The signal names and values in test.vcd can be hard to understand
  Especially for structures and enumerations

## Slide 7: Bluespec GUI Example
We use Bluespec GUI + gtkwave to view waveform of VCD files
  gtkwave Installed in vlsifarm matchines
SSH with -X
  ssh –X username@vlsifarm-03.mit.edu
  Windows may need some tools
    Cygwin/X
Use onecycle processor in lab5 as Example

## Slide 8: Bluespec project
We have set SceMi to generate it when building the project
  project.bld: workstation-project-file
  $ cd scemi/sim
  $ build –v onecycle
  onecycle.bspec is the project file

## Slide 9: Simulation: generate VCD file
$ cp ../../programs/build/assembly/vmh/simple.riscv.vmh
mem.vmh
$ ./bsim_dut –V out.vcd > log.txt &
$ ./tb

## Slide 10: Open Bluespec GUI
$ bluespec onecycle.bspec

## Slide 11: Open Module Browser
Window  Module Browser

## Slide 12: Module Browser
Module Hierarchy
Signals
Methods
Top level module

## Slide 14: Open Waveform Viewer

## Slide 15: Load VCD

## Slide 16: Waveform Viewer
Signal
names
Waveform

## Slide 17: Add Signals to View
Add clock

## Slide 18: Add Signals to View
Add PC

## Slide 19: Add Signals to View
Add csrf.wr method

## Slide 20: Add Signals to View
Add can_fire, will_filre for rule doProc

## Slide 21: Waveforms
Readable value

## Slide 22: Problem
No internal signals
  Optimized away during compilation
  But I want to see them for dubuggin
    For example: dInst

## Slide 23: Solution -- Probe
interface Probe#(type t);
method Action _write(t x);
endinterface
module mkProbe(Probe#(t)) provisos(
Bits#(t, sz));
Write to mkProbe will be recorded in VCD file
  Instantiate mkProbe for each signal that we want to record

## Slide 24: Probe Example
import Probe::*;
...
module mkProc(Proc);
mkProbe#(DecodedInst) dInstProbe <- mkProbe;
...
rule doProc;
...
let dInst = decode(inst);
dInstProbe <= dInst;
...
endrule
...
endmodule

## Slide 25: After Adding Probe

## Slide 27: Combine with Assembly
Assembly code of compiled tests are in
  programs/build/*/dump
Refer to the assembly code in debugging

## Slide 28: Debugging Scheduling
GUI: schedule Analysis
  The same as “-show-shedule” BSC flag

## Slide 29: Select mkProc

## Slide 30: Output of Schedule Analysis
Rule order: execution order of rules and methods
  From top to bottom

## Slide 31: Alternative for Schedule Analysis
Add –show-schedule to project.bld
  Generate info_dir/*.sched
  Contain same information as GUI outputs

## Slide 32: General Debugging Advice
Debugging is to guess what goes wrong
Check warnings in compiler outputs
  Scheduling warnings
  Understand all warnings in mkProc
Stare at your code – prove its correctness
Add $display – convenient & very useful
Look at assembly code, locate position
Dump VCD file and see waveform

## Slide 33: Note
Codes on the slide is a little different from our labs
Read src/includes to be familiar with out lab setup.