## Slide 1: EHR: Ephemeral History Register
A new primitive element to design modules with concurrent methods

## Slide 2: Ephemeral History Register (EHR) Dan Rosenband [MEMOCODE’04]
D
Q
0
1
w[0].data
w[0].en
r[0]
normal
bypass
r[1]
0
1
w[1].data
w[1].en
r[0] < w[0]
w[0] < w[1] < ….
r[1] < w[1]
r[1] returns:
– the current state if w[0] is not enabled
– the value being written (w[0].data) if w[0] is enabled
w[i+1] takes precedence over w[i]

## Slide 3: “Happens before” (<) relation
“happens before” relation between the methods of a module governs how the methods behave when called by a rule, action, method or exp
  f < g : f happens before g
  (g cannot affect f within an action)
  f > g : g happens before f
  C : f and g conflict and cannot be called together
  CF : f and g are conflict free and do not affect each
  other
This relation is defined as a conflict matrix (CM) for the methods of primitive modules like registers and EHRs and derived for the methods of all other modules

## Slide 4: Conflict Matrix of Primitive modules: Registers and EHRs
 | EHR.r0 | EHR.w0 | EHR.r1 | EHR.w1
EHR.r0 | CF | < | CF | <
EHR.w0 | > | C | < | <
EHR.r1 | CF | > | CF | <
EHR.w1 | > | > | > | C
 | reg.r | reg.w
reg.r | CF | <
reg.w | > | C
Register
EHR

## Slide 5: Designing FIFOs using EHRs
Conflict-Free FIFO: Both enq and deq are permitted concurrently as long as the FIFO is not-full and not-empty
  The effect of enq is not visible to deq, and vise versa
Pipeline FIFO: An enq into a full FIFO is permitted provided a deq from the FIFO is done simultaneously
Bypass FIFO: A deq from an empty FIFO is permitted provided an enq into the FIFO is done simultaneously

## Slide 6: One-Element Pipelined FIFO
module mkPipelineFifo(Fifo#(1, t));
Reg#(t) d <- mkRegU;
Ehr#(2, Bool) v <- mkEhr(False);
method Bool notFull = !v[1];
method Bool notEmpty = v[0];
method Action enq(t x);
d <= x;
v[1] <= True;
endmethod
method Action deq;
v[0] <= False;
endmethod
method t first;
return d;
endmethod
endmodule
Desired behavior
deq < enq
first < deq
first < enq
No double write error
In any given cycle:
If the FIFO is not empty then simultaneous enq and deq are permitted;
Otherwise, only enq is permitted

## Slide 7: One-Element Bypass FIFO
module mkBypassFifo(Fifo#(1, t));
Ehr#(2, t) d <- mkEhr(?);
Ehr#(2, Bool) v <- mkEhr(False);
method Bool notFull = !v[0];
method Bool notEmpty = v[1];
method Action enq(t x);
d[0] <= x;
v[0] <= True;
endmethod
method Action deq;
v[1] <= False;
endmethod
method t first;
return d[1];
endmethod
endmodule
Desired behavior
enq < deq
first < deq
enq < first
No double write error
In any given cycle:
If the FIFO is not full then simultaneous enq and deq are permitted;
Otherwise, only deq is permitted

## Slide 8: Two-Element Conflict-free FIFO
module mkCFFifo(Fifo#(2, t));
Ehr#(2, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(2, Bool) vb <- mkEhr(False);
method Bool notFull = !vb[0];
method Bool notEmpty = va[0];
method Action enq(t x);
db[0] <= x; vb[0] <= True; endmethod
method Action deq;
va[0] <= False; endmethod
method t first;
return da[0]; endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
db da
Desired behavior
enq CF deq
In any given cycle:
Simultaneous enq and deq are permitted only if the FIFO is not full and not empty
rule canonicalize;
if(vb[1] && !va[1])
(da[1] <= db[1];
va[1] <= True; vb[1] <= False) endrule
all methods are pairwise CF but rule canonicalize comes last

## Slide 9: Deriving the Conflict Matrix (CM) of a module
Let g1 and g2 be the two methods defined by a module, such that
  mcalls(g1)={g11,g12...g1n}
  mcalls(g2)={g21,g22...g2m}
conflict(x,y) = if x and y are methods of the same module then CM[x,y] else CF
Derivation
  CM[g1,g2] = conflict(g11,g21)  conflict(g11,g22) ...
   conflict(g12,g21)  conflict(g12,g22) ...
  …
   conflict(g1n,g21)  conflict(g12,g22) ...
Conflict relation is not transitive
  m1.g1 < m2.g2, m2.g2 < m3.g3 does not imply m1.g1 < m3.g3
Compiler can derive the CM for a module by starting with the innermost modules in the module instantiation tree

## Slide 10: Conflict ordering
This permits us to take intersections of conflict information, e.g.,
  {>}{<,>} = {>}
  {>}{<} = {}
CF = {<,>}
{<} {>}
C = {}

## Slide 11: Deriving CM for One-Element Pipeline FIFO
module mkPipelineFifo(Fifo#(1, t));
Reg#(t) d <- mkRegU;
Ehr#(2, Bool) v <- mkEhr(False);
method Bool notFull = !v[1];
method Bool notEmpty = v[0];
method Action enq(t x);
d <= x;
v[1] <= True;
endmethod
method Action deq;
v[0] <= False;
endmethod
method t first;
return d;
endmethod
endmodule
mcalls(enq) =
mcalls(deq) =
mcalls(first) =
{d.w, v.w1}
{v.w0}
{d.r}

## Slide 12: CM for One-Element Pipeline FIFO
mcalls(enq) = {d.w, v.w1}
mcalls(deq) = {v.w0}
mcalls(first) = {d.r}
CM[enq,deq] =
= {>}
conflict[d.w,v.w0]  conflict[v.w1,v.w0]
This is what we expected!
 | notFull | notEmpty | Enq | Deq | First
notFull | CF | CF | < | > | CF
notEmpty | CF | CF | < | < | CF
Enq | > | > | C | > | >
Deq | < | > | < | C | CF
First | CF | CF | < | CF | CF

## Slide 13: Deriving CM for One-Element Bypass FIFO
module mkBypassFifo(Fifo#(1, t));
Ehr#(2, t) d <- mkEhr(?);
Ehr#(2, Bool) v <- mkEhr(False);
method Bool notFull = !v[0];
method Bool notEmpty = v[1];
method Action enq(t x);
d[0] <= x;
v[0] <= True;
endmethod
method Action deq;
v[1] <= False;
endmethod
method t first;
return d[1];
endmethod
endmodule
mcalls(enq) =
mcalls(deq) =
mcalls(first) =
{d.w0, v.w0}
{v.w1}
{d.r1}

## Slide 14: CM for One-Element Bypass FIFO
mcalls(enq) = {d.w0, v.w0}
mcalls(deq) = {v.w1}
mcalls(first) = {d.r1}
CM[enq,deq] =
= {<}
conflict[d.w0,v.w1]  conflict[v.w0,v.w1]
This is what we expected!
 | notFull | notEmpty | Enq | Deq | First
notFull | CF | CF | < | < | CF
notEmpty | CF | CF | > | < | CF
Enq | > | < | C | < | <
Deq | > | > | > | C | CF
First | CF | CF | > | CF | CF

## Slide 15: CM for Two-Element Conflict-free FIFO
module mkCFFifo(Fifo#(2, t));
Ehr#(2, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(2, Bool) vb <- mkEhr(False);
rule canonicalize;
if(vb[1] && !va[1])
(da[1] <= db[1]|
va[1] <= True| vb[1] <= False) endrule
method Bool notFull = !vb[0];
method Bool notEmpty = va[0];
method Action enq(t x);
db[0] <= x; vb[0] <= True; endmethod
method Action deq;
va[0] <= False; endmethod
method t first;
return da[0]; endmethod
endmodule
db da
Derive the CM

## Slide 16: CM for Two-Element Conflict-free FIFO
mcalls(enq) = { }
mcalls(deq) = { }
mcalls(first) = { }
CM[enq,deq] =
 | notFull | notEmpty | Enq | Deq | First | Canon
notFull | CF | CF |  |  | CF | 
notEmpty | CF | CF |  |  | CF | 
Enq |  |  | C |  |  | 
Deq |  |  |  | C |  | 
First | CF | CF |  |  | CF | 
Canon |  |  |  |  |  | 
Fill the CM

## Slide 17: Rewriting Elastic pipeline as a multirule system
x
fifo1
inQ
f0
f1
f2
fifo2
outQ
rule stage1;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f0(inQ.first)); inQ.deq; end endrule
rule stage2;
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f1(fifo1.first)); fifo1.deq; end endrule
rule stage3;
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f2(fifo2.first)); fifo2.deq; end endrule
How does such a system function?

## Slide 18: Bluespec Execution Model
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
One-rule-at-a-time-semantics: Any legal behavior of a Bluespec program can be explained by observing the state updates obtained by applying only one rule at a time
Highly non-deterministic; User annotations can be used in rule selection
However, for performance we need to execute multiple rules concurrently if possible

## Slide 19: Multi-rule versus single rule elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule elasticPipeline;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first)); inQ.deq; end
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f2(fifo1.first)); fifo1.deq; end
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f3(fifo2.first)); fifo2.deq; end
endrule
How are these two systems the same (or different)?
rule stage1;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first)); inQ.deq; end endrule
rule stage2;
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f2(fifo1.first)); fifo1.deq; end endrule
rule stage3;
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f3(fifo2.first)); fifo2.deq; end endrule

## Slide 20: Elastic pipeline
Do these systems see the same state changes?
  The single rule system – fills up the pipeline and then processes a message at every pipeline stage for every rule firing – no more than one slot in any fifo would be filled unless the OutQ blocks
  The multirule system has many more possible states. It can mimic the behavior of one-rule system but one can also execute rules in different orders, e.g., stage1; stage1; stage2; stage1; stage3; stage2; stage3; … (assuming stage fifos have more than one slot)
When can some or all the rules in a multirule system execute concurrently?
Stay tuned