## Slide 1
Constructive Computer Architecture:
Multirule systems and Concurrent Execution of Rules
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Rewriting Elastic pipeline as a multirule system
x
fifo1
inQ
f0
f1
f2
fifo2
outQ
rule stage1;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f0(inQ.first)); inQ.deq; end endrule
rule stage2;
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f1(fifo1.first)); fifo1.deq; end endrule
rule stage3;
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f2(fifo2.first)); fifo2.deq; end endrule
How does such a system function?

## Slide 3: Bluespec Execution Model
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
One-rule-at-a-time-semantics: Any legal behavior of a Bluespec program can be explained by observing the state updates obtained by applying only one rule at a time
Highly non-deterministic; User annotations can be used in rule selection
However, for performance we need to execute multiple rules concurrently if possible

## Slide 4: Multi-rule versus single rule elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule elasticPipeline;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first)); inQ.deq; end
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f2(fifo1.first)); fifo1.deq; end
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f3(fifo2.first)); fifo2.deq; end
endrule
How are these two systems the same (or different)?
rule stage1;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first)); inQ.deq; end endrule
rule stage2;
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f2(fifo1.first)); fifo1.deq; end endrule
rule stage3;
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f3(fifo2.first)); fifo2.deq; end endrule

## Slide 5: Elastic pipeline
Do these systems see the same state changes?
  The single rule system – fills up the pipeline and then processes a message at every pipeline stage for every rule firing – no more than one slot in any fifo would be filled unless the OutQ blocks
  The multirule system has many more possible states. It can mimic the behavior of one-rule system but one can also execute rules in different orders, e.g., stage1; stage1; stage2; stage1; stage3; stage2; stage3; … (assuming stage fifos have more than one slot)
When can some or all the rules in a multirule system execute concurrently?

## Slide 6: Can these rules execute in parallel? (without violating the one-rule-at-a-time-semantics)
rule ra;
if (z>10)
x <= x+1;
endrule
rule rb;
if (z>20)
y <= y+2;
endrule
Yes, CF
Example 1
No, C
rule ra;
if (z>10)
x <= y+1;
endrule
rule rb;
if (z>20)
y <= x+2;
endrule
Example 2
rule ra;
if (z>10)
x <= y+1;
endrule
rule rb;
if (z>20)
y <= y+2;
endrule
Example 3
Yes, ra < rb

## Slide 7: some insight into Concurrent rule execution
There are more intermediate states in the rule semantics (a state after each rule step)
In the HW, states change only at clock edges
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 8: Parallel execution reorders reads and writes
In the rule semantics, each rule sees (reads) the effects (writes) of previous rules
In the HW, rules only see the effects from previous clocks, and only affect subsequent clocks
Rules
HW
clocks
rule
steps
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes

## Slide 9: Correctness
The compiler will schedule rules concurrently only if the net state change is equivalent to sequential rule execution (which is what our theorem ensures)
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 10: Evaluating or applying a rule
The state of the system s is defined as the value of all its registers
An expression is evaluated by computing its value on the current state
An action defines the next value of some of the state elements based on the current value of the state
A rule is evaluated by evaluating the corresponding action and simultaneously updating all the affected state elements
x y z ...
rule
x’ y’ z’ ...



Given action a and state S, let a(S) represent the state after the application of action a

## Slide 11: One-rule-at-a-time semantics
Given a program with a set of rules {rule ri ai} and an initial state S0 , S is a legal state if and only if there exists a sequence of rules rj1,…., rjn such that S= ajn(…(aj1(S0))…)

## Slide 12: Concurrent execution of two rules
Concurrent execution of two rules, rule r1 a1 and rule r2 a2, means executing a rule whose body looks like (a1; a2), that is a rule which is a parallel composition of the actions of the two rules with the following restrictions to preserve the one-rule-at-a-time semantics:
  Either S. (a1; a2)(S) = a2(a1(S))
  or S. (a1; a2)(S) = a1(a2(S))

## Slide 13: Concurrent scheduling of rules
rule r1 a1 to rule rn an can be scheduled concurrently, preserving one-rule-at-a-time semantics, if and only if there exists a permutation (p1,…,pn) of (1,…,n) such that
  S. (a1;…;an)(S) = apn(…(ap1(S))

## Slide 14: A compiler can determine if two rules can be executed in parallel without violating the one-rule-at-a-time semantics James Hoe, Ph.D., 2000
Construct a conflict matrix (CM) for rules

## Slide 15: Extending CM to rules
CM between two rules is computed exactly the same way as CM for the methods of a module
Given rule r1 a1 and rule r2 a2 such that
  mcalls(a1)={g11,g12...g1n}
  mcalls(a2)={g21,g22...g2m}
Compute
  Conflict(x,y) = if x and y are methods of the same
  module then CM[x,y] else CF
  CM[r1,r2] = conflict(g11,g21)  conflict(g11,g22) ...
   conflict(g12,g21)  conflict(g12,g22) ...
  …
   conflict(g1n,g21)  conflict(g12,g22) ...
Conflict relation is not transitive
  r1 < r2, r2 < r3 does not imply r1 < r3

## Slide 16: Using CMs for concurrent scheduling of rules
Two rules that are conflict free can be scheduled together without violating the one-rule-at-a-time semantics. In general, we use the following theorem
Theorem: Given a set of rules {rule ri ai}, if there exists a permutation {p1, p2 … pn} of {1..n} such that
 i < j. CM(api, apj) is CF or <
  then the rules r1, r2 … rn can be scheduled concurrently with the effect  i, j. rpi < rpj

## Slide 17: Example 2: Compiler Analysis
Rules ra and rb cannot be scheduled together without violating the one-rule-at-a-time-semantics
rule ra;
if (z>10)
x <= y+1;
endrule
rule rb;
if (z>20)
y <= x+2;
endrule
= {>}  {<}
= C
mcalls(ra) = {z.r, x.w, y.r}
mcalls(rb) = {z.r, y.w, x.r}
CM(ra, rb) =
conflict(z.r, z.r)  conflict(z.r, y.w)
conflict(z.r, x.r)  conflict(x.w, z.r)
conflict(x.w, y.w)  conflict(x.w, x.r)
conflict(y.r, z.r)  conflict(y.r, y.w)
Conflict(y.r, x.r)

## Slide 18: Example 3: Compiler Analysis
Rules ra and rb can be scheduled together without violating the one-rule-at-a-time-semantics. Rule ra < rb
rule ra;
if (z>10)
x <= y+1;
endrule
rule rb;
if (z>20)
y <= y+2;
endrule
mcalls(ra) = {z.r, x.w, y.r}
mcalls(rb) = {z.r, y.w, y.r}
CM(ra, rb) =
conflict(z.r, z.r)  conflict(z.r, y.w)
conflict(z.r, y.r)  conflict(x.w, z.r)
conflict(x.w, y.w)  conflict(x.w, y.r)
conflict(y.r, z.r)  conflict(y.r, y.w)
Conflict(y.r, y.r)
= {<}  CF
= {<}

## Slide 19: Multi-rule versus single rule elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule elasticPipeline;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first)); inQ.deq; end
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f2(fifo1.first)); fifo1.deq; end
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f3(fifo2.first)); fifo2.deq; end
endrule
rule stage1;
if(inQ.notEmpty && fifo1.notFull)
begin fifo1.enq(f1(inQ.first)); inQ.deq; end endrule
rule stage2;
if(fifo1.notEmpty && fifo2.notFull)
begin fifo2.enq(f2(fifo1.first)); fifo1.deq; end endrule
rule stage3;
if(fifo2.notEmpty && outQ.notFull)
begin outQ.enq(f3(fifo2.first)); fifo2.deq; end endrule
If we do concurrent scheduling in the multirule system then the multi-rule system behaves like the single rule system

## Slide 20: Concurrency when the FIFOs do not permit concurrent enq and deq
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
not empty
not empty
&
not full
not empty
&
not full
not full
At best alternate stages in the pipeline will be able to fire concurrently