## Slide 1
Constructive Computer Architecture:
Non-Pipelined Processors - 2
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Reading Registers and Executing Instructions
execute
dInst
addr
brTaken
data
iType
dst
ALU
Branch
Address
pc
rVal2
rVal1
Pure combinational logic
either for memory reference or branch target
either for rf write or St
ALUBr
missPredict
RF
src2
src1
Notes: 2
ALU should be split…

## Slide 3: Output type of exec function
typedef struct {
IType iType;
Maybe#(RIndx) dst;
Data data;
Addr addr;
Bool mispredict;
Bool brTaken;
} ExecInst deriving(Bits, Eq);
Notes: Here is the complete typedef:
typedef struct {
IType iType;
Maybe#(RIndx) dst;
Maybe#(CsrIndx) csr;
Data data;
Addr addr;
Bool mispredict;
Bool brTaken;
} ExecInst deriving(Bits, Eq, FShow);

## Slide 4: Execute Function
function ExecInst exec(DecodedInst dInst, Data rVal1,
Data rVal2, Addr pc);
ExecInst eInst = ?;
Data aluVal2 =
let aluRes =
eInst.iType =
eInst.data =
let brTaken =
let brAddr =
eInst.brTaken =
eInst.addr =
eInst.dst =
return eInst;
endfunction
fromMaybe(rVal2, dInst.imm);
alu(rVal1, aluVal2, dInst.aluFunc);
dInst.iType;
dInst.iType==St ? rVal2 :
(dInst.iType==J || dInst.iType==Jr) ?
(pc+4) : dInst.iType==Auipc ?
(pc+fromMaybe(?, dInst.imm)) : aluRes;
aluBr(rVal1, rVal2, dInst.brFunc);
brAddrCalc(pc, rVal1, dInst.iType,
fromMaybe(?, dInst.imm), brTaken);
brTaken;
(dInst.iType==Ld || dInst.iType==St)?
aluRes : brAddr;
dInst.dst;
Notes: Add Auipc in eInst.data

## Slide 5: Single-Cycle SMIPS atomic state updates
if(eInst.iType == Ld)
eInst.data <- dMem.req(MemReq{op: Ld,
addr: eInst.addr, data: ?});
else if (eInst.iType == St) let dummy <- dMem.req(MemReq{op: St,
addr: eInst.addr, data: data});
if(isValid(eInst.dst)) rf.wr(fromMaybe(?, eInst.dst), eInst.data);
pc <= eInst.brTaken ? eInst.addr : pc + 4;
endrule
endmodule
state updates
The whole processor is described using one rule; lots of big combinational functions
Notes: 5

## Slide 6: Processor interface
interface Proc;
method Action hostToCpu(Addr startpc);
method ActionValue#(CpuToHost) cpuToHost;
endinterface
typedef struct {CpuToHostType c2hType; Bit#(16) data;} CpuToHost deriving(Bits, Eq);
typedef enum {ExitCode, PrintChar, PrintIntLow, PrintIntHigh} CpuToHostType deriving(Bits, Eq);
Exit code
& stdout
6.175 convention

## Slide 7: Control and Status Registers (CSR)
CSRs are used to record and control the machine state
  cycle (clock cycles) // read only
  instret (instruction counts) // read only
  hartid (hardware thread ID) // read only
  mtohost (output to host) // write only
  mepc, mcause etc. will be used for exception handleling later
typedef Bit#(12) CsrIndx; // CSR index is 12-bit
CSR is needed as an additional field in DecodedInst and ExecInst types
    Maybe#(CsrIndex) csr;
Notes: I currently implement the 4 CSRs (cycle, instret, hartid, mtohost) in the slide.
There are many other CSRs: e.g. mstatus
We need to implement mepc and mcause when handling exceptions.
cycle, instret, hartid – read-only
mtohost – write-only
  Complete instructions to access CSR: CSRRW[I], CSRRS[I], CSRRC[I]
These instructions will read-modify-write CSRs.
CSRR and CSRW are easiest cases where only read or write happens.

## Slide 8: Instructions to Read and Write CSR
  opcode = SYSTEM
  CSRW rs1, csr (funct3 = CSRRW, rd = x0): csr  rs1
  CSRR csr, rd (funct3 = CSRRS, rs1 = x0): rd  csr
  New enums in IType: Csrr, Csrw
csr
funct3
rs1
rd
opcode
12
5
3
5
7
Notes: I currently implement the 4 CSRs (cycle, instret, hartid, mtohost) in the slide.
There are many other CSRs: e.g. mstatus
We need to implement mepc and mcause when handling exceptions.
cycle, instret, hartid – read-only
mtohost – write-only
  Complete instructions to access CSR: CSRRW[I], CSRRS[I], CSRRC[I]
These instructions will read-modify-write CSRs.
CSRR and CSRW are easiest cases where only read or write happens.

## Slide 9: Code with CSRs
// csrf: module that implements all CSRs
let csrVal = csrf.rd(fromMaybe(?, dInst.csr)); let eInst = exec(dInst, rVal1, rVal2, pc, csrVal);
csrf.wr(eInst.iType == Csrw ? eInst.csr : Invalid, eInst.data);
write CSR (CSRW instruction) and indicate the completion of an instruction
pass CSR values to execute CSRR
We did not show these lines in our processor to avoid cluttering the slides

## Slide 10: Communicating with the host
We will provide you C library functions like print and you will almost never encode anything directly to communicate with tthe host

## Slide 11: Single-Cycle RISC-V: Clock Speed
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
tClock > tM + tDEC + tRF + tALU+ tM+ tWB
We can improve the clock speed if we execute each instruction in two clock cycles
tClock > max {tM , (tDEC + tRF + tALU+ tM+ tWB )}
However, this may not improve the performance because each instruction will now take two cycles to execute
Notes: 11

## Slide 12: Structural Hazards
Sometimes multicycle implementations are necessary because of resource conflicts, aka, structural hazards
  Princeton style architectures use the same memory for instruction and data and consequently, require at least two cycles to execute Load/Store instructions
  If the register file supported less than 2 reads and one write concurrently then most instructions would take more than one cycle to execute
Usually extra registers are required to hold values between cycles

## Slide 13: Two-Cycle RISC-V
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
f2d
state
Introduce register “f2d” to hold a fetched instruction and register “state” to remember the state (fetch/execute) of the processor
Notes: 13

## Slide 14: Two-Cycle RISC-V
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Reg#(Data) f2d <- mkRegU;
Reg#(State) state <- mkReg(Fetch);
rule doFetch (state == Fetch);
let inst = iMem.req(pc);
f2d <= inst;
state <= Execute;
endrule

## Slide 15: Two-Cycle RISC V The Execute Cycle
rule doExecute(stage==Execute);
let inst = f2d;
let dInst = decode(inst);
let rVal1 = rf.rd1(fromMaybe(?, dInst.src1));
let rVal2 = rf.rd2(fromMaybe(?, dInst.src2));
let eInst = exec(dInst, rVal1, rVal2, pc);
if(eInst.iType == Ld)
eInst.data <- dMem.req(MemReq{op: Ld, addr:
eInst.addr, data: ?});
else if(eInst.iType == St)
let d <- dMem.req(MemReq{op: St, addr:
eInst.addr, data: eInst.data});
if (isValid(eInst.dst))
rf.wr(fromMaybe(?, eInst.dst), eInst.data);
pc <= eInst.brTaken ? eInst.addr : pc + 4;
state <= Fetch;
endrule endmodule
no change from single-cycle
Notes: 15

## Slide 16: Two-Cycle RISC-V: Analysis
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
fr
stage
In any given clock cycle, lot of unused hardware !
Execute
Fetch
Pipeline execution of instructions to increase the throughput
Notes: 16

## Slide 17: Problems in Instruction pipelining
Control hazard: Insti+1 is not known until Insti is at least decoded. So which instruction should be fetched?
Structural hazard: Two instructions in the pipeline may require the same resource at the same time, e.g., contention for memory
Data hazard: Insti may affect the state of the machine (pc, rf, dMem) – Insti+1must be fully cognizant of this change
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
+4
f2d
Insti
Insti+1
none of these hazards were present in the FFT pipeline

## Slide 18: Arithmetic versus Instruction pipelining
The data items in an arithmetic pipeline, e.g., FFT, are independent of each other
The entities in an instruction pipeline affect each other
  This causes pipeline stalls or requires other fancy tricks to avoid stalls
  Processor pipelines are significantly more complicated than arithmetic pipelines
sReg1
sReg2
x
inQ
f0
f1
f2
outQ

## Slide 19: The power of computers comes from the fact that the instructions in a program are not independent of each other
 must deal with hazard

## Slide 20: Control Hazards
General solution – speculate, i.e., predict the next instruction address
  requires the next-instruction-address prediction machinery; can be as simple as pc+4
  prediction machinery is usually elaborate because it dynamically learns from the past behavior of the program
What if speculation goes wrong?
  machinery to kill the wrong-path instructions, restore the correct processor state and restart the execution at the correct pc
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
+4
f2d
Insti
Insti+1
Insti+1 is not known until Insti is at least decoded. So which instruction should be fetched?

## Slide 21: Two-stage Pipelined SMIPS
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
nap
f2d
Fetch stage must predict the next instruction to fetch to have any pipelining
Fetch stage
Decode-RegisterFetch-Execute-Memory-WriteBack stage
In case of a misprediction the Execute stage must kill the mispredicted instruction in f2d
kill
misprediction
correct pc
Notes: 21

## Slide 22: Pipelining Two-Cycle RISC-V singlerule
rule doPipeline ;
let newInst = iMem.req(pc);
let newPpc = nap(pc); let newPc = ppc;
let newIr=Valid(Fetch2Decode{pc:newPc,ppc:newPpc,
inst:newIinst});
if(isValid(ir)) begin
let x = fromMaybe(?, ir); let irpc = x.pc;
let ppc = x.ppc; let inst = x.inst;
let dInst = decode(inst);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, irpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin newIr = Invalid;
newPc = eInst.addr; end
end
pc <= newPc; ir <= newIr;
endrule
fetch
execute