## Slide 1
6.175: Constructive Computer Architecture
Tutorial 1
Bluespec SystemVerilog (BSV)
Quan Nguyen
(Only crashed PowerPoint three times)

## Slide 2: What’s Bluespec?
“A synthesizable subset of SystemVerilog”
Rule-based execution
Formal semantics, type safety, object-oriented programming, higher-order functions
A way for you to express hardware designs
  But you still have to know the syntax

## Slide 3: BSV Lineage
Bluespec
(2003)
SystemVerilog
(2002)
Haskell
(1990)
Verilog
(1984)
Lisp
(1958)
ML
(1973)
C/C++
(1972; 1983)
“Bluespec is pretty much a port of Haskell”
-- anonymous grad student

## Slide 4: Outline
Standard types
User-defined types
Modules, interfaces, and methods
Writing and debugging BSV

## Slide 5: Standard Types

## Slide 6: Bit#(numeric type n)
Literal values:
  Decimal: 0, 1, 2, … (each has type Bit#(n))
  Binary: 5’b01101, 2’b11
  Hex: 5’hD, 2’h3, 16’h1FF0
Common functions:
  Bitwise Logic: |, &, ^, ~, etc.
  Arithmetic: +, -, *, %, etc.
  Indexing: a[i], a[3:1]
  Concatenation: {a, b}
  truncate(), truncateLSB()
  zeroExtend(), signExtend()

## Slide 7: Bool
Literal values: True, False
Boolean Logic: ||, &&, !, ==, !=, etc.
All comparison operators (==, !=, >, <, >=, <=) return Bools

## Slide 8: Int#(n), UInt#(n)
Literal values:
  Decimal:
    0, 1, 2, … (Int#(n) and UInt#(n))
    -1, -2, … (Int#(n))
`int` a synonym for Int#(32)
Common functions:
  Arithmetic: +, -, *, %, etc.
    Int#(n) performs signed operations
    UInt#(n) performs unsigned operations
  Comparison: >, <, >=, <=, ==, !=, etc.

## Slide 9: Numeric types, Integers, Ints, oh my!
Bit
Int / UInt
Integer
numeric type
valueOf() or ValueOf()
fromInteger()
fromInteger()
pack()
unpack()
    typedef 5 NumWidth;
    for (Integer i = 0;
    i < 5; i = i + 1)
    Int#(NumWidth) a = 5;
    Bit#(NumWidth) a = 5;

## Slide 10: User-defined types

## Slide 11: Constructing new types
“Renaming” types:
  typedef
Enumeration types:
  enum
Compound types:
  struct
  Vector
  Maybe
  tagged union

## Slide 12: typedef keyword
Syntax:
  typedef <type> <new_type_name>;
Basic:
  typedef 8 BitsPerWord;
  typedef Bit#(BitsPerWord) Word;
    Can’t be used with parameter: Word#(n)
Parameterized:
  typedef Bit#(TMul#(BitsPerWord, n)) Word#(numeric type n);
    Can’t be used without parameter: Word

## Slide 13: enum keyword
Creates the type Color with values Red and Blue
Can create registers containing colors
  Reg#(Color)
Values can be compared with == and !=
  (Why?)
    typedef enum {Red, Blue} Color deriving (Bits, Eq);

## Slide 14: struct keyword
Elements from MemReq x can be accessed with x.addr, x.data, x.wren
Struct expression
  x = MemReq{addr: 0, data: 1, wren: True};
typedef struct {
Bit#(12) addr;
Bit#(8) data;
Bool wren;
} MemReq deriving (Bits, Eq);

## Slide 15: struct keyword
Parameterized struct
typedef struct {
t a;
Bit#(n) b;
} Req#(type t, numeric type n) deriving (Bits, Eq);

## Slide 16: Tuple
Types:
  Tuple2#(type t1, type t2)
  Tuple3#(type t1, type t2, type t3)
  up to Tuple8
  Consider using structs for large[r] aggregate types
Construct tuple: tuple2(x, y), tuple3(x, y, z) …
Accessing an element:
  tpl_1(tuple2(x, y)) // x
  tpl_2(tuple3(x, y, z)) // y
  Pattern matching
Tuple2#(Bit#(2), Bool) tup = tuple2(2, True);
match {.a, .b} = tup; // a = 2, b = True

## Slide 17: Vector
Type:
  Vector#(numeric type size, type data_type)
Values:
  newVector(), replicate(val)
Functions:
  Access an element: []
  Rotate functions
  Advanced functions: zip, map, fold
Can contain registers or modules
Must have ‘import Vector::*;’ in BSV file

## Slide 18: Maybe#(t)
Type:
  Maybe#(type t)
Values:
  tagged Invalid
  tagged Valid x (where x is a value of type t)
Functions:
  isValid(x)
    Returns true if x is valid
  fromMaybe(default, m)
    If m is valid, returns the valid value of m if m is valid, otherwise returns default
    Commonly used as `fromMaybe(?, m)`

## Slide 19: tagged union
Maybe is a special type of tagged union
Tagged unions are collections of types and tags. The type contained in the union depends on the tag of the union.
  If tagged Valid, this type contains a value of type t
typedef union tagged {
void Invalid;
t Valid;
} Maybe#(type t) deriving (Eq, Bits);

## Slide 20: tagged union
Values:
  tagged <tag> value
Pattern matching to get values:
case (x) matches
tagged Valid .a : return a;
tagged Invalid : return 0;
endcase

## Slide 21: Pattern matching and `&&&`
Use `.*` to skip a part of the struct
Use `&&&` to “filter” `matches` expressions with ordinary conditional statements
Tuple2#(Bit#(2), Bool) tup = tuple2(2, True);
match {.a, .*} = tup; // a = 2, b not assigned
function tup_even(Tuple2#(Bit#(2), Bool) tup) =
tup matches {.a, .*} &&&
a [0] == 0 ? True : False;
if (a matches tagged Valid .v &&& v == 5) …

## Slide 22: Reg#(t)
Main state element in BSV
Type: Reg#(type data_type)
Instantiated differently from normal variables
  Uses <- notation
Written to differently from normal variables
  Uses <= notation
  Can only be done inside of rules and methods
Reg#(Bit#(32)) a_reg <- mkReg(0); // value set to 0
Reg#(Bit#(32)) b_reg <- mkRegU(); // uninitialized

## Slide 23: Reg and Vector
Register of Vectors
  Reg#(Vector#(32, Bit#(32))) rfile;
  rfile <- mkReg(replicate(0));
Vector of Registers
  Vector#(32, Reg#(Bit#(32))) rfile;
  rfile <- replicateM(mkReg(0));
Each has its own advantages and disadvantages

## Slide 24: Partial Writes
Reg#(Bit#(8)) r;
  r[0] <= 0 counts as a read & write to the entire reg r
    let r_new = r; r_new[0] = 0; r <= r_new;
Reg#(Vector#(8, Bit#(1))) r;
  Same problem, r[0] <= 0 counts as a read and write to the entire register
  r[0] <= 0; r[1] <= 1 counts as two writes to register
    double write problem
Vector#(8,Reg#(Bit#(1))) r;
  r is 8 different registers
  r[0] <= 0 is only a write to register r[0]
  r[0] <= 0 ; r[1] <= 1 is not a double write problem

## Slide 25: Modules, interfaces, and methods

## Slide 26: Modules
Modules are building blocks for larger systems
  Modules contain other modules and rules
  Modules are accessed through their interface
module mkAdder(Adder#(32));
  Adder#(32) is the interface
Module can be parameterized
  module name#(params)(args …, interface);
  module mkMul#(Bool signed)(Adder#(n) a, Mul#(n) x);

## Slide 27: Interfaces
Contain methods for other modules to interact with the given module
  Interfaces can also contain sub-interfaces
Special interface: Empty
  No method, used in testbench
interface MyIfc#(numeric type n);
method ActionValue#(Bit#(n)) f();
interface SubIfc#(n) s;
endinterface
module mkTb(Empty);
module mkTb(); // () are necessary

## Slide 28: Interface Methods
Method
  Returns value, doesn’t change state
  method Bit#(32) first;
Action
  Changes state, doesn’t return value
  method Action enq(Bit#(32) x);
ActionValue
  Changes state, returns value
  method ActionValue#(Bit#(32)) deq;
  Must use <- operator

## Slide 29: Implement Interface of Module (variant 1)
Instantiate methods at the end of module
interface MyIfc#(numeric type n);
method ActionValue#(Bit#(n)) f();
interface SubIfc#(n) s;
endinterface
module mkDut(MyIfc#(n));
……
method ActionValue#(Bit#(n)) f();
……
endmethod
interface SubIfc s; // no param “n”
// methods of SubIfc
endinterface
endmodule

## Slide 30: Implement Interface of Module (variant 2)
Return interface at the end of module
  Interface expression
module mkDut(MyIfc#(n));
……
MyIfc ret = (interface MyIfc;
method ActionValue#(Bit#(n)) f();
……
endmethod
interface SubIfc s; // no param “n”
// methods of SubIfc
endinterface
endinterface);
return ret;
endmodule

## Slide 31: Vector Sub-interface
Sub-interface can be vector
BSV Reference Guide Section 5
interface VecIfc#(numeric type m, numeric type n);
interface Vector#(m, SubIfc#(n)) s;
endinterface
Vector#(m, SubIfc) vec = ?;
for (Integer i = 0; i < valueOf(m); i = i + 1) begin
// implement vec[i]
end
VecIfc ifc = (interface VecIfc;
interface Vector s = vec; // interface s = vec;
endinterface);

## Slide 32: Writing and debugging BSV

## Slide 33: Best way to learn BSV
BSV Reference Guide
Lab code
Try it
  Makefile in lab 1,2,3…

## Slide 34: Debugging
$display()
  Can only use where Actions allowed
  Works like C printf() or Python str.format()
FShow typeclass
  Creates “pretty-printed” strings for user-defined types
  Typeclasses covered in Tutorial 2

## Slide 35: Scheduling
Compile flag (BSV User Guide [not Reference])
  -aggressive-conditions (Section 7.12)
    predicated implicit guards
  -show-schedule (Section 8.2.2)
    method/rule schedule information
    Output file: buildDir/*.sched
  -show-rule-rel r1 r2 (Section 8.2.2)
    Print conflict information

## Slide 36: Credits
Considerable previous material adapted from last year’s tutorial by Sizhuo Zhang and Andy Wright