## Slide 1
6.175: Constructive Computer Architecture
Tutorial 8
Project Part 2: Coherence
Quan Nguyen
(Will try to stay coherent)

## Slide 2: Debugging Techniques
Deficiency about $display()
  Everything shows up together
Distinct log file for each module: write to file
  Also see src/unit_test/sc-test/Tb.bsv
Ehr#(2, File) file <- mkEhr(InvalidFile);
Reg#(Bool) opened <- mkReg(False);
rule doOpenFile(!opened);
let f <- $fopen("a.txt", "w");
if (f == InvalidFile) $finish;
file[0] <= f; opened <= True;
endrule
rule doPrint;
$fwrite(file[1], "Hello world\n");
endrule
Writing to InvalidFile will cause segfault.
Use EHR if the logic will call $fwrite() in the first cycle

## Slide 3: Debugging Techniques
Deficiency about cycle counter
  Rule for printing cycle may be scheduled before/after the rule we are interested in
  Don’t want to create a counter in each module
Use simulation time
  $display(“%t: evict cache line”, $time);
  $time() returns Bit#(64) representing time
  In SceMi simulation, $time() outputs: 10, 30, ...

## Slide 4: Debugging Techniques
Add sanity checks
Example 1
  Parent is handling upgrade request
  No other child has incompatible state
  Parent decides to send upgrade response
  Check: parent is not waiting for any child (waitc)
Example 2
  D$ receives upgrade response from memory
  Check: must be in WaitFillResp state
  Process the upgrade response
  Check: if in I state, then data in response must be valid, otherwise data must be invalid (data field is Maybe type in the lab)

## Slide 5: Coherence Protocol: Differences From Lecture
In lecture: address type for byte address
  Implementation: only uses cache line address
  (addr >> 6) for 64-byte cache line
In lecture: parent reads data in zero cycles
  Implementation: read from memory, long latency
In lecture: voluntary downgrade rule
  No need in implementation
In lecture: Parent directory tracks states for all address
  32-bit address space → huge directory
  Implementation: usually parent is an L2 cache, so only track address in L2 cache
  But we don’t have an L2 cache

## Slide 6: Coherence Protocol: Differences From Lecture
Workaround for large directory
  For each child, only tracks addresses in its L1 D$
  To get MSI state for address a in core i
Vector#(CoreNum, Vector#(CacheRows, Reg#(CacheTag)))
tags <- replicateM(replicateM(mkRegU));
Vector#(CoreNum, Vector#(CacheRows, Reg#(MSI))
states <- replicateM(replicateM(mkReg(I)));
MSI s = tags[i][getIndex(a)] == getTag(a) ? states[i][getIndex(a)] : I;

## Slide 7: Load-Reserve (lr.w) and Store-Conditional (sc.w)
New state in D$
  Reg#(Maybe#(CacheLineAddr)) la <- mkReg(Invalid);
  Cache line address reserved by lr.w
Load-reserved: lr.w rd, 0(rs1)
  rd <= mem[rs1]
  Make reservation: la <= Valid(getLineAddr(rs1));
Store-conditional: sc.w rd, rs2, 0(rs1)
  Check la: la invalid or addresses don’t match: rd <= 1
  Otherwise: get exclusive permission (upgrade to M)
    Check la again
    If address match: mem[rs1] <= rs2; rd <= 0
    Otherwise: rd <= 1
    If cache hit, no need to check again (address already match)
  Always clear reservation: la <= Invalid

## Slide 8: Load-Reserve (lr.w) and Store-Conditional (sc.w)
Cache line eviction
  Due to replacement, invalidation request ...
  May lose track of reserved cache line
    Then clear reservation
  Compare evicted cache line with la
    If match: la <= invalid
  This is how an LR/SC pair ensures atomicity

## Slide 9: Reference Memory Model
Debug interface returned by reference model is passed into every D$
  D$ calls the into debug interface refDMem
  Reference model will for coherence violations
Reference model: src/ref
interface RefDMem;
method Action issue(MemReq req);
method Action commit(MemReq req,
Maybe#(CacheLine) line, Maybe#(MemResp) resp);
endinterface
module mkDCache#(CoreID id)(
MessageGet fromMem, MessagePut toMem,
RefDMem refDMem, DCache ifc);

## Slide 10: Reference Memory Model
issue(MemReq req)
  Called when req issued to D$
  in req() method of D$
  Give program order to reference model
commit(MemReq req, Maybe#(CacheLine) line, Maybe#(MemResp) resp);
  Called when req() finishes processing (commit)
  line: cache line accessed by req, set to Invalid if unknown
  resp: response to the core, set to Invalid if no repsonse
When commit() is called, reference model checks whether:
  req can be committed
  line value is correct (not checked if Invalid)
  resp is correct

## Slide 11: Adding Store Queue
New behavior for memory requests
  Ld: can start processing when store queue is not empty
  St: enqueue to store queue
  Lr, Sc: wait for store queue to be empty
  Fence: wait for all previous requests to commit (i.e. store queue must be empty)
    Ordering memory accesses
Issuing stores from store queue to process
  Only stall when there is a Ld request

## Slide 12: Multicore Programs
Run programs on 2-core system
Single-thread programs
  Found in programs/assembly, programs/benchmarks
  core 1 starts looping forever at the very beginning
Multithread programs
  Find them in programs/mc_bench
  startup code (crt.S): allocate 128KB local stack for each core
  main() function: fork based on core id
int main() {
int coreid = getCoreId();
if (coreid == 0) { return core0(); }
else { return core1(); }
}

## Slide 13: Multicore Programs: mc_print
Easiest one
Two cores print “0” and “1” respectively
Sample output:
  (no cycle/inst count printed)
---- ../../programs/build/mc_bench/vmh/mc_print.riscv.vmh ----
01
PASSED

## Slide 14: Multicore Programs: mc_hello
Core 0 passes each character of a string to core 1
Core 1 prints each character it receives
Sample output:
  (no cycle/inst count printed)
---- ../../programs/build/mc_bench/vmh/mc_hello.riscv.vmh ----
Hello World!
This message has been written to a software FIFO by core 0 and read and printed by core 1.
PASSED

## Slide 15: Multicore Programs: mc_produce_consume
Larger version of mc_hello
Core 1 passes each element of an array to core 0
Core 0 checks the data
Sample output:
---- ../../programs/build/mc_bench/vmh/mc_produce_consume.riscv.vmh ----
Benchmark mc_produce_consume
Cycles (core 0) = xxx
Insts (core 0) = xxx
Cycles (core 1) = xxx
Insts (core 1) = xxx
Cycles (total) = xxx
Insts (total) = xxx
Return 0
PASSED
Instruction counts may vary due to variation in busy waiting time, so IPC is not a good performance metric.
Execute time is a better metric.

## Slide 16: Multicore Programs: mc_{median,vvadd,multiply}
Data parallel: fork-join style
Core 0 calculates first half results
Core 1 calculates second half results
Sample output:
---- ../../programs/build/mc_bench/vmh/mc_median.riscv.vmh ----
Benchmark mc_median
Cycles (core 0) = xxx
Insts (core 0) = xxx
Cycles (core 1) = xxx
Insts (core 1) = xxx
Cycles (total) = xxx
Insts (total) = xxx
Return 0
PASSED

## Slide 17: Multicore Programs: mc_dekker
Two cores contend for a mutex (Dekker’s algorithm)
After getting into critical section
  increment/decrement shared counter, print core ID
Sample output:
---- ../../programs/build/mc_bench/vmh/mc_dekker.riscv.vmh ----
Benchm1ark mc_1dekker1
100110...000
Core 0 decrements counter by 600
Core 1 increments counter by 900
Final counter value = 300
Cycles (core 0) = xxx
Insts (core 0) = xxx
Cycles (core 1) = xxx
Insts (core 1) = xxx
Cycles (total) = xxx
Insts (total) = xxx
Return 0
PASSED
For implementation with store queue, a fence is inserted in mc_dekker.

## Slide 18: Multicore Programs: mc_spin_lock
Similar to mc_dekker, but use spin lock implemented by lr.w/sc.w
Sample output:
---- ../../programs/build/mc_bench/vmh/mc_spin_lock.riscv.vmh ----
Bench1mark mc1_spin_l1ock
10101...000
Core 0 increments counter by 300
Core 1 increments counter by 600
Final counter value = 900
Cycles (core 0) = xxx
Insts (core 0) = xxx
Cycles (core 1) = xxx
Insts (core 1) = xxx
Cycles (total) = xxx
Insts (total) = xxx
Return 0
PASSED

## Slide 19: Multicore Programs: mc_incrementers
Similar to mc_dekker, but use atomic fetch-and-add implemented by lr.w/sc.w
Core ID is not printed
Sample output:
---- ../../programs/build/mc_bench/vmh/mc_incrementers.riscv.vmh ----
Benchmark mc_incrementers
core0 had 1000 successes out of xxx tries
core1 had 1000 successes out of xxx tries
shared_count = 2000
Cycles (core 0) = xxx
Insts (core 0) = xxx
Cycles (core 1) = xxx
Insts (core 1) = xxx
Cycles (total) = xxx
Insts (total) = xxx
Return 0
PASSED

## Slide 20: Some Reminders
Use CF regfile and scoreboard
  Compiler creates a conflict in Sizhuo’s implementation with bypass regfile and pipelined scoreboard
Sign up for project meeting
Project deadline: 3:00pm Dec 14
Final presentation (10min)