## Slide 1
Constructive Computer Architecture
Modules with Guarded Interfaces
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Notes: (Andy) Changed course website to correct website

## Slide 2: Guarded interfaces
Make the life of the programmers easier: Include some checks (readyness, fullness, ...) in the method definition itself, so that the user does not have to test the applicability of the method from outside
Guarded Interface:
  Every method has a guard (rdy wire)
  The value returned by a method is meaningful only if its guard is true
  Every action method has an enable signal (en wire) and it can be invoked (en can be set to true) only if its guard is true
not full
not empty
not empty
n
n
rdy
en
rdy
en
rdy
enq
deq
first
FIFO
interface Fifo#(numeric type size, type t);
method Action enq(t x);
method Action deq;
method t first;
endinterface
notice, en and rdy wires are implicit

## Slide 3: One-Element FIFO Implementation with guards
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x)
v <= True; d <= x;
endmethod
method Action deq
v <= False;
endmethod
method t first
return d;
endmethod
endmodule
not full
not empty
not empty
n
n
rdy
en
rdy
en
rdy
enq
deq
first
FIFO
if (!v);
if (v);
if (v);
Notice, no semicolon turns the if into a guard

## Slide 4: Rules with guards
Like a method, a rule can also have a guard
A rule can execute only if it’s guard is true, i.e., if the guard is false the rule has no effect
True guards can be omitted
rule foo (p);
begin x1 <= e1; x2 <= e2 end
endrule
guard

## Slide 5: Streaming a function using a FIFO with guarded interfaces
inQ
f
outQ
rule stream;
if(inQ.notEmpty && outQ.notFull)
begin outQ.enq(f(inQ.first)); inQ.deq; end endrule
rule stream (True);
outQ.enq(f(inQ.first)); inQ.deq;
endrule

## Slide 6: Implicit Guards

## Slide 7: Switch using FIFOs with guarded interfaces
inQ
redQ
greenQ
switch
rule switch;
if (inQ.notEmpty)
if (inQ.first.color == Red) begin1
if (redQ.notFull) begin2
redQ.enq(inQ.first.value); inQ.deq;
end2
end1
else begin3
if (greenQ.notFull) begin4
greenQ.enq(inQ.first.value); inQ.deq;
end4
end3
endrule
All the red stuff can be deleted

## Slide 8: Switch using FIFOs with guarded interfaces
inQ
redQ
greenQ
switch
rule switch (True);
if (inQ.first.color == Red)
begin redQ.enq (inQ.first.value); inQ.deq; end
else begin greenQ.enq(inQ.first.value); inQ.deq; end
endrule
Implicit guard?

## Slide 9: GCD with and without guards
start
GCD
busy
getResult
ready
start
GCD
getResult
ready
busy
en
en
en
Interface without guards
Interface with guards
en
interface GCD;
method Action start (Bit#(32) a, Bit#(32) b);
method ActionValue#(Bit#(32)) getResult;
method Bool busy;
method Bool ready;
endinterface

## Slide 10: Using GCD module with guarded interfaces
outQ
inQ
rule invokeGCD;
gcd.start(inQ.first); inQ.deq;
endrule;
invoke
GCD
get
result
rule getResult;
let x <- gcd.getResult; outQ.enq(x);
endrule;
start
GCD
getResult
A rule can be executed only if guards of all of its actions are true

## Slide 11: GCD with guarded interfaces implementation
module mkGCD (GCD);
Reg#(Bit#(32)) x <- mkReg(0);
Reg#(Bit#(32)) y <- mkReg(0);
Reg#(Bool) busy <- mkReg(False);
rule gcd;
if (x >= y) begin x <= x – y; end //subtract
else if (x != 0) begin x <= y; y <= x; end //swap
endrule
method Action start(Bit#(32) a, Bit#(32) b)
x <= a; y <= b; busy <= True;
endmethod
method ActionValue (Bit#(32)) getResult
busy <= False; return y;
endmethod
endmodule
Assume b /= 0
interface GCD;
method Action start
(Bit#(32) a,Bit#(32) b);
method ActionValue(Bit#(32))
getResult;
endinterface
if (!busy);
if (x==0);

## Slide 12: Guards vs Ifs
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action enq(t x);
if (!v) begin v <= True; d <= x; end
endmethod
versus
guard is !v; enq can be applied only if v is false
guard is True, i.e., the method is always applicable.
if v is true then x would get lost;
bad

## Slide 13: Pipelining combinational circuits

## Slide 14: Pipelining Combinational Functions
Lot of area and long combinational delay
Folded or multi-cycle version can save area and reduce the combinational delay but throughput per clock cycle gets worse
Pipelining: a method to increase the circuit throughput by evaluating multiple inputs
xi
xi-1
xi+1
3 different datasets in the pipeline
f0
f1
f2

## Slide 15: Inelastic vs Elastic pipeline
x
fifo1
inQ
f0
f1
f2
fifo2
outQ
x
sReg1
inQ
f0
f1
f2
sReg2
outQ
Inelastic: all pipeline stages move synchronously
Elastic: A pipeline stage can process data if its input FIFO is not empty and output FIFO is not Full
Most complex processor pipelines are a combination of the two styles

## Slide 16: Elastic pipeline Use FIFOs instead of pipeline registers
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1;
fifo1.enq(f1(inQ.first));
inQ.deq(); endrule
rule stage2;
fifo2.enq(f2(fifo1.first));
fifo1.deq; endrule
rule stage3;
outQ.enq(f3(fifo2.first));
fifo2.deq; endrule
When can stage1 rule fire?
Can tokens be left in the pipeline?
Can these rules execute concurrently?
- inQ has an element
- fifo1 has space
No
no need for valid bits

## Slide 17: Elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1;
fifo1.enq(f1(inQ.first));
inQ.deq(); endrule
rule stage2;
fifo2.enq(f2(fifo1.first));
fifo1.deq; endrule
rule stage3;
outQ.enq(f3(fifo2.first));
fifo2.deq; endrule
If these rules cannot execute concurrently, it is hardly a pipelined system
When can rules execute concurrently?
What hardware is synthesized to execute rules concurrently?

## Slide 18: Multi-rule Systems
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
One-rule-at-a-time-semantics: Any legal behavior of a Bluespec program can be explained by observing the state updates obtained by applying only one rule at a time
Non-deterministic choice; User annotations can be used in rule selection
However, for performance we execute multiple rules concurrently whenever possible
stay tuned …

## Slide 20: Inelastic pipeline
x
sReg1
inQ
f0
f1
f2
sReg2
outQ
rule sync_pipeline;
inQ.deq;
sReg1 <= f0(inQ.first);
sReg2 <= f1(sReg1);
outQ.enq(f2(sReg2))
endrule
When can this rule execute?

## Slide 21: Pipeline bubbles
x
sReg1
inQ
f0
f1
f2
sReg2
outQ
rule sync_pipeline;
inQ.deq;
sReg1 <= f0(inQ.first);
sReg2 <= f1(sReg1);
outQ.enq(f2(sReg2))
endrule
- Red and Green tokens must move even if there is nothing in inQ!
Modify the rule to deal with these conditions
- Also if there is no token in sReg2 then nothing should be enqueued in the outQ
Introduce a valid bit
Some issues

## Slide 22: Explicit encoding of data presence
rule sync_pipeline;
if(outQ.notFull || sReg2v != true)
if (inQ.notEmpty)
begin sReg1 <= f0(inQ.first); inQ.deq;
sReg1v <= true end
else sReg1v <= false;
sReg2 <= f1(sReg1); sReg2v <= sReg1v;
if (sReg2v == true) outQ.enq(f2(sReg2)))
endrule
sReg1
sReg2
x
inQ
f0
f1
f2
outQ
valid bit