## Slide 1
Constructive Computer Architecture
Folded “Combinational” circuits
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Notes: (Andy) Changed course website to correct website

## Slide 2: Design Alternatives
f1
f2
f3
f1
f2
f3
fi
Combinational (C)
Pipeline (P)
Folded (F)
Reuse a block,
multicycle
Clock?
Area?
Throughput?
Clock: C < P  F
Area: F < C < P
Throughput: F < C < P

## Slide 3: Content
How to implement loop computations?
  Need registers to hold the state from one iteration to the next
Request-Response Latency-Insensitive modules
A common way to implement large combinational circuits is by folding or as loops
  Multiplication
Polymorphic Multiply

## Slide 4: Expressing a loop using registers
int s = s0;
while (p(s)) { s = f(s); } return s; C-code
sel = start
en = start | notDone
s
p
notDone
s0
f
sel
en
Such a loop cannot be implemented by unfolding because the number of iterations is input-data dependent
A register is needed to hold s from one iteration to the next
s has to be initialized when the computation starts, and updated every cycle until the computation terminates

## Slide 5: Expressing a loop in BSV
sel = start
en = start | notDone
Reg#(t) s <- mkRegU();
rule step;
if (p(s)) begin s <= f(s);
end endrule
When a rule executes:
  the register s is read at the beginning of a clock cycle
  computations to evaluate the next value of the register and the sen are performed
  If sen is True then s is updated at the end of the clock cycle
A mux is needed to initialize the register
p
notDone
s0
f
sel
s
en
How should this circuit be packaged for proper use?

## Slide 6: Packaging a computation as a Latency-Insensitive Module
Interface with guards
interface F#(t);
method Action start (t a);
method ActionValue#(t) getResult;
endinterface
startF
F
getResultF
ready
busy
en
en

## Slide 7: Request-Response Module
module mkF (F#(t));
Reg#(t) s <-mkRegU();
Reg#(Bool) busy <- mkReg(False);
rule step;
if (p(s)) begin s <= f(s);
end endrule
method Action start(t a) if (!busy);
s <= a; busy <= True;
endmethod
method ActionValue t getResult if (!p(s)&& busy);
busy <= False; return s;
endmethod
endmodule

## Slide 8: Using F
outQ
inQ
rule invokeF;
f.start(inQ.first); inQ.deq;
endrule
invoke
F
get
result
rule getResult;
let x <- f.getResult; outQ.enq(x);
endrule
start
F
getResult
A rule can be executed only if guards of all of its actions are true
This system is insensitive to the latency of F
F#(t) f <- mkF(…)

## Slide 9: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) tp = 0; Bit#(32) prod = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0];
tp = sum[32:1];
end return {tp,prod}; endfunction
Combinational circuit uses 31 add32 circuits
We can reuse the same add32 circuit if we store the partial results in a register

## Slide 10: Multiply using registers
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i:i] = sum[0]; tp = sum[32:1]; end return {tp,prod}; endfunction
Need registers to hold a, b, tp, prod and i
Update the registers every cycle until we are done
Combinational version

## Slide 11: Sequential Circuit for Multiply
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep;
if (i < 32) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] <= sum[0]; tp <= sum[32:1];
i <= i+1;
end endrule
state elements
a rule to describe the dynamic behavior
So that the rule has no effect until i is set to some other value
similar to the loop body in the combinational version

## Slide 12: Dynamic selection requires a mux
a[i]
a
i
a[0],a[1],a[2],…
a
>>
0
when the selection indices are regular then it is better to use a shift operator (no gates!)

## Slide 13: Replacing repeated selections by shifts
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= a >> 1; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], prod[31:1]}; tp <= sum[32:1];
i <= i+1; endrule

## Slide 14: Circuit for Sequential Multiply
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
s1 = start_en
s2 = start_en | !done
result (high)
31
0
add
0
0
32:1
0
<<

## Slide 15: Circuit analysis
Number of add32 circuits has been reduced from 31 to one, though some registers and muxes have been added
The longest combinational path has been reduced from 62 FAs to one add32 plus a few muxes
The sequential circuit will take 31 clock cycles to compute an answer
Notes: (Andy) longest combinational path was effectively 63 1-bit adders.

## Slide 16: Packaging Multiply as a Latency-Insensitive Module
Interface with guards
interface Multiply;
method Action startMul (Bit#(32) a, Bit#(32) b);
method ActionValue#(Bit#(64)) getResultMul;
endinterface
startMul
Multiply
getMulResult
ready
busy
en
en
64
32
32

## Slide 17: Multiply Module
Module mkMultiply (Multiply);
Reg#(Bit#(32)) a<-mkRegU(); Reg#(Bit#(32)) b<-mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
Reg#(Bool) busy <- mkReg(False);
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= a >> 1; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], prod[31:1]}; tp <= sum[32:1]; i <= i+1;
endrule
method Action startMul(Bit#(32) x, Bit#(32) y) if (!busy);
a <= x; b <= y; busy <= True; i <= 0; endmethod
method ActionValue Bit#(64) getMulRes if ((i==32) && busy);
busy <= False; return {tp,prod}; endmethod

## Slide 18: Circuit for Sequential Multiply
s1 = start_en
s2 = start_en | !done
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
result (high)
31
0
add
0
0
32:1
0
<<
a
b
en
rdy
startMul
en
rdy
getMulRes
busy

## Slide 19: Polymorphic Multiply Module
Polymorphic Interface
interface Multiply#(32);
method Action startMul (Bit#(32) a, Bit#(32) b);
method ActionValue#(Bit#(64)) getResultMul;
endinterface
startMul
Multiply
getMulResult
ready
busy
en
en
64
32
32
t
t
Tmul#(t,2)
Tmul#(t,2)
t
t

## Slide 20: Polymorphic Multiply
Module mkMultiply (Multiply#(t));
Reg#(Bit#(t)) a<-mkRegU(); Reg#(Bit#(t)) b<-mkRegU();
Reg#(Bit#(t)) prod <-mkRegU(); Reg#(Bit#(t)) tp <- mkReg(0); vt = valueOf(t);
Reg#(Bit#(TAdd#(1, TLog#(t)))) i <- mkReg(vt);
Reg#(Bool) busy <- mkReg(False); rule mulStep if (i < vt); Bit#(t) m = (a[0]==0)? 0 : b;
a <= a >> 1; Bit#(Tadd#(t)) sum = addN(m,tp,0); prod <= {sum[0], prod[(vt-1):1]}; tp <= sum[vt:1]; i <= i+1;
endrule
method Action startMul(Bit#(t) x, Bit#(t) y) if (!busy);
a <= x; b <= y; busy <= True; i<=0; endmethod
method ActionValue#(Bit#(TMul#(t,2)) getMulRes if
((i==vt)&& busy);
busy <= False; return {tp,prod}; endmethod