## Slide 1
Constructive Computer Architecture:
RISC-V Instruction Set Architecture (ISA)
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: ISA: The software interface of programmable machine
Instruction set architecture is a set of instructions
Each instruction defines a way to transform the machine state
ISA is a contract that an architect must follow while designing a machine a for a specific Performance, Power and Area (PPA) objective
ISA
Software tools
assembler compilers interpreters OS, ...
non-pipelined pipelined OOO ...
Micro-architectures

## Slide 3: RISC-V
A new, open, free ISA from Berkeley
Several variants
  RV32, RV64, RV128 – Different data widths
  ‘I’ – Base Integer instructions
  ‘M’ – Multiply and Divide
  ‘A’ – Atomic memory instructions
  ‘F’ and ‘D’ – Single and Double precision floating point
  ‘V’ – Vector extension
  And many other modular extensions
We will design an RV32I processor which is the base 32-bit variant

## Slide 4: RV32I Register State
32 general purpose registers (GPR)
  x0, x1, …, x31
  32-bit wide integer registers
  x0 is hard-wired to zero
Program counter (PC)
  32-bit wide
CSR (Control and Status Registers)
  User-mode
    cycle (clock cycles) // read only
    instret (instruction counts) // read only
  Machine-mode
    hartid (hardware thread ID) // read only
    mepc, mcause etc. used for exception handling
  Custom
    mtohost (output to host) // write only – custom extension
Memory

## Slide 5: Instruction Types
Register-to-Register Arithmetic and Logical operations
Control Instructions alter the sequential control flow
Memory Instructions move data to and from memory
CSR Instructions move data between CSRs and GPRs; the instructions often perform read-modify-write operations on CSRs
Privileged Instructions are needed by the operating systems, and most cannot be executed by user programs

## Slide 6: Instruction Formats
funct7
rs2
funct3
rs1
rd
opcode
7
5
5
3
5
7
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
R-type instruction
I-type instruction & I-immediate (32 bits)
S-type instruction & S-immediate (32 bits)
imm[11:5]
rs2
funct3
rs1
imm[4:0]
opcode
7
5
5
3
5
7
S-imm = signExtend({inst[31:25], inst[11:7]})
I-imm = signExtend(inst[31:20])
source reg
destination reg

## Slide 7: Instruction Formats cont.
SB-type instruction & B-immediate (32 bits)
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7
B-imm = signExtend({inst[31], inst[7], inst[30:25], inst[11:8], 1’b0})
U-type instruction & U-immediate (32 bits)
rd
opcode
5
7
imm[31:12]
20
U-imm = signExtend({inst[31:12], 12’b0})
UJ-type instruction & J-immediate (32 bits)
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7
J-imm = signExtend({inst[31], inst[19:12], inst[20], inst[30:21], 1’b0})
Immediate constants have strange encodings!

## Slide 8: Computational Instructions
Register-Register instructions (R-type)
  opcode=OP: rd  rs1 (funct3, funct7) rs2
  funct3 = SLT/SLTU/AND/OR/XOR/SLL
  funct3= ADD
    funct7 = 0000000: rs1 + rs2
    funct7 = 0100000: rs1 – rs2
  funct3 = SRL
    funct7 = 0000000: logical shift right
    funct7 = 0100000: arithmetic shift right
funct7
rs2
funct3
rs1
rd
opcode
7
5
5
3
5
7

## Slide 9: Computational Instructions cont
Register-immediate instructions (I-type)
  opcode = OP-IMM: rd  rs1 (funct3) I-imm
  I-imm = signExtend(inst[31:20])
  funct3 = ADDI/SLTI/SLTIU/ANDI/ORI/XORI
A slight variant in coding for shift instructions - SLLI / SRLI / SRAI
  rd  rs1 (funct3, inst[30]) I-imm[4:0]
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
Notes: What is the role of inst[30]?

## Slide 10: Computational Instructions cont.
Register-immediate instructions (U-type)
  opcode = LUI : rd  U-imm
  opcode = AUIPC : rd  pc + U-imm
  U-imm = {inst[31:12], 12’b0}
rd
opcode
5
7
imm[31:12]
20

## Slide 11: Control Instructions
  Unconditional jump and link (UJ-type)
  opcode = JAL: rd  pc + 4; pc  pc + J-imm
  J-imm = signExtend({inst[31], inst[19:12], inst[20], inst[30:21], 1’b0})
  Jump ±1MB range
Unconditional jump via register and link (I-type)
  opcode = JALR: rd  pc + 4; pc  (rs1 + I-imm) & ~0x01
  I-imm = signExtend(inst[31:20])
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
Notes:   Effect of ~0x01

## Slide 12: Control Instructions cont.
Conditional branches (SB-type)
  opcode = BRANCH: pc  compare(funct3, rs1, rs2) ? pc + B-imm : pc + 4
  B-imm = signExtend({inst[31], inst[7], inst[30:25], inst[11:8], 1’b0})
  Jump 4KB range
  funct3 = BEQ/BNE/BLT/BLTU/BGE/BGEU
imm[12]
imm[10:5]
rs2
rs1
funct3
imm[4:1]
imm[11]
opcode
1
6
5
5
3
4
1
7

## Slide 13: Load & Store Instructions
Load (I-type)
  opcode = LOAD: rd  mem[rs1 + I-imm]
  I-imm = signExtend(inst[31:20])
  funct3 = LW/LB/LBU/LH/LHU
Store (S-type)
  opcode = STORE: mem[rs1 + S-imm]  rs2
  S-imm = signExtend({inst[31:25], inst[11:7]})
  funct3 = SW/SB/SH
imm[11:0]
funct3
rs1
rd
opcode
12
5
3
5
7
imm[11:5]
rs2
funct3
rs1
imm[4:0]
opcode
7
5
5
3
5
7
Notes: Ignore byte and half word instructions: LB, LBU, LH, LHU, SB, SH

## Slide 14: Instructions to Read and Write CSR
  opcode = SYSTEM
  CSRW rs1, csr (funct3 = CSRRW, rd = x0): csr  rs1
  CSRR csr, rd (funct3 = CSRRS, rs1 = x0): rd  csr
csr
funct3
rs1
rd
opcode
12
5
3
5
7
Notes: I currently implement the 4 CSRs (cycle, instret, hartid, mtohost) in the slide.
There are many other CSRs: e.g. mstatus
We need to implement mepc and mcause when handling exceptions.
cycle, instret, hartid – read-only
mtohost – write-only
  Complete instructions to access CSR: CSRRW[I], CSRRS[I], CSRRC[I]
These instructions will read-modify-write CSRs.
CSRR and CSRW are easiest cases where only read or write happens.

## Slide 15: Assembly Code VS Binary
Its too tedious to write programs in binary
To simplify writing programs, assemblers provide:
  mnemonics for instructions
    add x1, x2, x3
  pseudo instructions
    mov x1, x2 // short for add x1, x2, x0
    li x1, 6175 // short for lui x1, 2 ; addi x1, x1, -2017 (exact sequence depends on immediate value)
  symbols for program locations and data
    bnz x1, loop_begin
    lw x1, flag
Assemblers translate programs into machine code for the processor to execute

## Slide 16: GCD in C
// require: x >= 0 && y > 0
int gcd(int a, int b) {
int t;
while(a != 0) {
if(a >= b) {
a = a - b;
}
else {
t = a; a = b; b = t;
}
}
return b;
}

## Slide 17: GCD in RISC-V Assembler
// a: x1, b: x2, t: x3
begin:
beqz x1, done // if(x1 == 0) goto done
blt x1, x2, b_bigger // if(x1 < x2) goto b_bigger
sub x1, x1, x2 // x1 := x1 - x2
j begin // goto begin
b_bigger:
mv x3, x1 // x3 := x1
mv x1, x2 // x1 := x2
mv x2, x3 // x2 := x3
j begin // goto begin
done: // now x2 contains the gcd

## Slide 18: Application Binary Interface (ABI)
Specifies rules for register usage in passing arguments and results for function calls
  Callee-saved registers vs Caller-saved registers
Assigns aliases for registers x1-x31
  a0 to a7 – function argument registers (caller-saved)
  a0 and a1 – function return value registers
  s0 to s11 – Saved registers (callee-saved)
  t0 to t6 – temporary registers (caller-saved)
  ra – return address (caller-saved)
  sp – stack pointer (callee-saved)
  gp (global pointer), and tp (thread pointer) point to specific locations in memory used by the program for global and thread-local variables respectively

## Slide 19: Calling GCD Using the ABI
// assume we want to do the gcd of s0 and s1
// and put the result in s2
mov a0, s0
mov a1, s1
addi sp, sp, -8 // saving registers in the stack
// as needed by the caller
sw t0, 4(sp)
sw t1, 0(sp)
jal gcd // call gcd function
lw t0, 4(sp) // restoring caller-saved registers
lw t1, 0(sp)
addi sp, sp, 8
mov s2, a0
preparing arguments in a0, a1, etc.
temporary

## Slide 20: GCD in RISC-V Assembler Using the ABI
// a: a0, b: a1, t: t0
gcd:
beqz a0, done
blt a0, a1, b_bigger
sub a0, a0, a1
j gcd
b_bigger:
mv t0, a0
mv a0, a1
mv a1, t0
j gcd
done: // now a1 contains the gcd
mv a0, a1 // move to a0 for returning
ret // jr ra
argument
temporary
ABI dictates that the result must come back in a0
// a: x1, b: x2, t: x3
begin:
beqz x1, done
blt x1, x2, b_bigger
sub x1, x1, x2
j begin
b_bigger:
mv x3, x1
mv x1, x2
mv x2, x3
j begin
done:

## Slide 21: Multiply
mul x1, x2, x3 is an instruction in the ‘M’ extension (x1 := x2 * x3)
  If ‘M’ is not implemented, this is an illegal instruction
What happens if we run code from an RV32IM machine on an RV32I machine?
  mul causes an illegal instruction exception
An exception handler can take over and abort the program or emulate the instruction

## Slide 22: Exception handling
When an exception is caused
  Hardware saves the information about the exception in CSRs:
    mepc – exception PC
    mcause – cause of the exception
    mstatus.mpp – privilege mode of exception
  Processor jumps to the address of the trap handler (stored in the mtvec CSR) and increases the privilege level
An exception handler, a software program, takes over and performs the necessary action

## Slide 23: Software for interrupt handling
Hardware transfers control to the common software interrupt handler (CH) which:
  Saves all GPRs into the memory pointed by mscratch
  Passes mcause, mepc, stack pointer to the IH (a C function) to handle the specific interrupt
  On the return from the IH, writes the return value to mepc
  Loads all GPRs from the memory
  Execute ERET, which does:
    set pc to mepc
    pop mstatus (mode, enable) stack
IH
IH
IH
CH
1
2
3
4
5
GPR

## Slide 24: Common Interrupt Handler- SW
common_handler: # entry point for exception handler # get the pointer to HW-thread local stack
csrrw sp, mscratch, sp # swap sp and mscratch
# save x1, x3 ~ x31 to stack (x2 is sp, save later)
addi sp, sp, -128
sw x1, 4(sp)
sw x3, 12(sp)
...
sw x31, 124(sp)
# save original sp (now in mscratch) to stack
csrr s0, mscratch # store mscratch to s0
sw s0, 8(sp)

## Slide 25: Common handler- SW cont. Setting up and calling IH_Dispacher
common_handler:
... # we have saved all GPRs to stack
# call C function to handle interrupt
csrr a0, mcause # arg 0: cause
csrr a1, mepc # arg 1: epc
mv a2, sp # arg 2: sp – pointer to all saved GPRs
jal ih_dispatcher # calls ih_dispatcher which may
# have been written in C
# return value is the PC to resume
csrw mepc, a0
# restore mscratch and all GPRs
addi s0, sp, 128; csrw mscratch, s0
lw x1, 4(sp); lw x3, 12(sp); ...; lw x31, 124(sp)
lw x2, 8(sp) # restore sp at last
mret # finish handling interrupt

## Slide 26: IH Dispatcher (in C)
long ih_dispatcher(long cause, long epc, long *regs) {
// regs[i] refers to GPR xi stored in stack
if(cause == 0x02)
// illegal instruction
return illegal_ih(cause, epc, regs);
else if(cause == 0x08)
// ecall (environment-call) instruction
return syscall_ih(cause, epc, regs);
else ... // other causes
}
Notes: Reg 26 and 27 are temporary registers available to the kernel (specified by Application Binary Interface (ABI))

## Slide 27: SW emulation of MULT instruction
With proper exception handlers we can implement unsupported instructions in SW
MUL returns the low 32-bit result of rs1*rs2 into rd
MUL is decoded as an unsupported instruction and will throw an Illegal Instruction exception
SW handles the exception in illegal_inst_ih() function
  illegal_inst_ih() checks the opcode and function code of MUL to call the emulated multiply function
Control is resumed to epc + 4 after emulation is done (ERET)
mul rd, rs1, rs2

## Slide 28: Illegal Instruction IH (in C)
long illegal_inst_ih(long cause, long epc, long *regs)
{ uint32_t inst = *((uint32_t*)epc); // fetch inst
// check opcode & function codes
if((inst & MASK_MUL) == MATCH_MUL) {
// is MUL, extract rd, rs1, rs2 fields
int rd = (inst >> 7) & 0x01F;
int rs1 = ...; int rs2 = ...;
// emulate regs[rd] = regs[rs1] * regs[rs2]
emulate_multiply(rd, rs1, rs2, regs);
return epc + 4; // done, resume at epc+4
} else abort();
}