## Slide 1
Constructive Computer Architecture:
Control Hazards
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Synchronous 2-Stage Pipeline
Fetch and Execute are concurrently active on two different instructions; Fetch guesses the next pc and Execute corrects it when necessary
we will
call it pcF
pc
ir
Execute
Fetch
invalid
real pc
guessed next pc
fetched instruction, ...
pc
ir
next state

## Slide 3: Synchronous 2-Stage Pipeline
rule doPipeline ;
let newInst = iMem.req(pcF);
let newPcF = nap(pcF);
let newIR= Valid(Fetch2Decode{pc:pcF,ppc:newPcF,
inst:newInst});
if(isValid(ir)) begin
let x = fromMaybe(?, ir); let pc = x.pc;
let inst = x.inst;
let dInst = decode(inst);
... register fetch, exec, memory op, rf update ...
let nextPC = eInst.brTaken ? eInst.addr : pc + 4;
if (x.ppc != nextPC) begin newIR = Invalid;
newPcF = nextPC; end
end
pcF <= newPcF; ir <= newIR;
endrule
fetch
execute
pass pcF and predicted pc to the execute stage
pc
ir
Execute
Fetch
invalid
real pc
guessed next pc
fetched instruction, ...
pc
ir

## Slide 4: Performance?
rule doPipeline ;
let newInst = iMem.req(pcF);
let newPcF = nap(pcF);
let newIR=Valid(Fetch2Decode{pc:pcF,
ppc:newPcF,
inst:newInst});
if(isValid(ir)) begin
let x = fromMaybe(?, ir); let pc = x.pc;
let inst = x.inst;
let dInst = decode(inst);
... register fetch, exec, memory op,
rf update, nextPC ...
if (x.ppc != nextPC)
begin newIR = Invalid;
newPcF = nextPC; end
end
pcF <= newPcF; ir <= newIR;
endrule
fetch
execute
pc
ir
Execute
Fetch
invalid
real pc
guessed next pc
fetched instruction, ...
pc
ir
Notice there is always a bubble (dead cycle) after every miss-prediction
The critical path:
  max{tnewPcF, tnewIr}
   max{
  max{tnap, texec},
  max{tiMem, texec}}
   max{tiMem, texec}
texec includes tdecode etc.
The critical path is not (tiMem + texec)

## Slide 5: Elastic two-stage pipeline
<inst, pc, ppc>
We replace f2d register by a FIFO to make the machine more elastic, that is, Fetch keeps putting instructions into f2d and Execute keeps removing and executing instructions from f2d
Fetch passes the pc and predicted pc in addition to the inst to Execute; Execute redirects the PC in case of a miss-prediction
Fetch
Execute
PC
pc redirect
f2d

## Slide 6: An elastic Two-Stage pipeline
rule doFetch ;
let inst = iMem.req(pcF);
let newPcF = nap(pcF); pcF <= newPcF;
f2d.enq(Fetch2Decode{pc:pcF, ppc:newPcF, inst:inst});
endrule
rule doExecute ;
let x = f2d.first; let pc = x.pc;
let inst = x.inst;
... register fetch, exec, memory op, rf update,
nextPC ...
if (x.ppc != nextPC) begin pcF <= eInst.addr;
f2d.clear; end
else f2d.deq;
endrule
Can these rules execute concurrently assuming the FIFO allows concurrent enq, deq and clear?
No,
double writes in pc
These rules can execute in any order, however, the execution of doExecute may throw away fetched instructions
clear vs deq ?
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 7: For concurrency make pc into an EHR design 1
rule doFetch ;
let inst = iMem.req(pcF[0]);
let newPcF = nap(pcF[0]);
pcF[0] <= newPcF;
f2d.enq(Fetch2Decode{pc:pcF[0], ppc:newPcF, inst:inst});
endrule
rule doExecute ;
let x = f2d.first; let pc = x.pc;
let inst = x.inst;
... register fetch, exec, memory op, rf update,
nextPC ...
if (x.ppc != nextPC) begin pcF[1] <= eInst.addr;
f2d.clear; end
else f2d.deq;
endrule
Notice, for concurrency, f2d implementation must guarantee that (enq < clear)
doFetch < doExecute
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 8: Concurrency and Correctness Fetch < Execute
<inst, pc, ppc>
Once Execute redirects the PC,
  no wrong path instruction should be executed
  the next instruction executed must be the redirected one
Fetch
Execute
PC
pc redirect
f2d
Performance?
A dead-cycle or pipeline bubble after each miss prediction
Thus, concurrent execution requires (enq < clear)

## Slide 9: Design 1 Performance
rule doFetch ;
let inst = iMem.req(pcF[0]);
let newPcF = nap(pcF[0]);
pcF[0] <= newPcF;
f2d.enq(Fetch2Decode{pc:pcF[0], ppc:newPcF, inst:inst});
endrule
rule doExecute ;
let x = f2d.first; let pc = x.pc;
let inst = x.inst;
... register fetch, exec, memory op, rf update,
nextPC ...
if (x.ppc != nextPC) begin pcF[1] <= eInst.addr;
f2d.clear; end
else f2d.deq;
endrule
f2d is guaranteed to be empty after each misprediction (the same as the synchronous design)
doFetch < doExecute
enq < clear
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 10: Design 2
rule doFetch ;
let inst = iMem.req(pcF[1]);
let newPcF = nap(pcF[1]);
pcF[1] <= newPcF;
f2d.enq(Fetch2Decode{pc:pcF[1], ppc:newPcF, inst:inst});
endrule
rule doExecute ;
let x = f2d.first; let pc = x.pc;
let inst = x.inst;
... register fetch, exec, memory op, rf update,
nextPC ...
if (x.ppc != nextPC) begin pcF[0] <= eInst.addr;
f2d.clear; end
else f2d.deq;
endrule
doExecute < doFetch
1. Concurrency: should (clear < enq ) ?
2. Does this design have better performance?
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 11: Design 2 correctness/concurrency Execute < Fetch
<inst, pc, ppc>
Once Execute redirects the PC,
  no wrong path instruction should be executed
  the next instruction executed must be the redirected one
Fetch
Execute
PC
pc redirect
f2d
Performance?
No dead-cycle but the critical path length is
Thus, concurrent execution requires
(clear < enq)
(tiMem + texec)
Slower clock means every instruction will take longer!

## Slide 12: Takeaway
Get the functionality right before worrying about concurrency
Introduce EHRs systematically to avoid rule conflicts; analyze various designs for dead cycles and critical path lengths
  BSV compiler produces information about conflicts
  Dead cycles can be estimated by running suitable benchmark programs
  Estimation of critical paths is often difficult and requires hardware synthesis tools

## Slide 13: Killing fetched instructions
In the simple design with combinational memory we have discussed so far, all the mispredicted instructions were present in f2d. So the Execute stage can atomically:
  Clear f2d
  Set pc to the correct target
In highly pipelined machines there can be multiple mispredicted and partially executed instructions in the pipeline; it will generally take more than one cycle to kill all such instructions
Need a more general solution then clearing the f2d FIFO

## Slide 14: Epoch: a method to manage control hazards
Add an epoch register in the processor state
The Execute stage changes the epoch whenever the pc prediction is wrong and sets the pc to the correct value
The Fetch stage associates the current epoch with every instruction when it is fetched
PC
iMem
nap
f2d
Epoch
Fetch
Execute
inst
targetPC
The epoch of the instruction is examined when it is ready to execute. If the processor epoch has changed the instruction is thrown away

## Slide 15: An epoch based solution
rule doFetch ;
let instF=iMem.req(pcF[0]);
let ppcF=nap(pcF[0]); pcF[0]<=ppcF;
f2d.enq(Fetch2Decode{pc:pcF[0],ppc:ppcF,epoch:epoch,
inst:instF});
endrule
rule doExecute;
let x=f2d.first; let pc=x.pc; let inEp=x.epoch;
let inst = x.inst;
if(inEp == epoch) begin
...decode, register fetch, exec, memory op,
rf update nextPC ...
if (x.ppc != nextPC) begin pcF[1] <= eInst.addr;
epoch <= next(epoch); end
end
f2d.deq; endrule
Can these rules execute concurrently ?
yes
two values for epoch are sufficient
Notes: Fetch reads and writes PC, writes epoch and enqs ir
Execute writes PC, writes epoch and deqs ir
Fetch < Execute within the same cycle
The machine works with both CF and Bypass FIFOs for ir, but only CF Fifo gives pipelined behavior
If inEp was replaced by epoch in Execute, then Fetch and Execute can not be scheduled concurrently

## Slide 16: Discussion
Epoch based solution kills one wrong-path instruction at a time in the execute stage
It may be slow, but it is more robust in more complex pipelines, if you have multiple stages between fetch and execute or if you have outstanding instruction requests to the iMem
It requires the Execute stage to set the pc and epoch registers simultaneously which may result in a long combinational path from Execute to Fetch

## Slide 17: Decoupled Fetch and Execute
<inst, pc, ppc, epoch>
<corrected pc, new epoch>
In decoupled systems a subsystem reads and modifies only local state atomically
  In our solution, pc and epoch are read by both rules
Properly decoupled systems permit greater freedom in independent refinement of subsystems
Fetch
Execute

## Slide 18: A decoupled solution using epochs
Add fEpoch and eEpoch registers to the processor state; initialize them to the same value
The epoch changes whenever Execute detects the pc prediction to be wrong. This change is reflected immediately in eEpoch and eventually in fEpoch via a message from Execute to Fetch
Associate fEpoch with every instruction when it is fetched
In the execute stage, reject, i.e., kill, the instruction if its epoch does not match eEpoch
fEpoch
eEpoch
Fetch
Execute

## Slide 19: Control Hazard resolution A robust two-rule solution
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
f2d
FIFO
FIFO
redirect
Execute sends information about the target pc to Fetch, which updates fEpoch and pc whenever it examines the redirect (PC) fifo
fEpoch
eEpoch
Notes: 19

## Slide 20: Two-stage pipeline Decoupled code structure
module mkProc(Proc);
Fifo#(Fetch2Execute) f2d <- mkFifo; Fifo#(Addr) redirect <- mkFifo; Reg#(Bool) fEpoch <- mkReg(False); Reg#(Bool) eEpoch <- mkReg(False);
rule doFetch; let inst = iMem.req(pcF); ...
f2d.enq(... inst ..., fEpoch); endrule
rule doExecute;
if(inEp == eEpoch) begin Decode and execute the instruction; update state;
In case of misprediction, redirect.enq(correct pc); end f2d.deq; endrule
endmodule

## Slide 21: The Fetch rule
rule doFetch;
let inst = iMem.req(pcF);
if(!redirect.notEmpty)
begin let newPcF = nap(pcF);
pcF <= newPcF; f2d.enq(Fetch2Execute{pc: pcF, ppc: newPcF,
inst: inst, epoch: fEpoch});
end
else
begin fEpoch <= !fEpoch; pcF <= redirect.first;
redirect.deq;
end endrule
Notice: In case of PC redirection, nothing is enqueued into f2d

## Slide 22: The Execute rule
rule doExecute; let x = f2d.first;
let inst = x.inst; let pc = x.pc; let inEp = x.epoch; if(inEp == eEpoch) begin ...decode, register fetch, exec, memory op,
rf update nextPC ...
if (x.ppc != nextPC) begin redirect.enq(eInst.addr);
eEpoch <= !inEp; end
end
f2d.deq;
endrule
Can doFetch and doExecute execute concurrently?
yes, assuming CF FIFOs

## Slide 23: Epoch mechanism is independent of the sophisticated branch prediction schemes that we will study later