## Slide 1
Constructive Computer Architecture
Caches and store buffers
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Inside a Cache
A cache line usually holds more than one word to
  exploit spatial locality
  transport large data sets more efficiently
  reduce the number of tag bits needed to identify a cache line
cache line
tag data
Data from locations 100, 101, ...
Data
Byte
Data
Byte
100
304
6848
valid bit
Notes: Tag only needs enough bits to uniquely identify the block (jse)

## Slide 3: Extracting address tags & index
Processor requests are for a single word but cache line size is 2L words (typically L=2)
Processor uses word-aligned byte addresses, i.e. the two least significant bits of the address are 00
Need getIndex, getTag, getOffset functions
tag index L 2
Cache size in bytes
Byte addresses

## Slide 4: Direct-Mapped Cache The simplest implementation
Tag
Data Block
V
=
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
Cache line number
What is a bad reference pattern?
Strided and
stride = size of cache
req address
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)

## Slide 5: Loads
Search the cache for the processor generated address
Found in cache
a.k.a. hit
Return a copy of the word from the cache-line
Not in cache
a.k.a. miss
Bring the missing cache-line from Main Memory
May require writing back a cache-line to create space
…
Update cache and
return word to processor

## Slide 6: Stores
On a write hit: write only to cache and update the next level memory when line is evacuated
On a write miss: allocate – because of multi-word lines we first fetch the line, and then update a word in it
Notes: Write through vs. write back
WT:
+read miss never results in writes to main memory + main memory always has the most current copy of the data (consistent) - write is slower - every write needs a main memory access - as a result uses more memory bandwidth
WB:
+ writes occur at the speed of the cache memory + multiple writes within a block require only one write to main memory + as a result uses less memory bandwidth - main memory is not always consistent with cache - reads that result in replacement may cause writes of dirty blocks to main memory
Write Back with No Write Allocate: on hits it writes to cache setting dirty bit for the block, main memory is not updated; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the same block, if the block originally caused a miss, will generate misses all the way and result in very inefficient execution.
Hence, WB+WA more common combination.
Write Through with No Write Allocate: on hits it writes to cache and main memory; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the block will update main memory anyway, so write misses aren’t helped. Only read misses helped with allocate.
Hence, WT, no WA usually.
Re-look at these options when the next level is a cache; not a memory.
Write back with no allocate? Why is this

## Slide 7: Blocking vs. Non-Blocking cache
Blocking cache:
  At most one outstanding miss
  Cache must wait for memory to respond
  Cache does not accept requests in the meantime
Non-blocking cache:
  Multiple outstanding misses
  Cache can continue to process requests while waiting for memory to respond to misses
We will design a write-back, Write-miss allocate, Direct-mapped, blocking cache

## Slide 8: Cache Interface
interface Cache; method Action req(MemReq r);
// (op: Ld/St, addr: ..., data: ...)
method ActionValue#(Data) resp;
// no response for St
method ActionValue#(MemReq) memReq;
method Action memResp(Line r);
endinterface
cache
req
resp
memReq
memResp
Processor
DRAM or next level cache
hitQ
mReqQ
mRespQ
mshr
Miss request Handling Register(s)
Requests are tagged for non-blocking caches
Can be replaced by first and deq methods
Notes: Miss Status Handling Registers (MSHRs)

## Slide 9: Interface dynamics
The cache either gets a hit and responds immediately, or it gets a miss, in which case it takes several steps to process the miss
Reading the response dequeues it
  Resp can be replaced by first and deq methods
Methods are guarded, e.g., cache may not be ready to accept a request because it is processing a miss
A mshr register keeps track of the state of the request while processing it
typedef enum {Ready, StartMiss, SendFillReq, WaitFillResp} ReqStatus deriving (Bits, Eq);

## Slide 10: Blocking cache state elements
RegFile#(CacheIndex, Line) dataArray <- mkRegFileFull;
RegFile#(CacheIndex, Maybe#(CacheTag))
tagArray <- mkRegFileFull;
RegFile#(CacheIndex, Bool) dirtyArray <- mkRegFileFull;
Fifo#(1, Data) hitQ <- mkBypassFifo;
Reg#(MemReq) missReq <- mkRegU;
Reg#(ReqStatus) mshr <- mkReg(Ready);
Fifo#(2, MemReq) memReqQ <- mkCFFifo;
Fifo#(2, Line) memRespQ <- mkCFFifo;
CF Fifos are preferable because they provide better decoupling. An extra cycle here may not affect the performance by much
Tag and valid bits are kept together as a Maybe type
mshr and missReq go together

## Slide 11: Req method Blocking cache
method Action req(MemReq r) if(mshr == Ready);
let idx = getIdx(r.addr); let tag = getTag(r.addr);
let wOffset = getOffset(r.addr);
let currTag = tagArray.sub(idx);
let hit = isValid(currTag)?
fromMaybe(?,currTag)==tag : False;
if(hit) begin
let x = dataArray.sub(idx);
if(r.op == Ld) hitQ.enq(x[wOffset]);
else begin x[wOffset]=r.data;
dataArray.upd(idx, x);
dirtyArray.upd(idx, True); end
else begin missReq <= r; mshr <= StartMiss; end
endmethod
overwrite the appropriate word of the line

## Slide 12: Miss processing
mshr = StartMiss 
  if the slot is occupied by dirty data, initiate a write back of data
  mshr <= SendFillReq
mshr = SendFillReq 
  send request to the memory
  mshr <= WaitFillReq
mshr = WaitFillReq 
  Fill the slot when the data is returned from the memory and put the load response in hitQ
  mshr <= Ready
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready

## Slide 13: Start-miss and Send-fill rules
rule startMiss(mshr == StartMiss);
let idx = getIdx(missReq.addr);
let tag=tagArray.sub(idx); let dirty=dirtyArray.sub(idx);
if(isValid(tag) && dirty) begin // write-back
let addr = {fromMaybe(?,tag), idx, 4'b0};
let data = dataArray.sub(idx);
memReqQ.enq(MemReq{op: St, addr: addr, data: data});
end
mshr <= SendFillReq;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule sendFillReq (mshr == SendFillReq);
memReqQ.enq(missReq); mshr <= WaitFillResp;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready

## Slide 14: Wait-fill rule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule waitFillResp(mshr == WaitFillResp);
let idx = getIdx(missReq.addr);
let tag = getTag(missReq.addr);
let data = memRespQ.first;
tagArray.upd(idx, Valid (tag));
if(missReq.op == Ld) begin
dirtyArray.upd(idx,False);dataArray.upd(idx, data);
hitQ.enq(data[wOffset]); end
else begin data[wOffset] = missReq.data;
dirtyArray.upd(idx,True); dataArray.upd(idx, data);
end
memRespQ.deq; mshr <= Ready;
endrule
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 15: Rest of the methods
method ActionValue#(Data) resp;
hitQ.deq;
return hitQ.first;
endmethod
method ActionValue#(MemReq) memReq;
memReqQ.deq;
return memReqQ.first;
endmethod
method Action memResp(Line r);
memRespQ.enq(r);
endmethod
Memory side methods

## Slide 16: Hit and miss performance
Hit
  Directly related to the latency of L1
  0-cycle latency if hitQ is a bypass FIFO
Miss
  No evacuation: memory load latency plus combinational read/write
  Evacuation: memory store followed by memory load latency plus combinational read/write
Adding a few extra cycles in the miss case does not have a big impact on performance

## Slide 17: Speeding up Store Misses
Unlike a load, a store does not require memory system to return any data to the processor; it only requires the cache to be updated for future load accesses
Instead of delaying the pipeline, a store can be performed in the background; In case of a miss the data does not have to be brought into L1 at all (Write-miss no allocate policy)
mReqQ
mRespQ
L1
Store buffer(stb)
a small FIFO of (a,v) pairs
Store Buffer

## Slide 18: Store Buffer
A St req is enqueued into stb
  input reqs are blocked if there is no space in stb
A Ld req simultaneously searches L1 and stb;
  If Ld gets a hit in stb – it selects the most recent matching entry; L1 search result is discarded
  If Ld gets a miss in stb but a hit in L1, the L1 result is returned
  If no match in either stb and L1, miss-processing commences
In background, oldest store in stb is dequed and processed
  If St address hits in L1: update L1; if write-through then also send to it to memory
  If it misses:
    Write-back write-miss-allocate: fetch the cache line from memory (miss processing) and then process the store
    Write-back/Write-through write-miss-no-allocate: pass the store to memory
mReqQ
mRespQ
L1
Store buffer(stb)
a small FIFO of (a,v) pairs

## Slide 19: L1+Store Buffer (write-back, write-miss-allocate): Req method
method Action req(MemReq r) if(mshr == Ready);
... get idx, tag and wOffset
if(r.op == Ld) begin // search stb
let x = stb.search(r.addr);
if (isValid(x)) hitQ.enq(fromMaybe(?, x));
else begin // search L1
let currTag = tagArray.sub(idx);
let hit = isValid(currTag) ?
fromMaybe(?,currTag)==tag : False;
if(hit) begin
let x = dataArray.sub(idx); hitQ.enq(x[wOffset]); end
else begin missReq <= r; mshr <= StartMiss; end
end end
else stb.enq(r.addr,r.data); // r.op == St
endmethod
No change in miss handling rules
Entry into store buffer

## Slide 20: L1+Store Buffer (write-back, write-miss-allocate): Exit from Store Buff
rule mvStbToL1 (mshr == Ready);
stb.deq; match {.addr, .data} = stb.first;
// move the oldest entry of stb into L1
// may start allocation/evacuation
... get idx, tag and wOffset
let currTag = tagArray.sub(idx);
let hit = isValid(currTag) ?
fromMaybe(?,currTag)==tag : False;
if(hit) begin
let x = dataArray.sub(idx); x[wOffset] = data;
dataArray.upd(idx,x); dirtyArray.upd(idx, True); end
else begin missReq <= r; mshr <= StartMiss; end
endrule

## Slide 21: Give priority to req method in accessing L1
method Action req(MemReq r) if(mshr == Ready);
... get idx, tag and wOffset
if(r.op == Ld) begin // search stb
let x = stb.search(r.addr);
if (isValid(x)) hitQ.enq(fromMaybe(?, x));
else begin // search L1
...
else stb.enq(r.addr,r.data) // r.op == St
endmethod
lockL1[0] <= True;
rule clearL1Lock; lockL1[1] <= False; endrule
&& !lockL1[1]
Lock L1 while processing processor requests
rule mvStbToL1 (mshr == Ready);
stb.deq; match {.addr, .data} = stb.first;
... get idx, tag and wOffset
endrule

## Slide 22: Functions to extract cache tag, index, word offset
tag index L 2
Cache size in bytes
Byte addresses
function CacheIndex getIndex(Addr addr) = truncate(addr>>4);
function Bit#(2) getOffset(Addr addr) = truncate(addr >> 2);
function CacheTag getTag(Addr addr) = truncateLSB(addr);
truncate = truncateMSB