## Slide 1
Constructive Computer Architecture:
Branch Prediction:
Direction Predictors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Multiple Predictors: BTB + Branch Direction Predictors
Suppose we maintain a table of how a particular Br has resolved before. At the decode stage we can consult this table to check if the incoming (pc, ppc) pair matches our prediction. If not redirect the pc
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
correct mispred
correct mispred

## Slide 3: Branch Prediction Bits Remember how the branch was resolved previously
Assume 2 BP bits per instruction
Use saturating counter
On ¬taken  |  On taken | 1 | 1 | Strongly taken
 |  | 1 | 0 | Weakly taken
 |  | 0 | 1 | Weakly ¬taken
 |  | 0 | 0 | Strongly ¬taken
Direction prediction changes only after two successive bad predictions

## Slide 4: Two-bit versus one-bit Branch prediction
Consider the branch instruction needed to implement a loop
  with one bit, the prediction will always be set incorrectly on loop exit
  with two bits the prediction will not change on loop exit
A little bit of hysteresis is good in changing predictions

## Slide 5: Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct direction predictions
0
0
Fetch PC
Branch?
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?
Target PC
+
After decoding
At the Decode stage:
For a branch instruction consult the BHT to determine the direction prediction;
Use the prediction to compute the nextPC;
If the nextPC is different from the incoming ppc, redirect the Fetch
No need to keep the target PC because it can be computed

## Slide 6: Where does BHT fit in the processor pipeline?
BHT can only be used after instruction decode
We still need the next instruction address predictor (e.g., BTB) at the fetch stage
Predictor training: On a pc misprediction, information about redirecting the pc has to be passed to the fetch stage. However for training the direction predictor the direction information has to be passed after every branch execution (misprediction or not)

## Slide 7: Multiple predictors in a pipeline
At each stage we need to take two decisions:
  Determine if the current instruction is a wrong path instruction: Requires looking at epochs
  Determine if the prediction (ppc) following the current instruction is good: Requires consulting BTB at Decode, and later determining the actual branch resolution at Execute
No redirections should be generated by known wrong path instructions
Redirections from Execute stage are always correct, and cannot be ignored
  Should training also be avoided by wrong path instruction?
  Generally yes, but may have some benefits

## Slide 8: N-Stage pipeline with BHT
Both Decode and Execute can redirect the PC; Execute redirect should never be overruled
Use separate epochs for each redirecting stage
  eEp for Execute redirections and dEp for Decode redirections
Execute can update both BTB and BHT
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
redirect PC
dEp
...
eEp
BTB
BHT
{pc,ppc,ieEp,...}
{pc,ppc,ieEp,idEp,...}
{pc, newPc, taken}
{pc, newPc}

## Slide 9: N-Stage pipeline with BHT Decode stage branch prediction activity
Is ieEp = eEP ?
Is idEp = dEp ?
yes
no
yes
no
Current instruction is OK; Consult BHT for branches
Wrong path instruction; drop it
increment dEp; redirect
Wrong path instruction; drop it
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
dEp
...
eEp
BTB
BHT
{pc,ppc,ieEp,...}
{pc,ppc,ieEp,idEp,...}
{pc, newPc, taken}
{pc, newPc,}
!misprediction
misprediction
No action
See the code at the end

## Slide 10: A small problem
Consider the entry in BTB for a branch at the end of a loop
  Execute will delete it on loop exit
  This will cause a misprediction when the loop is executed again!
  Decode will redirect again after consulting BHT!
How to prevent Execute from deleting the entry?

## Slide 11: Possible Fixes
Execute could read the BHT entry and not delete the entry from BTB
  To avoid reading the BHT from two places, the direction prediction bits could be passed from the Decode to Execute
We can keep the history bits for branches in the BTB also and update as necessary;
We can set the branches to be always-taken
Fixing the code, which is given at the end, is left as an exercise

## Slide 12: Discussion
The number of entries in BTB is small both because of the need for fast access and the need to store the target address (small and fat)
The number entries in BHT is large (thin and tall)
Jumps through registers (JALR) are problematic and perhaps should not be kept in the BTB

## Slide 13: Uses of Jump Register (JALR)
Dispatching to an array of functions (jump to specific trap handler)
Dynamic function call (jump to run-time function address)
Subroutine returns (jump to return address)
How can we improve subroutine call transfers?
BTB will work well only if the same function is invoked repeatedly
BTB will work well only if the same function is called repeatedly, (e.g., in C++ programming, when objects have same type in virtual function call)
BTB is not likely to work because a function is called from many distinct call sites!

## Slide 14: Return Address Stack
Maintain RAS, a small structure which holds pcs to accelerate JR for subroutine returns
pc of fb call
pc of fc call
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
pc of fd call
k entries
(typically k=8-16)
Pop return address when subroutine return decoded
Push call address when function call executed
Don’t enter these instructions in BTB
RAS

## Slide 15: Multiple Predictors: BTB + BHT + Ret Predictors
The system must work even if every prediction is wrong
Multiple predictors are common;
Performance analysis is quite difficult – depends upon the sizes of various tables and program behavior
In superscalar architectures the branch prediction problem changes to the cache-line prediction problem
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
Wrong path insts must be filtered
Br Dir Pred, RAS
correct
JR pred
correct mispred

## Slide 16: Takeaway
Branch-prediction has first order effect on the performance of your machine
There are just too many branch prediction schemes to be covered in class but the three discussed here – BTB, BHT and RAS – will take you very far
  Just for curious we will discuss one more
The exact choice depends upon the other features of the microarchitecture as well

## Slide 17: Exploiting Spatial Correlation Yeh and Patt, 1992
History register, H, records the direction of the last N branches executed by the processor and the predictor uses this information to predict the resolution of the next branch
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;
If first condition is false then so is second condition

## Slide 18: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Taken/¬Taken?
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Four
2k, 2-bit
Entry
BHT

## Slide 19: Direction Predictor interface
interface DirectionPred; method Addr ppcDP(Addr pc, Addr targetPC); method Action update(Addr pc, Bool taken); endinterface

## Slide 20: BHT predictor
module mkBHT(DirectionPred); Vector#(BhtEntries, Reg#(Bit#(2)))
bhtArr <- replicateM(mkReg(2’b01));
function BhtIndex getBhtIndex(Addr pc)= ...;
function Addr computeTarget(Addr pc, Addr targetPC,
Bool taken)= ...; define functions extractDir; getBhtEntry, newDpBits; ...
method Addr ppcDP(Addr pc, Addr targetPC); BtbIndex index = getBhtIndex(pc);
let direction = extractDir(bhtArr[index]); return computeTarget(pc, targetPC, direction); endmethod
method Action update(Addr pc, Bool taken);
BtbIndex index = getBhtIndex(pc);
let dpBits = getBhtEntry(index);
bhtArr[index] <= newDpBits(dpBits,taken); endmethod
endmodule

## Slide 21: 4-Stage-pipeline with BTB and BHT fetch
rule fetch; iMem.enq(pc[1]);
let ppcF = btb.nap(pc[1]); pc[1] <= ppcF ;
f2d.enq(Fetch2Decode{pc:pc[1], ppc:ppcF, eEp:eEp[1],
dEp:dEp[1]});
endrule

## Slide 22: 4-Stage-pipeline with BTB and BHT decode
rule decode;
let inst = iMem.first; let x = f2d.first;
let pcD=x.pc; let ppcD=x.ppc; let ieEp=x.eEp; let idEp=x.dEp;
if (eEp[1] != ieEp) begin iMem.deq; f2d.deq; end //wrong-path
else begin
if (dEp[0] != idEp) begin iMem.deq; f2d.deq; end //wrong-path
else begin //right-path instruction
let dInst = decode(inst);
let stall = ...; // normal execution
if(!stall) begin
let ppcDP = isBranch(dInst)? bht.ppcDP(pcD,dInst.add) : ppcD;
if (ppcDP!= ppcD) begin dEp[0]<= !dEp[0]; pc[1]<= ppcDP; end …fetch register values d2e.enq(Decode2Execute{ pc: pcD, ppc: ppcDP, eEp: ieEp,
dIinst: dInst, rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); iMem.deq; f2d.deq end end
endrule

## Slide 23: 4-Stage-pipeline with BTB and BHT execute
rule execute; let x = d2e.first; ...
if(eEp[0] != inEp) begin e2w.enq(Invalid); d2e.deq; end
else begin
let eInst = exec(dInstE, rVal1E, rVal2E, pcE);
if(eInst.iType == Ld)
dMem.enq(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) begin
dMem.enq(MemReq{op:St, addr:eInst.addr,
data:eInst.data}); end
let nextPC = eInst.brTaken ? eInst.addr : pcE + 4;
if (x.ppc != nextPC) begin pc[0] <= eInst.addr;
epoch[0] <= !epoch[0];
btb.update(pcE, nextPC, eInst.brTaken); end
if (isBranch(dInstE)) bht.update(pcE, eInst.brTaken);
e2w.enq(Valid Exec12Exec2{eInst:eInst, pc:pcE});
d2e.deq; end
endrule

## Slide 24: 4-Stage-pipeline with BTB and BHT writeback
rule writeBack;
let vx = e2w.first;
if (vx matches tagged Valid .x) begin
let pcE=x.pc; let eInst=x.eInst;
if (isValid(eInst.dst)) begin
let data = eInst.iType==Ld ? dMem.first: eInst.data;
rf.wr(fromMaybe(?, eInst.dst), data);
end
if(eInst.iType == Ld) dMem.deq;
end
sb.remove; endrule