## Slide 1: Stmt FSM
Richard S. Uhler
Computer Science & Artificial Intelligence Lab
Massachusetts Institute of Technology
(based on a lecture prepared by Arvind)

## Slide 2: Motivation
Some common design patterns are tedious to express in BSV
  Testbenchs
  Sequential machines (FSMs)
    especially sequential looping structures
These are tedious to express in Verilog as well (but not in C)

## Slide 3: Testing the IP Lookup Design
Input: IP Address
Output: Route Value
Need to test many different input/output sequences
done?
RAM
fifo
enter
getResult
outQ
cbuf
yes
no
getToken

## Slide 4: Testing IP Lookup
Call many streams of requests responses from the device under test (DUT)
Case 1
dut.enter(17.23.12.225)
dut.getResult()
dut.enter(17.23.12.25)
dut.getResult()
Case 2
dut.enter(128.30.90.124)
dut.enter(128.30.90.126)
dut.getResult()
dut.getResult()
Check correct with 1 request at a time
Check correct with 2 concurrent requests

## Slide 5: But we usually want more counters, display, ...
function Action makeReq(x);
action
reqCnt <= reqCnt + 1;
dut.enter(x);
$display(“[Req #: ”,fshow(reqCnt),“] = ”,fshow(x));
endaction
endfunction
function Action getResp();
action
resCnt <= resCnt + 1;
let x <- dut.getResult();
$display(“[Rsp #:”,fshow(resCnt),“] = ”,fshow(x));
endaction
endfunction

## Slide 6: Writing a Testbench (Case 1)
rule step0(pos==0);
makeReq(17.23.12.225);
pos <= 1;
endrule
rule step1(pos==1);
getResp();
pos <= 2;
endrule
rule step2(pos==2);
makeReq(17.23.12.25);
pos <= 3;
endrule
rule step3(pos==3);
getResp();
pos <= 4;
endrule
rule finish(pos==4);
$finish;
endrule
A lot of text!
Wait until response is ready
How should we do it for a sequence of 100 actions?

## Slide 7: A more complicated Case: Initializing memory
 |  | f(i) |  |  |  |  | 
nI
i
addr0
int i; Addr addr=addr0;
bool done = False;
for(i=0; i<nI; i++){
mem.write(addr++,f(i));
}
done = True;
C
Need an FSM in HW as memory can only do one write per cycle
Reg#(int) i <-mkReg(0);
Reg#(Addr) addr <-mkReg(addr0);
Reg#(Bool) done <-mkReg(False);
rule initialize (i < nI);
mem.write (addr, f(i));
addr <= addr + 1;
i <= i + 1;
if (i+1 == nI) done<=True;
endrule
BSV

## Slide 8: Initialize a memory with a 2-D pattern
Reg#(int) i <-mkReg(0);
Reg#(int) j <-mkReg(0);
Reg#(Addr) addr <-mkReg(addr0);
Reg#(Bool) done <-mkReg(False);
rule loop ((i < nI) && (j < nJ));
mem.write (addr, f(i,j));
addr <= addr + 1;
if (j < nJ-1)
j <= j + 1;
else begin
j <= 0;
if (i < nI-1) i <= i + 1;
else done <= True;
end
endrule
 |  | f(i,j) |  |  |  |  | 
nJ
nI
i
j
addr0
Bluespec code gets messier as compared to C even with small changes in C, e.g.,
  initialization based on old memory values
  initialization has to be done more than once
Shall we do triply-nested loops?

## Slide 9: An imperative view
void doTest(){
makeReq(17.23.12.225);
getResp();
makeReq(17.23.12.25);
getResp();
exit(0);
}
seq
makeReq(17.23.12.225);
getResp();
makeReq(17.23.12.25);
getResp();
$finish();
endseq;
It is easy to write a sequence in C
Writing this in rules is tedious:
Can we just write the actions and have the compiler make the rules?

## Slide 10: From Action Lists to FSMs
FSM interface
Creating an FSM
interface FSM;
method Action start();
method Bool done();
endinterface
module mkFSM#(Stmt s)(FSM);
Stmt s
done
start

## Slide 11: The Stmt Sublanguage
Stmt =
<Bluespec Action>
| seq s1..sN endseq
| par s1..sN endpar
| if-then / if-then-else
| for-, while-, repeat(n)-
(w/ break and continues)
BSV Action
Sequence of Stmt
List of Parallel Stmts
Conditional Stmts
Loop Stmts

## Slide 12: Translation Example: Seq to FSM
Stmt s = seq
makeReq(17.23.12.225);
getResp();
makeReq(17.23.12.25);
getResp();
$finish();
endseq;
FSM f <- mkFSM(s);
module mkFSM_s(FSM)
Reg#(Bit#(3)) pos <- mkReg(0);
rule step1(pos==1);
makeReq(17.23.12.225); pos <= 2;
endrule
rule step2(pos==2);
getResp(); pos <= 3; endrule
rule step3(pos==3);
makeReq(17.23.12.25); pos <= 4;
endrule
rule step4(pos==4);
getResp(); pos <= 5; endrule
rule step5(pos==5);
$finish; pos <= 0; endrule
method Action start() if(pos==0);
pos <= 1;
endmethod
method Bool done()
return (pos == 0);
endmethod
endmodule

## Slide 13: Parallel Tasks
seq
refReq(x);
refRes(rReg);
dutReq(x);
dutRes(dReg);
checkMatch(rReg,dReg);
endseq
We want to check dut and ref have same result
Do each, then check results
But it doesn’t matter that ref finishes before dut starts…

## Slide 14: Start ref and dut at the same time
Seq. for each implementation
Start together
Both run at own rate
Wait until both are done
seq
par
seq refReq(x);
refRes(refv);endseq
seq dutReq(x);
dutRes(dutv); endseq
endpar
checkMatch(refv,dutv);
endseq

## Slide 15: What exactly is the translation?
The Stmt sublanguage is clearer for the designer; but, what FSM do we get?
Let’s examine each Stmt Construction case and see how it can be implemented

## Slide 16: Base Case: Primitive Action: a
Reg#(Bool) doneR <- mkReg(True);
rule dowork(!doneR);
a;
doneR <= True;
endrule
method Action start() if (doneR);
doneR <= False;
endmethod
method Bool done(); return doneR; endmethod

## Slide 17: Sequential List - seq
seq s1...sN endseq: sequential composition
Reg#(int) s <- mkReg(0);
FSM s1 <- mkFSM (s1); … ; FSM sN <- mkFSM (sN);
Bool flag =
rule one (s==1); s1.start(); s <= 2; endrule
rule two (s==2&& s1.done());
s2.start(); s <= 3; endrule
…
rule n (s==n && sN-1.done());
sN.start(); s <= 0; endrule
method Action start() if (flag); s <= 1; endmethod
method Bool done(); return flag; endmethod
What is wrong if we just had this?
s1.done() && … sN.done();

## Slide 18: Implementation - par
par s1...sN endpar: parallel composition
FSM s1 <- mkFSM (s1); … ; FSM sN <- mkFSM (sN);
Bool flag =
method Action start() if (flag);
s1.start(); s2.start(); …; sN.start();
endmethod
method Bool done(); return flag; endmethod
s1.done() && … && sN.done();

## Slide 19: Implementation - if
if p then sT else sF: conditional composition
FSM sT <- mkFSM (sT); FSM sF <- mkFSM (sF);
Bool flag =
method Action start() if (flag);
if (p) then sT.start() else sF.start();
endmethod
method Bool done(); return flag; endmethod
sT.done()&& sF.done();

## Slide 20: Implementation - while
while p do s: loop composition
s <- mkFSM(s);
Reg#(Bool) busy <- mkReg(False);
Bool flag =
rule restart_loop(busy && s.done());
if (p) begin s.start(); busy <= True;
else busy <= False;
endrule
method Action start() if (flag);
if (p) begin s.start(); busy <= True;
else busy <= False;
endmethod
method Bool done(); return flag; endmethod
!busy;
what if this was replaced by
busy <= True

## Slide 21: The StmtFSM library
This IS the Library (almost)
  Some optimizations for seq/base case
  Stmt syntax added for readability
Good but not great HW (users can do better by handcoding)
  state-encoding
    Use a single wide register (i,j) instead of two
    Use 1 log(n)-bit register instead of n 1-bit registers
    See if state can be inferred from other data registers
  Unnecessary dead cycles can be eliminated

## Slide 22: FSM atomicity
FSM Actions are made into rules
  rule atomicity governs statement interactions
Stmt s1 = seq
action f1.enq(x); f2.enq(x); endaction
action f1.deq(); x<=x+1; endaction
action f2.deq(); y<=y+1; endaction
endseq;
Stmt s2 = seq
action f1.enq(y); f2.enq(y); endaction
action f1.deq(); $display(“%d”, y); endaction
action f2.deq(); $display(“%d”, x); endaction
endseq;
rule s1(…); f1.enq(x);
f2.enq(x); …;endrule
rule s2(…); f1.deq();
x<=x+1; … endrule
rule s3(…); f2.deq();
y<=y+1; … endrule
rule s1(…); f1.enq(y);
f2.enq(y); …endrule
rule s2(…); f1.deq();
$display(“%d”, y);…endrule
rule s3(…); f2.deq();
y<=y+1; …endrule

## Slide 23: FSM Atomicity
We’re writing actions, not rules
  Do they execute atomically?
Seq. Stmt
  Only one at a time
   Safe
Par. Stmt
  all at once
   What about conflicts?
par x <= x + 1;
x <= 2 * x;
x <= x ** 2;
endpar
What happens here?
rule p1; x <= x + 1;…endrule
rule p2; x <= 2 * x;…endrule
rule p3; x <=x ** 2;…endrule
Each rule happens once.
Order is arbitrary

## Slide 24: FSM summary
Stmt sublanguage captures certain common and useful FSM idioms:
  sequencing, parallel, conditional, iteration
FSM modules automatically implement Stmt specs
FSM interface permits composition of FSMs
Most importantly, same Rule semantics
  Actions in FSMs are atomic
  Actions automatically block on implicit conditions
  Parallel actions, (in the same FSM or different FSMs) automatically arbitrated safely (based on rule atomicity)