## Slide 1
Combinational Circuits in Bluespec
Arvind
Computer Science & Artificial Intelligence Lab
Massachusetts Institute of Technology

## Slide 2: Combinational circuits are acyclic interconnections of gates
And, Or, Not
Nand, Nor, Xor
…

## Slide 3: Arithmetic-Logic Unit (ALU)
ALU performs all the arithmetic and logical functions
Op
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Each individual function can be described as a combinational circuit

## Slide 4: Full Adder: A one-bit adder
function fa(a, b, c_in);
s = (a ^ b)^ c_in;
c_out = (a & b) | (c_in & (a ^ b));
return {c_out,s};
endfunction
Structural code – only specifies interconnection between boxes
Not quite correct –needs type annotations

## Slide 5: Full Adder: A one-bit adder corrected
function Bit#(2) fa(Bit#(1) a, Bit#(1) b,
Bit#(1) c_in);
Bit#(1) s = (a ^ b)^ c_in;
Bit#(1) c_out = (a & b) | (c_in & (a ^ b));
return {c_out,s};
endfunction
“Bit#(1) a” type declaration says that a is one bit wide
{c_out,s} represents bit concatenation
How big is {c_out,s}?
2 bits

## Slide 6: Types
A type is a grouping of values:
  Integer: 1, 2, 3, …
  Bool: True, False
  Bit: 0,1
  A pair of Integers: Tuple2#(Integer, Integer)
  A function fname from Integers to Integers:
  function Integer fname (Integer arg)
Every expression and variable in a BSV program has a type; sometimes it is specified explicitly and sometimes it is deduced by the compiler
Thus we say an expression has a type or belongs to a type
The type of each expression is unique

## Slide 7: Type declaration versus deduction
The programmer writes down types of some expressions in a program and the compiler deduces the types of the rest of expressions
If the type deduction cannot be performed or the type declarations are inconsistent then the compiler complains
function Bit#(2) fa(Bit#(1) a, Bit#(1) b,
Bit#(1) c_in);
Bit#(1) s = (a ^ b)^ c_in;
Bit#(2) c_out = (a & b) | (c_in & (a ^ b));
return {c_out,s};
endfunction
type error
Type checking prevents lots of silly mistakes

## Slide 8: 2-bit Ripple-Carry Adder
function Bit#(3) add(Bit#(2) x, Bit#(2) y,
Bit#(1) c0);
Bit#(2) s = 0; Bit#(3) c=0; c[0] = c0;
let cs0 = fa(x[0], y[0], c[0]);
c[1] = cs0[1]; s[0] = cs0[0];
let cs1 = fa(x[1], y[1], c[1]);
c[2] = cs1[1]; s[1] = cs1[0];
return {c[2],s};
endfunction
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
fa can be used as a black-box long as we understand its type signature
The “let” syntax avoids having to write down types explicitly

## Slide 9: “let” syntax
The “let” syntax: avoids having to write down types explicitly
  let cs0 = fa(x[0], y[0], c[0]);
  Bits#(2) cs0 = fa(x[0], y[0], c[0]);
The same

## Slide 10: Parameterized types: #
A type declaration itself can be parameterized by other types
Parameters are indicated by using the syntax ‘#’
  For example Bit#(n) represents n bits and can be instantiated by specifying a value of n
  Bit#(1), Bit#(32), Bit#(8), …

## Slide 11: An w-bit Ripple-Carry Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(w+1) c=0; c[0] = c0;
for(Integer i=0; i<w; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[w],s};
endfunction
Not quite correct
Unfold the loop to get the wiring diagram
fa
fa
x[0]
y[0]
c[0]
s[0]
x[1]
y[1]
c[1]
s[1]
c[2]
cs
fa
x[w-1]
y[w-1]
s[w-1]
c[w]
c[w-1]
…

## Slide 12: Instantiating the parametric Adder
function Bit#(w+1) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
// concrete instances of addN!
function Bit#(33) add32(Bit#(32) x, Bit#(32) y,
Bit#(1) c0) = addN(x,y,c0);
function Bit#(4) add3(Bit#(3) x, Bit#(3) y,
Bit#(1) c0) = addN(x,y,c0);
Define add32, add3 … using addN

## Slide 13: valueOf(w) versus w
Each expression has a type and a value and these come from two entirely disjoint worlds
w in Bit#(w) resides in the types world
Sometimes we need to use values from the types world into actual computation. The function valueOf allows us to do that
  Thus
  i<w is not type correct
  i<valueOf(w)is type correct

## Slide 14: TAdd#(w,1) versus w+1
Sometimes we need to perform operations in the types world that are very similar to the operations in the value world
  Examples: Add, Mul, Log
We define a few special operators in the types world for such operations
  Examples: TAdd#(m,n), TMul#(m,n), …

## Slide 15: A w-bit Ripple-Carry Adder corrected
function Bit#(TAdd#(w,1)) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(TAdd#(w,1)) c=0; c[0] = c0;
let valw = valueOf(w);
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[valw],s};
endfunction

## Slide 16: A w-bit Ripple-Carry Adder
function Bit#(TAdd#(w,1)) addN(Bit#(w) x, Bit#(w) y,
Bit#(1) c0);
Bit#(w) s; Bit#(TAdd#(w,1)) c; c[0] = c0;
let valw = valueOf(w);
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end
return {c[valw],s};
endfunction
types world
equivalent of w+1
Lifting a type into the value world
Structural interpretation of a loop – unfold it to generate an acyclic graph

## Slide 17: Static Elaboration phase
When BSV programs are compiled, first type checking is done and then the compiler gets rid of many constructs which have no direct hardware meaning, like Integers, loops
cs0 = fa(x[0], y[0], c[0]); c[1]=cs0[1]; s[0]=cs0[0];
cs1 = fa(x[1], y[1], c[1]); c[2]=cs1[1]; s[1]=cs1[0];
…
csw = fa(x[valw-1], y[valw-1], c[valw-1]);
c[valw] = csw[1]; s[valw-1] = csw[0];
for(Integer i=0; i<valw; i=i+1) begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 18: Integer versus Int#(32)
In mathematics integers are unbounded but in computer systems integers always have a fixed size
BSV allows us to express both types of integers, though unbounded integers are used only as a programming convenience
for(Integer i=0; i<valw; i=i+1)
begin
let cs = fa(x[i],y[i],c[i]);
c[i+1] = cs[1]; s[i] = cs[0];
end

## Slide 19: Type synonyms
typedef bit [7:0] Byte;
typedef Bit#(8) Byte;
typedef Bit#(32) Word;
typedef Tuple2#(a,a) Pair#(type a);
typedef Int#(n) MyInt#(type n);
typedef Int#(n) MyInt#(numeric type n);
The same
The same

## Slide 20: Complex combinational circuits
IFFT

## Slide 21: Combinational IFFT
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
All numbers are complex and represented as two sixteen bit quantities. Fixed-point arithmetic is used to reduce area, power, ...
*
*
*
*
+
-
-
+
+
-
-
+
*j
t2
t0
t3
t1
Notes: Constants t0 to t3 are different for each box and can have dramatci impact on optimizations.

## Slide 22: 4-way Butterfly Node
function Vector#(4,Complex) bfly4
(Vector#(4,Complex) t, Vector#(4,Complex) x);
t’s (twiddle coefficients) are mathematically derivable constants for each bfly4 and depend upon the position of bfly4 the in the network
*
*
*
*
+
-
-
+
+
-
-
+
*i
x0
x1
x2
x3
t0
t1
t2
t3

## Slide 23: BSV code: 4-way Butterfly
function Vector#(4,Complex#(s)) bfly4
(Vector#(4,Complex#(s)) t, Vector#(4,Complex#(s)) x);
Vector#(4,Complex#(s)) m, y, z;
m[0] = x[0] * t[0]; m[1] = x[1] * t[1];
m[2] = x[2] * t[2]; m[3] = x[3] * t[3];
y[0] = m[0] + m[2]; y[1] = m[0] – m[2];
y[2] = m[1] + m[3]; y[3] = i*(m[1] – m[3]);
z[0] = y[0] + y[2]; z[1] = y[1] + y[3];
z[2] = y[0] – y[2]; z[3] = y[1] – y[3];
return(z);
endfunction
Polymorphic code: works on any type of numbers for which *, + and - have been defined
*
*
*
*
+
-
-
+
+
-
-
+
*i
m
y
z
Note: Vector does not mean storage; just a group of wires with names

## Slide 24: Language notes: Sequential assignments
Sometimes it is convenient to reassign a variable (x is zero every where except in bits 4 and 8):
This will usually result in introduction of muxes in a circuit as the following example illustrates:
Bit#(32) x = 0;
let y = x+1;
if(p) x = 100;
let z = x+1;
x
0
100
p
+1
+1
z
y
Bit#(32) x = 0;
x[4] = 1; x[8] = 1;

## Slide 25: Complex Arithmetic
Addition
  zR = xR + yR
  zI = xI + yI
Multiplication
  zR = xR * yR - xI * yI
  zI = xR * yI + xI * yR

## Slide 26: Representing complex numbers as a struct
typedef struct{
Int#(t) r;
Int#(t) i;
} Complex#(numeric type t) deriving (Eq,Bits);
Notice the Complex type is parameterized by the size of Int chosen to represent its real and imaginary parts
If x is a struct then its fields can be selected by writing x.r and x.i

## Slide 27: BSV code for Addition
typedef struct{
Int#(t) r;
Int#(t) i;
} Complex#(numeric type t) deriving (Eq,Bits);
function Complex#(t) cAdd
(Complex#(t) x, Complex#(t) y);
Int#(t) real = x.r + y.r;
Int#(t) imag = x.i + y.i;
return(Complex{r:real, i:imag});
endfunction
What is the type of this + ?

## Slide 28: Overloading (Type classes)
The same symbol can be used to represent different but related operators using Type classes
A type class groups a bunch of types with similarly named operations. For example, the type class Arith requires that each type belonging to this type class has operators +,-, *, / etc. defined
We can declare Complex type to be an instance of Arith type class

## Slide 29: Overloading +, *
instance Arith#(Complex#(t));
function Complex#(t) \+
(Complex#(t) x, Complex#(t) y);
Int#(t) real = x.r + y.r;
Int#(t) imag = x.i + y.i;
return(Complex{r:real, i:imag});
endfunction
function Complex#(t) \*
(Complex#(t) x, Complex#(t) y);
Int#(t) real = x.r*y.r – x.i*y.i;
Int#(t) imag = x.r*y.i + x.i*y.r;
return(Complex{r:real, i:imag});
endfunction
…
endinstance
The context allows the compiler to pick the appropriate definition of an operator

## Slide 30: Combinational IFFT
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
stage_f function
repeat stage_f three times
function Vector#(64, Complex#(n)) stage_f
(Bit#(2) stage, Vector#(64, Complex#(n)) stage_in);
function Vector#(64, Complex#(n)) ifft
(Vector#(64, Complex#(n)) in_data);
to be continued

## Slide 31: BSV Code: Combinational IFFT
function Vector#(64, Complex#(n)) ifft
(Vector#(64, Complex#(n)) in_data);
//Declare vectors
Vector#(4,Vector#(64, Complex#(n))) stage_data;
stage_data[0] = in_data;
for (Bit#(2) stage = 0; stage < 3; stage = stage + 1)
stage_data[stage+1] = stage_f(stage,stage_data[stage]);
return(stage_data[3]);
endfunction
The for-loop is unfolded and stage_f is inlined during static elaboration
Note: no notion of loops or procedures during execution

## Slide 32: BSV Code for stage_f
function Vector#(64, Complex#(n)) stage_f
(Bit#(2) stage, Vector#(64, Complex#(n)) stage_in);
Vector#(64, Complex#(n)) stage_temp, stage_out;
for (Integer i = 0; i < 16; i = i + 1)
begin
Integer idx = i * 4;
Vector#(4, Complex#(n)) x;
x[0] = stage_in[idx]; x[1] = stage_in[idx+1];
x[2] = stage_in[idx+2]; x[3] = stage_in[idx+3];
let twid = getTwiddle(stage, fromInteger(i));
let y = bfly4(twid, x);
stage_temp[idx] = y[0]; stage_temp[idx+1] = y[1];
stage_temp[idx+2] = y[2]; stage_temp[idx+3] = y[3];
end
//Permutation
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
twid’s are mathematically derivable constants