## Slide 1
Folded Combinational Circuits as an example of Sequential Circuits
Arvind
Computer Science & Artificial Intelligence Lab
Massachusetts Institute of Technology

## Slide 2: Multiplication by repeated addition
1101 (13)
1011 (11)
1101
+ 1101
+ 0000
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
add4
add4
add4
a0
a1
a2
a3
m0
m1
m2
m3
0
mi = (a[i]==0)? 0 : b;

## Slide 3: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin let m = (a[i]==0)? 0 : b; let sum = add32(m,tp,0); prod[i] = sum[0]; tp = truncateLSB(sum); end return {tp,prod}; endfunction
Combinational circuit uses 31 add32 circuits

## Slide 4: Design issues with combinational multiply
Lot of hardware
  32-bit multiply uses 31 add32 circuits
Long chains of gates
  32-bit ripple carry adder has a 31-long chain of gates
  32-bit multiply has 31 ripple carry adders in sequence!
The speed of a combinational circuit is determined by its longest input-to-output path
Can we do better?

## Slide 5: We can reuse the same add32 circuit if we can store the partial results in some storage device, e.g., register

## Slide 6: Combinational circuits
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
Sel
O0
O1
On-1
A
Demux
.
.
.
lg(n)
A
Decoder
.
.
.
O0
O1
On-1
lg(n)
Such circuits have no cycles (feedback) or state elements

## Slide 7: A simple synchronous state element
ff
Q
D
C
C
D
Q
Metastability
Data is sampled at the rising edge of the clock
Edge-Triggered Flip-flop
Notes: Metastability?

## Slide 8: Flip-flops with Write Enables
ff
Q
D
C
EN
C
D
Q
EN
ff
Q
D
C
EN
0
1
ff
Q
D
C
EN
dangerous!
Data is captured only if EN is on
Notes: Why dangerous?
Glitches

## Slide 9: Registers
Register: A group of flip-flops with a common
clock and enable
Register file: A group of registers with a common
clock, input and output port(s)
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
Q
Q
Q
Q
Q
Q
Q
Q
D
C
En

## Slide 10: We can build useful and compact circuits using registers
Circuits containing state elements are called sequential circuits

## Slide 11: Expressing a loop using registers
int s = s0;
for (int i = 0; i < 32; i = i+1) { s = f(s); } return s; C-code
sel
< 32
0
notDone
+1
i
en
sel = start
en = start | notDone
s0
f
sel
s
en
We need two registers to hold s and i values from one iteration to the next.
These registers are initialized when the computation starts and updated every cycle until the computation terminates

## Slide 12: Expressing sequential circuits in BSV
Sequential circuits, unlike combinational circuits, are not expressed structurally (as wiring diagrams) in BSV
For sequential circuits a designer defines:
  State elements by instantiating modules
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
  Rules which define how state is to be transformed atomically
  rule step if (i < 32); s <= f(s); i <= i+1; endrule
make a 32-bit register which is uninitialized
make a 6-bit register with initial value 32
the rule can execute only when its guard is true
actions to be performed when the rule executes

## Slide 13: Rule Execution
< 32
notDone
+1
sel
0
i
en
sel = start
en = start | notDone
f
s0
sel
s
en
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule step if (i < 32); s <= f(s); i <= i+1; endrule
When a rule executes:
  all the registers are read at the beginning of a clock cycle
  the guard and computations to evaluate the next value of the registers are performed
  at the end of the clock cycle registers are updated iff the guard is true
Muxes are need to initialize the registers

## Slide 14: Multiply using registers
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin let m = (a[i]==0)? 0 : b; let sum = add32(m,tp,0); prod[i] = sum[0]; tp = truncateLSB(sum); end return {tp,prod}; endfunction
Need registers to hold a, b, tp, prod and i
Update the registers every cycle until we are done
Combinational version

## Slide 15: Sequential multiply
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); let m = (a[i]==0)? 0 : b; let sum = add32(m,tp,0); prod[i] <= sum[0]; tp <= sum[32:1];
i <= i+1; endrule
state elements
a rule to describe the dynamic behavior
So that the rule won’t fire until i is set to some other value
similar to the loop body in the combinational version

## Slide 16: Dynamic selection requires a mux
a[i]
a
i
a[0],a[1],a[2],…
a
>>
0
when the selection indices are regular then it is better to use a shift operator (no gates!)

## Slide 17: Replacing repeated selections by shifts
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); let m = (a[0]==0)? 0 : b;
a <= a >> 1; let sum = add32(m,tp,0); prod <= {sum[0], (prod >> 1)[30:0]}; tp <= sum[32:1];
i <= i+1; endrule

## Slide 18: Circuit for Sequential Multiply
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
<<
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
s1 = start_en
s2 = start_en | !done
result (high)
31
0
add
0
0
32:1
0

## Slide 19: Circuit analysis
Number of add32 circuits has been reduced from 31 to one, though some registers and muxes have been added
The longest combinational path has been reduced from 31 serial add32’s to one add32 plus a few muxes
The sequential circuit will take 31 clock cycles to compute an answer

## Slide 20: Combinational IFFT
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
Reuse the same circuit three times
to reduce area

## Slide 21: BSV Code for stage_f
function Vector#(64, Complex#(n)) stage_f
(Bit#(2) stage, Vector#(64, Complex#(n)) stage_in);
Vector#(64, Complex#(n)) stage_temp, stage_out;
for (Integer i = 0; i < 16; i = i + 1)
begin
Integer idx = i * 4;
Vector#(4, Complex#(n)) x;
x[0] = stage_in[idx]; x[1] = stage_in[idx+1];
x[2] = stage_in[idx+2]; x[3] = stage_in[idx+3];
let twid = getTwiddle(stage, fromInteger(i));
let y = bfly4(twid, x);
stage_temp[idx] = y[0]; stage_temp[idx+1] = y[1];
stage_temp[idx+2] = y[2]; stage_temp[idx+3] = y[3];
end
//Permutation
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
twid’s are mathematically derivable constants

## Slide 22: Higher-order functions: Stage functions f1, f2 and f3
function f0(x)= stage_f(0,x);
function f1(x)= stage_f(1,x);
function f2(x)= stage_f(2,x);
What is the type of f0(x) ?
function Vector#(64, Complex) f0
(Vector#(64, Complex) x);

## Slide 23: Folded Combinational Ckts
rule folded-pipeline (True);
let sxIn = ?;
if (stage==0)
begin sxIn= inQ.first(); inQ.deq(); end
else sxIn= sReg;
let sxOut = f(stage,sxIn);
if (stage==n-1) outQ.enq(sxOut);
else sReg <= sxOut;
stage <= (stage==n-1)? 0 : stage+1;
endrule
x
sReg
inQ
f
outQ
stage
notice stage is a dynamic parameter now!
no for-loop

## Slide 24: Shared Circuit
The Twiddle constants can be expressed in a table or in a case or nested case expression
stage
getTwiddle0
getTwiddle1
getTwiddle2
twid
The rest of stage_f, i.e. Bfly-4s and permutations (shared)
sx

## Slide 25: Superfolded pipeline One Bfly-4 case
f will be invoked for 48 dynamic values of stage
  each invocation will modify 4 numbers in sReg
  after 16 invocations a permutation would be done on the whole sReg

## Slide 26: Superfolded IFFT: stage function f
function Vector#(64, Complex) stage_f
(Bit#(2) stage, Vector#(64, Complex) stage_in);
Vector#(64, Complex#(n)) stage_temp, stage_out;
for (Integer i = 0; i < 16; i = i + 1)
begin Bit#(2) stage
Integer idx = i * 4;
let twid = getTwiddle(stage, fromInteger(i));
let y = bfly4(twid, stage_in[idx:idx+3]);
stage_temp[idx] = y[0]; stage_temp[idx+1] = y[1];
stage_temp[idx+2] = y[2]; stage_temp[idx+3] = y[3];
end
//Permutation
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
Bit#(2+4) (stage,i)
should be done only when i=15

## Slide 27: Code for the Superfolded stage function
Function Vector#(64, Complex) f
(Bit#(6) stagei, Vector#(64, Complex) stage_in);
let i = stagei `mod` 16;
let twid = getTwiddle(stagei `div` 16, i);
let y = bfly4(twid, stage_in[i:i+3]);
let stage_temp = stage_in;
stage_temp[i] = y[0];
stage_temp[i+1] = y[1];
stage_temp[i+2] = y[2];
stage_temp[i+3] = y[3];
let stage_out = stage_temp;
if (i == 15)
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
One Bfly-4 case

## Slide 28: 802.11a Transmitter [MEMOCODE 2006] Dave, Gerding, Pellauer, Arvind
Design Lines of Relative
Block Code (BSV) Area
Controller 49 0%
Scrambler 40 0%
Conv. Encoder 113 0%
Interleaver 76 1%
Mapper 112 11%
IFFT 95 85%
Cyc. Extender 23 3%
Complex arithmetic libraries constitute another 200 lines of code

## Slide 29: 802.11a Transmitter Synthesis results (Only the IFFT block is changing)
IFFT Design | Area (mm2) | Throughput Latency (CLKs/sym) | Min. Freq Required
Pipelined | 5.25 | 04 | 1.0 MHz
Combinational | 4.91 | 04 | 1.0 MHz
Folded (16 Bfly-4s) | 3.97 | 04 | 1.0 MHz
Super-Folded (8 Bfly-4s) | 3.69 | 06 | 1.5 MHz
SF(4 Bfly-4s) | 2.45 | 12 | 3.0 MHz
SF(2 Bfly-4s) | 1.84 | 24 | 6.0 MHz
SF (1 Bfly4) | 1.52 | 48 | 12 MHZ
TSMC .18 micron; numbers reported are before place and route.
The same source code
All these designs were done in less than 24 hours!

## Slide 30: Why are the areas so similar
Folding should have given a 3x improvement in IFFT area
BUT a constant twiddle allows low-level optimization on a Bfly-4 block
  a 2.5x area reduction!