## Slide 1
BSV execution model and concurrent rule scheduling
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: BSV Execution Model
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
A legal behavior of a BSV program can be explained by observing the state updates obtained by applying only one rule at a time
Highly non-deterministic; User annotations can be used in rule selection
One-rule-at-time semantics

## Slide 3: Concurrent scheduling of rules
The one-rule-at-a-time semantics plays the central role in defining functional correctness and verification but for meaningful hardware design it is necessary to execute multiple rules concurrently without violating the one-rule-at-a-time semantics
What do we mean by concurrent scheduling?
  First - some hardware intuition
  Second - semantics of rule execution
  Third - semantics of concurrent scheduling

## Slide 4: Hardware intuition for concurrent scheduling

## Slide 5: BSV Rule Execution
A BSV program consists of state elements and rules, aka, Guarded Atomic Actions (GAA) that operate on the state elements
Application of a rule modifies some state elements of the system in a deterministic manner
current
state
next
state
values
next state
computation
f
x
f
x
guard
reg en’s
nextState
AND

## Slide 6: some insight into Concurrent rule firing
There are more intermediate states in the rule semantics (a state after each rule step)
In the HW, states change only at clock edges
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 7: Parallel execution reorders reads and writes
In the rule semantics, each rule sees (reads) the effects (writes) of previous rules
In the HW, rules only see the effects from previous clocks, and only affect subsequent clocks
Rules
HW
clocks
rule
steps
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes

## Slide 8: Correctness
Rules are allowed to fire in parallel only if the net state change is equivalent to sequential rule execution
Consequence: the HW can never reach a state unexpected in the rule semantics
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 9: Compiling a Rule
f
x
current
state
next
state
d
p
guard
f
x
rule r (f.first() > 0) ;
x <= x + 1 ; f.deq ();
endrule
rdy signals
read methods
next state values
Notes: In a circuit, pi maps to combination logic that looks at the current state and generates a boolean enable signal for this rule
The delta functions is another combination logic that computes the next state value from the current state value. Actually, delta has to compute the control signals to set the state element to the new value

## Slide 10: Combining State Updates: strawman
next state
value
latch
enable
R
OR
p1
pn
d1,R
dn,R
OR
p’s from the rules
that update R
d’s from the rules
that update R
What if more than one rule is enabled?
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 11: Combining State Updates
next state
value
latch
enable
R
Scheduler:
Priority
Encoder
OR
f1
fn
p1
pn
d1,R
dn,R
OR
d’s from the rules
that update R
Scheduler ensures that at most one fi is true
p’s from all
the rules
one-rule-at-a-time
scheduler is
conservative
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 12: Concurrent scheduling
The BSV compiler determines which rules among the rules whose guards are ready can be executed concurrently
It then divides the rules into disjoint sets such that the rules within each set are conflict free
Among conflicting sets of enabled rules it picks one set by some predetermined priority and this process is repeated until no rules are enabled

## Slide 13: A compiler test for concurrent rule firing James Hoe, Ph.D., 2000
Let RS(r) be the set of registers rule r may read
Let WS(r) be the set of registers rule r may write
Rules ra and rb are conflict free (CF) if
  (RS(ra)WS(rb) = )  (RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
Rules ra and rb are sequentially composable (SC) (ra<rb) if
(RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
If Rules ra and rb conflict if they are not CF or SC

## Slide 14: Scheduling and control logic
Modules
(Current state)
Rules
d1
p1
Scheduler
f1
fn
p1
pn
Muxing
d1
dn
dn
pn
Modules
(Next state)
cond
action
“CAN_FIRE”
“WILL_FIRE”
Compiler synthesizes a scheduler such that at any given time f’s for only non-conflicting rules are true
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 15: Bluespec semantics

## Slide 16: Bluespec: Two-Level Compilation
Object code
(Verilog/C)
Rules and Actions
(Term Rewriting System)
Rule conflict analysis
Rule scheduling
James Hoe & Arvind
@MIT 1997-2000
Bluespec
(Objects, Types,
Higher-order functions)
Level 1 compilation
Type checking
Massive partial evaluation and static elaboration
Level 2 synthesis
Lennart Augustsson
@Sandburst 2000-2002
Now we call this Guarded Atomic Actions

## Slide 17: Static Elaboration
.exe
compile
design2
design3
design1
elaborate
w/params
run1
run1
run2.1
…
run1
run1
run3.1
…
run1
run1
run1.1
…
run w/
params
run w/
params
run1
run1
…
run
At compile time
  Inline function calls and unroll loops
  Instantiate modules with specific parameters
  Resolve polymorphism/overloading, perform most data structure operations
source
Software
Toolflow:
source
Hardware
Toolflow:

## Slide 18: The language after type checking and static elaboration
rule name e a
a ::= x<= e register assignment
| a ; a parallel actions
| if (e) a conditional action
| a when e guarded action
| m.g(e) action method call
| t = e ; a binding
e ::= c | t | x | op(e,e) | m.f(e) | t= e; e
guard
action
expression
register read
value method call
Register names (x, …) are global while bindings (t. …) follow usual lexical scoping rules

## Slide 19: Guard Lifting rules
All the guards can be “lifted” to the top of a rule
  (a1 when p) ; a2 
  a1 ; (a2 when p) 
  if (p when q) a 
  if (p) (a when q) 
  (a when p1) when p2 
  x <= (e when p) 
  m.gB(e when p) 
similarly for expressions ...
  Rule r (a when p) 
  (a1 ; a2) when p
  (a1 ; a2) when p
  (if (p) a) when q
  (if (p) a) when (q | !p)
  a when (p1 & p2)
  (x <= e) when p
  m.gB(e) when p
  Rule r (if (p) a)
We will give a procedure to evaluate rules after guard lifting

## Slide 20: Rule evaluation
evalA :: (Bindings, State, a) -> (Bindings, StateUpdates)
evalE :: (Bindings, State, e) -> Value
register values
variable bindings
rule name e a
a ::= x<= e register assignment
| a ; a parallel actions
| if (e) a conditional action
| m.g(e) action method call
| t = e ; a binding
e ::= c | t | x | op(e,e) | m.f(e) | t= e; e

## Slide 21: Action evaluator no method calls
evalA(bs, s, [[x <= e]]) = (bs, (x,evalE(bs, s, e)))
evalA(bs, s, [[a1 ; a2]]) =
let (bs’, u1) = evalA(bs, s, a1)
(bs’’, u2) = evalA(bs’, s, a2)
in (bs’’, u1 + u2)
evalA(bs, s, [[if (e) a]]) =
if evalE(bs, s, e) then evalA(bs, s, a)
else (bs, {})
evalA(bs, s, [[t = e; a]]) =
let v = evalE(bs, s, e)
in evalA(bs + (t,v), s, a)
evalA :: (Bindings, State, a) -> (Bindings, StateUpdates)
initially bs is empty and state contains old register values
merges two sets of updates; the rule is illegal if there are multiple updates for the same register
extends the bindings by including one for t

## Slide 22: Expression evaluator no method calls
evalE (bs, s, [[c]]) = c
evalE (bs, s, [[t]]) = lookup(bs,t)
evalE (bs, s, [[x]]) = s.x
evalE (bs, s, [[op(e1,e2)]]) =
OP(evalE(bs, s, e1), evalE(bs, s, e2))
evalE :: (Bindings, State, exp) -> Value
Method calls can be evaluated by substituting the body of the method call, i.e., m.g(e) is a[e/x] where the definition of m.g is method g(x) = a
if t does not exist in bs then the rule is illegal
To apply a rule, we first evaluate its guard and then if the guard is true we compute the state updates and then simultaneously update all the state variables

## Slide 23: Legal BSV rules
A legal BSV rule does not contain multiple assignments to the same state element or combinational cycles
Examples: legal?
rule ra if (z>10);
x <= x+1; endrule
rule rb;
x <= x+1; if (p) x <= 7 endrule
rule rc;
x <= y+1; y <= x+2 endrule
rule rd;
t1 = f(t2); t2 = g(t1); x <= t1; endrule
no
yes
yes
no
In general the legality of a rule can be determined only at run time.

## Slide 24: Concurrent scheduling: Semantic view
Suppose rule ra a and rule rb b are legal rules and a’ = (if impCondOf(a) then a) and b’ = (if impCondOf(b) then b). ra and rb are said to be concurrently schedulable, iff,
  rule rab (a’;b’) is legal
  for all s, (a’;b’)(s) = a(b(s)) or b(a(s))
  Notice (a’,b’) = (b’,a’); and rule rab will produce the correct result if only one of the rules fired
  Theorm1: If rules ra and rb are conflict free (CF) then s, (a’;b’)(s) = a(b(s)) = b(a(s))
  Theorm2: If rules ra and rb are sequentially composable (SC) (ra<rb) then s, (a’;b’)(s) = b(a(s))

## Slide 25: Example 1
{x0,y0,30} ra {x0+1,y0,30} rb {x0+1,y0+2,30}
{x0,y0,30} rb {x0,y0+2,30} ra {x0+1,y0+2,30}
{x0,y0,30} ra_rb {x0+1,y0+2,30}
{x0,y0,15} ra {x0+1,y0,15} rb {x0+1,y0,15}
{x0,y0,15} rb {x0,y0,15} ra {x0+1,y0,15}
{x0,y0,15} ra_rb {x0+1,y0,15}
Parallel execution behaves like
ra < rb (i.e., rb(ra(s))
= rb < ra (i.e., ra(rb(s))
rule ra if (z>10);
x <= x+1;
endrule
rule rb if (z>20);
y <= y+2;
endrule
rule ra_rb;
if (z>10) x <= x+1;
if (z>20) y <= y+2;
endrule

## Slide 26: Example 2
{x0,y0,30} ra {y0+1,y0,30} rb {y0+1,y0+1+2,30}
{x0,y0,30} rb {x0,x0+2,30} ra {x0+2+1,x0+2,30}
{x0,y0,30} ra_rb {y0+1,x0+2,30}
rule ra if (z>10);
x <= y+1;
endrule
rule rb if (z>20);
y <= x+2;
endrule
rule ra_rb;
if (z>10) x <= y+1;
if (z>20) y <= x+2;
endrule
Rule ra_rb is legal but does not behave like either ra < rb or rb < ra
Rules ra and rb conflict and can’t be scheduled concurrently

## Slide 27: Example 3
{x0,y0,30} ra {y0+1,y0,30} rb {y0+1,y0+2,30}
{x0,y0,30} rb {x0,y0+2,30} ra {y0+2+1,y0+2,30}
{x0,y0,30} ra_rb {y0+1,y0+2,30}
rule ra if (z>10);
x <= y+1;
endrule
rule rb if (z>20);
y <= y+2;
endrule
rule ra_rb;
if (z>10) x <= y+1;
if (z>20) y <= y+2;
endrule
Rule ra_rb is legal and behaves like ra < rb (i.e., rb(ra(s)))
Rules ra and rb can be scheduled concurrently with the functionality ra < rb

## Slide 28: Example 4
rule ra;
x <= y+1; u <= u+2;
endrule
rule rb;
y <= y+2; v <= u+1;
endrule
rule ra_rb;
x <= y+1; u <=u+2;
y <= y+2; v <=u+1;
endrule
Rule ra_rb is legal but does not behave like either ra < rb or rb < ra
Notice read/write accesses to y can be resolved by ordering ra < rb while accesses to u can be resolved by ordering rb < ra. Since these orderings are contradictory these rules conflict and cannot be scheduled concurrently