## Slide 1
Pipelined Processors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Two-Cycle SMIPS: Analysis
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
fr
stage
In any given clock cycle, lot of unused hardware !
Execute
Fetch
Pipeline execution of instructions to increase the throughput
Notes: 2

## Slide 3: Problems in Instruction pipelining
Control hazard: Insti+1 is not known until Insti is at least decoded. So which instruction should be fetched?
Structural hazard: Two instructions in the pipeline may require the same resource at the same time, e.g., contention for memory
Data hazard: Insti may affect the state of the machine (pc, rf, dMem) – Insti+1must be fully cognizant of this change
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
+4
f2d
Insti
Insti+1
none of these hazards were present in the IFFT pipeline

## Slide 4: Arithmetic versus Instruction pipelining
The data items in an arithmetic pipeline, e.g., IFFT, are independent of each other
The entities in an instruction pipeline affect each other
  This causes pipeline stalls or requires other fancy tricks to avoid stalls
  Processor pipelines are significantly more complicated than arithmetic pipelines
sReg1
sReg2
x
inQ
f0
f1
f2
outQ

## Slide 5: The power of computers comes from the fact that the instructions in a program are not independent of each other  must deal with hazard

## Slide 6: Control Hazards
Insti+1 is not known until Insti is at least decoded. So which instruction should be fetched?
General solution – speculate, i.e., predict the next instruction address
  requires the next-instruction-address prediction machinery; can be as simple as pc+4
  prediction machinery is usually elaborate because it dynamically learns from the past behavior of the program
What if speculation goes wrong?
  machinery to kill the wrong-path instructions, restore the correct processor state and restart the execution at the correct pc
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
+4
f2d
Insti
Insti+1

## Slide 7: Two-stage Pipelined SMIPS
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
pred
f2d
Fetch stage must predict the next instruction to fetch to have any pipelining
Fetch stage
Decode-RegisterFetch-Execute-Memory-WriteBack stage
In case of a misprediction the Execute stage must kill the mispredicted instruction in f2d
kill
misprediction
correct pc
Notes: 7

## Slide 8: Pipelining Two-Cycle SMIPS –singlerule
rule doPipeline ;
let inst = iMem.req(pc);
let ppc = nextAddr(pc); let newPc = ppc;
let newIr=Valid(Fetch2Decode{pc:pc,ppc:ppc,inst:inst});
if(isValid(ir)) begin
let x = validValue(ir); let irpc = x.pc;
let ppc = x.ppc; let inst = x.inst;
let dInst = decode(inst);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, irpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
newIr = Invalid;
newPc = eInst.addr; end
end
pc <= newPc; ir <= newIr;
endrule
fetch
execute

## Slide 9: Inelastic versus Elastic pipeline
The pipeline presented is inelastic, that is, it relies on executing Fetch and Execute together or atomically
In a realistic machine, Fetch and Execute behave more asynchronously; for example memory latency or a functional unit may take variable number of cycles
If we replace ir by a FIFO (f2d) then it is possible to make the machine more elastic, that is, Fetch keeps putting instructions into f2d and Execute keeps removing and executing instructions from f2d.

## Slide 10: An elastic Two-Stage pipeline
rule doFetch ;
let inst = iMem.req(pc);
let ppc = nextAddr(pc); pc <= ppc;
f2d.enq(Fetch2Decode{pc:pc,ppc:ppc,inst:inst});
endrule
rule doExecute;
let x = f2d.first; let inpc = x.pc;
let ppc = x.ppc; let inst = x.inst;
let dInst = decode(inst);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, inpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc <= eInst.addr; f2d.clear; end
else f2d.deq;
endrule
Can these rules execute concurrently assuming the FIFO allows concurrent enq, deq and clear?
no – double writes in pc
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 11: An elastic Two-Stage pipeline: for concurrency make pc into an EHR
rule doFetch ;
let inst = iMem.req(pc[0]);
let ppc = nextAddr(pc[0]); pc[0] <= ppc;
f2d.enq(Fetch2Decode{pc:pc[0],ppc:ppc,inst:inst});
endrule
rule doExecute;
let x = f2d.first; let inpc = x.pc;
let ppc = x.ppc; let inst = x.inst;
let dInst = decode(inst);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, inpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc[1] <= eInst.addr; f2d.clear; end
else f2d.deq;
endrule
These rules execute concurrently assuming the FIFO has
(enq CF deq) and
(enq < clear)
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 12: Conflict-free FIFO with a Clear method
module mkCFFifo(Fifo#(2, t)) provisos(Bits#(t, tSz));
Ehr#(3, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(3, Bool) vb <- mkEhr(False);
rule canonicalize if(vb[2] && !va[2]);
da[2] <= db[2]; va[2] <= True; vb[2] <= False; endrule
method Action enq(t x) if(!vb[0]);
db[0] <= x; vb[0] <= True; endmethod
method Action deq if (va[0]);
va[0] <= False; endmethod
method t first if(va[0]);
return da[0]; endmethod
method Action clear;
va[1] <= False ; vb[1] <= False endmethod
endmodule
If there is only one element in the FIFO it resides in da
db da
first CF enq
deq CF enq
first < deq
enq < clear
Canonicalize must be the last rule to fire!

## Slide 13: Why canonicalize must be last rule to fire
first CF enq
deq CF enq
first < deq
enq < clear
rule foo ;
f.deq; if (p) f.clear
endrule
Consider rule foo. If p is false then canonicalize must fire after deq for proper concurrency.
If canonicalize uses EHR indices between deq and clear, then canonicalize won’t fire when p is false

## Slide 14: Correctness issue
<inst, pc, ppc>
Once Execute redirects the PC,
  no wrong path instruction should be executed
  the next instruction executed must be the redirected one
This is true for the code shown because
  Execute changes the pc and clears the FIFO atomically
  Fetch reads the pc and enqueues the FIFO atomically
Fetch
Execute
PC

## Slide 15: Killing fetched instructions
In the simple design with combinational memory we have discussed so far, the mispredicted instruction was present in the f2d. So the Execute stage can atomically
  Clear the f2d
  Set the pc to the correct target
In highly pipelined machines there can be multiple mispredicted and partially executed instructions in the pipeline; it will generally take more than one cycle to kill all such instructions

## Slide 16: Epoch: a method for managing control hazards
Add an epoch register in the processor state
The Execute stage changes the epoch whenever the pc prediction is wrong and sets the pc to the correct value
The Fetch stage associates the current epoch with every instruction when it is fetched
PC
iMem
pred
f2d
Epoch
Fetch
Execute
inst
targetPC
The epoch of the instruction is examined when it is ready to execute. If the processor epoch has changed the instruction is thrown away

## Slide 17: Discussion
Epoch based solution kills one wrong-path instruction at a time in the execute stage
It may be slow, but it is more robust in more complex pipelines, if you have multiple stages between fetch and execute or if you have outstanding instruction requests to the iMem
It requires the Execute stage to set the pc and epoch registers simultaneously which may result in a long combinational path from Execute to Fetch

## Slide 18: An epoch based solution
rule doFetch ;
let inst=iMem.req(pc[0]);
let ppc=nextAddr(pc[0]); pc[0]<=ppc;
f2d.enq(Fetch2Decode{pc:pc[0],ppc:ppc,epoch:epoch,
inst:inst});
endrule
rule doExecute;
let x=f2d.first; let inpc=x.pc; let inEp=x.epoch;
let ppc = x.ppc; let inst = x.inst;
if(inEp == epoch) begin
let dInst = decode(inst); ... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, inpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc[1] <= eInst.addr; epoch <= epoch + 1; end
end
f2d.deq; endrule
Can these rules execute concurrently ?
yes
two values for epoch are sufficient
Notes: Fetch reads and writes PC, writes epoch and enqs ir
Execute writes PC, writes epoch and deqs ir
Fetch < Execute within the same cycle
The machine works with both CF and Bypass FIFOs for ir, but only CF Fifo gives pipelined behavior
If inEp was replaced by epoch in Execute, then Fetch and Execute can not be scheduled concurrently

## Slide 19: Decoupled Fetch and Execute
<inst, pc, ppc, epoch>
<corrected pc, new epoch>
In decoupled systems a subsystem reads and modifies only local state atomically
  In our solution, pc and epoch are read by both rules
Properly decoupled systems permit greater freedom in independent refinement of subsystems
Fetch
Execute

## Slide 20: A decoupled solution using epochs
Add fEpoch and eEpoch registers to the processor state; initialize them to the same value
The epoch changes whenever Execute detects the pc prediction to be wrong. This change is reflected immediately in eEpoch and eventually in fEpoch via a message from Execute to Fetch
Associate the fEpoch with every instruction when it is fetched
In the execute stage, reject, i.e., kill, the instruction if its epoch does not match eEpoch
fEpoch
eEpoch
fetch
execute

## Slide 21: Control Hazard resolution A robust two-rule solution
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
f2d
FIFO
FIFO
redirect
Execute sends information about the target pc to Fetch, which updates fEpoch and pc whenever it looks at the redirect PC fifo
fEpoch
eEpoch
Notes: 21

## Slide 22: Two-stage pipeline Decoupled code structure
module mkProc(Proc);
Fifo#(Fetch2Execute) f2d <- mkFifo; Fifo#(Addr) execRedirect <- mkFifo; Reg#(Bool) fEpoch <- mkReg(False); Reg#(Bool) eEpoch <- mkReg(False);
rule doFetch; let inst = iMem.req(pc); ...
f2d.enq(... inst ..., fEpoch); endrule
rule doExecute;
if(inEp == eEpoch) begin Decode and execute the instruction; update state;
In case of misprediction, execRedirect.enq(correct pc); end f2d.deq; endrule
endmodule

## Slide 23: The Fetch rule
rule doFetch;
let inst = iMem.req(pc);
if(!execRedirect.notEmpty)
begin let ppc = nextAddrPredictor(pc);
pc <= ppc; f2d.enq(Fetch2Execute{pc: pc, ppc: ppc,
inst: inst, epoch: fEpoch});
end else
begin fEpoch <= !fEpoch; pc <= execRedirect.first;
execRedirect.deq;
end endrule
pass the pc and predicted pc to the execute stage
Notice: In case of PC redirection, nothing is enqueued into f2d

## Slide 24: The Execute rule
rule doExecute; let inst = f2d.first.inst; let pc = f2d.first.pc; let ppc = f2d.first.ppc; let inEp = f2d.first.epoch; if(inEp == eEpoch) begin let dInst = decode(inst); let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <- dMem.req(MemReq{op: Ld, addr: eInst.addr, data: ?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op: St, addr: eInst.addr, data: eInst.data}); if (isValid(eInst.dst)) rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin execRedirect.enq(eInst.addr); eEpoch <= !inEp;
end end f2d.deq; endrule
exec returns a flag if there was a fetch misprediction
Can these rules execute concurrently?
yes, assuming CF FIFOs

## Slide 25
Data Hazards

## Slide 26: Consider a different two-stage pipeline
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
pred
f2d
Suppose we move the pipeline stage from Fetch to after Decode and Register fetch
Fetch
Execute, Memory, WriteBack
Insti
Insti+1
What hazards will the pipeline have?
Decode,
RegisterFetch
Control?
yes
Any other?
Notes: 26

## Slide 27: A different 2-Stage pipeline: 2-Stage-DH pipeline
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
d2e
redirect
fEpoch
eEpoch
pred
Fifos
Use the same epoch solution for control hazards as before
Fetch, Decode, RegisterFetch
Execute, Memory, WriteBack
Modify the code for the 2-Stage-CHO pipeline
Notes: 27

## Slide 28: Type Decode2Execute
typedef struct {
Addr pc; Addr ppc; Bool epoch;
DecodedInst dInst; Data rVal1; Data rVal2;
} Decode2Execute deriving (Bits, Eq);
value instead of register names
The Fetch stage, in addition to fetching the instruction, also decodes the instruction and fetches the operands from the register file. It passes these operands to the Execute stage
Notes: 28

## Slide 29: 2-Stage-DH pipeline
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkFifo;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) execRedirect <- mkFifo;
rule doFetch …
rule doExecute …
Notes: 29

## Slide 30: 2-Stage-DH pipeline doFetch rule first attempt
rule doFetch; let inst = iMem.req(pc); if(execRedirect.notEmpty) begin fEpoch <= !fEpoch; pc <= execRedirect.first;
execRedirect.deq; end else
begin let ppc = nextAddrPredictor(pc); pc <= ppc;
let dInst = decode(inst); let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppc,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
end endrule
moved from Execute

## Slide 31: 2-Stage-DH pipeline doExecute rule first attempt
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst) &&
validValue(eInst.dst).regType == Normal) rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin execRedirect.enq(eInst.addr); eEpoch <= !eEpoch; end end d2e.deq; endrule
no change
Not quite correct. Why?
Fetch is potentially reading stale values from rf

## Slide 32: Data Hazards
fetch & decode
execute
d2e
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
FDstage FD1 FD2 FD3 FD4 FD5
EXstage EX1 EX2 EX3 EX4 EX5
I1 Add(R1,R2,R3)
I2 Add(R4,R1,R2)
I2 must be stalled until I1 updates the register file
pc
rf
dMem
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
FDstage FD1 FD2 FD2 FD3 FD4 FD5
EXstage EX1 EX2 EX3 EX4 EX5
next lecture: Resolving Data Hazards
Notes: 32