## Slide 1
Introduction to Bluespec: A new methodology for designing Hardware
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: What is needed to make hardware design easier
Extreme IP reuse
  Multiple instantiations of a block for different performance and application requirements
  Packaging of IP so that the blocks can be assembled easily to build a large system (black box model)
Ability to do modular refinement
Whole system simulation to enable concurrent hardware-software development
“Intellectual Property”

## Slide 3: IP Reuse sounds wonderful until you try it ...
data_in push_req_n pop_req_n clk rstn
data_out full empty
Example: Commercially available FIFO IP block
These constraints are spread over many pages of the documentation...
No machine verification of such informal constraints is feasible
Bluespec can change all this

## Slide 4: Bluespec promotes composition through guarded interfaces
not full
not empty
not empty
theModuleA
theModuleB
theFifo.enq(value1);
theFifo.deq();
value2 = theFifo.first();
theFifo.enq(value3);
theFifo.deq();
value4 = theFifo.first();
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
theFifo
Enqueue arbitration control
Dequeue arbitration control
Self-documenting interfaces;
Automatic generation of logic to eliminate conflicts in use.

## Slide 5: Bluespec: A new way of expressing behavior using Guarded Atomic Actions
Formalizes composition
  Modules with guarded interfaces
  Compiler manages connectivity (muxing and associated control)
Powerful static elaboration facility
  Permits parameterization of designs at all levels
Transaction level modeling
  Allows C and Verilog codes to be encapsulated in Bluespec modules
Smaller, simpler, clearer, more correct code
not just simulation, synthesis as well
Bluespec

## Slide 6: Bluespec: State and Rules organized into modules
All state (e.g., Registers, FIFOs, RAMs, ...) is explicit.
Behavior is expressed in terms of atomic actions on the state:
Rule: guard  action
Rules can manipulate state in other modules only via their interfaces.
interface
module

## Slide 7
GCD: A simple example to explain hardware generation from Bluespec

## Slide 8: Programming with rules: A simple example
Euclid’s algorithm for computing the Greatest Common Divisor (GCD):
15 6
9 6 subtract
3 6 subtract
6 3 swap
3 3 subtract
0 3 subtract
answer:

## Slide 9: GCD in BSV
module mkGCD (I_GCD);
Reg#(Int#(32)) x <- mkRegU;
Reg#(Int#(32)) y <- mkReg(0);
rule swap ((x > y) && (y != 0));
x <= y; y <= x;
endrule
rule subtract ((x <= y) && (y != 0));
y <= y – x;
endrule
method Action start(Int#(32) a, Int#(32) b)
if (y==0);
x <= a; y <= b;
endmethod
method Int#(32) result() if (y==0);
return x;
endmethod
endmodule
Internal
behavior
External
interface
State
Assume a/=0
x
y
swap
sub
If (a==0) then 0 else b

## Slide 10: GCD Hardware Module
rdy
enab
Int#(32)
Int#(32)
rdy
start
result
GCD
module
Int#(32)
y == 0
y == 0
implicit conditions
interface I_GCD;
method Action start (Int#(32) a, Int#(32) b);
method Int#(32) result();
endinterface
t
#(type t)
t
t
t
t
t
In a GCD call t could be
Int#(32),
UInt#(16),
Int#(13), ...
The module can easily be made polymorphic
Many different implementations can provide the same interface: module mkGCD (I_GCD)

## Slide 11: GCD: Another implementation
module mkGCD (I_GCD);
Reg#(Int#(32)) x <- mkRegU;
Reg#(Int#(32)) y <- mkReg(0);
rule swapANDsub ((x > y) && (y != 0));
x <= y; y <= x - y;
endrule
rule subtract ((x<=y) && (y!=0));
y <= y – x;
endrule
method Action start(Int#(32) a, Int#(32) b)
if (y==0);
x <= a; y <= b;
endmethod
method Int#(32) result() if (y==0);
return x;
endmethod
endmodule
Combine swap and subtract rule
Does it compute faster ?
Does it take more resources ?

## Slide 12: High-level Synthesis from Bluespec
VCD output
Debussy
Visualization
Bluesim
Cycle Accurate
Bluespec SystemVerilog source
Verilog 95 RTL
Verilog sim
Bluespec Compiler
RTL synthesis
gates
Physical
Place &
Route
Tapeout
FPGA
Power estimation tool
First simulate
Second run on FPGAs
We won’t explore the chip design path

## Slide 13: Generated Verilog RTL: GCD
module mkGCD(CLK,RST_N,start_a,start_b,EN_start,RDY_start,
result,RDY_result);
input CLK; input RST_N;
// action method start
input [31 : 0] start_a; input [31 : 0] start_b; input EN_start;
output RDY_start;
// value method result
output [31 : 0] result; output RDY_result;
// register x and y
reg [31 : 0] x;
wire [31 : 0] x$D_IN; wire x$EN;
reg [31 : 0] y;
wire [31 : 0] y$D_IN; wire y$EN;
...
// rule RL_subtract
assign WILL_FIRE_RL_subtract = x_SLE_y___d3 && !y_EQ_0___d10 ;
// rule RL_swap
assign WILL_FIRE_RL_swap = !x_SLE_y___d3 && !y_EQ_0___d10 ;
...

## Slide 14: Generated Hardware
next state values
predicates
x_en
y_en
x_en =
y_en =
x
y
>
!(=0)
swap?
subtract?
sub
x
y
en
rdy
x
rdy
start
result
swap?
swap? OR subtract?
rule swap ((x>y)&&(y!=0));
x <= y; y <= x; endrule
rule subtract ((x<=y)&&(y!=0));
y <= y – x; endrule

## Slide 15: Generated Hardware Module
x_en
y_en
x_en = swap?
y_en = swap? OR subtract?
x
y
>
!(=0)
swap?
subtract?
sub
x
y
en
rdy
x
rdy
start
result
rdy =
start_en
start_en
OR start_en
(y==0)
OR start_en

## Slide 16: GCD: A Simple Test Bench
module mkTest ();
Reg#(Int#(32)) state <- mkReg(0);
I_GCD gcd <- mkGCD();
rule go (state == 0);
gcd.start (423, 142);
state <= 1;
endrule
rule finish (state == 1);
$display (“GCD of 423 & 142 =%d”,gcd.result());
state <= 2;
endrule
endmodule
Why do we need the state variable?
Is there any timing issue in displaying the result?
No. Because the finish rule cannot execute until gcd.result is ready

## Slide 17: GCD: Test Bench
module mkTest ();
Reg#(Int#(32)) state <- mkReg(0);
Reg#(Int#(4)) c1 <- mkReg(1);
Reg#(Int#(7)) c2 <- mkReg(1);
I_GCD gcd <- mkGCD();
rule req (state==0);
gcd.start(signExtend(c1), signExtend(c2));
state <= 1;
endrule
rule resp (state==1);
$display (“GCD of %d & %d =%d”, c1, c2, gcd.result());
if (c1==7) begin c1 <= 1; c2 <= c2+1; end
else c1 <= c1+1;
if (c1==7 && c2==63) state <= 2 else state <= 0;
endrule
endmodule
Feeds all pairs (c1,c2)
1 < c1 < 7
1 < c2 < 63
to GCD

## Slide 18: GCD: Synthesis results
Original (16 bits)
  Clock Period: 1.6 ns
  Area: 4240 mm2
Unrolled (16 bits)
  Clock Period: 1.65ns
  Area: 5944 mm2
Unrolled takes 31% fewer cycles on the testbench

## Slide 19: Hardware synthesis and rule scheduling

## Slide 20: Rule: As a State Transformer
A rule may be decomposed into two parts p(s) and d(s) such that
snext = if p(s) then d(s) else s
p(s) is the condition (predicate) of the rule, a.k.a. the “CAN_FIRE” signal of the rule. p is a conjunction of explicit and implicit conditions
d(s) is the “state transformation” function, i.e., computes the next-state values from the current state values
Notes: Abstractly, we can think of a rule having to parts, a pi function and a delta function.
The pi function tells us whetherule can be applied to a term s
If the the pievaluates to true, then the delta function tells us what is the new term.
And if pi is false, the rule cannot change s

## Slide 21: Compiling a Rule
f
x
current
state
next
state
values
d
p
enable
f
x
rule r (f.first() > 0) ;
x <= x + 1 ; f.deq ();
endrule
p = enabling condition
d = action signals & values
rdy signals
read methods
enable signals
action parameters
Notes: In a circuit, pi maps to combination logic that looks at the current state and generates a boolean enable signal for this rule
The delta functions is another combination logic that computes the next state value from the current state value. Actually, delta has to compute the control signals to set the state element to the new value

## Slide 22: Combining State Updates: strawman
next state
value
latch
enable
R
OR
p1
pn
d1,R
dn,R
OR
p’s from the rules
that update R
d’s from the rules
that update R
What if more than one rule is enabled?
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 23: Need for a rule scheduler

## Slide 24: GAA Execution model
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
Highly non-deterministic
Implementation concern: Schedule multiple rules concurrently without violating one-rule-at-a-time semantics
User annotations can help in rule selection

## Slide 25: Combining State Updates
next state
value
latch
enable
R
Scheduler:
Priority
Encoder
OR
f1
fn
p1
pn
d1,R
dn,R
OR
d’s from the rules
that update R
Scheduler ensures that at most one fi is true
p’s from all
the rules
one-rule-at-a-time
scheduler is
conservative
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 26: A compiler can determine if two rules can be executed in parallel without violating the one-rule-at-a-time semantics James Hoe, Ph.D., 2000

## Slide 27: Scheduling and control logic
Modules
(Current state)
Rules
d1
p1
Scheduler
f1
fn
p1
pn
Muxing
d1
dn
dn
pn
Modules
(Next state)
cond
action
“CAN_FIRE”
“WILL_FIRE”
Compiler synthesizes a scheduler such that at any given time f’s for only non-conflicting rules are true
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 28: The plan
Combinational circuits in Bluespec
Sequential circuits using rules
Inelastic pipelines
  single-rule systems; no scheduling issues
Multiple rule systems and concurrency issues
  Eliminating dead cycles
Elastic pipelines and processors
Each idea would be illustrated via examples
Minimal discussion of Bluespec syntax in the lectures; you are suppose to learn that by yourself and in the lab sessions