## Slide 1
Folded Combinational Circuits as an example of Sequential Circuits
Arvind
Computer Science & Artificial Intelligence Lab
Massachusetts Institute of Technology

## Slide 2: Folding large combinational circuits
A common way to implement large combinational circuits is by folding where registers hold the state from one iteration to the next
  Implementing imperative loops
  Multiplication
  IFFT

## Slide 3: Flip flop: The basic building block of Sequential Circuits
ff
Q
D
C
C
D
Q
Metastability
Data is sampled at the rising edge of the clock
Edge-Triggered Flip-flop
Notes: Metastability?

## Slide 4: Flip-flops with Write Enables
ff
Q
D
C
EN
C
D
Q
EN
ff
Q
D
C
EN
0
1
ff
Q
D
C
EN
dangerous!
Data is captured only if EN is on
Notes: Why dangerous?
Glitches

## Slide 5: Registers
Register: A group of flip-flops with a common
clock and enable
Register file: A group of registers with a common
clock, input and output port(s)
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
Q
Q
Q
Q
Q
Q
Q
Q
D
C
En

## Slide 6: Expressing a loop using registers
int s = s0;
for (int i = 0; i < 32; i = i+1) { s = f(s); } return s; C-code
sel
< 32
0
notDone
+1
i
en
sel = start
en = start | notDone
s0
f
sel
s
en
We need two registers to hold s and i values from one iteration to the next.
These registers are initialized when the computation starts and updated every cycle until the computation terminates

## Slide 7: Expressing sequential circuits in BSV
Sequential circuits, unlike combinational circuits, are not expressed structurally (as wiring diagrams) in BSV
For sequential circuits a designer defines:
  State elements by instantiating modules
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
  Rules which define how state is to be transformed atomically
  rule step if (i < 32); s <= f(s); i <= i+1; endrule
make a 32-bit register which is uninitialized
make a 6-bit register with initial value 32
the rule can execute only when its guard is true
actions to be performed when the rule executes

## Slide 8: Rule Execution
< 32
notDone
+1
sel
0
i
en
sel = start
en = start | notDone
f
s0
sel
s
en
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule step if (i < 32); s <= f(s); i <= i+1; endrule
When a rule executes:
  all the registers are read at the beginning of a clock cycle
  the guard and computations to evaluate the next value of the registers are performed
  at the end of the clock cycle registers are updated iff the guard is true
Muxes are need to initialize the registers

## Slide 9: Multiplication by repeated addition
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
a1
m1
a2
m2
a3
m3
add4
0
add4
add4
a0
m0

## Slide 10: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) tp = 0; Bit#(32) prod = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i:i] = sum[0];
tp = sum[32:1];
end return {tp,prod}; endfunction
Combinational multiply uses 31 add32 circuits
We can reuse the same add32 circuit if we store the partial results in a register

## Slide 11: Design issues with combinational multiply
Lot of hardware
  32-bit multiply uses 31 add32 circuits
Long chains of gates
  32-bit ripple carry adder has a 31-long chain of gates
  32-bit multiply has 31 ripple carry adders in sequence! Total delay ?
The speed of a combinational circuit is determined by its longest input-to-output path
Can we do better?
Yes – Sequential Circuits; Circuits with state
  2(n-1) FAs?

## Slide 12: Multiply using registers
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i:i] = sum[0]; tp = sum[32:1]; end return {tp,prod}; endfunction
Need registers to hold a, b, tp, prod and i
Update the registers every cycle until we are done
Combinational version

## Slide 13: Sequential Circuit for Multiply
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] <= sum[0]; tp <= sum[32:1];
i <= i+1; endrule
state elements
a rule to describe the dynamic behavior
So that the rule has no effect until i is set to some other value
similar to the loop body in the combinational version

## Slide 14: Dynamic selection requires a mux
a[i]
a
i
a[0],a[1],a[2],…
a
>>
0
when the selection indices are regular then it is better to use a shift operator (no gates!)

## Slide 15: Replacing repeated selections by shifts
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= a >> 1; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], prod[31:1]}; tp <= sum[32:1];
i <= i+1; endrule

## Slide 16: Circuit for Sequential Multiply
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
s1 = start_en
s2 = start_en | !done
result (high)
31
0
add
0
0
32:1
0
<<

## Slide 17: Circuit analysis
Number of add32 circuits has been reduced from 31 to one, though some registers and muxes have been added
The longest combinational path has been reduced from 62 FAs to to one add32 plus a few muxes
The sequential circuit will take 31 clock cycles to compute an answer
Notes: (Andy) longest combinational path was effectively 63 1-bit adders.

## Slide 18: Combinational IFFT
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
Reuse the same circuit three times
to reduce area

## Slide 19: Folded IFFT: Reusing the Stage computation
in0
…
in1
in2
in63
in3
in4
out0
…
out1
out2
out63
out3
out4
…
Bfly4
Bfly4
Permute
Stage Counter

## Slide 20: BSV Code for stage_f
function Vector#(64, Complex#(n)) stage_f
(Bit#(2) stage, Vector#(64, Complex#(n)) stage_in);
Vector#(64, Complex#(n)) stage_temp, stage_out;
for (Integer i = 0; i < 16; i = i + 1)
begin
Integer idx = i * 4;
Vector#(4, Complex#(n)) x;
x[0] = stage_in[idx]; x[1] = stage_in[idx+1];
x[2] = stage_in[idx+2]; x[3] = stage_in[idx+3];
let twid = getTwiddle(stage, fromInteger(i));
let y = bfly4(twid, x);
stage_temp[idx] = y[0]; stage_temp[idx+1] = y[1];
stage_temp[idx+2] = y[2]; stage_temp[idx+3] = y[3];
end
//Permutation
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
twid’s are mathematically derivable constants

## Slide 21: Higher-order functions: Stage functions f1, f2 and f3
function f0(x)= stage_f(0,x);
function f1(x)= stage_f(1,x);
function f2(x)= stage_f(2,x);
What is the type of f0(x) ?
function Vector#(64, Complex) f0
(Vector#(64, Complex) x);

## Slide 22: Folded Combinational Ckts
rule folded-pipeline (True);
let sxIn = ?;
if (stage==0)
begin sxIn= inQ.first(); inQ.deq(); end
else sxIn= sReg;
let sxOut = f(stage,sxIn);
if (stage==n-1) outQ.enq(sxOut);
else sReg <= sxOut;
stage <= (stage==n-1)? 0 : stage+1;
endrule
x
sReg
inQ
f
outQ
stage
notice stage is a dynamic parameter now!
no for-loop

## Slide 23: Shared Circuit
The Twiddle constants can be expressed in a table or in a case or nested case expression
stage
getTwiddle0
getTwiddle1
getTwiddle2
twid
The rest of stage_f, i.e. Bfly-4s and permutations (shared)
sx

## Slide 24: Superfolded IFFT: Just one Bfly-4 node!
in0
…
in1
in2
in63
in3
in4
out0
…
out1
out2
out63
out3
out4
Bfly4
Permute
Index == 15?
Index:
0 to 15
64, 2-way Muxes
4, 16-way Muxes
4, 16-way DeMuxes
Stage
0 to 2
f will be invoked for 48 dynamic values of stage; each invocation will modify 4 numbers in sReg
after 16 invocations a permutation would be done on the whole sReg

## Slide 25: Superfolded IFFT: stage function f
function Vector#(64, Complex) stage_f
(Bit#(2) stage, Vector#(64, Complex) stage_in);
Vector#(64, Complex#(n)) stage_temp, stage_out;
for (Integer i = 0; i < 16; i = i + 1)
begin Bit#(2) stage
Integer idx = i * 4;
let twid = getTwiddle(stage, fromInteger(i));
let y = bfly4(twid, stage_in[idx:idx+3]);
stage_temp[idx] = y[0]; stage_temp[idx+1] = y[1];
stage_temp[idx+2] = y[2]; stage_temp[idx+3] = y[3];
end
//Permutation
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
Bit#(2+4) (stage,i)
should be done only when i=15

## Slide 26: Code for the Superfolded stage function
Function Vector#(64, Complex) f
(Bit#(6) stagei, Vector#(64, Complex) stage_in);
let i = stagei `mod` 16;
let twid = getTwiddle(stagei `div` 16, i);
let y = bfly4(twid, stage_in[i:i+3]);
let stage_temp = stage_in;
stage_temp[i] = y[0];
stage_temp[i+1] = y[1];
stage_temp[i+2] = y[2];
stage_temp[i+3] = y[3];
let stage_out = stage_temp;
if (i == 15)
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
One Bfly-4 case

## Slide 27: Syntax: Vector of Registers
Register
  suppose x and y are both of type Reg. Then
  x <= y means x._write(y._read())
Vector of Int
  x[i] means sel(x,i)
  x[i] = y[j] means x = update(x,i, sel(y,j))
Vector of Registers
  x[i] <= y[j] does not work. The parser thinks it means (sel(x,i)._read)._write(sel(y,j)._read), which will not type check
  (x[i]) <= y[j] parses as sel(x,i)._write(sel(y,j)._read), and works correctly
Don’t ask me why

## Slide 28: 802.11a Transmitter [MEMOCODE 2006] Dave, Gerding, Pellauer, Arvind
Design Lines of Relative
Block Code (BSV) Area
Controller 49 0%
Scrambler 40 0%
Conv. Encoder 113 0%
Interleaver 76 1%
Mapper 112 11%
IFFT 95 85%
Cyc. Extender 23 3%
Complex arithmetic libraries constitute another 200 lines of code

## Slide 29: 802.11a Transmitter Synthesis results (Only the IFFT block is changing)
IFFT Design | Area (mm2) | Throughput Latency (CLKs/sym) | Min. Freq Required
Pipelined | 5.25 | 04 | 1.0 MHz
Combinational | 4.91 | 04 | 1.0 MHz
Folded (16 Bfly-4s) | 3.97 | 04 | 1.0 MHz
Super-Folded (8 Bfly-4s) | 3.69 | 06 | 1.5 MHz
SF(4 Bfly-4s) | 2.45 | 12 | 3.0 MHz
SF(2 Bfly-4s) | 1.84 | 24 | 6.0 MHz
SF (1 Bfly4) | 1.52 | 48 | 12 MHZ
TSMC .18 micron; numbers reported are before place and route.
The same source code
All these designs were done in less than 24 hours!

## Slide 30: Why are the areas so similar
Folding should have given a 3x improvement in IFFT area
BUT a constant twiddle allows low-level optimization on a Bfly-4 block
  a 2.5x area reduction!