## Slide 1
6.375 Tutorial 1
BSV
Ming Liu

## Slide 2: Overview
Parts of a BSV module
Lab 2 topics
More types in BSV

## Slide 3: Modules
Interfaces
  Methods provide a way for the outside world to interact with the module
State elements and sub-modules
  Registers, FIFOs, BRAMs, FIR filters (Lab 1)
Rules
  Guarded atomic actions to describe how the state elements should change

## Slide 4: Part 1: Declare Interfaces
Contain methods for other modules to interact with the given module
  Interfaces can also contain sub-interfaces
Special interface: Empty
  No method, used in testbench
interface MyIfc;
method ActionValue#(Bit#(32)) f();
interface SubIfc s;
endinterface
module mkTb(Empty);
module mkTb(); // () are necessary

## Slide 5: Interface Methods
Value
  Returns value, doesn’t change state
  method Bit#(32) first;
Action
  Changes state, doesn’t return value
  method Action enq(Bit#(32) x);
ActionValue
  Changes state, returns value
  method ActionValue#(Bit#(32)) deqAndGet;

## Slide 6: Calling Interface Methods
Value: Call inside or outside of a rule since it only returns a value
  Bit#(32) a = aQ.first;
  Bit#(32) sum = aQ.first + aQ.first + bQ.first;
Action: Can call once within a rule
  aQ.enq(sum);
ActionValue: Can call once within a rule
  Use “<-” operator inside a rule to apply the action and return the value
  Bit#(32) prod <- multiplier.deqAndGet;

## Slide 7: Part 2: Defining a Module
module mkAdder( Adder#(32) );
  Adder#(32) is the interface
Module can be parametrized
  module name#(params)(args …, interface);
  module mkMul#(Bool signed)(Adder#(n) a, Mul#(n) x);

## Slide 8: Part 3: Instantiating sub-modules
Examples: Registers, FIFOs, RAMs, FIR filter (from Lab 1)
Instantiation:
  The “ <- “ outside a rule is used to instantiate a module
  MyIfc instOfModule <- mkModule();
  Reg#(Bit#(32)) counter <- mkReg(0);
  FIFO#(Uint#(32)) aQ <- mkFIFO();

## Slide 9: Part 4: Rules
Rules describe the actions to be applied atomically
  Modifies state
Rules have guards to determine when they can fire
  Implicit or explicit

## Slide 10: Rule Execution
One rule at a time:
  Choose an enabled rule
  Apply all of the actions of the rule
  Repeat
Conceptually rules execute one at a time in global order, but compiler aggressively schedules multiple rules to execute in the same clock cycle
  Scheduling will be covered in detail in upcoming lectures

## Slide 11: Hello World
What does this do?
  Print “hello, world” infinitely
module mkHelloWorld (Empty);
rule sayhello (True);
$display("hello, world");
endrule
endmodule

## Slide 12: Hello World with State
module mkHelloWorldOnce ();
Reg#(Bool) said <- mkReg(False);
rule sayhello (!said);
$display("hello, world");
said <= True;
endrule
rule goodbye (said);
$finish();
endrule
endmodule

## Slide 13: When can a rule fire?
Guard is true (explicit)
All actions/methods in rule are ready (implicit)
Will it fire?
  That depends on scheduling
rule doCompute if (started);
Bit#(32) a = aQ.first(); //aQ is a FIFO
Bit#(32) b = bQ.first(); //bQ is a FIFO
aQ.deq();
bQ.deq();
outQ.enq( {a, b} ); //outQ is a FIFO
endrule

## Slide 14: Part 5: Implement Interface
Methods, just like rules, have can have implicit and explicit guards
interface MyIfc#(numeric type n);
method ActionValue#(Bit#(n)) f();
interface SubIfc#(n) s;
endinterface
module mkDut(MyIfc#(n));
……
method ActionValue#(Bit#(n)) f();
……
endmethod
interface SubIfc s; // no param “n”
// methods of SubIfc
endinterface
endmodule

## Slide 15: Multiplier Example
Is this correct?
interface Multiplier;
method Action putOperands(Int#(32) a, Int#(32) b);
method ActionValue#(Int#(32)) getResult();
endinterface
module mkMultiplier (Multiplier);
FIFO#(Int#(32)) results <- mkFIFO();
method Action putOperands(Int#(32) a, Int#(32) b);
results.enq(a * b);
endmethod
method ActionValue#(Int#(32)) getResult();
results.deq();
return results.first();
endmethod
endmodule
module mkCalculator ( Calc );
Reg#(Int#(32)) a <- mkReg(0);
Reg#(Int#(32)) b <- mkReg(0);
Reg#(Int#(32)) res <- mkReg(0);
Multiplier mult <- mkMultiplier();
Reg#(Bool) sentReq <- mkReg(False);
rule doStartMult if (!sentReq);
mult.putOperands(a, b);
sentReq <= True;
endrule
rule doFinishMult if (sentReq);
Int#(32) prod <- mult.getResult();
res <= prod;
sentReq <= False;
endrule
… //interface definition
endmodule

## Slide 16: Multiplier Example
Is this correct?
module mkCalculator2 ( Calc );
Reg#(Int#(32)) a <- mkReg(0);
Reg#(Int#(32)) b <- mkReg(0);
Reg#(Int#(32)) res <- mkReg(0);
Multiplier mult <- mkMultiplier();
rule doStartMult;
mult.putOperands(a, b);
endrule
rule doFinishMult;
Int#(32) prod <- mult.getResult();
res <= prod;
endrule
… //interface definition
endmodule
module mkCalculator ( Calc );
Reg#(Int#(32)) a <- mkReg(0);
Reg#(Int#(32)) b <- mkReg(0);
Reg#(Int#(32)) res <- mkReg(0);
Multiplier mult <- mkMultiplier();
Reg#(Bool) sentReq <- mkReg(False);
rule doStartMult if (!sentReq);
mult.putOperands(a, b);
sentReq <= True;
endrule
rule doFinishMult if (sentReq);
Int#(32) prod <- mult.getResult();
res <= prod;
sentReq <= False;
endrule
… //interface definition
endmodule

## Slide 17: Useful Lab 2 Topics

## Slide 18: Vector
Type:
  Vector#(numeric type size, type data_type)
Values:
  newVector(), replicate(val)
Functions:
  Access an element: []
  Range of vectors: take, takeAt
  Rotate functions
  Advanced functions: zip, map, fold
Can contain registers or modules
Must have ‘import Vector::*;’ in BSV file

## Slide 19: Vectors: Example
FIFO#(Vector#(FFT_POINTS, ComplexSample)) inputFIFO <- mkFIFO();
  Instantiating a single FIFO, holding vectors of samples
Vector#(TAdd#(1,FFT_LOG_POINTS),Vector#(FFT_POINTS, ComplexSample)) stage_data = newVector();
  Declaring a vector of vectors
for (Integer i=0; i < 10; i=i+1) begin
stage_data[i][0] = func(i);
end
Assigning values to a vector

## Slide 20: Reg and Vector
Register of Vectors
  Reg#( Vector#(32, Bit#(32) ) ) rfile;
  rfile <- mkReg( replicate(0) );
Vector of Registers
  Vector#( 32, Reg#(Bit#(32)) ) rfile;
  rfile <- replicateM( mkReg(0) );
  Similarly:
  fifoVec <- replicateM( mkFIFO() );
Each has its own advantages and disadvantages

## Slide 21: Partial Writes
Reg#(Bit#(8)) r;
  r[0] <= 0 counts as a read & write to the entire reg r
    let r_new = r; r_new[0] = 0; r <= r_new
Reg#(Vector#(8, Bit#(1))) r
  Same problem, r[0] <= 0 counts as a read and write to the entire register
  r[0] <= 0; r[1] <= 1 counts as two writes to register
    double write problem
Vector#(8,Reg#(Bit#(1))) r
  r is 8 different registers
  r[0] <= 0 is only a write to register r[0]
  r[0] <= 0 ; r[1] <= 1 is not a double write problem

## Slide 22: Polymorphic Interfaces
Declaring a polymorphic interface
Using polymorphic interfaces
Instantiating a module with polymorphic ifc
interface DSP#(numeric type w, type dType);
method Action putSample(Bit#(w) a, dType b);
method Vector#(w, dType) getVal();
endinterface
module mkDSP ( DSP#(w, dType) );
Reg#(Bit#(w)) aReg <- mkReg(0);
Reg#(dType) bReg <- mkRegU();
…
endmodule
module mkTb();
DSP#(8, UInt#(32)) dspInst <- mkDSP();
endmodule

## Slide 23: Get/Put Interfaces
Pre-defined interface in BSV
Provides a simple handshaking mechanism for getting data from a module or putting data into it
import GetPut::*
interface Get#(type t);
method ActionValue#(t) get();
endinterface
interface Put#(type t);
method Action put(t x);
endinterface

## Slide 24: Using Get/Put Interfaces
import FIFO::*;
import GetPut::*;
interface FooIfc;
interface Put#(Bit#(32)) request;
interface Get#(Bit#(32)) response;
endinterface
module mkFoo (FooIfc);
FIFO#(Bit#(32)) reqQ <- mkFIFO;
FIFO#(Bit#(32)) respQ <- mkFIFO;
interface Put request;
method Action put (Bit#(32) req);
reqQ.enq (req);
endmethod
endinterface
interface Get response;
method ActionValue#(Bit#(32)) get ();
let resp = respQ.first;
respQ.deq;
return resp;
endmethod
endinterface
endmodule

## Slide 25: Get/Put with FIFOs
import FIFO::*;
import GetPut::*;
interface FooIfc;
interface Put#(Bit#(32)) request;
interface Get#(Bit#(32)) response;
endinterface
module mkFoo (FooIfc);
FIFO#(Bit#(32)) reqQ <- mkFIFO;
FIFO#(Bit#(32)) respQ <- mkFIFO;
interface request = toPut(reqQ);
interface response = toGet(respQ);
endmodule

## Slide 26: Server Interfaces
Extension of Get/Put
import ClientServer::*;
interface Server #(type req_t, type rsp_t);
interface Put#(req_t) request;
interface Get#(rsp_t) response;
endinterface

## Slide 27: Server Interfaces
import FIFO::*;
import GetPut::*;
import ClientServer::*;
typedef Server#(Bit#(32), Bit#(32)) FooIfc;
module mkFoo (FooIfc);
FIFO#(Bit#(32)) reqQ <- mkFIFO;
FIFO#(Bit#(32)) respQ <- mkFIFO;
interface Put request = toPut(reqQ);
interface Get response = toGet(respQ);
endmodule

## Slide 28: Provisos
Tell compiler that type t can do “+”
  Add provisos (compile error without provisos)
Provisos
  Tell compiler additional information about the parametrized types
  Compiler can type check based on the info
function t adder(t a, t b) provisos(Arith#(t));
return a + b;
endfunction

## Slide 29: Type Conversions
Numeric type: type parameters
  Often natural numbers
  Bit#(w); Vector#(n, Uint#(w))
Integers
  Not synthesizable in hardware (vs Int#())
  Often used in static elaboration (for loops)
Numeric type -> Integer: valueOf(w)
Integer -> Numeric type: not possible
Integer -> Bit#(), Int#() etc.: fromInteger(i)
Numeric type -> Bit#(), Int#() etc: fromInteger(valueOf(w))

## Slide 30: Best way to learn BSV
BSV Reference guide
Lab code
Try it

## Slide 31: More Types

## Slide 32: Bit#(numeric type n)
Literal values:
  Decimal: 0, 1, 2, … (each have type Bit#(n)
  Binary: 5’b01101, 2’b11
  Hex: 5’hD, 2’h3, 16’h1FF0
Common functions:
  Bitwise Logic: |, &, ^, ~, etc.
  Arithmetic: +, -, *, %, etc.
  Indexing: a[i], a[3:1]
  Concatenation: {a, b}
  truncate, truncateLSB
  zeroExtend, signExtend

## Slide 33: Bool
Literal values:
  True, False
Common functions:
  Boolean Logic: ||, &&, !, ==, !=, etc.
All comparison operators (==, !=, >, <, >=, <=) return Bools

## Slide 34: Int#(n), UInt#(n)
Literal values:
  Decimal:
    0, 1, 2, … (Int#(n) and UInt#(n))
    -1, -2, … (Int#(n))
Common functions:
  Arithmetic: +, -, *, %, etc.
    Int#(n) performs signed operations
    UInt#(n) performs unsigned operations
  Comparison: >, <, >=, <=, ==, !=, etc.

## Slide 35: Constructing new types
Renaming types:
  typedef
Enumeration types:
  enum
Compound types:
  struct
  vector
  maybe
  tagged union

## Slide 36: typedef
Syntax:
  typedef <type> <new_type_name>;
Basic:
  typedef 8 BitsPerWord;
  typedef Bit#(BitsPerWord) Word;
    Can’t be used with parameter: Word#(n)
Parameterized:
  typedef Bit#(TMul#(BitsPerWord,n)) Word#(numeric type n);
    Can’t be used without parameter: Word

## Slide 37: enum
    Creates the type Color with values Red and Blue
    Can create registers containing colors
  Reg#(Color)
    Values can be compared with == and !=
    typedef enum {Red, Blue} Color
    deriving (Bits, Eq);

## Slide 38: struct
  Elements from MemReq x can be accessed with x.addr, x.data, x.wren
  Struct Expression
    X = MemReq{addr: 0, data: 1, wren: True};
typedef struct {
Bit#(12) addr;
Bit#(8) data;
Bool wren;
} MemReq deriving (Bits, Eq);

## Slide 39: struct
Parametrized struct
typedef struct {
t a;
Bit#(n) b;
} Req#(type t, numeric type n) deriving (Bits, Eq);

## Slide 40: Tuple
Types:
  Tuple2#(type t1, type t2)
  Tuple3#(type t1, type t2, type t3)
  up to Tuple8
Construct tuple: tuple2( x, y ), tuple3( x, y, z ) …
Accessing an element:
  tpl_1( tuple2(x, y) ) // x
  tpl_2( tuple3(x, y, z) ) // y
  Pattern matching
Tuple2#(Bit#(2), Bool) tup = tuple2(2, True);
match {.a, .b} = tup;
// a = 2, b = True

## Slide 41: Maybe#(t)
Type:
  Maybe#(type t)
Values:
  tagged Invalid
  tagged Valid x (where x is a value of type t)
Functions:
  isValid(x)
    Returns true if x is valid
  fromMaybe(default, m)
    If m is valid, returns the valid value of m if m is valid, otherwise returns default
    Commonly used fromMaybe(?, m)

## Slide 42: Reg#(t)
Main state element in BSV
Type: Reg#(type data_type)
Instantiated differently from normal variables
  Uses <- notation
Written to differently from normal variables
  Uses <= notation
  Can only be done inside of rules and methods
Reg#(Bit#(32)) a_reg <- mkReg(0); // value set to 0
Reg#(Bit#(32)) b_reg <- mkRegU(); // uninitialized

## Slide 43: Implement Interface of Module
Return interface at the end of module
  Interface expression
module mkDut(MyIfc#(n));
……
MyIfc ret = (interface MyIfc;
method ActionValue#(Bit#(n)) f();
……
endmethod
interface SubIfc s; // no param “n”
// methods of SubIfc
endinterface
endinterface);
return ret;
endmodule

## Slide 44: Vector Sub-interface
Sub-interface can be vector
BSV reference guide Section 5
interface VecIfc#(numeric type m, numeric type n);
interface Vector#(m, SubIfc#(n)) s;
endinterface
Vector#(m, SubIfc) vec = ?;
for(Integer i=0; i<valueOf(m); i=i+1) begin
// implement vec[i]
end
VecIfc ifc = (interface VecIfc;
interface Vector s = vec; // interface s = vec;
Endinterface);