## Slide 1
6.375 Tutorial 3
Scheduling, Sce-Mi & FPGA Tools
Ming Liu

## Slide 2: Overview
Scheduling Example
Synthesis Boundaries
Sce-Mi
FPGA Architecture/Tools
Timing Analysis

## Slide 3: Scheduling Recap
1. Intra-rule: What makes a legal rule?
  No double write
  No combinational cycles
2. Inter-rule: When can rules fire in the same cycle?
  Parallel execution of rules appears as if rules executed in sequential one-rule-at-a-time order

## Slide 4: Packet Switching
Switch
UCLA
USC
MIT
Harvard
Demo
Notes: Show code on csgml. Which rules can fire together?
Compile and show schedule

## Slide 5: Synthesis Boundary
By default BSV compiles your design into a single flat Verilog module
  All methods/rules in-lined
Use synthesis pragma to generate separate modules (.v files)
(*synthesize*)
module mkMultiplier (Multiplier);

## Slide 6: Synthesis Boundary
Benefits:
  Faster compile times. Modules are reused
  Modularization at the circuit level
  Better for synthesis and reporting
Drawbacks:
  Polymorphic modules not supported
  More conservative guard lifting

## Slide 7: Synthesis Boundary Handling Polymorphism
Verilog does not support polymorphic interfaces
Wrap polymorphic modules with specific instantiations
FFT#(N, ComplexData) fft <- mkFFT()
(* synthesize *)
module mkSynthesizableFFT(FFT#(N, ComplexData));
FFT#(N, ComplexData) fft <- mkFFT();
return fft;
endmodule

## Slide 8: Synthesis Boundary Guard Logic (Example)
Synthesis boundaries simplifies guard logic
  Lifted guard without synthesis boundary:
    (x && aQ.notFull) || (!x && bQ.notFull)
  Lifted guard with synthesis boundary:
    aQ.notFull && bQ.notFull
method Action doAction( Bool x );
if( x ) begin
aQ.enq(a);
end else begin
bQ.enq(b);
end
endmethod

## Slide 9: Sce-Mi

## Slide 10: Sce-Mi Standard Co-Emulation Modeling Interface
Host Processor
A software/hardware communication framework
User SW
SceMi Library
PCIe Driver
FPGA
PCIe Endpoint
SceMi Xactors
SceMiLayer
DUT
(AP)
PCIe

## Slide 11: Sce-Mi Abstraction
Ports and proxies form a FIFO abstraction over a link
TCP (simulation)
or PCIe (HW)

## Slide 12: Sce-Mi Example: Calculator
Calculator
(DUT)
Link
ServerXactor
Testbench

## Slide 13: Sce-Mi: Hardware Calculator DUT
typedef Bit#(32) Value;
typedef enum { ADD, SUB, MUL} Operation deriving (Bits, Eq);
typedef union tagged {
void Clear;
struct {
Operation op;
Value val;
} Operate;
} Command deriving (Bits, Eq);
typedef Server#(Command, Value) Calculator;
module mkCalculator (Calculator);
…
endmodule
Server interface:
Put commands
Get results

## Slide 14: Sce-Mi: Hardware SceMiLayer
(* synthesize *)
module [Module] mkDutWrapper (Calculator);
Calculator calc <- mkCalculator();
return calc;
endmodule
module [SceMiModule] mkSceMiLayer();
SceMiClockConfiguration conf = defaultValue;
SceMiClockPortIfc clk_port <- mkSceMiClockPort(conf);
Calculator dut <- buildDut(mkDutWrapper, clk_port);
Empty calcxactor <- mkServerXactor(dut, clk_port);
Empty shutdown <- mkShutdownXactor();
endmodule
Wrap DUT in synthesis boundary
Instantiate the DUT
Create a Server transactor on the Calculator dut interface
Note: DutWrapper in Lab 4 is slightly more complex (discussed later)

## Slide 15: Sce-Mi: Software
#include "bsv_scemi.h“
#include "SceMiHeaders.h“
int main(int argc, char* argv[]){
//Initialize scemi …
InportProxyT<Command> inport ("", "scemi_calcxactor_req_inport", sceMi);
// Initialize the SceMi outport
OutportQueueT<Value> outport ("",
"scemi_calcxactor_resp_outport", sceMi);
Auto-generated classes based on your BSV types
SceMi auto-generates the Command class
Name of port is found in “scemi.params” file
Type of port

## Slide 16: Sce-Mi: Software Sending/Receiving
Command cmd;
cmd.the_tag = Command::tag_Operate; cmd.m_Operate.m_val = 100; cmd.m_Operate.m_op = Operation(Operation::e_ADD)
inport.sendMessage(cmd);
std::cout << outport.getMessage() << std::endl;;
Construct the cmd
Get results!
Send the cmd to hardware (blocking)

## Slide 17: Sce-Mi: Transactors
Many transactor available. See documentation

## Slide 18: Sce-Mi: Build Process
SceMi has its own build tool: build
  Lab 4: project.bld
Always simulate first:
  Wrap DUT in SceMiLayer in hardware
  Run build: “build –v”
    This creates scemi.params and C++ headers
  Write/update your software C++ code
  Re-run “build –v”

## Slide 19: Sce-Mi: Simulation
SceMi simulation is done over TCP sockets
“build –v” will generate two binaries
  bsim_dut: simulated hardware
  tb: the host software
Run both binaries. They will communicate with each other.

## Slide 20: Sce-Mi: Building Hardware
Run Build:
  vivado_setup build –v”
    Runs synthesis tool (for a long time) to create FPGA bitfile
    Compiles software tb
Log into a server with FPGA attached
  programfpga <path_to_bitfile>
Run software
  runtb ./tb 2.0
Demo
Notes: Show calculator SceMi simulation demo

## Slide 21: Clocks and Resets in BSV
All BSV modules have implicit clock and reset interfaces
  Compiled Verilog files will have these ports
Modules can also have additional clocks/resets as parameters
Can specify clocks/reset explicitly
module mkDut(DutIfc); //One default clk/rst
//Two clks, one default rst
module mkDut2Clk#(Clock clk_usr)(DutIfc);
DutIfc dut <- mkDut(clocked_by clk, reset_by rst);
DutIfc dut <- mkDut2Clk(clk_usr, clocked_by clk, reset_by rst);

## Slide 22: SceMi Clocks
SceMi transactors run at 50MHz
But our DUT runs faster in a different clock domain
Thus need clock domain crossing primitives at the DUT interface
  Synchronization FIFOs/Registers
  Bluespec provides these
//Scemi clock to user clock (dut) sync fifo
SyncFIFOIfc#(Sample) toApSyncQ <- mkSyncFIFOFromCC(2, clk_usr);
//User clock to Scemi clock sync fifo
SyncFIFOIfc#(Sample) fromApSyncQ <- mkSyncFIFOToCC(2, clk_usr, rst_usr);

## Slide 23: Running Design on FPGA

## Slide 24: FPGA Hardware Setup
PCIe
Xilinx VC707
(Virtex 7) Development Board

## Slide 25: FPGA Architecture Brief
CLB: configurable logic block
Routing switches
BRAMs (~1-8MB total)
DSP
IOB: I/O buffers
Hard IPs: PCIe, DRAM
Clocking network

## Slide 26: Tool Flow for FPGA
BSV
Bluespec Compiler
Synthesis
Verilog
Map
Place and Route
Bit File
Software TB Binary
C++/SceMi
g++
Constraints (.xdc)
Xilinx Vivado
SceMi build file invokes all tools

## Slide 27: Reading Timing Reports
Focus on Max Delay Path (setup)
Slack: Timing margin
Location: Physical location of the slice
Delay Type: which resource in the slice the path goes through
  FDRE: register, LUT: look up table, CARRY4: carry chain
  Net: routing delay
Incr (ns): Additional delay added
Path (ns): Total delay
Demo
Notes: Show failed 75MHz design on lightning; Open Vivado
~/6.375_test/mingliu/audio/scemi/fpga/xilinx_1_75mhz_fail/mkBridge/mkBridge.runs/impl_1

## Slide 28: Debugging Timing Errors
Search for “VIOLATED” in the timing report
Look at which module the error is from
  Source and destination
What logic is generally on the path
Remember that you are looking at one particular path – when there are timing failures on one path, there are typically many paths failing in the same way
  TNS Failing Endpoints tells you exactly how many
Resolve long combinational paths by pipelining/folding your design

## Slide 29: Examples of Long Paths
Multipliers/adders generally expensive
  Can be cheap for constants
  Proportional to width
rule doMult;
outR <= a * b;
endrule
Reg#(Bit#(32)) a <- mkReg(0); //value set dynamically
Reg#(Bit#(32)) b <- mkReg(0); //value set dynamically
method setInputs (Bit#(32) a, Bit#(32) b) …
Bit#(32) a = 2;
Reg#(Bit#(32)) b <- mkReg(0);
Reg#(Bit#(4)) a <- mkReg(0);
Reg#(Bit#(4)) b <- mkReg(0);

## Slide 30: Examples of Long Paths
Dynamic selection creates muxes
Many input muxes creates long comb paths
Vector#(N, Reg#(Bit#(32))
outVectR <- replicateM(mkReg(0))
rule doSel;
outR[sel] <= ..
endrule
Reg#(Bit#(TLog#(N))) sel <- mkReg(0); //dynamically set

## Slide 31: Examples of Long Paths
rule doPipe;
for (Integer sel=0; sel< n; sel=sel+1) begin
outFIFO[sel].enq( inpFIFO[sel].first );
inpFIFO[sel].deq;
end
endrule
for (Integer sel=0; sel< n; sel=sel+1) begin
rule doPipe;
outOneFIFO.enq( inpFIFO[sel].first );
inpFIFO[sel].deq;
endrule
end
Likely OK
Many conflicting rules -> large mux

## Slide 32: A Few Notes
Please don’t program the FPGA until design meets timing
  Send me an email if having issues with FPGA
Servers with FPGAs attached:
  bdbm[12-14].csail.mit.edu
  Do not use these for long compiles
Additional servers for compiling
  bdbm[10-11].csail.mit.edu
Sharing
  Use “w” and “top” to check who is using machine
  Only one person can use the FPGA at a time
  Change TCP port in project.bld in sim
Start early! Synthesis takes >30 minutes.

## Slide 33: Lab 4 Code