## Slide 1: 6.823 SPring15 Quiz 2 Review (L09-L14)
TA: Po-An Tsai, Hsin-Jung Yang

## Slide 2: Lecture 9-14 are all about ILP
Instruction-level parallelism (ILP)
  Execute as many instructions as possible at the same time to maximize throughput and hide long latency by memory/ALU
Why this is not easy?
  Dependencies between instructions

## Slide 3: Dependency
Data dependency
  RAW WAR WAW
Control dependency
  Branch jump
Structural dependency
  Only one ALU

## Slide 4: Ways to Solve Dependency
For false dependency
  Indirection
For true dependency
  Stall
  Bypass
  Speculate => best if you speculate mostly correctly

## Slide 5: Ways to Solve Dependency
Data dependency
  RAW WAR WAW
  => Scoreboard (L9) ROB, Register renaming (L10), Store queue(L13)
Control dependency
  Branch jump
  => Branch prediction (L11)
Structural dependency
  Only one ALU
  => Superscalar (L9)

## Slide 6: Speculation
We speculate a lot!
  Branch
  No exceptions
  Addresses for load/store are not the same
How to manage old and new values?
  Greedy/lazy (L12)

## Slide 7: Mis-speculation
Recovery according to your policy(L12)
  Snapshot
  Rollback

## Slide 8: Hide Long Latency
A cache miss takes 100 cycles
A divide takes 20 cycles
  Execute following instructions, but hold them until those long-latency instruction finish.
Use Little’s law to calculate how many instruction in flight

## Slide 9: Hide Long Latency
A cache miss takes 100 cycles
A divide takes 20 cycles
  Switch to another independent thread until they finish (L14)
Use Little’s law to calculate how many threads needed

## Slide 10: Example OoO Pipeline

## Slide 11: Branch Prediction

## Slide 12: Branch Prediction
Speculate what the next instruction is
  Static
  1 bit predictor
  2 bit predictor
  Global history (a history register and lots of predictor)
  Local history (many history registers and lots of predictor)
  Combined local and global history

## Slide 13: Branch Prediction
Data management

## Slide 14: Branch Target Buffer
Store the next PC of branch/jmp instructions seen last time
Get address earlier than predictor

## Slide 15: Combine BTB and Predictor(BHT)

## Slide 16: Out-of-Order Execution
Out-of-order Execute
In-order Fetch/Decode
In-order Commit
When can we execute an instruction out-of-order?
Need to consider data dependency
(register dependency, memory dependency)

## Slide 17: Data Dependency
Register Dependency
Output-dependence
      r3  (r1) op (r2) Write-after-Write
      r3  (r6) op (r7) (WAW) hazard
Anti-dependence
      r3  (r1) op (r2) Write-after-Read
      r1  (r4) op (r5) (WAR) hazard
Data-dependence
      r3  (r1) op (r2) Read-after-Write
      r5  (r3) op (r4) (RAW) hazard

## Slide 18: Data Dependency
Register Dependency
Output-dependence
      r3  (r1) op (r2) Write-after-Write
      r3  (r6) op (r7) (WAW) hazard
Anti-dependence
      r3  (r1) op (r2) Write-after-Read
      r1  (r4) op (r5) (WAR) hazard
Data-dependence
      r3  (r1) op (r2) Read-after-Write
      r5  (r3) op (r4) (RAW) hazard
Handled by register naming
Handled by register naming

## Slide 19: Data Dependency
Memory Dependency
When is the load dependent on the store?
When (r2 + 4) == (r4 + 8)
Do we know this issue when the instruction is decoded? No
st r1, 4(r2)
ld r3, 8(r4)

## Slide 20: Data Dependency
Memory Dependency
Solution:
(1) Stall: can execute load before store only if the addresses are known to be different
(2) Address speculation: guess r2+4 != r4+8 and execute load before store
st r1, 4(r2)
ld r3, 8(r4)
Speculative Load Buffer

## Slide 21: Data Dependency
Speculative Load Buffer
On load execute: mark entry valid, instruction number and tag On load commit: clear valid bit
On load abort: clear valid bit
On store execute: if tag matches and the instruction is younger than the store -> Abort!

## Slide 22: Speculative Data Management
When do we do speculation?
  Branch prediction
  Assume no exceptions/interrupts
  Assume no memory dependency
  …
How do we manage speculative data?
  Greedy (or Eager) Update
    Update the value in place
    Maintain a log of old values to use for recovery
  Lazy Update
    Buffer the new value and leave the old value in place
    Replace the old value only at ‘commit’ time

## Slide 23: Speculative Data Management
Type of speculative data
  Branch prediction
    history registers, prediction counters (see P.13)
  Register values
    Lazy update: store new values in the ROB and update registers during commit
    Hybrid: store both new and old values in the unified physical register file
  Store values to memory
    Laze update: store new values in the speculative store buffer and write to non-speculative store buffer/cache/memory during commit

## Slide 24: Speculative Data Management
Register Value Management
  Approach 1: store new values in the ROB and update registers during commit
Space Inefficient

## Slide 25: Speculative Data Management
Register Value Management
  Approach 2: keep all data values in a physical register file
  Reorder buffer contains only tags

## Slide 26: Out-of-Order Execution
Pre-Issue Check:
  The ROB is checked for available slots
  The free list is checked for free rename registers (if necessary)
  For store instructions, the non-speculative store buffer is checked for available slots

## Slide 27: Out-of-Order Execution
ROB Insert:
  The instruction is inserted into the ROB only if all the checks in the previous cycle (Pre-Issue check) pass
  The destination register is renamed

## Slide 28: Out-of-Order Execution
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld r1
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P0
P7
p

## Slide 29: Out-of-Order Execution
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 r1 P0
x add P0 r3 P1
x sub p P6 p P5 r6 P3
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 r3 P2
x ld P0 r6 P4
P3
P4
Ready to execute

## Slide 30: Out-of-Order Execution
Reg File Read:
  Operand values are read from the unified physical register file
Execute:
  Integer and floating point operations are sent to the appropriate functional units
  Stores enter the speculative store buffer
  Loads read from the store buffer or cache/memory

## Slide 31: Out-of-Order Execution
Reg File Write:
  The output from the functional units/memory is written into the unified register file and the ROB is notified.

## Slide 32: Out-of-Order Execution
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 r1 P0
x add P0 r3 P1
x sub p P6 p P5 r6 P3
x ld p P7 r1 P0
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 r3 P2
x ld P0 r6 P4
P3
P4
Execute
p
p
p
<R1>
x

## Slide 33: Out-of-Order Execution
Commit:
  Instructions are committed in-order
  Free the previously mapped physical register
  Data is written to cache/memory/non-speculative store buffer when a store is committed
  The ROB entry is freed after commit

## Slide 34: Out-of-Order Execution
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 r1 P0
x add P0 r3 P1
x sub p P6 p P5 r6 P3
x ld p P7 r1 P0
ld r1, 0(r3)
add r3, r1, #4
sub r6, r7, r6
add r3, r3, r6
ld r6, 0(r1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 r3 P2
x ld P0 r6 P4
P3
P4
Commit
p
p
p
<R1>
P8
x

## Slide 35: Multithreading

## Slide 36: Scheduling Policy

## Slide 37: Simultaneous Multithreading (SMT)
Share OOO structures between threads

## Slide 38: The end
Good luck!! 