## Slide 1
Computer Architecture: A Constructive Approach
Bypassing
Joel Emer
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Six Stage Pipeline
F
Fetch
fr
D
Decode
dr
R
Reg Read
rr
X
Execute
xr
M
Memory
mr
W
Write- back
pc
Writeback feeds back directly to ReadReg rather than through FIFO

## Slide 3: Register Read Stage
dr
R
Reg Read
rr
Read regs
RF
W
Scoreboard update signaled immediately
D
Decode
Decode
writeback register
update scoreboard
Notes: Will show new read_reg – but first a style update…

## Slide 4: Per stage architectural state
typedef struct {
MemResp instResp;
} FBundle;
typedef struct {
Rindx r_dest;
Rindx op1;
Rindx op2;
...
} DecBundle;
typedef struct {
Data src1;
Data src2;
} RegBundle;
typedef struct {
Bool cond;
Addr addr;
Data data;
} Ebundle;
No MemBundle –
data added to Ebundle
No WbBundle –
nothing added in WB
Notes: 4
Updated style for handling architectural and micro-architectural state.

## Slide 5: Per stage micro-architectural state
typedef struct {
FBundle fInst;
DecBundle decInst;
RegBundle regInst;
Inum inum;
Epoch epoch;
} RegData deriving(Bits,Eq);
function RegData newRegData(DecData decData);
RegData regData = ?;
regData.fInst = decData.fInst;
regData.decInst = decData.decInst;
regData.inum = decData.inum;
regData.epoch = decData.epoch;
return regData;
endfunction
Architectural state from prior stages
Passthrough and (optional) new micro-architectural state
New architectural state for this stage
Copy architectural state from prior stages
Copy uarch state from prior stages
In “uarch_types”
Utility function
Notes: 5
Struct per stage with state to use in current stage and pass to next stage.

## Slide 6: Example of stage state use
rule doRegRead;
let regData = newRegData(dr.first());
let decInst = regData.decInst;
case (reg_read.readRegs(decInst)) matches
tagged Valid .rfdata:
begin
if( writes_register(decInst))
reg_read.markUnavail(decInst.r_dest);
regData.regInst.src1 = rfdata.src1;
regData.regInst.src2 = rfdata.src2;
rr.enq(regData);
dr.deq();
end
endcase
endrule
Initialize stage state
Set utility variables*
Set architectural state
Set uarch state if any
Enqueue outgoing state
Dequeue incoming state
*Don’t try to update!!!
Notes: 6

## Slide 7: Resource-based diagram key
R1 busy
Set R1 not busy
Fetch
(Fuschia)
ζ
Decode
(Denim)
ε
Execute
(Emerald)
γ
Memory
(Mustard)
β
Writeback
(Wheat)
α
Reg Read
(Red)
δ
η
ζ
ε
δ
γ
α
epoch change (color change)
δ = killed
writeback feedback
pc redirect
α = stalled
0 1

## Slide 8: Scoreboard clear bug!
β
α
α
γ
β
α
α = 00: add r1,r0,r0
β = 04: j 40
γ = 08: add ...
δ = 12: add ...
ε = 16: add ...
ζ = 40: add r1,r0, r0
η = 44: add r2, r1,r0
ζ
ε
δ
γ
β
α
ε
δ
γ
β
α
δ
γ
β
α
η
ζ
η
ζ
η
ζ
η
ζ
ε
β
Looks okay, but what if α is delayed?
F
D
R
X
M
W
0 1 2 3 4 5 6 7 8 9
η waits for write of R1 by ζ
Notes: Old code with flash clear of scoreboard on epoch change is broken….if α is delayed

## Slide 9: Scoreboard clear bug!
γ
β
α
β
α
α
ζ
ε
δ
γ
α
δ
γ
β
α
η
ζ
ε
α
η
ζ
α
η
ζ
β
ε
δ
γ
β
α
η
ζ
β
α
F
D
R
X
M
W
α = 00: ld r1,100(r0)
β = 04: j 40
γ = 08: add ...
δ = 12: add ...
ε = 16: add ...
ζ = 40: add r1,r0, r0
η = 44: add r2, r1,r0
Mistreatment of what did of data dependence?
WAW
0 1 2 3 4 5 6 7 8 9
η is released by earlier write of R1
Notes: Old code with flash clear of scoreboard on epoch change is broken….if α is delayed

## Slide 10: So don’t clear scoreboard!
γ
β
α
β
α
α
ζ
ε
δ
γ
α
δ
γ
β
α
η
ζ
ε
δ
α
η
ζ
ε
α
η
ζ
β
ε
δ
γ
β
α
ζ
β
α
Looks okay, but what if R1 written in branch shadow?
F
D
R
X
M
W
α = 00: ld r1,100(r0)
β = 04: j 40
γ = 08: add ...
δ = 12: add ...
ε = 16: add ...
ζ = 40: add r1,r0, r0
η = 44: add r2, r1,r0
0 1 2 3 4 5 6 7 8 9
ζ sees register is free by feedback, then sets it busy
Notes: Old code with flash clear of scoreboard on epoch change is broken….if α is delayed
Zeta executes because it sees the register is free (via arrow) and then sets it busy again…

## Slide 11: Dead instruction deadlock!
γ
β
α
β
α
α
ζ
ε
δ
γ
β
α
δ
γ
β
α
η
ζ
ε
δ
β
η
ζ
ε
ζ
ζ
ε
δ
γ
β
α
So, what can we do?
F
D
R
X
M
W
α = 00: add r3,r0,r0
β = 04: j 40
γ = 08: add ... δ = 12: add r1,...
ε = 16: add,...
ζ = 40: add r1,r0, r0
η = 44: add r2, r1,r0
0 1 2 3 4 5 6 7 8 9
ζ never sees register R1

## Slide 12: Poison bit uarch state
In exec:
  instead of dropping killed instructions mark them ‘poisoned’
In subsequent stages:
  DO NOT make architectural changes
  DO necessary bookkeeping

## Slide 13: Poison-bit solution
γ
β
α
β
α
α
ζ
ε
δ
γ
β
α
δ
γ
β
α
η
ζ
ε
δ
γ
β
η
ζ
ε
δ
γ
η
ζ
ε
ε
δ
γ
β
α
η
ζ
ε
δ
What stage generates poison bit?
F
D
R
X
M
W
α = 00: add r3,r0,r0
β = 04: j 40
γ = 08: add ...
δ = 12: add r1,...
ε = 16: add,...
ζ = 40: add r1,r0, r0
η = 44: add r2, r1,r0
0 1 2 3 4 5 6 7 8 9
Poisoned δ frees register, but value same, ζ marks it busy.
Notes: Poisoned δ frees register, which is immediately made busy by ζ. Then η will wait for ζ.

## Slide 14: Poison-bit generation
rule doExecute;
let execData = newExecData(rr.first);
let ...;
if (! epochChange)
begin
execData.execInst = exec.exec(decInst,src1,src2);
if (execInst.cond) ...
end
else
begin
execData.poisoned = True;
end
xr.enq(execData);
rr.deq();
endrule
Initialize stage state
Set utility variables
Set architectural state
Set uarch state
Enqueue outgoing state
Dequeue incoming state
What stages need to handle poison bit?
Notes: 14

## Slide 15: Poison-bit usage
rule doMemory;
let memData = newMemData(xr.first);
let ...;
if(! poisoned && memop(decInst))
memData.execInst.data <- mem.port(...);
mr.enq(memData);
xr.deq();
endrule
rule doWriteBack;
let wbData = newWBData(mr.first);
let ...;
reg_read.markAvailable(rdst);
if (!poisoned && regwrite(decInst)
rf.wr(rdst, data);
mr.deq;
endrule
Architectural activity if not poisoned
Unconditionally do bookkeeping
Architectural activity if not poisoned
Notes: 15

## Slide 16: Data dependence stalls
η
ζ
η
ζ
ζ
η
ζ
η
ζ
η
η
η
η
ζ
This is a data dependence. What kind?
RAW
F
D
R
X
M
W
0 1 2 3 4 5 6 7 8 9
ζ = 40: add r1,r0, r0
η = 44: add r2, r1,r0

## Slide 17: Bypass
RegRead
Execute
rr
If scoreboard says register is not available then RegRead needs to stall, unless it sees what it needs on the bypass line….
What does RegRead need to do?

## Slide 18: Register Read Stage
dr
R
rr
Read regs
RF
W
D
Decode
Writeback register
Update scoreboard
Bypass Net
X
Generate bypass

## Slide 19: Bypass Network
typedef struct { Rindx regnum; Data value;} BypassValue;
module mkBypass(BypassNetwork)
Rwire#(BypassValue) bypass;
method produceBypass(Rindx regnum, Data value);
bypass.wset(BypassValue{regname: regnum, value:value});
endmethod
method Maybe#(Data) consumeBypass1(Rindx regnum);
if (bypass matches tagged Valid .b && b.regnum == regnum)
return tagged Valid b.value;
else
return tagged Invalid;
endmethod
endmodule
Does bypass solve WAW hazard
No!

## Slide 20: Register Read (with bypass)
module mkRegRead#(RFile rf, BypassNetwork bypass)(RegRead);
method Maybe#(Sources) readRegs(DecBundle decInst);
let op1 = decInst.op1; let op2 = decInst.op2;
let rfdata1 = rf.rd1(op1); let rfdata2 = rf.rd2(op2);
let bypass1 = bypass.consumeBypass1(op1);
let bypass2 = bypass.consumeBypass2(op2);
let stall = isWAWhazard(scoreboard) ||
(isBusy(op1,scoreboard) && !isJust(bypass1)) ||
(isBusy(op2,scoreboard) && !isJust(bypass2)));
let s1 = fromMaybe(rfdata1, bypass1);
let s2 = fromMaybe(rfdata2, bypass2);
if (stall) return tagged Invalid;
else return tagged Valid Sources{src1:s1, src2:s2};
endmethod
Notes: 20

## Slide 21: Bypass generation in execute
rule doExecute;
let execData = newExecData(rr.first);
let ...;
if (! epochChange) begin
execData.execInst = exec.exec(decInst,src1,src2);
if (execInst.cond) ...
if ( )
bypass.generateBypass(decInst.r_dst, execInst.data);
end else begin
execData.poisoned = True;
end
xr.enq(execData);
rr.deq();
endrule
If have data destined for a register bypass it back to register read
decInst.i_type == ALU
Does bypass solve all RAW delays?
No – not for ld/st!
Notes: 21

## Slide 22: Full bypassing
F
fr
D
dr
R
rr
X
xr
M
mr
W
pc
Every stage that generates register writes can generate bypass data

## Slide 23: Multi-cycle execute
rr
xr
M
Incorporating a multi-cycle operation into a stage
R
m1
M2
m2
M3
M1
X
D
C
η
B
ζ
A

## Slide 24: Multi-cycle function unit
module mkMultistage(Multistage);
State1 m1 <- mkReg(); State2 m2 <- mkReg();
method Action request(Operand operand);
m1.enq(doM1(operand));
endmethod
rule s1;
m2.enq(doM2(m1.first)); m1.deq();
endrule
method ActionValue Result response();
return doM3(m2.first); m2.deq();
endmethod
endmodule
Perform first stage of pipeline
Perform middle stage(s) of pipeline
Perform last stage of pipeline and return result
Notes: 24

## Slide 25: Single/Multi-cycle pipe stage
rule doExec;
... initialization
let done = False;
if (! waiting) begin
if(isMulticycle(...)) begin
multicycle.request(...); waiting <= True;
end else begin
result = singlecycle.exec(...); done = True;
end
end else begin
result <- multicycle.response();
done = True; waiting <= False;
end
if (done)
...finish up
endrule
If not busy start multicycle operation, or…
…perform single cycle operation
If busy, wait for response
Finish up if have a result
Notes: 25