## Slide 1
Realistic Memories and Caches
Li-Shiuan Peh
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Three-Stage SMIPS
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
fr
Epoch
wbr
stall?
The use of magic memories makes this design unrealistic
Notes: 2

## Slide 3: A Simple Memory Model
Reads and writes are always completed in one cycle
  a Read can be done any time (i.e. combinational)
  If enabled, a Write is performed at the rising clock edge
  (the write address and data must be stable at the clock edge)
MAGIC
RAM
ReadData
WriteData
Address
WriteEnable
Clock
In a real DRAM the data will be available several cycles after the address is supplied

## Slide 4: Memory Hierarchy
size: RegFile << SRAM << DRAM why?
latency: RegFile << SRAM << DRAM why?
bandwidth: on-chip >> off-chip why?
On a data access:
  hit (data Î fast memory)  low latency access
  miss (data Ï fast memory)  long latency access (DRAM)
Small,
Fast Memory
SRAM
CPU
RegFile
Big, Slow Memory
DRAM
A
B
holds frequently used data
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)

## Slide 5: Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
copy of main memory
location 100
copy of main memory
location 101
Address
Tag
Line or data block
Data
Byte
Data
Byte
Data
Byte
100
304
6848
416
How many bits are needed in tag?
Enough to uniquely identify block
Notes: Tag only needs enough bits to uniquely identify the block (jse)

## Slide 6: Cache Algorithm (Read)
Look at Processor Address, search cache tags to find match. Then either
Found in cache
a.k.a. HIT
Return copy of data from cache
Not in cache
a.k.a. MISS
Read block of data from Main Memory – may require writing back a cache line
Wait …
Return data to processor and update cache
Which line do we replace?
Replacement policy
Notes: LRU, random, hash

## Slide 7: Write behavior
On a write hit
  Write-through: write to both cache and the next level memory
  Writeback: write only to cache and update the next level memory when line is evacuated
On a write miss
  Allocate – because of multi-word lines we first fetch the line, and then update a word in it
  Not allocate – word modified in memory
We will design a writeback, write-allocate cache
Notes: Write through vs. write back
WT:
+read miss never results in writes to main memory + main memory always has the most current copy of the data (consistent) - write is slower - every write needs a main memory access - as a result uses more memory bandwidth
WB:
+ writes occur at the speed of the cache memory + multiple writes within a block require only one write to main memory + as a result uses less memory bandwidth - main memory is not always consistent with cache - reads that result in replacement may cause writes of dirty blocks to main memory
Write Back with No Write Allocate: on hits it writes to cache setting dirty bit for the block, main memory is not updated; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the same block, if the block originally caused a miss, will generate misses all the way and result in very inefficient execution.
Hence, WB+WA more common combination.
Write Through with No Write Allocate: on hits it writes to cache and main memory; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the block will update main memory anyway, so write misses aren’t helped. Only read misses helped with allocate.
Hence, WT, no WA usually.
Re-look at these options when the next level is a cache; not a memory.
Write back with no allocate? Why is this

## Slide 8: Blocking vs. Non-Blocking cache
Blocking cache:
  1 outstanding miss
  Cache must wait for memory to respond
  Blocks in the meantime
Non-blocking cache:
  N outstanding misses
  Cache can continue to process requests while waiting for memory to respond to N misses
We will design a non-blocking, writeback, write-allocate cache

## Slide 9: What do caches look like
External interface
  processor side
  memory (DRAM) side
Internal organization
  Direct mapped
  n-way set-associative
  Multi-level
next lecture: Incorporating caches in processor pipelines

## Slide 10: Data Cache – Interface (0,n)
interface DataCache;
method ActionValue#(Bool) req(MemReq r);
method ActionValue#(Maybe#(Data)) resp;
endinterface
cache
req
accepted
resp
Processor
DRAM
hit
wire
missFifo
writeback wire
ReqRespMem
Resp method should be invoked every cycle to not drop values
Denotes if the request is accepted this cycle or not
Notes: Hit: hit wire will be toggled, and resp will contain the requested cache line;
Accepted: If the cache can absorb this request, which depends on whether the memory (DRAM) can absorb it.
Non-blocking cache: 2 outstanding misses: 2 slots in missFifo.
Writeback wire: If we are supposed to read

## Slide 11: ReqRespMem is an interface passed to DataCache
interface ReqRespMem; method Bool reqNotFull;
method Action reqEnq(MemReq req);
method Bool respNotEmpty;
method Action respDeq;
method MemResp respFirst;
endinterface
Notes: DRAM telling cache if it can accept requests (reqNotFull), or if it has DRAM blocks coming back waiting to be read by cache (respNotEmpty).

## Slide 12: Interface dynamics
Cache hits are combinational
Cache misses are passed onto next level of memory, and can take arbitrary number of cycles to get processed
Cache requests (misses) will not be accepted if it triggers memory requests that cannot be accepted by memory
One request per cycle to memory

## Slide 13: Direct mapped caches

## Slide 14: Direct-Mapped Cache
Tag
Data Block
V, D
=
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
Block number
Block offset
What is a bad reference pattern?
Strided = size of cache
req address
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
Dirty bit for writeback caches

## Slide 15: Direct Map Address Selection higher-order vs. lower-order address bits
Tag
Data Block
V
=
Offset
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
Tag
Why might this be undesirable?
Spatially local blocks conflict
Notes: Index and tag reversed
Why might this be undesirable? Spatially local blocks conflict.

## Slide 16: Data Cache – code structure
module mkDataCache#(ReqRespMem mem)(DataCache); // state declarations
RegFile#(Index, Data) dataArray <- mkRegFileFull;
RegFile#(Index, Tag) tagArray <- mkRegFileFull;
Vector#(Rows, Reg#(Bool)) tagValid <-
replicateM(mkReg(False));
Vector#(Rows, Reg#(Bool)) dirty <-
replicateM(mkReg(False));
FIFOF#(MemReq) missFifo <- mkSizedFIFOF(reqFifoSz);
RWire#(MemReq) hitWire <- mkUnsafeRWire;
Rwire#(Index) replaceIndexWire <- mkUnsafeRWire; method Action#(Bool) req(MemReq r) … endmethod;
method ActionValue#(Data) resp … endmethod; endmodule

## Slide 17: Data Cache typedefs
typedef 32 AddrSz;
typedef 256 Rows;
typedef Bit#(AddrSz) Addr;
typedef Bit#(TLog#(Rows)) Index;
typedef Bit#(TSub#(AddrSz, TAdd#(TLog#(Rows), 2))) Tag;
typedef 32 DataSz;
typedef Bit#(DataSz) Data;
Integer reqFifoSz = 6;
function Tag getTag(Addr addr);
function Index getIndex(Addr addr);
function Addr getAddr(Tag tag, Index idx);
Notes: Forming the tag: Address – Index (=Log Rows) – 2 (Byte offset)

## Slide 18: Data Cache req
method ActionValue#(Bool) req(MemReq r);
Index index = getIndex(r.addr);
if(tagArray.sub(index) == getTag(r.addr) &&
tagValid[index])
begin
hitWire.wset(r); return True;
end
else if(miss && evict) begin
… return False;
end
else if(miss && !evict) begin
... return True;
end
Combinational hit case
The request is
accepted
not accepted
accepted
Notes: Explain why miss && evict ->> have to return False: Because memory can only handle one request at a time, so while storing evicted line, it cannot load a new line.

## Slide 19: Data Cache req – miss case
...
else if(tagValid[index] && dirty[index])
begin
if(mem.reqNotFull)
begin
writebackWire.wset(index);
mem.reqEnq(MemReq{op: St,
addr:getAddr(tagArray.sub(index),index),
data: dataArray.sub(index)});
end
return False;
end
…
Need to evict?
victim is evicted
Notes: Writebackwire is internal signal

## Slide 20: Data Cache req
else if(mem.reqNotFull && missFifo.notFull)
begin
missFifo.enq(r); r.op = Ld; mem.reqEnq(r);
return True;
end
else
return False;
endmethod
miss&!evict&canhandle
miss&!evict&!canhandle
Notes: missFifo: is number of outstanding misses

## Slide 21: Data Cache resp – hit case
method ActionValue#(Maybe#(Data)) resp;
if(hitWire.wget matches tagged Valid .r)
begin
let index = getIndex(r.addr);
if(r.op == St)
begin
dirty[index] <= True;
dataArray.upd(index, r.data);
end
return tagged Valid (dataArray.sub(index));
end
…
Notes: Hitwire: Bluespec for hitwire being toggled
If it’s a store, we set the dirty bit because the cache line will be dirty
.sub: Reads out the indexed cache line and return as response.

## Slide 22: Data Cache resp
else if(writebackWire.wget matches tagged Valid .idx)
begin
tagValid[idx] <= False;
dirty[idx] <= False;
return tagged Invalid;
end
…
Writeback case: resp handles this to ensure that state (dirty, tagValid) is updated only in one place

## Slide 23: Data Cache resp – miss case
else if(mem.respNotEmpty)
begin
let index = getIndex(reqFifo.first.addr);
dataArray.upd(index, reqFifo.first.op == St?
reqFifo.first.data : mem.respFirst);
if(reqFifo.first.op == St)
dirty[index] <= True;
tagArray.upd(index, getTag(reqFifo.first.addr));
tagValid[index] <= True;
mem.respDeq; missFifo.deq;
return tagged Valid (mem.respFirst);
end
Notes: Miss line loaded from memory, returned from memory
Dequeues miss and returns response

## Slide 24: Data Cache resp
else
begin
return tagged Invalid;
end
endmethod
All other cases
(missResp not arrived,
no request given, etc)
Notes: Invalid is not to be confused with the Valid/Invalid bit of the cache line; This is saying whether the response line is enabled or not/toggled or not

## Slide 26: Multi-Level Caches
Inclusive vs. Exclusive
Memory
disk
L1 Icache
L1 Dcache
regs
L2
Cache
Processor
Options: separate data and instruction caches, or a unified cache

## Slide 27: Write-Back vs. Write-Through Caches in Multi-Level Caches
Write back
Writes only go into top level of hierarchy
Maintain a record of “dirty” lines
Faster write speed (only has to go to top level to be considered complete)
Write through
All writes go into L1 cache and then also write through into subsequent levels of hierarchy
Better for “cache coherence” issues
No dirty/clean bit records required
Faster evictions

## Slide 28: Write Buffer
Source: Skadron/Clark
Notes: What’s the benefit? Stuff things into a write buffer, then, happily resume pipeline.

## Slide 29: Summary
Choice of cache interfaces
  Combinational vs non-combinational responses
  Blocking vs non-blocking
  FIFO vs non-FIFO responses
Many possible internal organizations
  Direct Mapped and n-way set associative are the most basic ones
  Writeback vs Write-through
  Write allocate or not
  …
next integrating into the pipeline