## Slide 1
Computer Architecture: A Constructive Approach
Next Address Prediction –
Six Stage Pipeline
Joel Emer
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Six Stage Pipeline
F
Fetch
fr
D
Decode
dr
R
Reg Read
rr
X
Execute
xr
M
Memory
mr
W
Write- back
npc
Need to add a next address prediction

## Slide 3: Next Address Prediction
F
Fetch
fr
D
Decode
dr
R
Reg Read
rr
X
Execute
xr
M
Memory
mr
W
Write- back
fb
Next Address Prediction
Feedback is now redirect and prediction feedback
not just branch target PC

## Slide 4: Branch Target Buffer
F stage: If (hit) then nPC=target else nPC=PC+4
X stage: Check prediction, if wrong then kill younger instructions
and train BTB (sometimes even if prediction correct)
IMEM
PC
Branch
Target
Buffer
(2k entries)
k
predicted
target
target
tag
=
hit

## Slide 5: BTB Interface
typedef Addr NaInfo;
typedef Tuple2#(Addr, NaInfo) Prediction;
interface NextAddrPred;
method ActionValue#(Prediction) predict(Addr addr);
method Action train(NaInfo naInfo, Bool correct,
Addr realTarget);
endinterface
In lab code, NaInfo has more elements and “train” takes more arguments to allow for more sophisticated predictors
Predictor-specific information to save and use later to train predictor

## Slide 6: BTB State
typedef 64 BTBRows;
typedef Bit#(TLog#(BTBRows)) LineIndex;
module mkNextAddrPred(NextAddrPred);
// BTB State
RegFile#(LineIndex, Addr) tagArray <- mkRegFileFull();
RegFile#(LineIndex, Addr) targetArray <- mkRegFileFull();

## Slide 7: BTB Prediction
method ActionValue#(Prediction) predict(Addr currentAddr);
LineIndex index = truncate(CurrentAddr >> 2);
let tag = tagArray.sub(index);
let target = targetArray.sub(index);
Addr predNextAddr = ?;
if (tag == currentAddr)
predNextAddr = target;
else
predNextAddr = currentAddr+4;
return tuple2(predNextAddr, currentAddr);
endmethod

## Slide 8: BTB Training
method Action train(NaInfo naInfo, Bool correct,
Addr target);
let tag = naInfo;
LineIndex index = truncate(naInfo >> 2);
if (! correct)
begin
tagArray.upd(index, tag);
targetArray.upd(index, target);
end
endmethod
endmodule
Note: if BTB had been 2-way set associative naInfo would include ‘way’ and train() would not need to do a lookup to do its job.

## Slide 9: Epoch management
F
D
R
X
M
W
0 1 2 3 4 5 6 7 8 9
α.1
1
β.1
α.1
1
γ.1
β.1
α.1
1
δ.1
γ.1
β.1
α.1
1
1
δ.1
γ.1
β.1
α.1
2
1
ε.2
δ.1
γ.1
β.1
α.1
2
2
ζ.2
ε.2
δ.1
γ.1
β.1
2
2
η.2
ζ.2
ε.2
δ.1
γ.1
2
2
η.2
ζ.2
ε.2
δ.1
2
2
η.2
ζ.2
ε.2
2
2
α = 00: j 40 β = 80: add …
γ = 84: add ...
δ = 88: add ...
ε = 40: add ...
ζ = 44: add ...
η = 48: add ...
Next address mispredict on ‘jmp’. Corrected in execute
Notes: Local epoch registers justified on basis of locality of state.

## Slide 10: Pipeline feedback
// Epoch state
Reg#(Epoch) feEpoch <- mkReg(0); // epoch at Fetch
Reg#(Epoch) eeEpoch <- mkReg(0); // epoch at Execute
// Feedback information and mechanism
typedef struct {
Bool correct;
NaInfo naPredInfo;
Addr nextAddr;
} Feedback deriving (Bits, Eq);
FIFOF#(Tuple2#(Epoch, Feedback)) execFeedback <- mkFIFOF;

## Slide 11: Integration into Fetch
rule doFetch();
function Action enqInst();
action
let d <- mem.side(MemReq{op: Ld, addr: fetchPC, data:?};
match {.nAddrPred,.naPredInfo}<-naPred.predict(fetchPc);
FBundle fInst = FBundle{instResp: d};
FData fData = FData{pc: fetchPc, fInst: fInst,
inum: iNum, execEpoch: feEpoch,
naPredInfo: naPredInfo,
nextAddrPred: nAddrPred};
iNum <= iNum + 1;
fetchPc <= nAddrPred;
fr.enq(fData);
endaction
endfunction
FetchPC generation to FetchPC use is a tight dependency loop

## Slide 12: Fetch (continued)
if (execFeedback.notEmpty) begin
execFeedback.deq;
match {.execEpoch, .fb} = execFeedback.first;
naPred.train(fb.naPredInfo, fb.correct, fb.nextAddr);
if(!fb.correct) begin
feEpoch <= execEpoch;
fetchPc <= fb.nextAddr;
end
else begin
enqInst();
end
end
else
enqInst();
endrule
Since we train() and predict() [in enqInst()] in the same cycle naPredInfo helps avoid conflicts inside predictor.
Train() and redirect on mispredict. Bubble!
Train() and fetch next inst on correct prediction.

## Slide 13: Execute
rule doExecute;
ExecData execData = newExecData(rr.first());
let decInst = execData.decInst;
execData.poisoned = (eeEpoch != execData.execEpoch);
if (! execData.poisoned) begin
let src1 = execData.regInst.src1;
let src2 = execData.regInst.src2;
execData.execInst = exec.exec(decInst, src1, src2);
let cond = execData.execInst.cond;
let target = execData.execInst.addr;
let nPc = cond ? target: execData.pc+4;
let naPredInfo = execData.naPredInfo;
let correctPred = (nPC == execData.nextAddrPred);
Instruction execution
Check predicted
next address

## Slide 14: Execute (continued)
let newEeEpoch = eeEpoch;
if (! correctPred) newEeEpoch = eeEpoch + 1;
execFeedback.enq(
tuple2(newEeEpoch,
Feedback{correct: correctPred,
naPredInfo: naPredInfo,
nextAddr: nPC}));
eeEpoch <= newEeEpoch;
end // not poisoned
xr.enq(execData);
rr.deq();
endrule
If !correctPred, which instructions are bad and must be dropped?
Always send feedback to allow training for correctly predicted next addresses
Change epoch if next address mispredict
Always pass instruction to next stage

## Slide 15: Next Address Prediction
F
Fetch
fr
D
Decode
dr
R
Reg Read
rr
X
Execute
xr
M
Memory
mr
W
Write- back
fb
Next Address Prediction
Where else can we figure out that the prediction is wrong?

## Slide 16: Feedback from decode
F
Fetch
fr
D
Decode
dr
R
Reg Read
rr
X
Execute
xr
M
Memory
mr
W
Write- back
xf
Next Address Prediction
df

## Slide 17: Decode detected mispredicts
Non-branch
  When nextPC != PC+4
  => use PC+4
Unconditional target known at decode
  When nextPC != known target
  => use known target
Conditional branch
  When nextPC != PC+4 or decoded target
  => use PC+4

## Slide 18: Add a ‘decode’ epoch
Reg#(Epoch) fdEpoch <- mkReg(0); // decode epoch @ fetch
Reg#(Epoch) feEpoch <- mkReg(0); // exec epoch @ fetch
Reg#(Epoch) ddEpoch <- mkReg(0); // decode epoch @ decode
Reg#(Epoch) deEpoch <- mkReg(0); // exec epoch @ decode
Reg#(Epoch) eeEpoch <- mkReg(0); // exec epoch @ exec
typedef struct {
Bool correct;
NaInfo naPredInfo;
Addr nextAddr;
} Feedback deriving (Bits, Eq);
FIFOF#(Tuple3#(Epoch,Epoch,Feedback)) decFeedback<-mkFIFOF;
FIFOF#(Tuple2#(Epoch,Feedback)) execFeedback <- mkFIFOF;
Send back both decode and exec epochs as feedback from decode.

## Slide 19: NA mispredict - jmp
γ.1.2
β.1.1
α.1.1
β.1.1
α.1.1
α.1.1
ζ.1.2
ε.1.2
δ.1.2
γ.1.2
α.1.1
δ.1.2
γ.1.2
α.1.1
η.1.2
ζ.1.2
ε.1.2
δ.1.2
γ.1.2
η.1.2
ζ.1.2
ε.1.2
δ.1.2
γ.1.2
η.1.2
ζ.1.2
ε.1.2
ε.1.2
δ.1.2
γ.1.2
α.1.1
η.1.2
ζ.1.2
ε.1.2
δ.1.2
F
D
R
X
M
W
α = 00: j 40 β = 04: add …
γ = 40: add ...
δ = 44: add ...
ε = 48: add ...
ζ = 52: add ...
η = 56: add ...
0 1 2 3 4 5 6 7 8 9
1
1
1
1
1
1
1
1.1
1.1
1.1
1.2
1.2
1.2
1.2
1.2
1.2
1.2
1.1
1.2
1.2
1.2
1.2
1.2
1.2
Next address mispredict on ‘jmp’. Corrected in decode!

## Slide 20: NA mispredict - add
γ.1.2
β.1.1
α.1.1
β.1.1
α.1.1
α.1.1
ζ.1.2
ε.1.2
δ.1.2
γ.1.2
α.1.1
δ.1.2
γ.1.2
α.1.1
η.1.2
ζ.1.2
ε.1.2
δ.1.2
γ.1.2
η.1.2
ζ.1.2
ε.1.2
δ.1.2
γ.1.2
η.1.2
ζ.1.2
ε.1.2
ε.1.2
δ.1.2
γ.1.2
α.1.1
η.1.2
ζ.1.2
ε.1.2
δ.1.2
F
D
R
X
M
W
α = 00: add ... β = 80: add …
γ = 04: add ...
δ = 08: add ...
ε = 12: add ...
ζ = 16: add ...
η = 20: add ...
0 1 2 3 4 5 6 7 8 9
1
1
1
1
1
1
1
1.1
1.1
1.1
1.2
1.2
1.2
1.2
1.2
1.2
1.2
1.1
1.2
1.2
1.2
1.2
1.2
1.2
Next address mispredict on ‘add’ corrected in decode

## Slide 21: NA mispredict - beq
γ.1.1
β.1.1
α.1.1
β.1.1
α.1.1
α.1.1
ζ.2.1
ε.2.1
δ.1.1
γ.1.1
β.1.1
α.1.1
δ.1.1
γ.1.1
β.1.1
α.1.1
η.2.1
ζ.2.1
ε.2.1
δ.1.1
γ.1.1
β.1.1
η.2.1
ζ.2.1
ε.2.1
δ.1.1
γ.1.1
η.2.1
ζ.2.1
ε.2.1
ε.2.1
δ.1.1
γ.1.1
β.1.1
α.1.1
η.2.1
ζ.2.1
ε.2.1
δ.1.1
F
D
R
X
M
W
α = 00: beq r0,r0 40 β = 04: add …
γ = 08: add ...
δ = 12: add ...
ε = 40: add ...
ζ = 44: add ...
η = 48: add ...
0 1 2 3 4 5 6 7 8 9
1
2
2
2
2
2
2
1.1
1.1
1.1
1.1
1.1
2.1
2.1
2.1
2.1
2.1
1.1
1.1
1.1
1.1
1.1
2.1
2.1
Next address mispredict on ‘beq’. Corrected in execute.

## Slide 22: NA mispredict – late shadow
γ.1.1
β.1.1
α.1.1
β.1.1
α.1.1
α.1.1
ζ.2.1
ε.2.1
γ.1.1
β.1.1
α.1.1
δ.1.1
γ.1.1
β.1.1
α.1.1
η.2.1
ζ.2.1
ε.2.1
γ.1.1
β.1.1
η.2.1
ζ.2.1
ε.2.1
γ.1.1
η.2.1
ζ.2.1
ε.2.1
ε.2.1
δ.1.1
γ.1.1
β.1.1
α.1.1
η.2.1
ζ.2.1
ε.2.1
F
D
R
X
M
W
α = 00: beq r0,r0,40 β = 04: add …
γ = 08: add ...
δ = 80: add ...
ε = 40: add ...
ζ = 16: add ...
η = 20: add ...
0 1 2 3 4 5 6 7 8 9
1
2
2
2
2
2
2
1.1
1.1
1.1
1.1
1.1
2.1
1.2
1.2
1.2
1.2
1.1
1.1
1.1
1.2
1.2
2.1
2.1
Next address mispredict on ‘beq’. Corrected in execute.
With next address mispredict late in shadow.

## Slide 23: NA mispredict – early shadow
γ.1.1
β.1.1
α.1.1
β.1.1
α.1.1
α.1.1
ζ.2.2
ε.2.2
δ.1.2
β.1.1
α.1.1
δ.1.2
γ.1.1
β.1.1
α.1.1
η.2.2
ζ.2.2
ε.2.2
δ.1.2
β.1.1
η.2.2
ζ.2.1
ε.2.2
δ.1.2
η.2.2
ζ.2.2
ε.2.2
ε.2.2
δ.1.2
β.1.1
α.1.1
η.2.2
ζ.2.2
ε.2.2
δ.1.2
F
D
R
X
M
W
α = 00: beq r0,r0,40 β = 04: add …
γ = 80: add ...
δ = 84: add ...
ε = 40: add ...
ζ = 16: add ...
η = 20: add ...
0 1 2 3 4 5 6 7 8 9
1
2
2
2
2
2
2
1.1
1.1
1.1
1.1
1.2
2.2
1.2
1.2
1.2
1.2
1.1
1.1
1.2
1.2
1.2
2.2
2.2
Next address mispredict on ‘beq’. Corrected in execute.
With next address mispredict earlier in shadow.
Notes: Any later decode redirects on old exec epoch will be ignored!

## Slide 24: Epoch management
Fetch
  On exec redirect – update to new exec epoch
  On decode redirect – if for current exec epoch then update to new decode epoch
Decode
  On new exec epoch – update exec and decode epochs
  Otherwise,
    On decode epoch mismatch – drop instruction
  Always, on next addr mispredict – move to new decode epoch and redirect.
Execute
  On exec epoch mismatch - poison instruction
  Otherwise, on mispredict – move to new exec epoch and redirect.

## Slide 25: Decode with mispredict detect
rule doDecode;
let decData = newDecData(fr.first);
let correctPath = (decData.execEpoch != deEpoch)
||(decData.decEpoch == ddEpoch);
let instResp = decData.fInst.instResp;
let pcPlus4 = decData.pc+4;
if (correctPath)
begin
decData.decInst = decode(instResp, pcPlus4);
let target = knownTargetAddr(decData.decInst);
let decodedTarget = ?;
let brClass = getBrClass(decData.decInst);
let predTarget = decData.nextAddrPred;
Determine if epoch of incoming instruction is on good path
New exec epoch
Same dec epoch

## Slide 26: Decode with mispredict detect
if (brClass == NonBranch) decodedTarget = pcPlus4
else if(brClass == CondBranch) decodedTarget = target;
else if(brClass == UncondKnown) decodedTarget = target;
else decodedTarget = decData.nextAddrPred;
if ((decodedTarget != predTarget) ||
(brClass == CondBranch && pcPlus4 != predTarget)) begin
decData.decEpoch = decData.decEpoch + 1;
decData.nextAddrPred = decodedTarget;
decFeedback.enq(
tuple3(decData.execEpoch, decData.decEpoch,
Feedback{correct: False,
naPredInfo: decData.naPredInfo,
nextAddr: decodedTarget}));
end
dr.enq(decData); end // of correct path
Wrong next address?
Tell exec addr of next instruction!
Send feedback
New dec epoch
Enqueue to next stage on correct path

## Slide 27: Decode with mispredict detect
else
begin // incorrect path
decData.decEpoch = ddEpoch;
decData.execEpoch = deEpoch;
end
ddEpoch <= decData.decEpoch;
deEpoch <= decData.execEpoch;
fr.deq;
endrule
Preserve current epoch if instruction on incorrect path
decData.*Epoch have been set properly so we always save them.

## Slide 28: Handling redirect from decode
if(execFeedback.notEmpty) begin /* same as before */ end
else if(decFeedback.notEmpty) begin
decFeedback.deq;
match {.eEpoch,.dEpoch,.feedback} = decFeedback.first;
if (eEpoch == feEpoch) begin
if (!feedback.correct) begin
fdEpoch <= dEpoch;
fetchPc <= feedback.nextAddr;
end
else
enqInst; // decode feedback for correct prediction
end else
enqInst; // decode feedback for wrong exec epoch
end else
enqInst; // no feedback from anyone
endrule
Note: no training since it will be done by feedback from exec
Respond if decode feedback is for current exec epoch