## Slide 1
Interrupts / Exceptions / Faults
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Interrupts: altering the normal flow of control
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
interrupt
handler

## Slide 3: Causes of Interrupts events that request the attention of the processor
Asynchronous: an external event
  input/output device service-request
  timer expiration
  power disruptions, hardware failure
Synchronous: an internal event (a.k.a exceptions, faults and traps)
  undefined opcode, privileged instruction
  arithmetic overflow, FPU exception
  misaligned memory access
  virtual memory exceptions: page faults, TLB misses, protection violations
  traps: system calls, e.g., jumps into kernel

## Slide 4: Asynchronous Interrupts: invoking the interrupt handler
An I/O device requests attention by asserting one of the prioritized interrupt request lines
When the processor decides to process the interrupt
  Precise interrupt: It stops the current program at instruction Ii, completing all the instructions up to Ii-1
  It saves the PC of instruction Ii in a special register (EPC)
  It disables interrupts and transfers control to a designated interrupt handler running in the kernel mode

## Slide 5: Interrupt Handler
Saves EPC before enabling interrupts to allow nested interrupts 
  need an instruction to move EPC into GPRs
  need a way to mask further interrupts at least until EPC can be saved
Needs to read a status register that indicates the cause of the interrupt
Uses a special indirect jump instruction ERET (return-from-exception) which
  enables interrupts
  restores the processor to the user mode
  restores hardware status and control state

## Slide 6: Synchronous Interrupts
A synchronous interrupt is caused by a particular instruction and behaves like a control hazard
  requires undoing the effect of one or more partially executed instructions. Comes in two varieties:
Exception: The instruction cannot be completed and needs to be restarted after the exception has been handled
  information about the exception has to be recorded and conveyed to the exception handler
Faults (aka Trap): Like a system call and the instruction is considered to have been completed
  requires a special jump instruction involving a change to privileged kernel mode

## Slide 7: Synchronous Interrupt Handling
Overflow
Illegal Opcode
PC address Exception
Data address Exceptions
...
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception

## Slide 8: Exception Handling
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Ex
D
PC
D
Ex
E
PC
E
Ex
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point
1. An instruction may cause multiple exceptions; which one should we process?
2. When multiple instructions are causing exceptions; which one should we process first?

## Slide 9: Exception Handling - priorities
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions for a given instruction
Inject external interrupts at commit point (override others)
If exception at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 10: A specific example to illustrate the transfer of control back and forth between hardware and software
A multiply instruction that is implemented in software (Fault/Trap)

## Slide 11: 2-Stage pipeline
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
itr
nextPC
fEpoch
eEpoch
+4
stall
Notes: 11

## Slide 12: Additional Features for Exceptions/Faults
instruction: mult ra, rb
  causes a fault
instruction: eret
  returns from an exception/fault handler sub-routine
register: epc
  holds pc+4 of instruction that causes exception/fault
Notes: 12

## Slide 13: Decode – additional type defs
Bit#(6) fcMULT = 6'b011000;
Bit#(5) rsERET = 5'b10000;
typedef enum {None, Mult, Eret}
Excep deriving (Bits, Eq);
typedef struct {
...
Excep excep;
} DecodedInst deriving(Bits, Eq);
typedef enum {Nop, Alu, Ld, St, J, Jr, Jal, Jalr, Br}
IType deriving(Bits, Eq);
See L07-15 for details
Notes: 13

## Slide 14: Decode
function DecodedInst decode(Data Inst);
DecodedInst dInst = ?;
...
RAlu: begin
dInst.iType = funct==fcMULT ? Nop : Alu;
if(funct==fcMULT) dInst.excep = Mult;
...
end
Other: begin
if(rs==rsERET) begin
dInst.iType = Nop;
dInst.excep = Eret;
end
...
end
return dInst;
endfunction
Notes: 14

## Slide 15: Execute
typedef struct {
...
Excep excep;
} ExecInst deriving(Bits, Eq);
function ExecInst exec(DecodedInst dInst, Data rVal1,
Data rVal2, Addr pc, Addr epc);
ExecInst eInst = ?;
...
eInst.addr =
dInst.excep==Eret ? epc :
dInst.excep==Mult ? 32'h1010 :
memType(dInst.iType) ? aluRes :
brAddr;
eInst.excep = dInst.excep;
return eInst;
endfunction
Notes: 15

## Slide 16: 2-Stage pipeline with Exceptions
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
Reg#(Addr) epc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
SPipeReg#(TypeDecode2Execute) itr
<- mkSPipeReg(getDstD2E);
FIFOF#(TypeNextPCE) nextPC
<- mkBypassFIFOF;
Notes: 16

## Slide 17: 2-Stage pipeline with Exceptions doFecth Rule
rule doFetch (itr.notFull);
let inst = iMem(pc);
let dInst = decode(inst);
let stall = itr.search(dInst.src1, dInst.src2);
if(!stall) begin
let rVal1 = rf.rd1(fromMaybe(dInst.src1));
let rVal2 = rf.rd2(fromMaybe(dInst.src2));
itr.enq(TypeDecode2Execute{pc:pc,
epoch:fEpoch, dInst:dInst,
rVal1:rVal1, rVal2:rVal2});
if(nextPC.notEmpty) begin
npc = nextPC.first.npc;
nepoch = nextPC.first.nepoch;
pc <= npc; fEpoch <= nepoch; nextPC.deq;
end
else pc <= pc+4; end
endrule
Notes: 17

## Slide 18: 2-Stage pipeline with Exceptions doExecute Rule
rule doExecute (itr.notEmpty);
let itrpc=itr.first.pc; let dInst=itr.first.dInst;
let rVal1=itr.first.rVal1;
let rVal2=itr.first.rVal2;
if(itr.first.epoch==eEpoch) begin
let eInst = execute(dInst, rVal1, rVal2,
itrpc, epc);
let memData <- dMemAction(eInst, dMem);
regUpdate(eInst, memData, rf);
if(eInst.missPrediction || eInst.excep!=None)begin
let nepoch = next(epoch); eEpoch <= nepoch;
nextPC.enq(TypeNextPCE{npc:eInst.addr,
nepoch:nepoch}); end
if(eInst.excep!=None) epc <= itrpc + 4;
end
itr.deq;
endrule endmodule
Notes: 18

## Slide 19
Software Considerations
00001000 <__start>:
1000: 3c1d0002 lui $sp,0x2
1004: 0c000449 jal 1124 <main>
1008: 00000000 nop
100c: 00000000 nop
1010: 08000408 j 1020 <mult_excep>
...
00001020 <mult_excep>:
1020: 24890000 addiu $t1,$a0,0
1024: 24aa0000 addiu $t2,$a1,0
1028: 24020000 li $v0,0
102c: 24070020 li $a3,32
...
104c: 42000018 eret
00001124 <main>:
...
11a0: 00850018 mult $a0,$a1
Notes: 19

## Slide 20: Realistic exception handling
State per instruction for storing the cause of exception (cause)
State per instruction for storing pc of the instruction that causes exception (epc)
Instructions to transfer cause and epc to/from GPRs
Processor state for enabling/disabling interrupts to allow nested interrupts (status)
Privileged/user mode to prevent user programs from causing harm to other users or OS
Usually speed is not a paramount concern in handling exceptions