## Slide 1: Caches and in-order pipelines
Arvind (with Asif Khan)
Computer Science & Artificial Intelligence Lab
Massachusetts Institute of Technology

## Slide 2: Multi-Stage SMIPS
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
ir
Epoch
cr
itr
er
Next
Addr
Pred
scoreboard
insert bypass FIFO’s to deal with (0,n) cycle memory response
fr
mr
Notes: 2

## Slide 3: Multi-Stage SMIPS
module mkProc(Proc);
EHR#(2, Addr) pc <- mkEHRU;
RFile rf <- mkBypassRFile;
Scoreboard#(4) sb <- mkScoreboard;
EHR#(2, Bool) epoch <- mkEHR(False);
NextAddrPred bpred <- mkBTB;
CombCache iCache <- mkICache;
CombCache dCache <- mkDCache;
BFIFO#(TypeFetch2Fetch) fr <- mkBypassFIFO;
PFIFO#(TypeFetch2Decode) ir <- mkPipeFIFO;
PFIFO#(TypeDecode2Execute) itr <- mkPipeFIFO;
PFIFO#(TypeExecute2Memory) er <- mkPipeFIFO;
BFIFO#(TypeMemory2Memory) mr <- mkBypassFIFO;
PFIFO#(TypeMemory2Commit) cr <- mkPipeFIFO;
The choice of type of FIFOs, Reg vs EHR depends upon the architecture
PC
iMem
Dec
Register File
Exe
dMem
ir
Epoch
cr
itr
er
Pred
scoreboard
fr
mr
state declarations
Notes: 3

## Slide 4: Different architectures require different scheduling
if ir is a pipelined FIFO (deq<enq) then reg file has to be a bypass register file (wr < {rd1,rd2})
  a design with bypass paths
if ir is normal FIFO (deq CF enq) then reg file can be either ordinary or bypass register file, resulting in two different architectures
Fetch
Execute
Reg File
ir
wr
rd1,rd2

## Slide 5: Design 1: Processor Rule ordering
doCommit <
(doMem1 < doMem2) <
doExecute <
doDecode <
(doFetch1 < doFetch2)
 mr, fr are bypass FIFO
(enq < first < deq)
 cr, er, itr, ir are pipeline FIFOs (first < deq < enq)
PC
iMem
Dec
Register File
Exe
dMem
ir
Epoch
cr
itr
er
Pred
scoreboard
fr
mr
Cache
req < (resp < respDeq)
Scoreboard
remove < (search < insert)
Register File
wr < {rd1, rd2}
NextAddrPred
prediction < update
epoch and pc
r0 < w0 < r1 < w1
Register File
wr < {rd1, rd2}

## Slide 6: Scoreboard: Keeping track of instructions in execution
Scoreboard: a data structure to keep track of the destination registers of the instructions beyond the fetch stage
  method insert: inserts the destination (if any) of an instruction in the scoreboard when the instruction is decoded
  method search(src1,src2): searches the scoreboard for data hazards
  method remove: deletes the oldest entry when an instruction commits

## Slide 7: Scoreboard
module mkScoreboard(Scoreboard#(size));
Vector#(size, EHR#(2, Maybe#(Rindx))) sb
<- replicateM(mkEHR(Invalid));
Reg#(Bit#(TAdd#(TLog#(size),1))) iidx <- mkReg(0);
Reg#(Bit#(TAdd#(TLog#(size),1))) ridx <- mkReg(0);
EHR#(2, Bit#(TAdd#(TLog#(size),1))) cnt <- mkEHR(0);
Integer vsize = valueOf(size);
Bit#(TAdd#(TLog#(size),1)) sz = fromInteger(vsize);
method Action insert(Maybe#(Rindx) r)
if(cnt.r1!==sz);
sb[iidx].w1(r);
iidx <= iidx==(sz-1) ? 0 : iidx + 1;
cnt.w1(cnt.r1 + 1);
endmethod
insert prt
rem ptr
insert prt
remove prt
Counter
Notes: 7

## Slide 8: Scoreboard cont
method Action remove if (cnt.r0!=0);
sb[ridx].w0(Invalid);
ridx <= ridx==sz-1 ? 0 : ridx + 1;
cnt.w0(cnt.r0 – 1);
endmethod
method Bool search(Maybe#(Rindx) s1,
Maybe#(Rindx) s2);
Bool j = False;
for (Integer i=0; i<vsize; i=i+1)
j = j || dataHazard(s1, s2, sb[i].r1);
return j;
endmethod
endmodule
http://csg.csail.mit.edu/6.S078
remove < search < insert
Notes: 8

## Slide 9: Data Hazard
Given two source registers and a destination register determine if there is a potential for data hazard
src1, src2 and rDst in decodedInst are changed from Rindx to Maybe#(Rindx)
function Bool dataHazard(Maybe#(Rindx) src1,
Maybe#(Rindx) src2,
Maybe#(Rindx) dst);
return (isValid(dst) &&
( (isValid(src1) &&
fromMaybe(dst) == fromMaybe(src1))
|| (isValid(src2) &&
fromMaybe(dst)== fromMaybe(src2))));
endfunction

## Slide 10: Cache Interface
interface Cache; method Action req(MemReq r); method MemResp resp; method Action respDeq; method ActionValue#(MemReq) mReq; method Action mResp(MemResp r); endinterface
cache
req
resp
mReqDeq
mResp
Processor
DRAM
hitQ
mReqQ
mRespQ
missReq
respDeq
processor side
memory side
we will assume caches respond in a FIFO manner and can take 0 to n cycles to respond

## Slide 11: Fetch rules
rule doFetch1 (fr.notFull);
iCache.req(TypeMemReq{op:Ld, addr:pc.r1, data:?});
let ppc = bpred.prediction(pc.r1);
fr.enq(TypeFecth2Fetch{pc:pc.r1, ppc:ppc,
epoch:epoch.r1});
pc.w1(ppc);
endrule
rule doFetch2 (fr.notEmpty && ir.notFull);
let frpc = fr.first.pc;
let frppc = fr.first.ppc;
let frepoch = fr.first.epoch;
let inst = iCache.resp; iCache.respDeq;
ir.enq(TypeFetch2Decode{pc:frpc, ppc:frppc,
epoch:frepoch, inst:inst});
fr.deq;
endrule
PC
iMem
ir
Epoch
Pred
fr
Notes: 11

## Slide 12: Decode rule
rule doDecode (ir.notEmpty && itr.notFull);
let irpc = ir.first.pc;
let irppc = ir.first.ppc;
let irepoch = ir.first.epoch;
let inst = ir.first.inst;
let dInst = decode(inst);
let stall = sb.search(dInst.src1, dInst.src2);
if(!stall) begin
let rVal1 = rf.rd1(fromMaybe(dInst.src1));
let rVal2 = rf.rd2(fromMaybe(dInst.src2));
itr.enq(TypeDecode2Execute{pc:irpc, ppc:irppc,
epoch:irepoch, dInst:dInst,
rVal1:rVal1, rVal2:rVal2});
sb.insert(dInst.rDst);
ir.deq; end
endrule
Notes: 12

## Slide 13: Execute rule
rule doExecute (itr.notEmpty && er.notFull);
let itrpc=itr.first.pc; let itrppc=itr.first.ppc;
let dInst=itr.first.dInst;
let rVal1=itr.first.rVal1; let rVal2=itr.first.rVal2;
if(itr.first.epoch==epoch.r0) begin
let eInst=execute(dInst,rVal1,rVal2,itrpc,itrppc);
er.enq(TypeExecute2Memory{eInst:eInst, memData:?});
if(eInst.misprediction) begin
let npc = eInst.brTaken ? eInst.addr : itrpc+4;
pc.w0(npc); epoch.w0(!epoch.r0);
bpred.update(itrpc, npc);
end end
else begin
ExecInst eInst = ?; eInst.iType = Nop;
er.enq(TypeExecute2Memory{eInst:eInst, memData:?});
end
itr.deq;
endrule
Notes: 13

## Slide 14: Data Memory rules
rule doMemory1 (er.notEmpty && mr.notFull);
let eInst = er.first.eInst;
if(memType(eInst.iType))
dCache.req(MemReq{op:eInst.iType==Ld ? Ld : St,
addr:eInst.addr, data:eInst.data});
mr.enq(TypeMemory2Memory{eInst:eInst, memData:?});
er.deq;
endrule
rule doMemory2 (mr.notEmpty && cr.notFull);
let eInst = mr.first.eInst;
if(eInst.iType==Ld) begin
let md = dCache.resp;
dCache.respDeq; end
cr.enq(TypeMemory2Commit{eInst:eInst, memData:md});
mr.deq;
endrule
Notes: 14

## Slide 15: Commit rule
rule doCommit (cr.notEmpty);
let eInst = cr.first.eInst;
let memData = cr.first.memData;
regUpdate(eInst, memData, rf);
cr.deq;
sb.remove;
endrule
endmodule
Notes: 15

## Slide 16: Cache implementations
Blocking vs Non-blocking
X
Direct mapped vs Set-associative
X
FIFO vs Tags (Out-of-order)
X
I-Cache
D-Cache

## Slide 17: Direct-mapped Blocking Cache state declarations
module mkCache(Cache); Vector#(Rows, Reg#(LineStatus)) sArray <-
replicateM(mkReg(False)); Vector#(Rows, Reg#(Tag)) tagArray <-
replicateM(mkRegU); Vector#(Rows, Reg#(Data)) dataArray <-
replicateM(mkRegU);
BFIFO#(MemReq) hitQ <- mkBypassFIFO; Reg#(MemReq) missReq <- mkRegU; Reg#(CacheStatus) status <- mkReg(Rdy);
FIFOF#(MemReq) mReqQ <- mkFIFOF; FIFOF#(MemResp) mRespQ <- mkFIFOF;
rule doMiss … endrule; method ....; endmodule

## Slide 18: typedefs
typedef 32 AddrSz;
typedef 256 Rows;
typedef Bit#(AddrSz) Addr;
typedef Bit#(TLog#(Rows)) Index;
typedef Bit#(TSub#(AddrSz, TAdd#(TLog#(Rows), 2))) Tag;
typedef 32 DataSz;
typedef Bit#(DataSz) Data;
typedef enum {Invalid, Clean, Dirty}
LineStatus deriving(Bits, Eq);
tyepdef enum {Rdy, WrBack, FillReq, FillResp, FillHit}
CacheStatus deriving(Bits, Eq);

## Slide 19: memory-side methods
method ActionValue#(MemReq) mReqDeq; mReqQ.deq; return mReqQ.first; endmethod
method Action memResp(MemResp r); mRespQ.enq(r); endmethod

## Slide 20: Blocking D-Cache processor-side methods
method Action req(MemReq r) if (status==Rdy); Index idx = truncate(r.addr>>2); Tag tag = truncateLSB(r.addr); let lnSt = sArray[idx]; Bool tagMatch = tagArray[idx]==tag; if(lnSt!=Invalid && tagMatch)
hitQ.enq(r); else begin
missReq <= r;
status <= lnSt==Dirty ? WrBack : FillReq;
end endmethod
hitQ is a bypass FIFO
It is straightforward to extend the cache interface to include a cacheline flush command

## Slide 21: Blocking D-Cache processor-side methods cont.
method MemResp resp if (hitQ.first.op==Ld); let r = hitQ.first; Index idx = truncate(r.addr>>2); return dataArray[idx]; endmethod
method Action respDeq if (hitQ.first.op==Ld);
hitQ.deq;
endmethod
rule doStore(hitQ.first.op==St);
let r = hitQ.first;
Index idx = truncate(r.add>>2);
dataArray[idx] <= r.data;
sArray[idx] <= Dirty;
hitQ.deq;
endrule
In case of multiword cache line, we only overwrite the appropriate word of the line

## Slide 22: Blocking D-Cache Rules to process cache miss: cache-to-mem
rule doWrBack (status==WrBack);
Index idx = truncate(missReq.addr>>2);
mReqQ.enq(MemReq{op:St,
addr:{tagArray[idx],idx,2’b00},
data:dataArray[idx]}); status <= FillReq; endrule
rule doFillReq (status==FillReq); mReqQ.enq(MemReq{op:Ld, addr:missReq.addr, data:?}); status <= FillResp; endrule
Both load miss and store miss generate a memory load request

## Slide 23: Blocking D-Cache Rules to process cache miss: mem-to-cache
rule doFillResp (status==FillResp); let data = mRespQ.first; mRespQ.deq;
Index idx = truncate(missReq.addr>>2);
Tag tag = truncateLSB(missReq.addr);
sArray[idx] <= Clean; tagArray[idx] <= tag; dataArray[idx] <= data;
hitQ.enq(missReq); status <= FillHit; endrule
rule doFillHit (status==FillHit); hitQ.enq(missReq); status <= Rdy; endrule

## Slide 24: Hit and miss behaviors
Hit
  Combinational read/write, i.e. 0-cycle response
  Cache works correctly even if the processor does not immediately (combinationally) pick up the response
Miss
  No evacuation: memory load latency plus combinational read/write
  Evacuation: memory store followed by memory load latency plus combinational read/write
next lecture - Non-blocking caches