## Slide 1: Non-blocking Caches
Arvind (with Asif Khan)
Computer Science & Artificial Intelligence Lab
Massachusetts Institute of Technology

## Slide 2: Non-blocking caches
Enable multiple outstanding cache misses
  It is like pipelining the memory system
Extremely important for hiding memory latency
Dramatically more complicated than blocking caches
  We will use the same processor interface for both blocking and non-blocking caches

## Slide 3: Non-blocking cache
Completion buffer controls the entries of requests and ensures that departures take place in order even if loads complete out-of-order
Processor
DRAM
cache
req
resp
mReq
mResp
mReqQ
mRespQ
respDeq
cbuf
req proc

## Slide 4: Non-blocking caches
Split the non-blocking cache in two parts
  The front end attaches tags to requests and ensures FIFO delivery of responses to the processor
  The backend is a non-locking cache which can return responses out-of-order
  One may merge the front end with the processor and directly expose the backend interface
respDeq
cache
req
resp
mReq
mResp
mReqQ
mRespQ
req proc
FIFO responses
inputs are tagged;
responses can be OOO
Processor
req
resp
respDeq
cbuf

## Slide 5: Completion buffer: Interface
interface CBuffer#(type t);
method ActionValue#(Token) getToken();
method Action put(Token tok, t d);
method t getResult();
method Action deqResult();
endinterface
cbuf
getResult
getToken
put (result & token)
deqResult
Concurrency requirement (needed to achieve (0,n), i.e., combinational responses)
getToken < put < getResult < deqResult

## Slide 6: Non-blocking FIFO Cache
module mkNBfifoCache(Cache); cBuf <- mkCompletionBuffer;
nbCache <- mkNBtaggedCache;
method Action req(MemReq x); tok <- cBuf.getToken;
nbCache.req({req:x, tag:tok});
endmethod
method MemResp resp return cBuf.getResult endmethod
method Action respDeq;
cBuf.deqResult;
endmethod
rule nbCacheResponse;
cBuf.put(nbCache.resp);
nbCache.respDeq;
endrule endmodule
req
resp
respDeq
cbuf

## Slide 7: Completion buffer: Implementation
I
I
V
I
V
I
cnt
iidx
ridx
buf
A circular buffer with two pointers iidx and ridx, and a counter cnt
Elements are of Maybe type
module mkCompletionBuffer(CompletionBuffer#(size));
Vector#(size, EHR#(Maybe#(t))) cb
<- replicateM(mkEHR3(Invalid));
Reg#(Bit#(TAdd#(TLog#(size),1))) iidx <- mkReg(0);
Reg#(Bit#(TAdd#(TLog#(size),1))) ridx <- mkReg(0);
EHR#(Bit#(TAdd#(TLog#(size),1))) cnt <- mkEHR(0);
Integer vsize = valueOf(size);
Bit#(TAdd#(TLog#(size),1)) sz = fromInteger(vsize);
rules and methods...
endmodule

## Slide 8: Completion Buffer cont
method ActionValue#(t) getToken() if(cnt.r0!==sz);
cb[iidx].w0(Invalid);
iidx <= iidx==sz-1 ? 0 : iidx + 1;
cnt.w0(cnt.r0 + 1);
return iidx;
endmethod
method Action put(Token idx, t data);
cb[idx].w1(Valid data);
endmethod
method t getResult() if(cnt.r1 !== 0 &&&
(cb[ridx].r2 matches tagged (Valid .x));
return x; endmethod
method Action deqResult if(cnt.r1!=0);
cb[ridx].w2(Invalid);
ridx <= ridx==sz-1 ? 0 : ridx + 1;
cnt.w1(cnt.r1 – 1);
endmethod
http://csg.csail.mit.edu/6.S078
getToken < put <
getResult < deqResult
Notes: 8

## Slide 9: Non-blocking Cache
St
Buff
Ld
Buff
Wait
Buff
Tag
Data
wbQ
mReqQ
mRespQ
hitQ
respDeq
resp
req
Holds reqs that must be deferred because the address is already being processed
Holds St’s because of no-allocate on a write-miss policy
V/C/D
Holds Ld misses that are being processed
Notes: 9

## Slide 10: Dynamics of NB cache processor side
A ld request is checked first for a
  cache hit  respond, then
  store buff hit  respond, then
  ld buffer addr match  put in wait buff, otherwise
  put it in the ld buff
A st request is checked first for a
  cache hit  respond, then
  ld buffer addr match  put in wait buff, otherwise
  put it in the store buff

## Slide 11: Dynamics of NB cache
Memory side: Responses for ld misses come back in the mRespQ
  retire the ld from the ld buff
  search wait buff for addr match, then
  if match is found go into the procWaitBuff mode and process all matching waiting misses. Proc requests are blocked off.
Ld buff keeps issuing WB and mem requests as long as there are unfullfilled ld misses

## Slide 12: Non-blocking Cache state declaration
module mkNBCache(NBCache);
RegFile#(Index, LineStatus) sArray <- mkRegFileFull;
RegFile#(Index, Tag) tagArray <- mkRegFileFull;
RegFile#(Index, Data) dataArray <- mkRegFileFull;
StBuff#(StBuffSz) stBuff <- mkStBuff;
LdBuff#(LdBuffSz) ldBuff <- mkLdBuff;
SPipeFIFO#(TaggedMemReq) waitBuff <- mkSPipeFIFO;
FIFOF#(MemReq) wbQ <- mkFIFOF;
FIFOF#(MemReq) mReqQ <- mkFIFOF;
FIFOF#(MemResp) mRespQ <- mkFIFOF;
EHRBypassReg#(TypeHit) hitQ <- mkEHRBypassReg;
Reg#(Bool) procWaitBuff <- mkReg(False);
Notes: 12

## Slide 13: Non-blocking Cache Processor-side request method
method Action req(TaggedMemReq x) if(!procWaitBuff);
Index idx = truncate(x.req.addr>>2);
Tag tag = truncateLSB(x.req.addr);
let lnSt = sArray.sub(idx);
Bool tagMatch = tagArray.sub(idx)==tag;
let sbMatch = stBuff.search(x.req.addr);
let lbMatch = ldBuff.search(x.req.addr);
if(lnSt!==Invalid && tagMatch)
hitQ.enq(TypeHit{tag:x.tag, req:x.req,
data:Invalid});
else if(lbMatch) waitBuff.enq(x);
else if(x.req.op==St) stBuff.insert(x.req);
else if(x.req.op==Ld && isValid(sbMatch))
hitQ.enq(TypeHit{tag:x.tag, req:x.req,
data:sbMatch});
else
ldBuff.insert(x, lnSt==Dirty ? WrBack : FillReq);
endmethod
Notes: 13

## Slide 14: Non-blocking Cache Processor-side response methods
method TaggedMemResp resp if(hitQ.first.req.op==Ld);
let x = hitQ.first.req;
Index idx = truncate(x.addr>>2);
Data d = isValid(hitQ.first.data) ?
fromMaybe(hitQ.first.data) :
dataArray.sub(idx);
return TaggedMemResp{tag:hitQ.first.tag, resp:d};
endmethod
method Action respDeq if(hitQ.first.req.op==Ld);
hitQ.deq;
endmethod
No response for stores
same as Blocking cache
Notes: 14

## Slide 15: Non-blocking Cache store hit rule
rule storeHit(hitQ.first.req.op==St);
let x = hitQ.first.req;
Index idx = truncate(x.addr>>2);
dataArray.upd(idx, x.data);
sArray.upd(idx, Dirty);
hitQ.deq;
endrule
same as Blocking cache
Notes: 15

## Slide 16: Non-blocking Cache load buff rule
rule ldBuffUpdate;
let u = ldBuff.usearch;
if(u.valid)
if(u.cst==FillReq) begin
mReqQ.enq(MemReq{op:Ld, addr:u.addr, data:?});
ldBuff.update(u.addr, FillResp);
end
else begin
Index idx = truncate(u.addr>>2);
wbQ.enq(MemReq{op:St,
addr:{tagArray.sub(idx),idx,2'b00},
data:dataArray.sub(idx)});
mReqQ.enq(MemReq{op:Ld, addr:u.addr, data:?});
compBuff.update(u.addr, FillResp);
end
endrule
Notes: 16

## Slide 17: Non-blocking Cache memory response rule
rule mRespAvailable;
let data = mRespQ.first.data;
let addr = mRespQ.first.addr;
Index idx = truncate(addr>>2);
Tag tag = truncateLSB(addr);
sArray.upd(idx, Clean);
tagArray.upd(idx, tag);
dataArray.upd(idx, data);
let x <- ldBuff.remove(addr);
hitQ.enq(TypeHit{tag:x.tag, req:x.req,
data:Valid (data)});
if(waitBuff.search(addr))
procWaitBuff <= True;
else
mRespQ.deq;
endrule
Notes: 17

## Slide 18: Non-blocking Cache wait buffer rule
rule goThroughWaitBuff(procWaitBuff);
let data = mRespQ.first.data;
let addr = mRespQ.first.addr;
let x = waitBuff.first;
waitBuff.deq;
if(x.req.addr==addr)
hitQ.enq(TypeHit{tag:x.tag, req:x.req,
data:Valid (data)});
else
waitBuff.enq(x);
if(!waitBuff.search(addr)) begin
procWaitBuff <= False;
mRespQ.deq;
end
endrule
Notes: 18

## Slide 19: Non-blocking Cache memory-side methods
method ActionValue#(MemReq) wb;
wbQ.deq;
return wbQ.first;
endmethod
method ActionValue#(MemReq) mReq;
mReqQ.deq;
return mReqQ.first;
endmethod
method Action mResp(MemResp x);
mRespQ.enq(x);
endmethod
endmodule
same as Blocking cache
Notes: 19

## Slide 20: Misc rules
rule stBuffRemove;
let x <- stBuff.remove;
wbQ.enq(x);
endrule

## Slide 21: Store buffer methods
insert: when a cache miss occurs on a store
search: associatively searched for Ld addresses
remove: when a store moves to the write-back queue
remove < search < insert

## Slide 22: Store Buffer
module mkStBuff(StBuff#(size));
Vector#(size, EHR2#(Maybe#(MemReq))) buff
<- replicateM(mkEHR2(Invalid));
Reg#(Bit#(TAdd#(TLog#(size),1))) iidx <- mkReg(0);
EHR2#(Bit#(TAdd#(TLog#(size),1))) ridx <- mkEHR2(0);
EHR2#(Bit#(TAdd#(TLog#(size),1))) cnt <- mkEHR2(0);
Integer vsize = valueOf(size));
Bit#(TAdd#(TLog#(size),1)) sz = fromInteger(vsize);
method ActionValue#(MemReq) remove if(cnt.r0!=0);
buff[ridx.r0].w0(Invalid);
ridx.w0(ridx.r0==sz-1 ? 0 : ridx.r0 + 1);
cnt.w0(cnt.r0 - 1);
return fromMaybe(buff[ridx.r0].r0);
endmethod
Notes: 22

## Slide 23: Store Buffer cont
method Maybe#(Data) search(Addr a);
Maybe#(Data) m = Invalid; let idx = ridx.r1;
for(Integer i=0; i<vsize); i=i+1) begin
if(isValid(buff[idx].r1) &&
fromMaybe(buff[idx].r1).addr==a)
m = Valid (fromMaybe(buff[idx].r1).data);
idx = idx + 1;
end
return m;
endmethod
method Action insert(MemReq x) if(cnt.r1!==sz);
buff[iidx].w1(Valid (x));
iidx <= iidx==sz-1 ? 0 : iidx + 1;
cnt.w1(cnt.r1 + 1);
endmethod
endmodule
Notes: 23

## Slide 24: Load buffer methods
insert: when a cache miss occurs on a store
search: associatively searched for Ld addresses
remove: when a store moves to the write-back queue
update: updates the ld status when a memory request is satisfied by the memory
usearch: this search is needed to see if a Ld is is in Wb state or Fill state

## Slide 25: Load Buffer
module mkLdBuff(LdBuff#(size));
Vector#(size, EHR3#(LdStatus)) ldstA
<- replicateM(mkEHR3(Invalid));
Vector#(size, EHR3#(TaggedMemReq)) buff
<- replicateM(mkEHR3U);
EHR3#(Bit#(TAdd#(TLog#(size),1))) cnt <- mkEHR3(0);
Integer vsize = valueOf(size));
Bit#(TAdd#(TLog#(size),1)) sz = fromInteger(vsize);
method ActionValue#(TaggedMemReq) remove(Addr a)
if(cnt.r0!=0);
Bit#(TLog#(size)) idx = 0;
for(Integer i=0; i<vsize; i=i+1)
if(buff[i].r0.req.addr==a)
idx = fromInteger(i);
ldstA[idx].w0(Invalid); cnt.w0(cnt.r0 - 1);
return buff[idx].r0;
endmethod
Notes: 25

## Slide 26: Load Buffer cont
method Action update(Addr a, LdStatus ldst);
for(Integer i=0; i<vsize; i=i+1)
if(ldstA[i].r2!==Invalid &&
buff[i].r2.req.addr==a)
ldstA[i].w2(ldst);
endmethod
method TypeUpdate usearch;
TypeUpdate u = TypeUpdate{valid:False, ldst:?,
addr:?};
for(Integer i=0; i<vsize; i=i+1)
if(ldstA[i].r2==WrBack || ldstA[i].r2==FillReq)
u = TypeUpdate{valid:True, ldstA:ldstA[i].r2,
addr:buff[i].r2.req.addr};
return u;
endmethod
Notes: 26

## Slide 27: Load Buffer cont
method Bool search(Addr a);
Bool s = False;
for(Integer i=0; i<vsize; i=i+1)
if(ldstA[i].r1!=Invalid &&
buff[i].r1.req.addr==a)
s = True;
return s;
endmethod
method Action insert(TaggedMemReq x, LdStatus ldst)
if(cnt.r1!=sz);
Bit#(TLog#(size)) idx = 0;
for(Integer i=0; i<vsize; i=i+1)
if(ldstA[i].r1==Invalid)
idx = fromInteger(i);
buff[idx].w1(x);
ldstA[idx].w1(ldst);
cnt.w1(cnt.r1 + 1);
endmethod
endmodule
Notes: 27