## Slide 1
Constructive Computer Architecture
Sequential Circuits
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Content
Introduce sequential circuits as a way of saving area
  Edge triggered Flipflop
  Register
New BSV concepts
  state elements
  rules and actions for describing dynamic behavior
  modules and methods

## Slide 4: Multiplication by repeated addition
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
a0
m0
a1
m1
a2
m2
a3
m3
add4
0
add4
add4
mi = (a[i]==0)? 0 : b;

## Slide 5: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) tp = 0; Bit#(32) prod = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i:i] = sum[0];
tp = sum[32:1];
end return {tp,prod}; endfunction
Combinational circuit uses 31 add32 circuits

## Slide 6: Design issues with combinational multiply
Lot of hardware
  32-bit multiply uses 31 add32 circuits
Long chains of gates
  32-bit ripple carry adder has a 31-long chain of gates
  32-bit multiply has 31 ripple carry adders in sequence!
The speed of a combinational circuit is determined by its longest input-to-output path
Can we do better?

## Slide 7: We can reuse the same add32 circuit if we can store the partial results in some storage device, e.g., register

## Slide 8: Combinational circuits
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
Sel
O0
O1
On-1
A
Demux
.
.
.
lg(n)
A
Decoder
.
.
.
O0
O1
On-1
lg(n)
Such circuits have no cycles (feedback) or state elements

## Slide 9: A simple synchronous state element
ff
Q
D
C
C
D
Q
Metastability
Data is sampled at the rising edge of the clock
Edge-Triggered Flip-flop
Notes: Metastability?

## Slide 10: Flip-flops with Write Enables
ff
Q
D
C
EN
C
D
Q
EN
ff
Q
D
C
EN
0
1
ff
Q
D
C
EN
dangerous!
Data is captured only if EN is on
Notes: Why dangerous?
Glitches

## Slide 11: Registers
Register: A group of flip-flops with a common
clock and enable
Register file: A group of registers with a common
clock, input and output port(s)
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
Q
Q
Q
Q
Q
Q
Q
Q
D
C
En

## Slide 12: We can build useful and compact circuits using registers
Circuits containing state elements are called sequential circuits
We will only use clocked or synchronous sequential circuits

## Slide 13: Expressing a loop using registers
int s = s0;
for (int i = 0; i < 32; i = i+1) { s = f(s); } return s; C-code
sel
< 32
0
notDone
+1
i
en
sel = start
en = start | notDone
s0
f
sel
s
en
We need two registers to hold s and i values from one iteration to the next.
These registers are initialized when the computation starts and updated every cycle until the computation terminates

## Slide 14: Expressing sequential circuits in BSV
Sequential circuits, unlike combinational circuits, are not expressed structurally (i.e., as wiring diagrams) in BSV
For sequential circuits a designer defines:
  State elements by instantiating modules
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
  Rules which define how state is to be transformed atomically
  rule step if (i < 32); s <= f(s); i <= i+1; endrule
make a 32-bit register which is uninitialized
make a 6-bit register with initial value 32
the rule can execute only when its guard is true
actions to be performed when the rule executes

## Slide 15: Rule Execution
< 32
notDone
+1
sel
0
i
en
sel = start
en = start | notDone
f
s0
sel
s
en
Reg#(Bit#(32)) s <- mkRegU();
Reg#(Bit#(6)) i <- mkReg(32);
rule step if (i < 32); s <= f(s); i <= i+1; endrule
When a rule executes:
  all the registers are read at the beginning of a clock cycle
  the guard and computations to evaluate the next value of the registers are performed
  at the end of the clock cycle registers are updated iff the guard is true
Muxes are need to initialize the registers

## Slide 16: Using registers in Multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) prod = 0; Bit#(32) tp = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i:i] = sum[0]; tp = sum[32:1]; end return {tp,prod}; endfunction
Need registers to hold a, b, tp, prod and i
Update the registers every cycle until we are done
Combinational version

## Slide 17: Sequential Circuit for Multiply
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] <= sum[0]; tp <= sum[32:1];
i <= i+1; endrule
state elements
a rule to describe the dynamic behavior
So that the rule won’t fire until i is set to some other value
similar to the loop body in the combinational version

## Slide 18: Dynamic selection requires a mux
a[i]
a
i
a[0],a[1],a[2],…
a
>>
0
when the selection indices are regular then it is better to use a shift operator (no gates!)

## Slide 19: Replacing repeated selections by shifts
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= a >> 1; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], prod[31:1]}; tp <= sum[32:1];
i <= i+1; endrule

## Slide 20: Circuit for Sequential Multiply
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
s1 = start_en
s2 = start_en | !done
result (high)
31
0
add
0
0
32:1
0
<<

## Slide 21: Circuit analysis
Number of add32 circuits has been reduced from 31 to one, though some registers and muxes have been added
The longest combinational path has been reduced from 31 serial add32’s to one add32 plus a few muxes
The sequential circuit will take 31 clock cycles to compute an answer

## Slide 22: Modules
We often package sequential circuits into modules to hide the details

## Slide 23: Multiply Module
rdy
en
Bit#(32)
Bit#(64)
rdy
start
result
Multiply
module
Bit#(32)
interface Multiply;
method Action start
(Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
A module in BSV is like an object in an object-oriented language and can only be manipulated via the methods of its interface
However, unlike software, a method in BSV can be applied only when it is “ready”
Furthermore, application of an action method, i.e., a method that changes the state of a module, is indicated by asserting the associated enable wire

## Slide 24: Multiply Module
module mkMultiply32 (Multiply);
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep if (i != 32);
Bit#(32) m = (a[0]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], prod[31:1]}; tp <= sum[32:1]; a <= a >> 1; i <= i+1;
endrule
method Action start(Bit#(32) aIn, Bit#(32) bIn)
if (i == 32);
a <= aIn; b <= bIn; i <= 0; tp <= 0; prod <= 0;
endmethod
method Bit#(64) result() if (i == 32);
return {tp,prod};
endmethod endmodule
State
Internal
behavior
External
interface
method guards

## Slide 25: Module: Method Interface
s1 = start_en
s2 = start_en | !done
== 32
0
done
+1
aIn
bIn
en
rdy
result
rdy
start
result
s1
OR
s1
s2
bIn
b
a
i
prod
result (low)
<<
[30:0]
aIn
<<
31:0
tp
result (high)
add
0
31
0
0
s1
s1
s1
s2
s2
s2
s2
s1
32:1
0

## Slide 26: Polymorphic Multiply Module
rdy
en
Bit#(32)
Bit#(64)
rdy
start
result
Multiply
module
Bit#(32)
implicit conditions
interface Multiply;
method Action start (Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
n
#(Numeric type n)
n
Tadd(n,n)
n
n
TAdd#(n,n)
n could be
Bit#(32),
Bit#(13), ...
The module can easily be made polymorphic

## Slide 27: Sequential n-bit multiply
module mkMultiplyN (MultiplyN#(n));
Reg#(Bit#(n)) a <- mkRegU();
Reg#(Bit#(n)) b <- mkRegU();
Reg#(Bit#(n)) prod <-mkRegU(); Reg#(Bit#(n)) tp <- mkReg(0);
let nv = fromInteger(valueOf(n)); Reg#(Bit#(TAdd#(TLog#(n),1))) i <- mkReg(nv);
rule mulStep if (i != nv);
Bit#(n) m = (a[0]==0)? 0 : b; Bit#(Tadd#(n,1)) sum = addN(m,tp,0); prod <= {sum[0], prod[(nv-1):1]}; tp <= sum[32:1]; a <= a >> 1; i <= i+1;
endrule
method Action start(Bit#(n) aIn, Bit#(n) bIn) if (i == nv);
a <= aIn; b <= bIn; i <= 0; tp <= 0; prod <= 0;
endmethod method Bit#(Tadd#(n,n)) result() if (i == nv);
return {tp,prod};
endmethod endmodule

## Slide 28: Multiply Module
interface Multiply;
method Action start (Bit#(32) a, Bit#(32) b);
method Bit#(64) result();
endinterface
The same interface can be implemented in many different ways:
  module mkMultiply (Multiply)
  module mkBlockMultiply (Multiply)
  module mkBoothMultiply (Multiply)…