## Slide 1
Constructive Computer Architecture
FFT: An example of complex combinational circuits
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Contents
FFT and IFFT: Another complex combinational circuit and its folded implementations
  FFT: Converts signals from time domain to frequency domain
  IFFT: Converts signals from frequency domain to time domain
  Two calculations are identical- the same hardware can be used
New BSV concepts
  structure type
  overloading

## Slide 4: Combinational IFFT
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
All numbers are complex and represented as two sixteen bit quantities. Fixed-point arithmetic is used to reduce area, power, ...
*
*
*
*
+
-
-
+
+
-
-
+
*j
t2
t0
t3
t1
Notes: Constants t0 to t3 are different for each box and can have dramatci impact on optimizations.

## Slide 5: 4-way Butterfly Node
function Vector#(4,Complex) bfly4
(Vector#(4,Complex) t, Vector#(4,Complex) x);
t’s (twiddle coefficients) are mathematically derivable constants for each bfly4 and depend upon the position of bfly4 the in the network
FFT and IFFT calculations differ only in the use of Twiddle coefficients in various butterfly nodes
*
*
*
*
+
-
-
+
+
-
-
+
*i
x0
x1
x2
x3
t0
t1
t2
t3

## Slide 6: BSV code: 4-way Butterfly
function Vector#(4,Complex#(s)) bfly4
(Vector#(4,Complex#(s)) t, Vector#(4,Complex#(s)) x);
Vector#(4,Complex#(s)) m, y, z;
m[0] = x[0] * t[0]; m[1] = x[1] * t[1];
m[2] = x[2] * t[2]; m[3] = x[3] * t[3];
y[0] = m[0] + m[2]; y[1] = m[0] – m[2];
y[2] = m[1] + m[3]; y[3] = i*(m[1] – m[3]);
z[0] = y[0] + y[2]; z[1] = y[1] + y[3];
z[2] = y[0] – y[2]; z[3] = y[1] – y[3];
return(z);
endfunction
Polymorphic code: works on any type of numbers for which *, + and - have been defined
*
*
*
*
+
-
-
+
+
-
-
+
*i
m
y
z
Note: Vector does not mean storage; just a group of wires with names

## Slide 7: Language notes: Sequential assignments
Sometimes it is convenient to reassign a variable (x is zero every where except in bits 4 and 8):
This will usually result in introduction of muxes in a circuit as the following example illustrates:
Bit#(32) x = 0;
let y = x+1;
if(p) x = 100;
let z = x+1;
x
0
100
p
+1
+1
z
y
Bit#(32) x = 0;
x[4] = 1; x[8] = 1;

## Slide 8: Complex Arithmetic
Addition
  zR = xR + yR
  zI = xI + yI
Multiplication
  zR = xR * yR - xI * yI
  zI = xR * yI + xI * yR

## Slide 9: Representing complex numbers as a struct
typedef struct{
Int#(t) r;
Int#(t) i;
} Complex#(numeric type t) deriving (Eq,Bits);
Notice the Complex type is parameterized by the size of Int chosen to represent its real and imaginary parts
If x is a struct then its fields can be selected by writing x.r and x.i

## Slide 10: BSV code for Addition
typedef struct{
Int#(t) r;
Int#(t) i;
} Complex#(numeric type t) deriving (Eq,Bits);
function Complex#(t) cAdd
(Complex#(t) x, Complex#(t) y);
Int#(t) real = x.r + y.r;
Int#(t) imag = x.i + y.i;
return(Complex{r:real, i:imag});
endfunction
What is the type of this + ?

## Slide 11: Overloading (Type classes)
The same symbol can be used to represent different but related operators using Type classes
A type class groups a bunch of types with similarly named operations. For example, the type class Arith requires that each type belonging to this type class has operators +,-, *, / etc. defined
We can declare Complex type to be an instance of Arith type class

## Slide 12: Overloading +, *
instance Arith#(Complex#(t));
function Complex#(t) \+
(Complex#(t) x, Complex#(t) y);
Int#(t) real = x.r + y.r;
Int#(t) imag = x.i + y.i;
return(Complex{r:real, i:imag});
endfunction
function Complex#(t) \*
(Complex#(t) x, Complex#(t) y);
Int#(t) real = x.r*y.r – x.i*y.i;
Int#(t) imag = x.r*y.i + x.i*y.r;
return(Complex{r:real, i:imag});
endfunction
…
endinstance
The context allows the compiler to pick the appropriate definition of an operator

## Slide 13: Combinational IFFT
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
stage_f function
repeat stage_f three times
function Vector#(64, Complex#(n)) stage_f
(Bit#(2) stage, Vector#(64, Complex#(n)) stage_in);
function Vector#(64, Complex#(n)) ifft
(Vector#(64, Complex#(n)) in_data);

## Slide 14: BSV Code: Combinational IFFT
function Vector#(64, Complex#(n)) ifft
(Vector#(64, Complex#(n)) in_data);
//Declare vectors
Vector#(4,Vector#(64, Complex#(n))) stage_data;
stage_data[0] = in_data;
for (Bit#(2) stage = 0; stage < 3; stage = stage + 1)
stage_data[stage+1] = stage_f(stage,stage_data[stage]);
return(stage_data[3]);
endfunction
The for-loop is unfolded and stage_f is inlined during static elaboration
Note: no notion of loops or procedures during execution

## Slide 15: BSV Code: Combinational IFFT- Unfolded
function Vector#(64, Complex#(n)) ifft
(Vector#(64, Complex#(n)) in_data);
//Declare vectors
Vector#(4,Vector#(64, Complex#(n))) stage_data;
stage_data[0] = in_data;
for (Bit#(2) stage = 0; stage < 3; stage = stage + 1)
stage_data[stage+1] = stage_f(stage,stage_data[stage]);
return(stage_data[3]);
endfunction
Stage_f can be inlined now; it could have been inlined before loop unfolding also.
Does the order matter?
stage_data[1] = stage_f(0,stage_data[0]);
stage_data[2] = stage_f(1,stage_data[1]);
stage_data[3] = stage_f(2,stage_data[2]);

## Slide 16: BSV Code for stage_f
function Vector#(64, Complex#(n)) stage_f
(Bit#(2) stage, Vector#(64, Complex#(n)) stage_in);
Vector#(64, Complex#(n)) stage_temp, stage_out;
for (Integer i = 0; i < 16; i = i + 1)
begin
Integer idx = i * 4;
Vector#(4, Complex#(n)) x;
x[0] = stage_in[idx]; x[1] = stage_in[idx+1];
x[2] = stage_in[idx+2]; x[3] = stage_in[idx+3];
let twid = getTwiddle(stage, fromInteger(i));
let y = bfly4(twid, x);
stage_temp[idx] = y[0]; stage_temp[idx+1] = y[1];
stage_temp[idx+2] = y[2]; stage_temp[idx+3] = y[3];
end
//Permutation
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
twid’s are mathematically derivable constants

## Slide 17: Higher-order functions: Stage functions f1, f2 and f3
function f0(x)= stage_f(0,x);
function f1(x)= stage_f(1,x);
function f2(x)= stage_f(2,x);
What is the type of f0(x) ?
function Vector#(64, Complex) f0
(Vector#(64, Complex) x);

## Slide 18: Suppose we want to reduce the area of the circuit
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
Reuse the same circuit three times
to reduce area

## Slide 19: Reusing a combinational block
f
g
we expect:
Throughput to
Area to
f
f
g
decrease – less parallelism
The clock needs to run faster for the same throughput
decrease – reusing a block
Introduce state elements to hold intermediate values

## Slide 20: Folded IFFT: Reusing the stage combinational circuit
in0
…
in1
in2
in63
in3
in4
out0
…
out1
out2
out63
out3
out4
…
Bfly4
Bfly4
Permute
Stage Counter

## Slide 21: Input and Output FIFOs
If IFFT is implemented as a sequential circuit it may take several cycles to process an input
Sometimes it is convenient to think of input and output of a combinational function being connected to FIFOs
FIFO operations:
  enq – when the FIFO is not full
  deq, first – when the FIFO is not empty
  These operations can be performed only when the guard condition is satisfied
inQ
outQ
IFFT

## Slide 22: Folded implementation rules
rule foldedEntry if (stage==0);
sReg <= f(stage, inQ.first()); stage <= stage+1;
inQ.deq();
endrule
rule foldedCirculate if (stage!=0)&(stage<(n-1));
sReg <= f(stage, sReg); stage <= stage+1;
endrule
rule foldedExit if (stage==n-1);
outQ.enq(f(stage, sReg)); stage <= 0;
endrule
x
sReg
inQ
f
outQ
stage
Disjoint firing conditions
Each rule has some additional implicit guard conditions associated with FIFO operations
notice stage is a dynamic parameter now!
no for-loop

## Slide 23: Folded implementation expressed as a single rule
rule folded-pipeline (True);
let sxIn = ?;
if (stage==0)
begin sxIn= inQ.first(); inQ.deq(); end
else sxIn= sReg;
let sxOut = f(stage,sxIn);
if (stage==n-1) outQ.enq(sxOut);
else sReg <= sxOut;
stage <= (stage==n-1)? 0 : stage+1;
endrule
x
sReg
inQ
f
outQ
stage

## Slide 24: Shared Circuit
The Twiddle constants can be expressed in a table or in a case or nested case expression
stage
getTwiddle0
getTwiddle1
getTwiddle2
twid
The rest of stage_f, i.e. Bfly-4s and permutations (shared)
sx

## Slide 25: Pipelining Combinational IFFT
Lot of area and long combinational delay
Folded or multi-cycle version can save area and reduce the combinational delay but throughput per clock cycle gets worse
Pipelining: a method to increase the circuit throughput by evaluating multiple IFFTs
in0
…
in1
in2
in63
in3
in4
Bfly4
Bfly4
Bfly4
x16
Bfly4
Bfly4
Bfly4
…
Bfly4
Bfly4
Bfly4
…
out0
…
out1
out2
out63
out3
out4
Permute
Permute
Permute
IFFTi
IFFTi-1
IFFTi+1
3 different datasets in the pipeline
Next lecture

## Slide 26: Design comparison
inQ
outQ
f2
f1
f3
Combinational
C
inQ
outQ
f2
f1
f3
Pipeline
P
inQ
outQ
f
Folded
F
Clock?
Area?
Throughput?
Clock: C < P  F
Area: F < C < P
Throughput: F < C < P

## Slide 27: Area estimates Tool: Synopsys Design Compiler
Comb. FFT
  Combinational area: 16536
  Noncombinational area: 9279
Folded FFT
  Combinational area: 29330
  Noncombinational area: 11603
Pipelined FFT
  Combinational area: 20610
  Noncombinational area: 18558
Explanation: Because of constant propagation optimization, each bfly4 gets reduced by 60% when twiddle factors are specified. Folded design disallows this optimization because of the sharing of bfly4’s
Why is folded implementation not smaller?
Are the results surprising?

## Slide 28: Syntax: Vector of Registers
Register
  suppose x and y are both of type Reg. Then
  x <= y means x._write(y._read())
Vector of Int
  x[i] means sel(x,i)
  x[i] = y[j] means x = update(x, i, sel(y,j))
Vector of Registers
  x[i] <= y[j] does not work. The parser thinks it means (sel(x,i)._read)._write(sel(y,j)._read), which will not type check
  (x[i]) <= y[j] parses as sel(x,i)._write(sel(y,j)._read), and works correctly
Don’t ask me why

## Slide 29: Optional: Superfolded FFT

## Slide 30: Superfolded IFFT: Just one Bfly-4 node!
in0
…
in1
in2
in63
in3
in4
out0
…
out1
out2
out63
out3
out4
Bfly4
Permute
Index == 15?
Index:
0 to 15
64, 2-way Muxes
4, 16-way Muxes
4, 16-way DeMuxes
Stage
0 to 2
f will be invoked for 48 dynamic values of stage; each invocation will modify 4 numbers in sReg
after 16 invocations a permutation would be done on the whole sReg
Optional

## Slide 31: Superfolded IFFT: stage function f
function Vector#(64, Complex) stage_f
(Bit#(2) stage, Vector#(64, Complex) stage_in);
Vector#(64, Complex#(n)) stage_temp, stage_out;
for (Integer i = 0; i < 16; i = i + 1)
begin Bit#(2) stage
Integer idx = i * 4;
let twid = getTwiddle(stage, fromInteger(i));
let y = bfly4(twid, stage_in[idx:idx+3]);
stage_temp[idx] = y[0]; stage_temp[idx+1] = y[1];
stage_temp[idx+2] = y[2]; stage_temp[idx+3] = y[3];
end
//Permutation
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
Bit#(2+4) (stage,i)
should be done only when i=15

## Slide 32: Code for the Superfolded stage function
Function Vector#(64, Complex) f
(Bit#(6) stagei, Vector#(64, Complex) stage_in);
let i = stagei `mod` 16;
let twid = getTwiddle(stagei `div` 16, i);
let y = bfly4(twid, stage_in[i:i+3]);
let stage_temp = stage_in;
stage_temp[i] = y[0];
stage_temp[i+1] = y[1];
stage_temp[i+2] = y[2];
stage_temp[i+3] = y[3];
let stage_out = stage_temp;
if (i == 15)
for (Integer i = 0; i < 64; i = i + 1)
stage_out[i] = stage_temp[permute[i]];
return(stage_out);
endfunction
One Bfly-4 case