## Slide 1
Constructive Computer Architecture:
Pipelining combinational circuits
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Contents
Inelastic versus Elastic pipelines
The role of FIFOs
Concurrency issues
BSV Concepts
  The Maybe Type
  Concurrency analysis

## Slide 4: Complex Combinational Functions
Lot of area and long combinational delay
Folded or multi-cycle version can save area and reduce the combinational delay but throughput per clock cycle gets worse
Pipelining: a method to increase the circuit throughput by evaluating multiple inputs
xi
xi-1
xi+1
3 different datasets in the pipeline
f0
f1
f2

## Slide 5: Inelastic vs Elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
x
sReg1
inQ
f0
f1
f2
sReg2
outQ
Inelastic: all pipeline stages move synchronously
Elastic: A pipeline stage can process data if its input FIFO is not empty and output FIFO is not Full
Most complex processor pipelines are a combination of the two styles

## Slide 6: Inelastic vs Elastic Pipelines
Inelastic pipeline:
  typically only one rule or mutually exclusive rules; the designer controls precisely which activities go on in parallel
  downside: The designer must program the starting and draining of the pipeline. The rule can get complicated -- easy to make mistakes; difficult to make changes
Elastic pipeline:
  several smaller rules, each easy to write, easier to make changes
  downside: sometimes rules do not fire concurrently when they should

## Slide 7: Inelastic pipeline
x
sReg1
inQ
f0
f1
f2
sReg2
outQ
rule sync-pipeline (True);
inQ.deq();
sReg1 <= f0(inQ.first());
sReg2 <= f1(sReg1);
outQ.enq(f2(sReg2));
endrule
This rule can fire only if
Atomicity: Either all or none of the state elements inQ, outQ, sReg1 and sReg2 will be updated
- inQ has an element
- outQ has space

## Slide 8: FIFO Module: methods with guarded interfaces
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
fifo.enq(x); // action method
fifo.deq(); // action method
y=fifo.first() // value method

## Slide 9: Inelastic pipeline Making implicit guard conditions explicit
x
sReg1
inQ
f0
f1
f2
sReg2
outQ
rule sync-pipeline (!inQ.empty() && !outQ.full);
inQ.deq();
sReg1 <= f0(inQ.first());
sReg2 <= f1(sReg1);
outQ.enq(f2(sReg2));
endrule
Suppose sReg1 and sReg2 have data, outQ is not full but inQ is empty. What behavior do you expect?
Leave green and red data in the pipeline?

## Slide 10: Pipeline bubbles
x
sReg1
inQ
f0
f1
f2
sReg2
outQ
rule sync-pipeline (True);
inQ.deq();
sReg1 <= f0(inQ.first());
sReg2 <= f1(sReg1);
outQ.enq(f2(sReg2));
endrule
Red and Green tokens must move even if there is nothing in inQ!
Modify the rule to deal with these conditions
Also if there is no token in sReg2 then nothing should be enqueued in the outQ
Valid bits or
the Maybe type

## Slide 11: Explicit encoding of Valid/Invalid data
rule sync-pipeline (True);
if (inQ.notEmpty())
begin sReg1 <= f0(inQ.first()); inQ.deq();
sReg1f <= Valid end
else sReg1f <= Invalid;
sReg2 <= f1(sReg1); sReg2f <= sReg1f;
if (sReg2f == Valid) outQ.enq(f2(sReg2));
endrule
sReg1
sReg2
x
inQ
f0
f1
f2
outQ
Valid/Invalid
typedef union tagged {void Valid; void Invalid;
} Validbit deriving (Eq, Bits);

## Slide 12: When is this rule enabled?
inQ sReg1f sReg2f outQ
NE V V NF
NE V V F
NE V I NF
NE V I F
NE I V NF
NE I V F
NE I I NF
NE I I F
E V V NF
E V V F
E V I NF
E V I F
E I V NF
E I V F
E I I NF
E I I F
yes
No
Yes
Yes
Yes
No
Yes
yes
yes
No
Yes
Yes
Yes
No
Yes1
yes
Yes1 = yes but no change
inQ sReg1f sReg2f outQ
rule sync-pipeline (True);
if (inQ.notEmpty())
begin sReg1 <= f0(inQ.first()); inQ.deq();
sReg1f <= Valid end
else sReg1f <= Invalid;
sReg2 <= f1(sReg1); sReg2f <= sReg1f;
if (sReg2f == Valid) outQ.enq(f2(sReg2));
endrule
sReg1
sReg2
inQ
f0
f1
f2
outQ
NE = Not Empty; NF = Not Full

## Slide 13: The Maybe type A useful type to capture valid/invalid data
typedef union tagged {
void Invalid;
data_T Valid;
} Maybe#(type data_T);
data
valid/invalid
Registers contain Maybe type values
Some useful functions on Maybe type:
isValid(x) returns true if x is Valid
fromMaybe(d,x) returns
the data value in x if x is Valid
the default value d if x is Invalid

## Slide 14: Using the Maybe type
typedef union tagged {
void Invalid;
data_T Valid;
} Maybe#(type data_T);
data
valid/invalid
Registers contain Maybe type values
rule sync-pipeline if (True);
if (inQ.notEmpty())
begin sReg1 <= Valid f0(inQ.first()); inQ.deq(); end
else sReg1 <= Invalid;
sReg2 <= isValid(sReg1)? Valid f1(fromMaybe(d, sReg1)) :
Invalid;
if isValid(sReg2) outQ.enq(f2(fromMaybe(d, sReg2)));
endrule

## Slide 15: Pattern-matching: An alternative syntax to extract datastructure components
The &&& is a conjunction, and allows pattern-variables to come into scope from left to right
case (m) matches
tagged Invalid : return 0;
tagged Valid .x : return x;
endcase
if (m matches (Valid .x) &&& (x > 10))
typedef union tagged {
void Invalid;
data_T Valid;
} Maybe#(type data_T);
x will get bound to the appropriate part of m

## Slide 16: The Maybe type data using the pattern matching syntax
typedef union tagged {
void Invalid;
data_T Valid;
} Maybe#(type data_T);
data
valid/invalid
Registers contain Maybe type values
rule sync-pipeline if (True);
if (inQ.notEmpty())
begin sReg1 <= Valid (f0(inQ.first())); inQ.deq(); end
else sReg1 <= Invalid;
case (sReg1) matches
tagged Valid .sx1: sReg2 <= Valid f1(sx1);
tagged Invalid: sReg2 <= Invalid; endcase
case (sReg2) matches
tagged Valid .sx2: outQ.enq(f2(sx2));
endcase
endrule
sx1 will get bound to the appropriate part of sReg1

## Slide 17: Generalization: n-stage pipeline
rule sync-pipeline (True);
if (inQ.notEmpty())
begin sReg[0]<= Valid f(1,inQ.first());inQ.deq();end
else sReg[0]<= Invalid;
for(Integer i = 1; i < n-1; i=i+1) begin
case (sReg[i-1]) matches
tagged Valid .sx: sReg[i] <= Valid f(i,sx);
tagged Invalid: sReg[i] <= Invalid; endcase end
case (sReg[n-2]) matches
tagged Valid .sx: outQ.enq(f(n-1,sx)); endcase
endrule
sReg[0]
inQ
sReg[1]
outQ
x
f(0)
f(1)
f(2)
f(n-1)
...
sReg[n-2]

## Slide 18: Elastic pipeline Use FIFOs instead of pipeline registers
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1 if (True);
fifo1.enq(f1(inQ.first());
inQ.deq(); endrule
rule stage2 if (True);
  fifo2.enq(f2(fifo1.first());
fifo1.deq(); endrule
rule stage3 if (True);
outQ.enq(f3(fifo2.first());
fifo2.deq(); endrule
What is the firing condition for each rule?
Can tokens be left inside the pipeline?
No need for Maybe types

## Slide 19: Firing conditions for reach rule
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
inQ fifo1 fifo2 outQ
NE NE,NF NE,NF NF
NE NE,NF NE,NF F
NE NE,NF NE,F NF
NE NE,NF NE,F F
….
Yes Yes Yes
Yes Yes No
Yes No Yes
Yes No No
….
rule1 rule2 rule3
This is the first example we have seen where multiple rules may be ready to execute concurrently
Can we execute multiple rules together?

## Slide 20: Informal analysis
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
inQ fifo1 fifo2 outQ
NE NE,NF NE,NF NF
NE NE,NF NE,NF F
NE NE,NF NE,F NF
NE NE,NF NE,F F
….
Yes Yes Yes
Yes Yes No
Yes No Yes
Yes No No
….
rule1 rule2 rule3
FIFOs must permit concurrent enq and deq for all three rules to fire concurrently

## Slide 21: Concurrency when the FIFOs do not permit concurrent enq and deq
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
not empty
not empty
&
not full
not empty
&
not full
not full
At best alternate stages in the pipeline will be able to fire concurrently

## Slide 22: Pipelined designs expressed using Multiple rules
If rules for different pipeline stages never fire in the same cycle then the design can hardly be called a pipelined design
If all the enabled rules fire in parallel every cycle then, in general, wrong results can be produced

## Slide 23: BSV Execution Model
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
A legal behavior of a BSV program can be explained by observing the state updates obtained by applying only one rule at a time
Highly non-deterministic; User annotations can be used in rule selection
One-rule-at-time semantics

## Slide 24: Concurrent scheduling of rules
The one-rule-at-a-time semantics plays the central role in defining functional correctness and verification but for meaningful hardware design it is necessary to execute multiple rules concurrently without violating the one-rule-at-a-time semantics
What do we mean by concurrent scheduling?
  First - some hardware intuition
  Later – the semantics of concurrent scheduling

## Slide 25: Hardware intuition for concurrent scheduling

## Slide 26: Rule Execution
Application of a rule modifies some state elements of the system in a deterministic manner
current
state
next
state
values
next state
computation
f
x
f
x
reg en’s
nextState

## Slide 27: Executing multiple rules in one clock cycle
Sequential composition preserves the one-rule-at-a-time semantics but generally increases the critical combinational path
Parallel composition does not create longer combinational paths but may not preserve the one-rule-at-a-time semantics
current
state
next
state
values
rule2
f
x
f
x
rule 1
Next
State
mux
Reg
en
Sequential composition
Forwards old values unless updated
Parallel composition
current
state
next
state
values
rule2
f
x
f
x
rule 1
merge
NextState
Reg en
ensures that no double updates are made on any register

## Slide 28: Violation of sequential semantics
rule ra
x <= y;
endrule
rule rb
y <= x;
endrule
Suppose initially x is x0 and y is y0
{x0,y0} ra {y0,y0} rb {y0,y0}
{x0,y0} rb {x0,x0} ra {x0,x0}
{x0,y0} rb||ra {y0,x0}
Parallel execution does not behave like either ra<rb or rb<ra
We do not want to allow concurrent execution of ra and rb
next time compiler analysis to determine which rules can be executed concurrently