## Slide 1: Constructive Computer Architecture: Concurrency Analysis and Designing FIFOs
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Contents
Hardware Intuition
Compiler analysis
Limitations of Registers
EHRs – Ephemeral History Registers
FIFOs with concurrent enq and deq

## Slide 4: some insight into Concurrent rule firing
There are more intermediate states in the rule semantics (a state after each rule step)
In the HW, states change only at clock edges
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 5: Parallel execution reorders reads and writes
In the rule semantics, each rule sees (reads) the effects (writes) of previous rules
In the HW, rules only see the effects from previous clocks, and only affect subsequent clocks
Rules
HW
clocks
rule
steps
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes

## Slide 6: Correctness
Rules are allowed to fire in parallel only if the net state change is equivalent to sequential rule execution
Consequence: the HW can never reach a state unexpected in the rule semantics
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 7: One-rule-at-a-time semantics
Rule execution ()
Legal states: S is a legal state if and only if given an initial state S0 , there exists a sequence of rules rj1,…., rjn such that S= rjn(…(rj1(S0))…)
Rule r a  P <S,{}> |- a  U
P |- S  update(S,U)
Where update(S,U)[x] = if (x,v)  U the v else S[x]
P |- S0 * S
S  LegalState(P,S0)
where * is the transitive reflexive closure of 

## Slide 8: Concurrent scheduling of rules
rule r1 a1 and rule r2 a2 can be scheduled concurrently, preserving one-rule-at-a-time semantics, if and only if
  for all S. (a1|a2)(S) = either a2(a1(S)) or a1(a2(S))
rule r1 a1 to rule rn an can be scheduled concurrently, preserving one-rule-at-a-time semantics, if and only if there exists a permutation (p1,…,pn) of (1,…,n) such that
  for all S. (a1|…|an)(S) = apn(…(ap1(S))

## Slide 9: Compiler test for concurrent scheduling
Rules ra and rb are conflict free (CF) if
  (RS(ra)WS(rb) = )  (RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
Rules ra and rb are sequentially composable (SC) (ra<rb) if
(RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
Rules ra and rb conflict if they are not CF or SC
Let RS(r) be the set of registers rule r may read
Let WS(r) be the set of registers rule r may write
Non-conflicting rules can be executed concurrently without violating the one-rule-at-a-time-semantics
James Hoe, Ph.D., 2000
Theorem: If ra < rb then for all S. (a|b) (S) = b(a(S))

## Slide 10: Example 1: Compiler Analysis
rule ra if (z>10);
x <= x+1;
endrule
rule rb if (z>20);
y <= y+2;
endrule
RS(ra) =
WS(ra) =
RS(rb) =
WS(rb) =
RS(ra)WS(rb) = RS(rb)WS(ra) = WS(ra)WS(rb) =
{z, x}
{x}
{z, y}
{y}



ra and rb are Conflict free
Rules ra and rb can be scheduled together without violating the one-rule-at-a-time-semantics
{x0,y0,30} ra {x0+1,y0,30} rb {x0+1,y0+2,30}
{x0,y0,30} rb {x0,y0+2,30} ra {x0+1,y0+2,30}
{x0,y0,30} rb|ra {x0+1,y0+2,30}
{x0,y0,15} ra {x0+1,y0,15} rb {x0+1,y0,15}
{x0,y0,15} rb {x0,y0,15} ra {x0+1,y0,15}
{x0,y0,15} rb|ra {x0+1,y0,15}

## Slide 11: Example 2: Compiler Analysis
RS(ra) =
WS(ra) =
RS(rb) =
WS(rb) =
RS(ra)WS(rb) = RS(rb)WS(ra) = WS(ra)WS(rb) =
{z, y}
{x}
{z, x}
{y}
y
x

ra and rb are neither CF or SC
Rules ra and rb cannot be scheduled together without violating the one-rule-at-a-time-semantics
rule ra if (z>10);
x <= y+1;
endrule
rule rb if (z>20);
y <= x+2;
endrule
{x0,y0,30} ra {y0+1,y0,30} rb {y0+1,y0+1+2,30}
{x0,y0,30} rb {x0,x0+2,30} ra {x0+2+1,x0+2,30}
{x0,y0,30} rb|ra {y0+1,x0+2,30}

## Slide 12: Example 3: Compiler Analysis
RS(ra) =
WS(ra) =
RS(rb) =
WS(rb) =
RS(ra)WS(rb) = RS(rb)WS(ra) = WS(ra)WS(rb) =
{z, y}
{x}
{z, y}
{y}
y


ra and rb are SC (ra<rb)
Rules ra and rb can be scheduled together without violating the one-rule-at-a-time-semantics
rule ra if (z>10);
x <= y+1;
endrule
rule rb if (z>20);
y <= y+2;
endrule
{x0,y0,30} ra {y0+1,y0,30} rb {y0+1,y0+2,30}
{x0,y0,30} rb {x0,y0+2,30} ra {y0+2+1,y0+2,30}
{x0,y0,30} ra|rb {y0+1,y0+2,30}

## Slide 13: Analysis of method calls for concurrent scheduling
Conflict analysis has to be performed in terms of the properties of the ports of a module rather than the module (e.g. register) it self
Register conflicts:
Let mcalls(x) represent the (multi-)set of methods called by x where x may be a method definition or a rule
 | reg.r | reg.w
reg.r | CF | <
reg.w | > | C

## Slide 14: Conflict ordering
This permits us to take intersections of conflict information, e.g.,
  {>}{<,>} = {>}
  {>}{<} = {}
CF = {<,>}
{<} {>}
C = {}

## Slide 15: Deriving the Conflict Matrix (CM) of a module
Let g1 and g2 be the two methods defined by a module, such that
  mcalls(g1)={g11,g12...g1n}
  mcalls(g2)={g21,g22...g2m}
Derivation
  CM[g1,g2] = conflict(g11,g21)  conflict(g11,g22) ...
   conflict(g12,g21)  conflict(g12,g22) ...
  …
   conflict(g1n,g21)  conflict(g12,g22) ...
  Conflict(x,y) = if x and y are methods of the same
  module then CM[x,y] else {<,>}
Conflict relation is not transitive
  m1.g1 < m2.g2, m2.g2 < m3.g3 does not imply m1.g1 < m3.g3
Compiler can derive the CM for a module by starting with the innermost modules in the module instantiation tree

## Slide 16: Shorthand notation for Conflict relation
h1<h2  conflict(h1, h2) = {<}
h1>h2  conflict(h1, h2) = {>}
h1 CF h2  conflict(h1, h2) = {<,>}
h1 C h2  conflict(h1, h2) = {}

## Slide 17: One-Element FIFO
module mkCFFifo (Fifo#(1, t));
Reg#(t) data <- mkRegU;
Reg#(Bool) full <- mkReg(False);
method Action enq(t x) if (!full);
full <= True; data <= x;
endmethod
method Action deq if (full);
full <= False;
endmethod
method t first if (full);
return (data);
endmethod
endmodule
enq and deq cannot even be enabled together much less fire concurrently!
n
not empty
not full
rdy
enab
rdy
enab
enq
deq
Fifo
module
Can enq and deq execute concurrently

## Slide 18: Two-Element FIFO
module mkCFFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False);
method Action enq(t x) if (!vb);
if va then begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if (va);
if vb then begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
method t first if (va);
return da;
endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
db da
Can enq and deq be ready concurrently?
Do enq and deq conflict?
yes, both read/write the same elements
yes

## Slide 19: Limitations of registers
Limitations of a language with only the register primitive
  No communication between rules or between methods or between rules and methods in the same atomic action i.e. clock cycle
  Can’t express a FIFO with concurrent enq and deq

## Slide 20: EHR: Ephemeral History Register
A new primitive element to design modules with concurrent methods

## Slide 21: EHR: Register with a bypass Interface
r[0] < w[0]
w[0] < r[1]
r[1] returns:
– the current state if write is not enabled
– the value being written if write is enabled
D
Q
0
1
w[0].data
w[0].en
r[0]
normal
bypass
r[1]

## Slide 22: Ephemeral History Register (EHR) Dan Rosenband [MEMOCODE’04]
D
Q
0
1
w[0].data
w[0].en
r[0]
normal
bypass
r[1]
0
1
w[1].data
w[1].en
r[0] < w[0]
w[i+1] takes precedence over w[i]
w[0] < w[1] < ….
r[1] < w[1]

## Slide 23: Conflict Matrix of Primitive modules: Registers and EHRs
 | EHR.r0 | EHR.w0 | EHR.r1 | EHR.w1
EHR.r0 | CF | < | < | <
EHR.w0 | > | C | < | <
EHR.r1 | > | > | CF | <
EHR.w1 | > | > | > | C
 | reg.r0 | reg.w0
reg.r0 | CF | <
reg.w0 | > | C
Register
EHR

## Slide 24: Designing FIFOs using EHRs
Conflict-Free FIFO: Both enq and deq are permitted concurrently as long as the FIFO is not-full and not-empty
  The effect of enq is not visible to deq, and vise versa
Pipeline FIFO: An enq into a full FIFO is permitted provided a deq from the FIFO is done simultaneously
Bypass FIFO: A deq from an empty FIFO is permitted provided an enq into the FIFO is done simultaneously

## Slide 25: One-Element Pipelined FIFO
module mkPipelineFifo(Fifo#(1, t)) provisos(Bits#(t, tSz));
Reg#(t) data <- mkRegU;
Ehr#(2, Bool) full <- mkEhr(False);
method Action enq(t x) if(!full[1]);
data <= x;
full[1] <= True;
endmethod
method Action deq if(full[0]);
full[0] <= False;
endmethod
method t first if(full[0]);
return data;
endmethod
endmodule
Desired behavior
deq < enq
first < deq
first < enq
No double write error
In any given cycle:
If the FIFO is not empty then simultaneous enq and deq are permitted;
Otherwise, only enq is permitted

## Slide 26: Deriving CM for One-Element Pipelined FIFO
module mkPipelineFifo(Fifo#(1, t)) provisos(Bits#(t, tSz));
Reg#(t) data <- mkRegU;
Ehr#(2, Bool) full <- mkEhr(False);
method Action enq(t x) if(!full[1]);
data <= x;
full[1] <= True;
endmethod
method Action deq if(full[0]);
full[0] <= False;
endmethod
method t first if(full[0]);
return data;
endmethod
endmodule
mcalls(enq) =
mcalls(deq) =
mcalls(first) =
{full.r1, data.w, full.w1}
{full.r0, full.w0}
{full.r0, data.r}

## Slide 27: CM for One-Element Pipelined FIFO
mcalls(enq) = {full.r1, data.w, full.w1}
mcalls(deq) = {full.r0, full.w0}
mcalls(first) = {full.r0, data.r}
CM[enq,deq] =
= {>}  {>}
 {<,>}  {<,>}
 {>}  {>}
= {>}
conflict[full.r1,full.r0]  conflict[full.r1,full.w0]
 conflict[data.w,full.r0]conflict[data.w,full.w0]
 conflict[full.w1,full.r0]conflict[full.w1,full.w0]
This is what we expected!

## Slide 28: One-Element Bypass FIFO
module mkBypassFifo(Fifo#(1, t)) provisos(Bits#(t, tSz));
Ehr#(2, t) data <- mkEhr(?);
Ehr#(2, Bool) full <- mkEhr(False);
method Action enq(t x) if(!full[0]);
data[0] <= x;
full[0] <= True;
endmethod
method Action deq if(full[1]);
full[1] <= False;
endmethod
method t first if(full[1]);
return data;
endmethod
endmodule
Desired behavior
enq < deq
first < deq
enq < first
No double write error
In any given cycle:
If the FIFO is not full then simultaneous enq and deq are permitted;
Otherwise, only deq is permitted

## Slide 29: Two-Element Conflict-free FIFO
module mkCFFifo(Fifo#(2, t)) provisos(Bits#(t, tSz));
Ehr#(2, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(2, Bool) vb <- mkEhr(False);
rule canonicalize if(vb[1] && !va[1]);
da[1] <= db[1];
va[1] <= True; vb[1] <= False; endrule
method Action enq(t x) if(!vb[0]);
db[0] <= x; vb[0] <= True; endmethod
method Action deq if (va[0]);
va[0] <= False; endmethod
method t first if(va[0]);
return da[0]; endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
db da
Desired behavior
enq CF deq
first < deq
first CF enq
In any given cycle:
Simultaneous enq and deq are permitted only if the FIFO is not full and not empty