## Slide 1: Constructive Computer Architecture: Hardware Compilation of Bluespec
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Contents
KBS syntax and well-formed programs
Hardware representation
  modules and method calls
Generating Hardware
  Linking
The Scheduler

## Slide 4: Bluespec: Two-Level Compilation
Object code
(Verilog/C)
Guarded Atomic Actions
(Rules, Modules)
Method & Rule conflict analysis
Rule scheduling
James Hoe & Arvind
@MIT 1997-2000
Bluespec
(Objects, Types,
Higher-order functions)
Level 1 compilation
Type checking
Massive partial evaluation and static elaboration
Level 2 synthesis
Lennart Augustsson
@Sandburst 2000-2002
Initially called Term Rewriting Systems (TRS)

## Slide 5: Static Elaboration
.exe
compile
design2
design3
design1
elaborate
w/params
run1
run1
run2.1
…
run1
run1
run3.1
…
run1
run1
run1.1
…
run w/
params
run w/
params
run1
run1
…
run
At compile time
  Inline function calls and unroll loops
  Instantiate modules with specific parameters
  Resolve polymorphism/overloading, perform most data structure operations
source
Software
Toolflow:
source
Hardware
Toolflow:

## Slide 6: Phase II compilation: From KBS1 to Circuits
We will assume that the type checking and static elaboration have been performed and all modules have been instantiated by the Phase I compiler

## Slide 7: KBS0: A simple language for describing Sequential ckts
<Program> ::= [rule <name> <a>]
[x <- mkReg] register instantiations
<a> ::= x.w(<e>) register assignment
| <a> | <a> parallel actions
| if (<e>) <a> conditional action
| let t = <e> in <a> binding
<e> ::= c constants
| t value of a binding
| x.r register read
| op(<e>,<e>) operators like And, Or, Not, +, ...
| let t = <e> in <e> binding
The names in the bindings (t …) can be defined only once
<a> is an action and <e> is an expression

## Slide 8: KBS1: KBS0+Modules
<Program> ::= [<Module>]
<Module> := Module <name> names; M, mkReg, mkFoo,…
[x <- mkReg] register instantiations; x,y..
[m <- <mkM>] module M instantiations; m,…
[rule <name> <a>] rules to describe behavior
[valueMethod <name> (<id>*) = <e>] interface
[actionMethod <name> (<id>*) = <a>] methods
<a> ::= KBS0 action
| m.g(<e>) call to action method m.g
<e> ::= KBS0 expression
| m.f(<e>) call to value method m.f
* Means zero or one occurrence

## Slide 9: KBS1EHR: KBS1+EHRs
<Program> ::= [<Module>]
<Module> := Module <name> names; M, mkReg, mkFoo,…
[x <- mkReg] register instantiations; x,y..
[x <- mkEHR] EHR instantiations; x,y..
[m <- <mkM>] module M instantiations; m,…
[rule <name> <a>] rules to describe behavior
[valueMethod <name> (<id>*) = <e>] interface
[actionMethod <name> (<id>*) = <a>] methods
<a> ::= KBS1 action
| x.w0(<e>) | x.w1 (<e>) … write actions into EHRs
<e> ::= KBS1 expression
| x.r0 | x.r1 reading EHRs
* Means zero or one occurrence

## Slide 10: Well-formed rules
A program with double-write error:
  x.w(5) | x.w(7)
Either such errors have to be detected during the execution or such programs have to be rejected at compile time
To avoid run-time errors the compiler accepts only those programs which follow two types of restrictions:
  A method (except for a zero-parameter value-method) can be called at most once by a rule
  Methods called by a rule must form a “partial order”

## Slide 11: Single-call restriction and zero-parameter value methods
Example
  y.w(x.r + x.r)
  This is a violation because x.r is called twice; however it can be transformed by the compiler into the following code
  let t = x.r in y.w(t+t)
We do not consider multiple calls to such methods as a violation

## Slide 12: Single-call restriction and conditional method calls
Example
  if (p) x.w(y.r + 1) ; if (q) x.w(z.r) ;
  This is a violation because x.w is called twice; however if the compiler can prove that p and q are mutually exclusive (e.g. q => !p) then only one of the calls will occur and there will be no violation
Compiler associates a predicate with each method call and accepts multiple calls to a method if it can prove that the predicates are mutually exclusive

## Slide 13: Syntax mandated Orderings
if (e) a
  mcalls(e) must precede the method calls in mcalls(a)
m.g(e)
  mcalls(e) must precede the method call m.g
let t = e in a
  mcalls(e) must precede the method calls in mcalls(a) if t is used in a
The compiler derives all the syntactic orderings and rejects a program if these orderings are violated by orderings imposed by the module definition

## Slide 14: Examples of violations
if (x.r1) x.w0(e)
  Syntax mandated:
  EHR mandated:
x.w0(y.r1) | y.w0(x.r1)
  Syntax mandated:
  EHR mandated:
contradiction!
  x.r1 < x.w0
  x.w0 < x.r1
y.r1 < x.w0, x.r1 < y.w0
  x.w0 < x.r1, y.w0 < y.r1
contradiction!

## Slide 15: Hardware representation registers and EHRs
A set of bindings can be thought of as a set of boxes which are connected by wires. A box represents an expression or the port of a module and wires are the variable names
w
r
en
arg
res
w1
r1
en
arg
res
w0
r0
en
arg
res
x_w_en
x_w_arg
Reg
EHR
x_r_res
x_w0_en
x_w0_arg
x_w1_en
x_w1_arg
x_r0_res
x_r1_res

## Slide 16: Hardware representation module
h
M1
h1
Scheduler
Rule r
Method h
en
arg
res
en
arg
res
h1.res
h1.en
h1.arg
r.en
h1.res
h1.arg
h1.en
h.en
M

## Slide 17: Method calls
A method call h(e) involves three sets of wires
  h_arg representing input argument (output of e)
  h_en, when true means that the method is to be used
  h_res representing the output of the method
The compiler collects all the input arguments for each method call as a sum of predicated expressions:
  h_arg = p1.e1+p2.e2+...
  h_en = p1 || p2 ||...
For each method h that can be called, the bindings are initialized with (h_arg, F.Bot) and (h_en, F)

## Slide 18: Hardware Compilation: Expressions
+
x_r_res
y_r1_res
t
=
0
t
Outputs of register x read, EHR y read
Expressions are structural and directly represent combinational circuits; some of their inputs are connected to x_r_res, m_g_res, …
let t = (x.r + y.r1) in t==0

## Slide 19: Hardware Compilation: Actions
x_w_en
…
y_w_arg
…
x_w_arg
…
.
.
y_w_en
…
Combine all the wires for each method call
m_g_arg = p1.e1 + p2.e2 + ....
m_g_en = p1 || p2 || ....
p
e1
e2
inputs are results of method calls
Actions use the circuits generated by compilation of expressions; their output wires are connected to x_w_en, x_w_arg, m_h_en, m_h_arg, …
if (p) (x.w(e1) | y.w(e2))

## Slide 20: Hardware Compilation: Rules and Methods
x_w_arg
…
r1
.
x_w_en
…
results
of r1 method calls
r2
.
…
r2_en
…
g
.
…
g_en
g_arg
results
of g’s method calls
to x_w_en
to x_w_arg
…
g_res

## Slide 21: Scheduler
A module may contain many rules but the Bluespec semantics dictates that all legal behaviors be derivable by executing only one rule at a time
Based on the conflict information about each of the called methods, a scheduler is constructed by the compiler to decide which rule(s) can be execute concurrently and the schedule indicates it choice by setting r_en, the enable signal, of the chosen rule.
The only dynamic input the scheduler needs is g_en for all of its defined methods g

## Slide 22: Hardware Compilation: Scheduler
x_w_arg
…
r1
.
x_w_en
…
results
of r1 method calls
r1_en
r2
.
…
r2_en
scheduler
…
g
.
…
g_en
g_arg
results
of g’s method calls
to x_w_en
to x_w_arg
…
g_res
r1_en
r2_en
g_en

## Slide 23: The scheduler circuit
Each specific scheduling strategy will result in a different scheduler circuit
For functional correctness, it is important that the scheduling circuit enforces the following invariant
  SC Invariant: Suppose r1, … rn are the rules of M being chosen to be scheduled in the current state, h1, … hk are the methods of M being called externally, then M preserves SC Invariant iff
  ∀i.∀(j > i).∀x ∈ mcalls(ri), ∀y ∈ mcalls(rj).
  ({<} ⊆ Conflict(x, y))
Theorem: If every module obeys the SC Invariant, then the system will obey one-rule-at-a-time semantics

## Slide 24: Detailed Hardware Compilation Procedure (optional)

## Slide 25: Compiling hardware
Expressions in KBS are structural and directly represent combinational circuits; some of their inputs are connected to x_r_res, m_g_res, …
Actions use the circuits generated by compilation of expressions; their output wires are connected to x_w_en, x_w_arg, m_h_en, m_h_arg, …
The compiler represents all connections as a set of bindings (next slide)
The compiler collects the bindings by threading the bindings through all rules and methods

## Slide 26: Syntax of bindings
B ::= [<b>]
b ::= <t> = <ei>
| <h>_arg = <pe>
| <h>_en = <ei>
ei ::= <c> | <t>
| <op>(<ei>, <ei>)
| <h>_res
pe ::= Bot
| <be>.<ei> // be is a boolean ei
| <be>.<pe>
| <pe> + <pe>

## Slide 27: Compiling Expressions
CE (bs,p,[[c]]) = (bs,c) ;
CE (bs,p,[[t]]) = (bs,t) ;
CE (bs,p,[[let t=e1 in e2]]) =
{ (bs1,e10) = CE(bs,p,[[e1]]);
(bs2,e20) = CE((bs1[t]:=p.e10),p,[[e2]]) return (bs2,e20)};
CE (bs,p,[[op(e1,e2)]]) =
{ (bs1,e10) = CE(bs,p,[[e1]]);
(bs2,e20) = CE(bs1,p,[[e2]]) return (bs2,op(e10,e20))};
CE (bs,p,[[h(e)]]) =
{ (bs1, e0) = CE(bs,p,[[e]]);
bs2 = (bs1[h_arg]:=bs1[h_arg]+p.e0);
bs3 = (bs2[h_en]:=bs2[h_en]+p.T) return (bs3,h_res)};
CE (bs,p,[[h()]]) = ((bs[h_en]:=bs[h_en]||p), h_res);
CE :: (Bindings, Predicate, Exp) -> (Bindings, Exp)
Notes: (let t1=m.f(0); t2=m.f(1) in if c then t1 else t2) will get rejected but not
if c then m.f(0) else m.f(1)

## Slide 28: Compiling Actions
CA (bs,p,[[let t=e in a]]) =
{ (bs1,e0) = CE(bs,p,[[e]]);
return CA((bs1[t]:=p.e0),p,[[a]])};
CA (bs,p,[[h(e)]]) =
{ (bs1,e0) = CE(bs,p,[[e]]);
bs2 = (bs1[h_arg]:=bs1[h_arg]+p.e0);
return (bs2[h_en]:=bs2[h_en]+p.T)};
CA (bs,p,[if (e) a]]) =
{ (bs1,e0) = CE(bs,p,[[e]])
return CA((bs1[t]:=p.e0),t,[[a]])}; where t is fresh
CA (bs,p,[[a1 | a2]]) =
{ bs1 = CA(bs,p,[[a1]]) return CA(bs1,p,[[a2]])}
CA :: (Bindings, Predicate, Action) -> Bindings

## Slide 29: Compiling Rules and Methods
CR : (Bindings, Rule) -> Bindings
CR (bs,[[rule r a]]) = CA(bs,r_en,[a]])
CVM : (Bindings, Value-method) -> Bindings
CVM (bs, [[valueMethod h(x)=e]]) =
{ bs0 = (bs[x]:= h_arg);
(bs1,e0) = CE(bs0,h_en,([[e]]);
bs2 = (bs1[h_res]:= e0); return bs2};
CAM : (Bindings, Action-method) -> Bindings
CAM (bs,[[actionMethod h(x)=a]]) =
CA((bs[x]:=h_arg),h_e,[[a]]);

## Slide 30: Compiling Modules and linking method calls
The compiler produces a set of bindings for each module by starting with an empty set of bindings and then threading the bindings produced by each rule and method defined inside the module
Modules are compiled inside out, that is, a module is compiled only after all the modules whose methods it calls have been compiled
For each method call h(e) the compiler links (connects) the bindings of the caller module with the bindings of the modules whose methods are called by connecting the wires representing the formal parameter h_x and actual parameter h_arg of method h

## Slide 31: One-rule-at-a-time semantics
Rule execution ()
Legal states: S is a legal state if and only if given an initial state S0 , there exists a sequence of rules rj1,…., rjn such that S= rjn(…(rj1(S0))…)
Rule r a  P <S,{}> |- a  U
P |- S  update(S,U)
Where update(S,U)[x] = if (x,v)  U the v else S[x]
P |- S0 * S
S  LegalState(P,S0)
where * is the transitive reflexive closure of 