## Slide 1
Constructive Computer Architecture:
Non-Pipelined Processors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Single-Cycle RISC Processor
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
Datapath and control are derived automatically from a high-level rule-based description
2 read & 1 write ports
separate Instruction & Data memories
As an illustrative example, we will use SMIPS, a 35-instruction subset of MIPS ISA without the delay slot
Notes: 3

## Slide 4: Single-Cycle Implementation code structure
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
rule doProc;
let inst = iMem.req(pc);
let dInst = decode(inst);
let rVal1 = rf.rd1(dInst.rSrc1);
let rVal2 = rf.rd2(dInst.rSrc2);
let eInst = exec(dInst, rVal1, rVal2, pc);
update rf, pc and dMem
to be explained later
extracts fields needed for execution
produces values needed to update the processor state
instantiate the state
Notes: 4

## Slide 5: SMIPS Instruction formats
Only three formats but the fields are used differently by different types of instructions
6 5 5 16
opcode rs rt immediate I-type
6 5 5 5 5 6
opcode rs rt rd shamt func R-type
6 26
opcode target J-type

## Slide 6: Instruction formats cont
Computational Instructions
Load/Store Instructions
opcode rs rt immediate rt  (rs) op immediate
6 5 5 5 5 6
0 rs rt rd 0 func rd  (rs) func (rt)
rs is the base register
rt is the destination of a Load or the source for a Store
6 5 5 16 addressing mode
opcode rs rt displacement (rs) + displacement
31 26 25 21 20 16 15 0

## Slide 7: Control Instructions
Conditional (on GPR) PC-relative branch
  target address = (offset in words)4 + (PC+4)
  range: 128 KB range
Unconditional register-indirect jumps
Unconditional absolute jumps
  target address = {PC<31:28>, target4}
  range : 256 MB range
6 5 5 16
opcode rs offset BEQZ, BNEZ
6 26
opcode target J, JAL
6 5 5 16
opcode rs JR, JALR
  jump-&-link stores PC+4 into the link register (R31)

## Slide 8: Decoding Instructions: extract fields needed for execution
decode
instruction
brComp
rDst
rSrc1
rSrc2
imm
ext
aluFunc
iType
31:26, 5:0
31:26
5:0
31:26
20:16
15:11
25:21
20:16
15:0
25:0
Type DecodedInst
Bit#(32)
IType
AluFunc
Maybe#(RIndx)
Maybe#(RIndx)
Maybe#(RIndx)
BrFunc
Maybe#(Bit#(32))
pure combinational logic: derived automatically from the high-level description
Notes: 8
Green is type…

## Slide 9: Decoded Instruction
typedef struct {
IType iType;
AluFunc aluFunc;
BrFunc brFunc;
Maybe#(FullIndx) dst;
Maybe#(FullIndx) src1;
Maybe#(FullIndx) src2;
Maybe#(Data) imm;
} DecodedInst deriving(Bits, Eq);
typedef enum {Unsupported, Alu, Ld, St, J, Jr, Br} IType deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu, LShift, RShift, Sra} AluFunc deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT} BrFunc deriving(Bits, Eq);
Instruction groups with similar executions paths
FullIndx is similar to RIndx; to be explained later
Destination register 0 behaves like an Invalid destination

## Slide 10: Decode Function
function DecodedInst decode(Bit#(32) inst);
DecodedInst dInst = ?;
let opcode = inst[ 31 : 26 ];
let rs = inst[ 25 : 21 ];
let rt = inst[ 20 : 16 ];
let rd = inst[ 15 : 11 ];
let funct = inst[ 5 : 0 ];
let imm = inst[ 15 : 0 ];
let target = inst[ 25 : 0 ];
case (opcode)
...
endcase
return dInst;
endfunction
initially undefined
opcode rs rt immediate
6 5 5 5 5 6
opcode rs rt rd shamt func
opcode target

## Slide 11: Naming the opcodes
Bit#(6) opADDIU = 6’b001001;
Bit#(6) opSLTI = 6’b001010;
Bit#(6) opLW = 6’b100011;
Bit#(6) opSW = 6’b101011;
Bit#(6) opJ = 6’b000010;
Bit#(6) opBEQ = 6’b000100;
…
Bit#(6) opFUNC = 6’b000000;
Bit#(6) fcADDU = 6’b100001;
Bit#(6) fcAND = 6’b100100;
Bit#(6) fcJR = 6’b001000;
…
Bit#(6) opRT = 6’b000001;
Bit#(6) rtBLTZ = 5’b00000;
Bit#(6) rtBGEZ = 5’b00100;
bit patterns are specified in the SMIPS ISA
Notes: Better as enum…

## Slide 12: Instruction Groupings instructions with common execution steps
case (opcode)
opADDIU, opSLTI, opSLTIU, opANDI, opORI, opXORI, opLUI: …
opLW: …
opSW: …
opJ, opJAL: …
opBEQ, opBNE, opBLEZ, opBGTZ, opRT: …
opFUNC: case (funct)
fcJR, fcJALR: …
fcSLL, fcSRL, fcSRA: …
fcSLLV, fcSRLV, fcSRAV: …
fcADDU, fcSUBU, fcAND, fcOR, fcXOR,
fcNOR, fcSLT, fcSLTU: … ;
default: // Unsupported
endcase
default: // Unsupported
endcase;
These groupings are somewhat arbitrary

## Slide 13: Decoding Instructions: I-Type ALU
opADDIU, opSLTI, opSLTIU, opANDI, opORI, opXORI, opLUI: begin
dInst.iType =
dInst.aluFunc =
dInst.dst =
dInst.src1 =
dInst.src2 =
dInst.imm =
dInst.brFunc =
end
almost like writing (Valid rt)
Alu;
case (opcode)
opADDIU, opLUI: Add;
opSLTI: Slt; opSLTIU: Sltu;
opANDI: And; opORI: Or;
opXORI: Xor;
endcase;
validReg(rt);
Valid (case(opcode)
opADDIU, opSLTI, opSLTIU: signExtend(imm);
opLUI: {imm, 16'b0};
endcase);
NT;
validReg(rs);
Invalid;

## Slide 14: Decoding Instructions: Load & Store
opLW: begin
dInst.iType = Ld;
dInst.aluFunc = Add;
dInst.rDst = validReg(rt);
dInst.rSrc1 = validReg(rs);
dInst.rSrc2 = Invalid;
dInst.imm = Valid (signExtend(imm));
dInst.brFunc = NT; end
opSW: begin
dInst.iType = St;
dInst.aluFunc = Add;
dInst.rDst = Invalid;
dInst.rSrc1 = validReg(rs);
dInst.rSrc2 = validReg(rt);
dInst.imm = Valid(signExtend(imm));
dInst.brFunc = NT; end
Notes: 14

## Slide 15: Decoding Instructions: Jump
opJ, opJAL:
begin
dInst.iType = J;
dInst.rDst = opcode==opJ ? Invalid :
validReg(31);
dInst.rSrc1 = Invalid;
dInst.rSrc2 = Invalid;
dInst.imm = Valid(zeroExtend(
{target, 2’b00}));
dInst.brFunc = AT;
end
Notes: 15

## Slide 16: Decoding Instructions: Branch
opBEQ, opBNE, opBLEZ, opBGTZ, opRT:
begin
dInst.iType = Br;
dInst.brFunc = case(opcode)
opBEQ: Eq; opBNE: Neq;
opBLEZ: Le; opBGTZ: Gt;
opRT: (rt==rtBLTZ ? Lt : Ge);
endcase;
dInst.dst = Invalid;
dInst.src1 = validReg(rs);
dInst.src2 = (opcode==opBEQ||opcode==opBNE)?
validReg(rt) : Invalid;
dInst.imm = Valid(signExtend(imm) << 2);
end
Notes: 16

## Slide 17: Decoding Instructions: opFUNC, JR
opFUNC:
case (funct)
fcJR, fcJALR:
begin
dInst.iType = Jr;
dInst.dst = funct == fcJR? Invalid:
validReg(rd);
dInst.src1 = validReg(rs);
dInst.src2 = Invalid;
dInst.imm = Invalid;
dInst.brFunc = AT;
end
fcSLL, fcSRL, fcSRA: …
JALR stores the pc in rd as opposed to JAL which stores the pc in R31
Notes: 17

## Slide 18: Decoding Instructions: opFUNC- ALU ops
fcADDU, fcSUBU, fcAND, fcOR, fcXOR, fcNOR, fcSLT, fcSLTU: begin
dInst.iType = Alu;
dInst.aluFunc = case (funct)
fcADDU: Add; fcSUBU: Sub;
fcAND : And; fcOR : Or;
fcXOR : Xor; fcNOR : Nor;
fcSLT : Slt; fcSLTU: Sltu; endcase;
dInst.dst = validReg(rd);
dInst.src1 = validReg(rs);
dInst.src2 = validReg(rt);
dInst.imm = Invalid;
dInst.brFunc = NT
end
default: // Unsupported
endcase
Notes: 18

## Slide 19: Decoding Instructions: Unsupported instruction
default:
begin
dInst.iType = Unsupported;
dInst.dst = Invalid;
dInst.src1 = Invalid;
dInst.src2 = Invalid;
dInst.imm = Invalid;
dInst.brFunc = NT;
end
endcase
Notes: 19

## Slide 20: Reading Registers
Read registers
RVal2
RVal1
RF
RSrc2
Pure combinational logic
RSrc1
Notes: 20

## Slide 21: Executing Instructions
execute
dInst
addr
brTaken
data
iType
dst
ALU
Branch
Address
pc
rVal2
rVal1
Pure combinational logic
either for memory reference or branch target
either for rf write or St
ALUBr
missPredict
Notes: 21
ALU should be split…

## Slide 22: Output of exec function
typedef struct {
IType iType;
Maybe#(FullIndx) dst;
Data data;
Addr addr;
Bool mispredict;
Bool brTaken;
} ExecInst deriving(Bits, Eq);

## Slide 23: Execute Function
function ExecInst exec(DecodedInst dInst, Data rVal1,
Data rVal2, Addr pc);
ExecInst eInst = ?;
Data aluVal2 =
let aluRes =
eInst.iType =
eInst.data =
let brTaken =
let brAddr =
eInst.brTaken =
eInst.addr =
eInst.dst =
return eInst;
endfunction
fromMaybe(rVal2, dInst.imm);
alu(rVal1, aluVal2, dInst.aluFunc);
dInst.iType;
dInst.iType==St? rVal2 :
(dInst.iType==J || dInst.iType==Jr)?
(pc+4) : aluRes;
aluBr(rVal1, rVal2, dInst.brFunc);
brAddrCalc(pc, rVal1, dInst.iType,
fromMaybe(?, dInst.imm), brTaken);
brTaken;
(dInst.iType==Ld || dInst.iType==St)?
aluRes : brAddr;
dInst.dst;

## Slide 24: Branch Address Calculation
function Addr brAddrCalc(Addr pc, Data val,
IType iType, Data imm, Bool taken);
Addr pcPlus4 = pc + 4;
Addr targetAddr = case (iType)
J : {pcPlus4[31:28], imm[27:0]};
Jr : val;
Br : (taken? pcPlus4 + imm : pcPlus4);
Alu, Ld, St, Unsupported: pcPlus4;
endcase;
return targetAddr;
endfunction
Notes: 24

## Slide 25: Single-Cycle SMIPS atomic state updates
if(eInst.iType == Ld)
eInst.data <- dMem.req(MemReq{op: Ld,
addr: eInst.addr, data: ?});
else if (eInst.iType == St) let dummy <- dMem.req(MemReq{op: St,
addr: eInst.addr, data: data});
if(isValid(eInst.dst)) rf.wr(validRegValue(eInst.dst), eInst.data);
pc <= eInst.brTaken ? eInst.addr : pc + 4;
endrule
endmodule
state updates
The whole processor is described using one rule; lots of big combinational functions
Notes: 25

## Slide 26: Processor interface
interface Proc;
method Action hostToCpu(Addr startpc);
method ActionValue#(Tuple2#(RIndx, Data)) cpuToHost;
endinterface
refers to coprocessor registers

## Slide 27: Coprocessor Registers
MIPS allows extra sets of 32-registers each to support system calls, floating point, debugging etc. These registers are known as coprocessor registers
  The registers in the nth set are written and read using instructions MTCn and MFCn, respectively
  Set 0 is used to get the results of program execution (Pass/Fail), the number of instructions executed and the cycle counts
  Type FullIndx is used to refer to the normal registers plus the coprocessor set 0 registers
  function validRegValue(FullIndx r) returns index of r
typedef Bit#(5) RIndx;
typedef enum {Normal, CopReg} RegType deriving (Bits, Eq);
typedef struct {RegType regType; RIndx idx;} FullIndx; deriving (Bits, Eq);

## Slide 28: Code with coprocessor calls
let copVal = cop.rd(validRegValue(dInst.src1)); let eInst = exec(dInst, rVal1, rVal2, pc, copVal);
cop.wr(eInst.dst, eInst.data);
write coprocessor registers (MTC0) and indicate the completion of an instruction
pass coprocessor register values to execute MFC0
We did not show these lines in our processor to avoid cluttering the slides

## Slide 29: Harvard-Style Datapath for MIPS
0x4
RegWrite
Add
Add
clk
WBSrc
MemWrite
addr
wdata
rdata
Data
Memory
we
RegDst
BSrc
ExtSel
OpCode
z
OpSel
clk
zero?
clk
addr
inst
Inst.
Memory
PC
rd1
GPRs
rs1
rs2
ws
wd
rd2
we
Imm
Ext
ALU
ALU
Control
31
PCSrc
br
rind
jabs
pc+4
old way

## Slide 30: Hardwired Control Table
Opcode | ExtSel | BSrc | OpSel | MemW | RegW | WBSrc | RegDst | PCSrc
ALU |  |  |  |  |  |  |  | 
ALUi |  |  |  |  |  |  |  | 
ALUiu |  |  |  |  |  |  |  | 
LW |  |  |  |  |  |  |  | 
SW |  |  |  |  |  |  |  | 
BEQZz=0 |  |  |  |  |  |  |  | 
BEQZz=1 |  |  |  |  |  |  |  | 
J |  |  |  |  |  |  |  | 
JAL |  |  |  |  |  |  |  | 
JR |  |  |  |  |  |  |  | 
JALR |  |  |  |  |  |  |  | 
BSrc = Reg / Imm WBSrc = ALU / Mem / PC
RegDst = rt / rd / R31 PCSrc = pc+4 / br / rind / jabs
*
*
*
no
yes
rind
PC
R31
rind
*
*
*
no
no
*
*
jabs
*
*
*
no
yes
PC
R31
jabs
*
*
*
no
no
*
*
pc+4
sExt16
*
0?
no
no
*
*
br
sExt16
*
0?
no
no
*
*
pc+4
sExt16
Imm
+
yes
no
*
*
pc+4
Imm
Op
no
yes
ALU
rt
pc+4
*
Reg
Func
no
yes
ALU
rd
sExt16
Imm
Op
pc+4
no
yes
ALU
rt
pc+4
sExt16
Imm
+
no
yes
Mem
rt
uExt16
old way