## Slide 1
Constructive Computer Architecture:
Non-Pipelined and Pipelined Processors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Single-Cycle RISC Processor
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
Datapath and control are derived automatically from a high-level rule-based description
2 read & 1 write ports
separate Instruction & Data memories
Notes: 3

## Slide 4: Single-Cycle Implementation code structure
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
rule doProc;
let inst = iMem.req(pc);
let dInst = decode(inst);
let rVal1 = rf.rd1(dInst.rSrc1);
let rVal2 = rf.rd2(dInst.rSrc2);
let eInst = exec(dInst, rVal1, rVal2, pc);
update rf, pc and dMem
produces values needed to update the processor state
instantiate the state
Notes: 4

## Slide 5: Execute Function
function ExecInst exec(DecodedInst dInst, Data rVal1,
Data rVal2, Addr pc);
ExecInst eInst = ?;
eInst.iType =
let aluVal2 =
let aluRes =
eInst.data =
let brTaken =
eInst.brTaken =
let brAddr =
eInst.addr =
eInst.dst =
return eInst;
endfunction
fromMaybe(rVal2, dInst.imm);
alu(rVal1, aluVal2, dInst.aluFunc);
dInst.iType;
dInst.iType==St? rVal2 :
(dInst.iType==J || dInst.iType==Jr)?
(pc+4) : aluRes;
aluBr(rVal1, rVal2, dInst.brFunc);
brAddrCalc(pc, rVal1, dInst.iType,
fromMaybe(?, dInst.imm), brTaken);
brTaken;
(dInst.iType==Ld || dInst.iType==St)?
aluRes : brAddr;
dInst.dst;

## Slide 6: Branch Address Calculation
function Addr brAddrCalc(Addr pc, Data val,
IType iType, Data imm, Bool taken);
Addr pcPlus4 = pc + 4;
Addr targetAddr = case (iType)
J : {pcPlus4[31:28], imm[27:0]};
Jr : val;
Br : (taken? pcPlus4 + imm : pcPlus4);
Alu, Ld, St, Unsupported: pcPlus4;
endcase;
return targetAddr;
endfunction
Notes: 6

## Slide 7: Single-Cycle SMIPS atomic state updates
if(eInst.iType == Ld)
eInst.data <- dMem.req(MemReq{op: Ld,
addr: eInst.addr, data: ?});
else if (eInst.iType == St) let dummy <- dMem.req(MemReq{op: St,
addr: eInst.addr, data: data});
if(isValid(eInst.dst)) rf.wr(validRegValue(eInst.dst), eInst.data);
pc <= eInst.brTaken ? eInst.addr : pc + 4;
endrule
endmodule
state updates
The whole processor is described using one rule; lots of big combinational functions
Notes: 7

## Slide 8: Processor interface
interface Proc;
method Action hostToCpu(Addr startpc);
method ActionValue#(Tuple2#(RIndx, Data)) cpuToHost;
endinterface
Stream of register values from the CPU

## Slide 9: Coprocessor Registers
MIPS allows extra sets of 32-registers each to support system calls, floating point, debugging etc. These registers are known as coprocessor registers
  The registers in the nth set are written and read using instructions MTCn and MFCn, respectively
  Set 0 is used to get the results of program execution (Pass/Fail), the number of instructions executed and the cycle counts
  Type FullIndx is used to refer to the normal registers plus the coprocessor set 0 registers
  function validRegValue(FullIndx r) returns index of r
typedef Bit#(5) RIndx;
typedef enum {Normal, CopReg} RegType deriving (Bits, Eq);
typedef struct {RegType regType; RIndx idx;} FullIndx; deriving (Bits, Eq);

## Slide 10: Code with coprocessor calls
let copVal = cop.rd(validRegValue(dInst.src1)); let eInst = exec(dInst, rVal1, rVal2, pc, copVal);
cop.wr(eInst.dst, eInst.data);
write coprocessor registers (MTC0) and indicate the completion of an instruction
pass coprocessor register values to execute MFC0
We did not show these lines in our processor to avoid cluttering the slides

## Slide 11: Single-Cycle SMIPS: Clock Speed
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
tClock > tM + tDEC + tRF + tALU+ tM+ tWB
We can improve the clock speed if we execute each instruction in two clock cycles
tClock > max {tM , (tDEC + tRF + tALU+ tM+ tWB )}
However, this may not improve the performance because each instruction will now take two cycles to execute
Notes: 11

## Slide 12: Structural Hazards
Sometimes multicycle implementations are necessary because of resource conflicts, aka, structural hazards
  Princeton style architectures use the same memory for instruction and data and consequently, require at least two cycles to execute Load/Store instructions
  If the register file supported less than 2 reads and one write concurrently then most instructions would take more than one cycle to execute
Usually extra registers are required to hold values between cycles

## Slide 13: Two-Cycle SMIPS
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
f2d
state
Introduce register “f2d” to hold a fetched instruction and register “state” to remember the state (fetch/execute) of the processor
Notes: 13

## Slide 14: Two-Cycle SMIPS
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Reg#(Data) f2d <- mkRegU;
Reg#(State) state <- mkReg(Fetch);
rule doFetch (state == Fetch);
let inst = iMem.req(pc);
f2d <= inst;
state <= Execute;
endrule

## Slide 15: Two-Cycle SMIPS
rule doExecute(stage==Execute);
let inst = f2d;
let dInst = decode(inst);
let rVal1 = rf.rd1(validRegValue(dInst.src1));
let rVal2 = rf.rd2(validRegValue(dInst.src2));
let eInst = exec(dInst, rVal1, rVal2, pc);
if(eInst.iType == Ld)
eInst.data <- dMem.req(MemReq{op: Ld, addr:
eInst.addr, data: ?});
else if(eInst.iType == St)
let d <- dMem.req(MemReq{op: St, addr:
eInst.addr, data: eInst.data});
if (isValid(eInst.dst))
rf.wr(validRegValue(eInst.dst), eInst.data);
pc <= eInst.brTaken ? eInst.addr : pc + 4;
state <= Fetch;
endrule endmodule
no change from single-cycle
Notes: 15

## Slide 16: Two-Cycle SMIPS: Analysis
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
fr
stage
In any given clock cycle, lot of unused hardware !
Execute
Fetch
Pipeline execution of instructions to increase the throughput
Notes: 16

## Slide 17: Problems in Instruction pipelining
Control hazard: Insti+1 is not known until Insti is at least decoded. So which instruction should be fetched?
Structural hazard: Two instructions in the pipeline may require the same resource at the same time, e.g., contention for memory
Data hazard: Insti may affect the state of the machine (pc, rf, dMem) – Insti+1must be fully cognizant of this change
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
+4
f2d
Insti
Insti+1
none of these hazards were present in the FFT pipeline

## Slide 18: Arithmetic versus Instruction pipelining
The data items in an arithmetic pipeline, e.g., FFT, are independent of each other
The entities in an instruction pipeline affect each other
  This causes pipeline stalls or requires other fancy tricks to avoid stalls
  Processor pipelines are significantly more complicated than arithmetic pipelines
sReg1
sReg2
x
inQ
f0
f1
f2
outQ

## Slide 19: The power of computers comes from the fact that the instructions in a program are not independent of each other
 must deal with hazard

## Slide 20: Control Hazards
Insti+1 is not known until Insti is at least decoded. So which instruction should be fetched?
General solution – speculate, i.e., predict the next instruction address
  requires the next-instruction-address prediction machinery; can be as simple as pc+4
  prediction machinery is usually elaborate because it dynamically learns from the past behavior of the program
What if speculation goes wrong?
  machinery to kill the wrong-path instructions, restore the correct processor state and restart the execution at the correct pc
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
+4
f2d
Insti
Insti+1

## Slide 21: Two-stage Pipelined SMIPS
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
pred
f2d
Fetch stage must predict the next instruction to fetch to have any pipelining
Fetch stage
Decode-RegisterFetch-Execute-Memory-WriteBack stage
In case of a misprediction the Execute stage must kill the mispredicted instruction in f2d
kill
misprediction
correct pc
Notes: 21

## Slide 22: Pipelining Two-Cycle SMIPS –singlerule
rule doPipeline ;
let newInst = iMem.req(pc);
let newPpc = nextAddr(pc); let newPc = ppc;
let newIr=Valid(Fetch2Decode{pc:newPc,ppc:newPpc,
inst:newIinst});
if(isValid(ir)) begin
let x = validValue(ir); let irpc = x.pc;
let ppc = x.ppc; let inst = x.inst;
let dInst = decode(inst);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, irpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin newIr = Invalid;
newPc = eInst.addr; end
end
pc <= newPc; ir <= newIr;
endrule
fetch
execute

## Slide 23: Inelastic versus Elastic pipeline
The pipeline presented is inelastic, that is, it relies on executing Fetch and Execute together or atomically
In a realistic machine, Fetch and Execute behave more asynchronously; for example memory latency or a functional unit may take variable number of cycles
If we replace ir by a FIFO (f2d) then it is possible to make the machine more elastic, that is, Fetch keeps putting instructions into f2d and Execute keeps removing and executing instructions from f2d.

## Slide 24: An elastic Two-Stage pipeline
rule doFetch ;
let inst = iMem.req(pc);
let ppc = nextAddr(pc); pc <= ppc;
f2d.enq(Fetch2Decode{pc:pc,ppc:ppc,inst:inst});
endrule
rule doExecute;
let x = f2d.first; let inpc = x.pc;
let ppc = x.ppc; let inst = x.inst;
let dInst = decode(inst);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, inpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc <= eInst.addr; f2d.clear; end
else f2d.deq;
endrule
Can these rules execute concurrently assuming the FIFO allows concurrent enq, deq and clear?
no –
double writes in pc
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 25: An elastic Two-Stage pipeline: for concurrency make pc into an EHR
rule doFetch ;
let inst = iMem.req(pc[0]);
let ppc = nextAddr(pc[0]); pc[0] <= ppc;
f2d.enq(Fetch2Decode{pc:pc[0],ppc:ppc,inst:inst});
endrule
rule doExecute;
let x = f2d.first; let inpc = x.pc;
let ppc = x.ppc; let inst = x.inst;
let dInst = decode(inst);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, inpc, ppc);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc[1] <= eInst.addr; f2d.clear; end
else f2d.deq;
endrule
These rules can execute concurrently assuming the FIFO has
(enq CF deq) and
(enq < clear)
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 26: Conflict-free FIFO with a Clear method
module mkCFFifo(Fifo#(2, t)) provisos(Bits#(t, tSz));
Ehr#(3, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(3, Bool) vb <- mkEhr(False);
rule canonicalize if(vb[2] && !va[2]);
da[2] <= db[2]; va[2] <= True; vb[2] <= False; endrule
method Action enq(t x) if(!vb[0]);
db[0] <= x; vb[0] <= True; endmethod
method Action deq if (va[0]);
va[0] <= False; endmethod
method t first if(va[0]);
return da[0]; endmethod
method Action clear;
va[1] <= False ; vb[1] <= False endmethod
endmodule
If there is only one element in the FIFO it resides in da
db da
first CF enq
deq CF enq
first < deq
enq < clear
Canonicalize must be the last rule to fire!

## Slide 27: Why canonicalize must be last rule to fire
first CF enq
deq CF enq
first < deq
enq < clear
rule foo ;
f.deq; if (p) f.clear
endrule
Consider rule foo. If p is false then canonicalize must fire after deq for proper concurrency.
If canonicalize uses EHR indices between deq and clear, then canonicalize won’t fire when p is false

## Slide 28: Correctness issue
<inst, pc, ppc>
Once Execute redirects the PC,
  no wrong path instruction should be executed
  the next instruction executed must be the redirected one
This is true for the code shown because
  Execute changes the pc and clears the FIFO atomically
  Fetch reads the pc and enqueues the FIFO atomically
Fetch
Execute
PC