## Slide 1
Constructive Computer Architecture:
Control Hazards
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Two-stage Pipelined SMIPS
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
pred
f2d
Fetch stage must predict the next instruction to fetch to have any pipelining
Fetch stage
Decode-RegisterFetch-Execute-Memory-WriteBack stage
In case of a misprediction the Execute stage must kill the mispredicted instruction in f2d
kill
misprediction
correct pc
Notes: 2

## Slide 3: Two-stage Pipelined SMIPS
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
pred
f2d
Fetch stage
Decode-RegisterFetch-Execute-Memory-WriteBack stage
kill
misprediction
correct pc
f2d must contain a Maybe type value because sometimes the fetched instruction is killed
Fetch2Decode type captures all the information that needs to be passed from Fetch to Decode, i.e.
Fetch2Decode {pc:Addr, ppc: Addr, inst:Inst}
Notes: 3

## Slide 4: Pipelining Two-Cycle SMIPS –single rule
rule doPipeline ;
let instF = iMem.req(pc);
let ppcF = nextAddr(pc); let nextPc = ppcF;
let newf2d = Valid (Fetch2Decode{pc:pc,ppc:ppcF,
inst:instF});
if(isValid(f2d)) begin
let x = fromMaybe(?,f2d); let pcD = x.pc;
let ppcD = x.ppc; let instD = x.inst;
let dInst = decode(instD);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, pcD, ppcD);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin nextPc = eInst.addr;
newf2d = Invalid; end
end
pc <= nextPc; f2d <= newf2d;
endrule
fetch
execute
these values are being redefined

## Slide 5: Inelastic versus Elastic pipeline
The pipeline presented is inelastic, that is, it relies on executing Fetch and Execute together or atomically
In a realistic machine, Fetch and Execute behave more asynchronously; for example memory latency or a functional unit may take variable number of cycles
If we replace f2d register by a FIFO then it is possible to make the machine more elastic, that is, Fetch keeps putting instructions into f2d and Execute keeps removing and executing instructions from f2d

## Slide 6: An elastic Two-Stage pipeline
rule doFetch ;
let instF = iMem.req(pc);
let ppcF = nextAddr(pc); pc <= ppcF;
f2d.enq(Fetch2Decode{pc:pc, ppc:ppcF, inst:instF});
endrule
rule doExecute;
let x = f2d.first; let pcD = x.pc;
let ppcD = x.ppc; let instD = x.inst;
let dInst = decode(instD);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, pcD, ppcD);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc <= eInst.addr; f2d.clear; end
else f2d.deq;
endrule
Can these rules execute concurrently assuming the FIFO allows concurrent enq, deq and clear?
No because of a possible double write in pc
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 7: An elastic Two-Stage pipeline: for concurrency make pc into an EHR
rule doFetch ;
let instF = iMem.req(pc[0]);
let ppcF = nextAddr(pc[0]); pc[0] <= ppcF;
f2d.enq(Fetch2Decode{pc:pc[0],ppc:ppcF,inst:inst});
endrule
rule doExecute;
let x = f2d.first; let pcD = x.pc;
let ppcD = x.ppc; let instD = x.inst;
let dInst = decode(instD);
... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, pcD, ppcD);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc[1] <= eInst.addr; f2d.clear; end
else f2d.deq;
endrule
These rules can execute concurrently assuming the FIFO has
(enq CF deq) and
(enq < clear)
Double writes in pc have been replaced by prioritized writes in pc
Notes: Fetch: reads and writes PC, enq ir
Execute: writes PC, clear and deq ir
The machine works correctly with Bypass and CF Fifos, but only CF Fifo will give us the pipelined behavior
So, Fetch < Execute in one cycle

## Slide 8: Conflict-free FIFO with a Clear method
module mkCFFifo(Fifo#(2, t)) provisos(Bits#(t, tSz));
Ehr#(3, t) da <- mkEhr(?);
Ehr#(3, Bool) va <- mkEhr(False);
Ehr#(3, t) db <- mkEhr(?);
Ehr#(3, Bool) vb <- mkEhr(False);
rule canonicalize if(vb[2] && !va[2]);
da[2] <= db[2]; va[2] <= True; vb[2] <= False; endrule
method Action enq(t x) if(!vb[0]);
db[0] <= x; vb[0] <= True; endmethod
method Action deq if (va[0]);
va[0] <= False; endmethod
method t first if(va[0]);
return da[0]; endmethod
method Action clear;
va[1] <= False ; vb[1] <= False endmethod
endmodule
If there is only one element in the FIFO it resides in da
db da
first CF enq
deq CF enq
first < deq
enq < clear
Canonicalize must be the last rule to fire!

## Slide 9: Why canonicalize must be the last rule to fire
first CF enq
deq CF enq
first < deq
enq < clear
rule foo ;
f.deq; if (p) f.clear
endrule
Consider rule foo. If p is false then canonicalize must fire after deq for proper concurrency.
If canonicalize uses EHR indices between deq and clear, then canonicalize won’t fire when p is false

## Slide 10: Correctness issue
<pc, ppc, inst>
Once Execute redirects the PC,
  no wrong path instruction should be executed
  the next instruction executed must be the redirected one
This is true for the code shown because
  Execute changes the pc and clears the FIFO atomically
  Fetch reads the pc and enqueues the FIFO atomically
Fetch
Execute
PC

## Slide 11: Killing fetched instructions
In the simple design with combinational memory we have discussed so far, the mispredicted instruction was present in the f2d. So the Execute stage can atomically
  Clear the f2d
  Set the pc to the correct target
In highly pipelined machines there can be multiple mispredicted and partially executed instructions in the pipeline; it will generally take more than one cycle to kill all such instructions
Need a more general solution then clearing the f2d FIFO

## Slide 12: Epoch: a method for managing control hazards
Add an epoch register in the processor state
The Execute stage changes the epoch whenever the pc prediction is wrong and sets the pc to the correct value
The Fetch stage associates the current epoch with every instruction when it is fetched
PC
iMem
pred
f2d
Epoch
Fetch
Execute
inst
targetPC
The epoch of the instruction is examined when it is ready to execute. If the processor epoch has changed the instruction is thrown away

## Slide 13: An epoch based solution
rule doFetch ;
let instF=iMem.req(pc[0]);
let ppcF=nextAddr(pc[0]); pc[0]<=ppcF;
f2d.enq(Fetch2Decode{pc:pc[0],ppc:ppcF,epoch:epoch,
inst:instF});
endrule
rule doExecute;
let x=f2d.first; let pcD=x.pc; let inEp=x.epoch;
let ppcD = x.ppc; let instD = x.inst;
if(inEp == epoch) begin
let dInst = decode(instD); ... register fetch ...;
let eInst = exec(dInst, rVal1, rVal2, pcD, ppcD);
...memory operation ...
...rf update ...
if (eInst.mispredict) begin
pc[1] <= eInst.addr; epoch <= epoch + 1; end
end
f2d.deq; endrule
Can these rules execute concurrently ?
yes
two values for epoch are sufficient
Notes: Fetch reads and writes PC, writes epoch and enqs ir
Execute writes PC, writes epoch and deqs ir
Fetch < Execute within the same cycle
The machine works with both CF and Bypass FIFOs for ir, but only CF Fifo gives pipelined behavior
If inEp was replaced by epoch in Execute, then Fetch and Execute can not be scheduled concurrently

## Slide 14: Discussion
Epoch based solution kills one wrong-path instruction at a time in the execute stage
It may be slow, but it is more robust in more complex pipelines, if you have multiple stages between fetch and execute or if you have outstanding instruction requests to the iMem
It requires the Execute stage to set the pc and epoch registers simultaneously which may result in a long combinational path from Execute to Fetch

## Slide 15: Decoupled Fetch and Execute
<inst, pc, ppc, epoch>
<corrected pc, new epoch>
In decoupled systems a subsystem reads and modifies only local state atomically
  In our solution, pc and epoch are read by both rules
Properly decoupled systems permit greater freedom in independent refinement of subsystems
Fetch
Execute

## Slide 16: A decoupled solution using epochs
Add fEpoch and eEpoch registers to the processor state; initialize them to the same value
The epoch changes whenever Execute detects the pc prediction to be wrong. This change is reflected immediately in eEpoch and eventually in fEpoch via a message from Execute to Fetch
Associate the fEpoch with every instruction when it is fetched
In the execute stage, reject, i.e., kill, the instruction if its epoch does not match eEpoch
fEpoch
eEpoch
fetch
execute

## Slide 17: Control Hazard resolution A robust two-rule solution
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
f2d
FIFO
FIFO
redirect
Execute sends information about the target pc to Fetch, which updates fEpoch and pc whenever it looks at the redirect PC fifo
fEpoch
eEpoch
Notes: 17

## Slide 18: Two-stage pipeline Decoupled code structure
module mkProc(Proc);
Fifo#(Fetch2Execute) f2d <- mkFifo; Fifo#(Addr) execRedirect <- mkFifo; Reg#(Bool) fEpoch <- mkReg(False); Reg#(Bool) eEpoch <- mkReg(False);
rule doFetch; let instF = iMem.req(pc); ...
f2d.enq(... instF ..., fEpoch); endrule
rule doExecute;
if(inEp == eEpoch) begin Decode and execute the instruction; update state;
In case of misprediction, execRedirect.enq(correct pc); end f2d.deq; endrule
endmodule

## Slide 19: The Fetch rule
rule doFetch;
let instF = iMem.req(pc);
if(!execRedirect.notEmpty)
begin let ppcF = nextAddrPredictor(pc);
pc <= ppcF; f2d.enq(Fetch2Execute{pc: pc, ppc: ppcF,
inst: instF, epoch: fEpoch});
end
else
begin fEpoch <= !fEpoch; pc <= execRedirect.first;
execRedirect.deq;
end endrule
pass the pc and predicted pc to the execute stage
Notice: In case of PC redirection, nothing is enqueued into f2d

## Slide 20: The Execute rule
rule doExecute; let instD = f2d.first.inst; let pcF = f2d.first.pc; let ppcD = f2d.first.ppc; let inEp = f2d.first.epoch; if(inEp == eEpoch) begin let dInst = decode(instD); let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); let eInst = exec(dInst, rVal1, rVal2, pcD, ppcD); if(eInst.iType == Ld) eInst.data <- dMem.req(MemReq{op: Ld, addr: eInst.addr, data: ?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op: St, addr: eInst.addr, data: eInst.data}); if (isValid(eInst.dst)) rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin execRedirect.enq(eInst.addr); eEpoch <= !inEp;
end end f2d.deq; endrule
exec returns a flag if there was a fetch misprediction
Can these rules execute concurrently?
yes, assuming CF FIFOs

## Slide 21: We will study more sophisticated branch prediction schemes later

## Slide 22: Consider a different two-stage pipeline
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
pred
f2d
Suppose we move the pipeline stage from Fetch to after Decode and Register fetch
Fetch
Execute, Memory, WriteBack
Insti
Insti+1
What hazards will the pipeline have?
Decode,
RegisterFetch
Control?
yes
Any other?
Notes: 22