## Slide 1
Constructive Computer Architecture:
Multistage Pipelined Processors and modular refinement
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Normal Register File
module mkRFile(RFile);
Vector#(32,Reg#(Data)) rfile <- replicateM(mkReg(0));
method Action wr(RIndx rindx, Data data);
if(rindx!=0) rfile[rindx] <= data;
endmethod
method Data rd1(RIndx rindx) = rfile[rindx];
method Data rd2(RIndx rindx) = rfile[rindx];
endmodule
{rd1, rd2} < wr
Notes: 3

## Slide 4: Bypass Register File using EHR
module mkBypassRFile(RFile);
Vector#(32,Ehr#(2, Data)) rfile <-
replicateM(mkEhr(0));
method Action wr(RIndx rindx, Data data);
if(rindex!=0) (rfile[rindex])[0] <= data;
endmethod
method Data rd1(RIndx rindx) = (rfile[rindx])[1];
method Data rd2(RIndx rindx) = (rfile[rindx])[1];
endmodule
wr < {rd1, rd2}
Notes: 4

## Slide 5: Bypass Register File with external bypassing
module mkBypassRFile(BypassRFile);
RFile rf <- mkRFile;
Fifo#(1, Tuple2#(RIndx, Data))
bypass <- mkBypassSFifo;
rule move;
let {.idx, .data} = bypass.first;
rf.wr(idx, data); bypass.deq;
endrule
method Action wr(RIndx rindx, Data data);
if(rindex!=0) bypass.enq(tuple2(rindx, data));
endmethod
method Data rd1(RIndx rindx) =
return (!bypass.search1(rindx))? rf.rd1(rindx)
: bypass.read1(rindx);
method Data rd2(RIndx rindx) =
return (!bypass.search2(rindx))? rf.rd2(rindx)
: bypass.read2(rindx);
endmodule
wr < {rd1, rd2}
rf
normal
move
rd
{rd1, rd2} < wr
Notes: 5

## Slide 6: Scoreboard implementation using searchable Fifos
module mkCFScoreboard(Scoreboard#(size));
SFifo#(size, Maybe#(RIndx), Maybe#(RIndx))
f <- mkCFSFifo(isFound);
method insert = f.enq;
method remove = f.deq;
method search1 = f.search1;
method search2 = f.search2;
endmodule
function Bool isFound
(Maybe#(RIndx) dst, Maybe#(RIndx) src);
return isValid(dst) && isValid(src) &&
(fromMaybe(?,dst)==fromMaybe(?,src));
endfunction

## Slide 7: 3-Stage-DH pipeline
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
d2e
redirect
fEpoch
eEpoch
pred
e2c
scoreboard
Exec2Commit{Maybe#(RIndx)dst, Data data};
Notes: 7

## Slide 8: 3-Stage-DH pipeline
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(1, Decode2Execute) d2e <- mkPipelineFifo;
Fifo#(1, Exec2Commit) e2c <- mkPipelineFifo;
Scoreboard#(2) sb <- mkPipelineScoreboard;
// contains two instructions
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) redirect <- mkBypassFifo;
Notes: 8

## Slide 9: 3-Stage-DH pipeline doFetch rule
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end else
begin let ppc = nextAddrPredictor(pc); let dInst = decode(inst);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2)
|| sb.search3(dInst.dst);;
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppc,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); pc <= ppc; end
end endrule
Unchanged from 2-stage

## Slide 10: 3-Stage-DH pipeline doExecute rule
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst))
rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin redirect.enq(eInst.addr); eEpoch <= !eEpoch; end end
d2e.deq; sb.remove; endrule
e2c.enq(Exec2Commit{dst:eInst.dst, data:eInst.data});
else e2c.enq(Exec2Commit{dst:Invalid, data:?});

## Slide 11: 3-Stage-DH pipeline doCommit rule
rule doCommit;
let dst = eInst.first.dst;
let data = eInst.first.data;
if(isValid(dst))
rf.wr(tuple2(fromMaybe(?,dst), data);
e2c.deq;
sb.remove;
endrule
Notes: 11

## Slide 12: Successive refinement & Modular Structure
fetch
execute
iMem
rf
CPU
decode
memory
pc
write-
back
dMem
Can we derive a multi-stage pipeline by successive refinement of a 2-stage pipeline?
fetch & decode
execute
pc
rf
CPU
d2e

## Slide 13: Architectural refinements
Separating Fetch and Decode
Replace magic memory by multicycle memory
Multicycle functional units
…
Nirav Dave, M.C. Ng, M. Pellauer, Arvind [Memocode 2010]
A design flow based on modular refinement

## Slide 14: 2-stage Processor Pipeline
Encapsulate Fetch and Execute in their own modules respectively
Pass methods of other modules as parameters
For correctness, an instruction should be deleted from sb only after rf has been updated
  remove and wr should happen atomically
  search and rd1, rd2 should happen atomically
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2

## Slide 15: Interface Arguments
Any subset of methods from a module interface can be used to define a partial interface
    interface FifoEnq#(t);
    method Action enq(t x);
    endinterface
A function can be defined to extract the desired methods from an interface
    function FifoEnq#(t) getFifoEnq(Fifo#(n, t) f); return
    interface FifoEnq#(t);
    method Action enq(t x) = f.enq(x);
    endinterface
    endfunction

## Slide 16: Modular Processor
module mkModularProc(Proc);
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkPipelineFifo;
Fifo#(Addr) redirect <- mkBypassFifo;
RFile rf <- mkBypassRFile;
Scoreboard#(1) sb <- mkPipelineScoreboard;
Fetch fetch <- mkFetch(iMem, getFifoEnq(d2e),
getFifoDeq(redirect)
getRfRead(rf),
getSbInsSearch(sb);
Execute execute <- mkExecute(dMem, getFifoDeq(d2e),
getFifoEnq(redirect),
getRfW(rf), getSbRem(sb);
endmodule
no rules – all communication takes place via method calls to shared modules
Notes: 16
Remember that an address is enqued in redirect whenever there is a misprediction. We will assume the eEpoch has been modified on a misprediction and fEpoch would be modified when pc is updated.

## Slide 17: Fetch Module
module mkFetch(Imemory iMem,
FifoEnq#(Decode2Execute) d2e,
FifoDeq#(Addr) redirect,
RegisterFileRead rf,
ScoreboardInsert sb)
Reg#(Addr) pc <- mkRegU;
Reg#(Bool) fEpoch <- mkReg(False);
rule fetch ; if(redirect.notEmpty) begin .... endrule
endmodule

## Slide 18: Fetch Module continued
rule fetch ; if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end else
begin let instF = iMem.req(pc);
let ppcF = nextAddrPredictor(pc);
let dInst = decode(instF);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppcF,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.dst); pc <= ppcF; end
end endrule
Unchanged from 2-stage

## Slide 19: Execute Module
module mkExecute(Dmemory dMem,
FifoDeq#(Decode2Execute) d2e,
FifoEnq#(Addr) redirect,
RegisterFileWrite rf,
ScoreboardInsert sb)
Reg#(Bool) eEpoch <- mkReg(False);
rule doExecute;
...
endrule
endmodule

## Slide 20: Execute Module continued
rule doExecute; let x = d2e.first; let dInstE = x.dInst;
let pcE = x.pc; let ppcE = x.ppc;
let epoch = x.epoch;
let rVal1E = x.rVal1; let rVal2E = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInstE, rVal1E, rVal2E, pcE, ppcE); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data});
if(isValid(eInst.dst))
rf.wr(fromMaybe(?, eInst.dst), eInst.data);
if(eInst.mispredict) begin redirect.enq(eInst.addr); eEpoch <= !eEpoch; end end
end d2e.deq; sb.remove;
endrule
Unchanged from 2-stage

## Slide 21: Modular refinement: Separating Fetch and Decode
fetch
iMem
rf
decode
pc

## Slide 22: Fetch Module refinement
module mkFetch(Imemory iMem,
FifoEnq#(Decode2Execute) d2e,
FifoDeq#(Addr) redirect,
RegisterFileRead rf,
ScoreboardInsert sb)
Reg#(Addr) pc <- mkRegU;
Reg#(Bool) fEpoch <- mkReg(False);
Fifo#(Fetch2Decode) f2d <- mkPipelineFifo;
rule fetch ; if(redirect.notEmpty) begin .... endrule
rule decode ; .... endrule
endmodule

## Slide 23: Fetch Module: Fetch rule
rule fetch ; if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end else
begin let instF = iMem.req(pc); let ppcF = nextAddrPredictor(pc);
f2d.enq(Fetch2Decode{pc: pc, ppc: ppcF,
inst: instF, epoch: fEpoch);
pc <= ppcF
end endrule

## Slide 24: Fetch Module: Decode rule
rule decode ; let x = f2d.first;
let instD = x.inst; let pcD = x.pc; let ppcD = x.ppc
let inEp = x.epoch
let dInst = decode(instD);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
|| sb.search3(dInst.dst);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pcD, ppc: ppcD,
dIinst: dInst, epoch: inEp;
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.dst);
f2d.deq end endrule

## Slide 25: Separate refinement
Notice our refined Fetch&Decode module should work correctly with the old Execute module or its refinements
This is a very important aspect of modular refinements

## Slide 26: Modular refinement: Replace magic memory by multicycle memory
fetch1
iMem
fetch2
pc

## Slide 27: Memory and Caches
Suppose iMem is replaced by a cache which takes 0 or 1 cycle in case of a hit and unknown number of variable cycles on a cache miss
View iMem as a request/response system and split the fetch stage into two rules – to send a req and to receive a res
PC
iMem
Decode
f2d
Epoch
Next
Addr
Pred

## Slide 28: Splitting the fetch stage
To split the fetch stage into two rules, insert a bypass FIFO’s to deal with (0,n) cycle memory response
PC
iMem
Decode
f2d
Epoch
Next
Addr
Pred
f12f2

## Slide 29: Fetch Module: 2nd refinement
module mkFetch(Imemory iMem,
FifoEnq#(Decode2Execute) d2e,
FifoDeq#(Addr) redirect,
RegisterFileRead rf,
ScoreboardInsert sb)
Reg#(Addr) pc <- mkRegU;
Reg#(Bool) fEpoch <- mkReg(False);
Fifo#(Fetch2Decode) f2d <- mkPipelineFifo;
Fifo#(Fetch2Decode) f12f2 <- mkBypassFifo;
rule fetch1 ; .... endrule
rule fetch1 ; .... endrule
rule decode ; .... endrule
endmodule
PC
iMem
f2d
Epoch
Pred
f12f2

## Slide 30: Fetch Module: Fetch1 rule
rule fetch1 ; if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end else
begin let ppcF = nextAddrPredictor(pc); pc <= ppc;
iCache.req(MemReq{op: Ld, addr: pc, data:?}); f12f2.enq(Fetch2Decoode{pc: pc, ppc: ppcF,
inst: ?, epoch: fEpoch});
end endrule
PC
iMem
f2d
Epoch
Pred
f12f2

## Slide 31: Fetch Module: Fetch2 rule
rule doFetch2;
let inst <- iCache.resp;
let x = f12f2.first;
x.inst = inst;
f12f2.deq;
f2d.enq(x);
endrule
PC
iMem
f2d
Epoch
Pred
f12f2

## Slide 32: Takeaway
Multistage pipelines are straightforward extensions of 2-stage pipelines
Modular refinement is a powerful idea; lets different teams work on different modules with only an early implementation of other modules
BSV compiler currently does not permit separate compilation of modules with interface parameters
Recursive call structure amongst modules is supported by the compiler in a limited way.
  The syntax is complicated
  Compiler detects and rejects truly cyclic method calls